KSME International Journal, Vol. 18 No. 1, pp. 1-11, 2004

A Study on the Control of an IPMC Actuator Using an Adaptive Fuzzy Algorithm

Sin-Jong Oh, Hunmo Kim*

School of Mechanical Engineering, Sungkyunkwan University,

Chunchun-dong Jangan-Gu Suwon 440-746, Korea

The Ionic Polymer Metal Composite (IPMC) is one of the electroactive polymers (EAP) that was shown to have potential application as an actuator. It bends by applying a low voltage current (1-3 V) to its surfaces when containing water. In this paper, the basic characteristics and the static & dynamic modeling of IPMC is discussed. In modeling and analysis, the equations of motion, which describe the total dynamics of the system, are driven. To control the position of the IPMC actuator, an adaptive fuzzy algorithm is used. IPMC is a time varying system because the some parameters vary with the passage of time. In this paper, the modeling and control of IPMC is introduced.

Key Words  IPMC, EAP, Adaptive Fuzzy Algorithm, FMRLC

KSME International Journal, Vol. 18 No. 1, pp. 12-19, 2004

Study on Residual Stress in Viscoelastic Thin Film Using Curvature Measurement Method

Young Tae Im, Seung Tae Choi*, Tae Sang Park

Department of Mechanical Engineering,

ME3053, KAIST, Science Town, Daejeon 305-701, Korea

Jae Hyun Kim

Micro system & Structural Mechanics Group,

KIMM (Korea Institute of Machinery and Materials),

171 Jang-dong, Yusung-ku, Daejeon 305-343, Korea

Using LSM (laser scanning method), the radius of curvature due to thermal deformation in polyimide film coated on Si substrate is measured. Since the polyimide film shows viscoelastic behavior, i.e., the modulus and deformation of the film vary with time and temperature, we estimate the relaxation modulus and the residual stresses of the polyimide film by measuring the radius of curvature and subsequently by performing viscoelastic analysis. The residual stresses relax by an amount of 10% at 100 oC and 20% at 150 oC for two hours.

Key Words  Residual Stress, Curvature, Viscoelastic, Elastic-Viscoelastic Correspondence

Principle, CTE Mismatch

KSME International Journal, Vol. 18 No. 1, pp. 20-29, 2004

Design of Elastomeric Bearing System and Analysis of it Mechanical Properties

Byung-Young Moon*, Gyung-Ju Kang, Beom-Soo Kang

Department of Aerospace Engineering, Pusan National University,

Gumjung-ku, Busan 609-735, Korea

Dae-Seung Cho

Department of Naval Architecture and Ocean Engineering, Pusan National University, Korea

This paper proposes a new type of bearing system. In this study, a method for design of on elastomeric bearing system and its mechanical property analysis are carried. Experimental and theoretical studies of the elastomeric bearings with fiber reinforcement were proved effective new lightweight bearing system. The fibers in the bearings for isolation are assumed to be flexible in extension, in contrast to the steel plates in the conventional bearing system. Several kinds of bearing systems in the form of long strips are designed, fabricated and tested. The results suggest that it is possible to produce the economical and effective fiber-reinforced elastomeric bearing that matches the behavior of a steel-reinforced bearing. Feasibility and advantages of the proposed bearings are illustrated by the application of the analytic procedure to the structure system. Results obtained here are reported to be an efficient approach with respect to bearing system and design of bearing against shock absorbing system when compared with other conventional one.

Key Words  Shock Absorbing System, Design of Elastomeric Bearing, Modeling of Bearing System, Stiffness Analysis, Shock Excitation, Energy Dissipation System

KSME International Journal, Vol. 18 No. 1, pp. 30-36, 2004

Operation Algorithm for a Parallel Hybrid Electric Vehicle with a Relatively Small Electric Motor

Kyoungcheol Oh, Donghyeon Kim

Graduate Student, School of Mechanical Engineering, Sungkyunkwan University,

300 Chunchun-dong, Suwon 440-746, Korea

Talchol Kim

Senior Research Engineer, Hyundai Motor Company,

772-1 Changduck-dong, Whasung 445-706, Korea

Chulsoo Kim

General Manager, Hyundai Motor Company,

772-1 Changduk-dong, Whasung 445-706, Korea

Hyunsoo Kim*

Professor, School of Mechanical Engineering, Sungkyunkwan University,

300 Chunchun-dong, Suwon 440-746, Korea

In this paper, operation algorithms for a parallel HEV equipped with a relatively small motor are investigated. For the HEV, the power assist and the equivalent fuel algorithms are proposed. In the power assist algorithm, an electric motor is used to assist the engine which provides the primary power source. In the equivalent fuel algorithm, the electric energy stored in the battery is considered to be an equivalent fuel, and an equivalent brake specific fuel consumption for the electric energy is proposed. From the equivalent fuel algorithm, distribution of the engine power and the motor power is determined to minimize the fuel consumption for a given battery state of charge (SOC) and a required vehicle power. It is found from the simulation results that the fuel economy and the final battery SOC depend on the motor discharge energy and it is the best way to charge the battery only by the regenerative braking, not by the engine to improve the overall fuel efficiency of the HEV with the relatively small motor.

Key Words  HEV, Fuel Economy, Power Assist Algorithm, Equivalent Fuel Algorithm

KSME International Journal, Vol. 18 No. 1, pp. 37-44, 2004

Head Slider Designs Using Approximation Methods

Sang-Joon Yoon,  Dong-Hoon Choi*

Center of Innovative Design Optimization Technology, Hanyang University,

Seoul 133-791, Korea

This paper presents an approach to optimally design the air bearing surface (ABS) of the head slider by using the approximation methods. The reduced basis concept is used to reduce the number of design variables. In the numerical calculation, the progressive quadratic response surface modeling (PQRSM) is used to handle the non-smooth and discontinuous cost function. A multi-criteria optimization problem is formulated to enhance the flying performances over the entire recording band during the steady state and track seek operations. The optimal solutions of the sliders, whose target flying heights are 12 nm and 9 nm, are automatically obtained. The flying heights during the steady state operation become closer to the target values and the flying height variations during the track seek operation are smaller than those for the initial one. The pitch and roll angles are also kept within suitable ranges over the recording band.

Key Words  Head Slider, Approximation Method, Optimun Design

KSME International Journal, Vol. 18 No. 1, pp. 45-54, 2004

H∞ Control System for Tandem Cold Mills with Roll Eccentricity

Seung-Soo Kim*

Research Center for Machine Part and Materials Processing, University of Ulsan,

29 Muger2-dong, Nam-gu 680-749, Korea

Jong-Shik Kim

School of Intelligent and Mechanical Engineering, Pusan National University,

Gumjung-gu, Busan 609-735, Korea

Soon-Yong Yang, Byung-Ryong Lee, Kyung-Kwan Ahn

School of Mechanical-Automotive Engineering, University of Ulsan,

29 Muger2-dong, Nam-gu 680-749, Korea

In order to meet the requirement for higher thickness accuracy in cold rolling processes, it is strongly desired to have high performance in control units. To meet this requirement, we have considered an output regulating control system with a roll-eccentricity estimator for each rolling stand of tandem cold mills. Considering entry thickness variation as well as roll eccentricity as the major disturbances, a synthesis of multivariable control systems is presented based on H# control theory, which can reflect the knowledge of input direction and spectrum of disturbance signals on the design. Then, to reject roll eccentricity effectively, a weight function having some poles on the imaginary axis is introduced. This leads to a non-standard H# control problem, and the design procedures for solving this problem are analytically presented. The effectiveness of the proposed control method is evaluated through computer simulations and compared to that of the conventional LQ control and feedforward control methods for roll eccentricity.

Key Words  Non-Standard H# Control, Roll Eccentricity Filter, Thickness Control, Tandem Cold Mills

KSME International Journal, Vol. 18 No. 1, pp. 55-64, 2004

An Evaluation Method of Probability of Elastic-Plastic Fracture by 2-Parameter Criterion

Tae-Sik Kim*

Major in Mechanical Engineering, Dong-A In Jae College,

22-1, Dokchon-ri, Haksan-myon, Youngam-gun, Chonnam 526-872, Korea

Han-Yong Yoon

Department of Mechanical Engineering, Mokpo National University,

61, Torim-ri, Chonggye-myon, Muan-gun, Chonnam 534-729, Korea

Myung-Hwan Lim

Training Ship, Mokpo Maritime University,

571, Jukkyo-dong, Mokpo, Chonnam 530-729, Korea

Ui-Jung Jung

Department of Mechanical Engineering, Mokpo National University,

61, Torim-ri, Chonggye-myon, Muan-gun, Chonnam 534-729, Korea

Many researchers have made a lot of progress in studying the evaluation of fracture probability of brittle materials. However, studies of fracture probability for elastic-plasticity have not been made yet. An evaluation method for fracture probability which is grafted onto a 2-parameter criterion and statistical probability analysis is not only introduced in this study, but also applied to the simple 2-dimensional model and carbon steel piping to vealuate the effect of statistical variables.

Key Words  Fracture Probability, Elastic-Plastic Fracture, 2-Parameter Criterion, Failure Assessmet Diagram, Carbon Steel Pipes

KSME International Journal, Vol. 18 No. 1, pp. 65-73, 2004

Ultrasonic Characterization on Sequences of CFRP Composites Based on Modeling and Motorized System

Kwang-Hee Im

Department of Automotive Eng., Woosuk University, Chonbuk 565-701, Korea

David K. Hsu

Center for Nondestructive Evaluation, Iowa State University, Ames, Iowa 50011, USA

Sung-Jin Song

School of Mechanical Engineering, Sungkyunkwan University, Kyonggi-do 440-746, Korea

Je-Woung Park, Jae-Ki Sim, In-Young Yang*

Factory Automation Research Center for Parts of Vehicles and School of Mechanical Engineering, Chosun University, Kwangju 501-759, Korea

Composites are a material class for which nondestructive material property characterization is as important as flaw detection. Laminates of fiber reinforced composites often possess strong in-plane elastic anisotropy attributable to the specific fiber orientation and layup sequence when waves are propagating in the thickness direction of composite laminates. So the layup orientation greatly influences its properties in a composite laminate. It could result in the part being rejected and discarded if the layup orientation of a ply is misaligned. A nondestructive technique would be very beneficial, which could be used to test the part after curing and requires less time than the optical test. Therefore a ply-by-ply vector decomposition model has been developed, simplified, and implemented for composite laminates fabricated from unidirectional plies. This model decomposes the transmission of a linearly polarized ultrasound wave into orthogonal components through each ply of a laminate. Also in order to develop these methods into practical inspection tools, motorized system have been developed for different measurement modalities for acquiring ultrasonic signals as a function of in-plane angle. It is found that high probability shows between the model and tests developed in characterizing cured layups of the laminates.

Key Words  Sequences, Composite Laminates, Ply-by-ply Vector

KSME International Journal, Vol. 18 No. 1, pp. 74-81, 2004

The Analysis of Flow-Induced Vibration and Design Improvement in KSNP Steam Generators of UCN 5, 6

Sang-Nyung Kim*, Yeon-Sik Cho

Department of Nuclear Engineering, Kyunghee University,

Seocheon-ri #1, Kiheung-up, Youngin-city, Kyung-gi-do 449-701, Korea.

The KSNP Steam Generators (Youngkwang Unit 3 and 4, Ulchin Unit 3 and 4) have a problem of U-tube fretting wear due to Flow Induced Vibration (FIV). In particular, the wear is localized and concentrated in a small area of upper part of U-bend in the Central Cavity region. The region has some conditions susceptible to the FIV, which are high flow velocity, high void fraction, and long unsupported span. Even though the FIV could be occurred by many mechanisms, the main mechanism would be fluid-elastic instability, or turbulent excitation. To remedy the problem, Eggcrate Flow Distribution Plate (EFDP) was installed in the Central Cavity region of Ulchin Unit 5 and 6 steam generators, so that it reduces the flow velocity in the region to a certain level. However, the cause of the FIV and the effectiveness of the EFDP was not thoroughly studied and checked. In this study, therefore the Stability Ratio (SR), which is the ratio of the actual velocity to the critical velocity, was compared between the value before the installation of EFDP and that after. Also the possibility of fluid-elastic instability of KSNP steam generator and the effectiveness of EFDP were checked based on the ATHOS3 code calculation and the Pettigrews experimental results. The calculated results were plotted in a fluid-elastic instability criteria-diagram (Pettigrew, 1998, Fig. 9). The plotted result showed that KSNP steam generator with EFDP had the margin of Fluid-Elastic Instability by almost 25%.

Key Words  Flow-Induced Vibration (FIV), Eggcrate Flow Distribution Plates (EFDP), Stability Ratio (SR) Fluid-Elastic Instability, Critical Velocity, Korea Standard Nuclear Plant (KSNP)

KSME International Journal, Vol. 18 No. 1, pp. 82-91, 2004

Minimum Energy Control of an S-CVT Equipped Power Transmission

Jungyun Kim*

School of Mechanical and Aerospace Engineering, Seoul National University,

Seoul 151-742, Korea

This article deals with a minimum energy control law of S-CVT connected to a dc motor. The S-CVT can smoothly transit between the forward, neutral, and reverse states without any brakes or clutches, and its compact and simple design and its relatively simple control make it particularly effective for mechanical systems in which excessively large torques are not required. And such an S-CVT equipped power transmission has the advantage of being able to operate the power sources in their regions of maximum efficiency, thereby improving the energy efficiency of the transmission system. The S-CVT was intended to primarily for use in small power capacity transmissions, thus a dc motor was considered here as the power source. We first review the structure and operating principles of the S-CVT, including experimental results of its performance. And then we describe a minimum energy control law of S-CVT connected to a dc motor. To do this, we describe the results of an analysis of the dynamics of an S-CVT equipped power transmission and the power efficiency of a DC motor. The minimum energy control design is carried out via B-spline parameterization. And we show numerical results obtained from simulations illustrate the validity of our minimum energy control design, benchmarked with a computed torque control algorithm for S-CVT.

Key Words  Minimum Energy Control, S-CVT, B-Spline Parameterization, Computed Torque Control

KSME International Journal, Vol. 18 No. 1, pp. 92-105, 2004

Path Space Approach for Planning 2D Shortest Path Based on Elliptic Workspace Geometry Mapping

Ihn Namgung*

Director, Intelligent Robot Center, Yusong-gu, Jang-Dong 48,

Daeduk college, Jungkok 3F, Daejon 305-715, Korea

A new algorithm for planning a collision-free path based on algebraic curve is developed and the concept of collision-free Path Space (PS) is introduced. This paper presents a Geometry Mapping (GM) based on two straight curves in which the intermediate connection point is organized in elliptic locus (, ). The GM produces two-dimensional PS that is used to create the shortest collision-free path. The elliptic locus of intermediate connection point has a special property in that the total distance between the focus points through a point on ellipse is the same regardless of the location of the intermediate connection point on the ellipse. Since the radial distance, , represents the total length of the path, the collision-free path can be found as the GM proceeds from #=0 (the direct path) to #=#_max(the longest path) resulting in the minimum time search. The GM of elliptic workspace (EWS) requires calculation of interference in circumferential direction only. The procedure for GM includes categorization of obstacles to reduce necessary calculation. A GM based on rectangular workspace (RWS) using Cartesian coordinate is also considered to show yet another possible GM. The transformations of PS among Circular Workspace Geometry Mapping (CWS GM), Elliptic Workspace Geometry Mapping (EWS GM), and Rectangular Workspace Geometry Mapping (RWS GM), are also considered. The simulations for the EWS GM on various computer systems are carried out to measure performance of algorithm and the results are presented.

Key Words  Robot Motion Planning, Path Space, Collision-free Path Space, Collision-free Path Planning, Geometry Mapping, Elliptic Workspace Geometry Mapping, Robot Task Planning

KSME International Journal, Vol. 18 No. 1, pp. 106-113, 2004

Fatigue Design of Various Type Spot Welded Lap Joints Using the Maximum Stress

Wonseok Jung, Dongho Bae*

Mechanical Engineering,

Sungkyunkwan University, Suwon, Kyonggi-do 440-746, Korea

Ilseon Sohn

Computer Applied Machine Design Engineering,

Osan College Osan, Kyunggi-Do 447-060, Korea

Recently, a new issue in designing spot welded structures such as automobile and train car bodies is to predict an economical fatigue design criterion. One of the most typical and traditional methods is to use a #P-N_f curve. However, since the fatigue data on the #P-N_f curve vary according to the welding conditions, materials, geometry of joint and fatigue loading conditions, it is necessary to perform the additional fatigue tests for determining a new fatigue design criterion of spot-welded lap joint having specific dimension and geometry. In this study, the stress distributions around spot welds of various spot welded lap joints such as in-plane bending type (IB type), tension shear type (TS type) and cross tension type (CT type) were numerically analyzed. Using these results, the  curves previously obtained from the fatigue tests for each type were rearranged into the ##-N^f relations with the maximum stresses at the nugget edge of the spot weld.

Key Words  Spot Welding, In-plane Bending Type Joint, Tension Shear Type Joint, Cross Tension Type Joint, Fatigue Design Criterion, Stress Concentration, Maximum Stress, Fatigue Limit

KSME International Journal, Vol. 18 No. 1, pp. 114-121, 2004

Corrosion Fatigue Characteristics in the Weld of Multi-Pass Welded A106 Gr B Steel Pipe

Dongho Bae*

School of Mechanical Engineering, Sungkyunkwan University,

Suwon, Kyonggi-do 440-746, Korea

Chul Han Kim

KNR System. Inc., Hwasung, Kyonggi-do 445-973, Korea

In order to investigate the corrosion fatigue characteristics in the weld of multi-pass welded A106 Gr B steel pipe, corrosion fatigue tests were performed under the various stress ratios

and 3.5 wt% NaCl solution at room temperature. The corrosion fatigue characteristic curves were represented using crack closure concept. The obtained results are as follows  when the

load frequency is 1.0 Hz, the crack opening point is transited in the region of K_max=20-32 MPa.m^1/2. In the low stress intensity factor range, the crack opening point is higher than            that in air. However, in the high stress intensity factor range, it is lower than that in air. In the cases of 0.1 Hz and 0.01 Hz, the crack opening point gradually decreases to K_min with K_max increase.

Key Words  Corrosion Fatigue, Multi-pass Weld, Crack Closer Concept, Crack Opening Point, Stress Intensity Factor, Electro-chemical Corrosion Characteristics, Corrosion Rate

KSME International Journal, Vol. 18 No. 1, pp. 122-131, 2004

Attitude Maneuver Control of Flexible Spacecraft by Observer-based Tracking Control

Hyochoong Bang*, Choong-Seok Oh

Division of Aerospace Engineering, KAIST

373-1, Kusong-Dong, Yousong-Gu, Daejon 305-701, Korea

A constraint equation-based control law design for large angle attitude maneuvers of flexible spacecraft is addressed in this paper. The tip displacement of the flexible spacecraft model is prescribed in the form of a constraint equation. The controller design is attempted in the way that the constraint equation is satisfied throughout the maneuver. The constraint equation leads to a two-point boundary value problem which needs backward and forward solution techniques to satisfy terminal constraints. An observer-based tracking control law takes the constraint equation as the input to the dynamic observer. The observer state is used in conjunction with the state feedback control law to have the actual system follow the observer dynamics. The observer-based tracking control law eventually turns into a stabilized system with inherent nature of robustness and disturbance rejection in LQR type control laws.

Key Words  Flexible Spacecraft Attitude Control, Constrain Equation, Tip Displacement, Two-point Boundary Value Problem, Observer-based Tracking Control Law, LQR

KSME International Journal, Vol. 18 No. 1, pp. 132-144, 2004

Local Collision Avoidance of Multiple Robots Using Avoidability Measure and Relative Distance

Nak Yong Ko*

Department Information, Control, and Instrumentation Engineering, Chosun University,

375 Seosuk-Dong, Dong-Gu, Gwangju 501-759, Korea

Dong Jin Seo

Department Control and Instrumentation Engineering, Chosun University

Koung Suk Kim

Department Mechanical Information Engineering, Chosun University, Korea

This paper presents a new method driving multiple robots to their goal position without collision. To consider the movement of the robots in a work area, we adopt the concept of avoidability measure. The avoidability measure figures the degree of how easily a robot can avoid other robots considering the velocity of the robots. To implement the concept to avoid collision among multiple robots, relative distance between the robots is proposed. The relative distance is a virtual distance between robots indicating the threat of collision between the robots. Based on the relative distance, the method calculates repulsive force against a robot from the other robots. Also, attractive force toward the goal position is calculated in terms of the relative distance. These repulsive force and attractive force are added to form the driving force for robot motion. The proposed method is simulated for several cases. The results show that the proposed method steers robots to open space anticipating the approach of other robots. In contrast, since the usual potential field method initiates avoidance motion later than the proposed method, it sometimes fails preventing collision or causes hasty motion to avoid other robots. The pro-            posed method works as a local collision-free motion coordination method in conjunction with higher level of task planning and path planning method for multiple robots to do a collaborative job.

Key Words  Relative Distance, Avoidability Measure, Motion Coordination, Multiple Robots, Collision Avoidance, Efficiency Measure

KSME International Journal, Vol. 18 No. 1, pp. 145-152, 2004

Effects of Various Baffle Designs on Acoustic Characteristics in Combustion Chamber of Liquid Rocket Engine

Chae Hoon Sohn*

Department of Aerospace Engineering, Chosun University, Gwangju 501-759, Korea

Seong-Ku Kim, Young-Mog Kim

Korea Aerospace Research Institute, POBox 113, Yusung, Daejeon 305-600, Korea

Effects of various baffle designs on acoustic characteristics in combustion chamber are numerically investigated by adopting linear acoustic analysis. A hub-blade configuration with five blades is selected as a candidate baffle and five variants of baffles with various specifications are designed depending on baffle height and hub position. As damping parameters, natural-frequency shift and damping factor are considered and the damping capacity of various baffle designs is evaluated. Increase in baffle height results in more damping capacity and the hub position affects appreciably the damping of the first radial resonant mode. Depending on baffle height, two close resonant modes could be overlapped and thereby the damping factor for one resonant mode is increased exceedingly. The present procedure based on acoustic analysis is expected to be a useful tool to predict acoustic field in combustion chamber and to design the passive control devices such as baffle and acoustic resonator.

Key Words  Baffle, Acoustic Characteristics, Damping Capacity, Resonant Modes, Combustion Chamber

KSME International Journal, Vol. 18 No. 1, pp. 153-166, 2004

Comparison of Turbulence Models in Shock-Wave/ Boundary-Layer Interaction

Sang Dug Kim

Department of Aerospace Engineering, University of Illinois at Urbana-Champaign Urbana,

IL 61801, USA

Chang Oh Kwon

Korea Institute of Industrial Technology, Incheon 404-254, Korea

Dong Joo Song*

School of Mechanical Engineering, Yeungnam University, Gyongsan 712-749, Korea

This paper presents a comparative study of a fully coupled, upwind, compressible Navier-

Stokes code with three two-equation models and the Baldwin-Lomax algebraic model in predicting transonic/supersonic flow. The k-# turbulence model of Abe performed well in predicting the pressure distributions and the velocity profiles near the flow separation over the axisymmetric bump, even though there were some discrepancies with the experimental data in the shear-stress distributions. Additionally, it is noted that this model has y* in damping functions instead of y^+. The turbulence model of Abe and Wilcox showed better agreements             in skin friction coefficient distribution with the experimental data than the other models did for a supersonic compression ramp problem. Wilcoxs model seems to be more reliable than the other models in terms of numerical stability. The two-equation models revealed that the redevelopment of the boundary layer was somewhat slow downstream of the reattachment portion.

Key Words  Turbulence Models, Shock-Wave/Boundary-Layer Interaction

CSCM method, k-# models of Abe, Bunpflow

KSME International Journal, Vol. 18 No. 1, pp. 167-172, 2004

Numerical Modeling of Turbulent Nonpremixed Lifted Flames

Hoojoong Kim, Yongmo Kim*

Department of Mechanical Engineering, Hanyang University,

17, Haengdang-Dong, Sungdong-Gu, Seoul 133-791, Korea

Kook-young Ahn

Korea Institute of Machinery and Materials

171, Jang Dong, Yusung Gu, 305-343, Daejon, Korea

The present study has focused on numerical investigation on the flame structure, flame lift-off and stabilization in the partially premixed turbulent lifted jet flames. Since the lifted jet flames have the partially premixed nature in the flow region between nozzle exit and flame base, level set approach is applied to simulate the partially premixed turbulent lifted jet flames for various fuel jet velocities and co-flow velocities. The flame stabilization mechanism and the flame structure near flame base are presented in detail. The predicted lift-off heights are compared with the measured ones.

Key Words  Lift-off, Partial Premix, Level-set Approach, Statilization

KSME International Journal, Vol. 18 No. 1, pp. 173-182, 2004

On the Large Eddy Simulation of High Prandtl Number Scalar Transport Using Dynamic Subgrid-Scale Model

Yang Na*

Center for Multidisciplinary Aerospace System Design, Department of Mechanical Engineering,

Konkuk University, Seoul 143-701, Korea

The present study investigates passive scalar transport using an eddy viscosity/diffusivity model in turbulent channel flow with Prandtl number range 1-10. Dynamic subgrid-scale model (DSM) was applied to the transport equation for passive scalar to determine the eddy diffusivity dynamically. To assess the feasibility of the DSM model applied for passive scalar, a priori test on direct numerical simulation data was conducted and the results are compared with those obtained from a large eddy simulation that uses DSM model a posteriori. As the Prandtl number increases, the discrepancy in subgrid-scale (SGS) heat flux amplifies but the shape of SGS temperature dissipation profiles shows reasonable agreement. This suggests that energy transfer between resolved and subgrid-scales are reasonably predicted regardless of the accuracy in SGS heat flux vectors. While a priori test shows that SGS turbulent Prandtl number changes significantly with Prandtl number, the actual LES results are found to be insensitive to Prandtl number away from the wall. Thus, the DSM model has some limitations in the prediction of high Prandtl number flows.

Key Words  Prandtl Number, Passive Scalar, Turbulent Flow, SGS Heat Flux, SGS Dissipation, Direct Numerical Simulation, Large Eddy Simulation

KSME International Journal, Vol. 18 No. 2, pp. 185-192, 2004

Aeroacoustic Characteristics and Noise Reduction of a Centrifugal Fan for a Vacuum Cleaner

Wan-Ho Jeon*, Ho Seon Rew, Chang-Joon Kim

Digital Appliance Research Lab. LG Electronics

327-23, Gasan-dong, Kumcheon-gu, Seoul 153-802, Korea

The aeroacoustic characteristics of a centrifugal fan for a vacuum cleaner and its noise reduc-            tion method are studied in this paper. The major noise source of a vacuum cleaner is the centrifugal fan. The impeller of the fan rotates at over 30000 rpm, and generates very high-level noise. It was revealed that the dominant noise source is the aerodynamic interaction between the rotating impeller and stationary diffuser. The directivity of acoustic pressure showed that most of the noise propagates backward direction of the fan-motor assembly. In order to reduce the high tonal sound generated from the aerodynamic interaction, unevenly pitched impeller and diffuser, and tapered impeller designs were proposed and experiments were performed. Uneven pitch design of the impeller changes the sound quality while the overall sound power level (SPL) and the performance remains similar. The effect of the tapered design of impeller was evaluated. The trailing edge of the tapered fan is inclined. This reduces the flow interaction between the rotating impeller and the stationary diffuser because of some phase shifts. The static efficiency of the new impeller design is slightly lower than the previous design. However, the overall SPL is reduced by about 4 dB(A). The SPL of the fundamental blade passing frequency (BPF) is reduced by about 6 dB(A) and the 2^nd BPF is reduced about 20 dB(A). The vacuum cleaner with the tapered impeller design produces lower noise level than the previous one, and the strong tonal sound was dramatically reduced.

Key Words  Vacuum Cleaner, Aeroacoustic Noise, Centrifugal Fan, Low Noise, Performance, Specific Noise Level

KSME International Journal, Vol. 18 No. 2, pp. 193-202, 2004

A Computer Method for the Dynamic Analysis of a System of Rigid Bodies in Plane Motion

Hazem Ali Attia*

Depertment of Mathematics, College of Science, King Saud University (Al-Qasseem Branch),

P.O.Box 237, Buraidah 81999, KSA

This paper presents a computer method for the dynamic analysis of a system of rigid bodies in plane motion. The formulation rests upon the idea of replacing a rigid body by a dynamically equivalent constrained system of particles. Newtons second law is applied to study the motion of the resulting system of particles without introducing any rotational coordinates. A velocity transformation is used to transform the equations of motion to a reduced set. For an open-chain, this process automatically eliminates all of the non-working constraint forces and leads to an efficient integration of the equations of motion. For a closed-chain, suitable joints should be cut and few cut-joints constraint equations should be included. An example of a closed-chain is used to demonstrate the generality and efficiency of the proposed method.

Key Words  Dynamic Analysis, Mechanisms, System of Rigid Bodies, Matrix Formulation, Recursive Formulation

KSME International Journal, Vol. 18 No. 2, pp. 203-210, 2004

Nonlinear Attitude Control for a Rigid Spacecraft by Feedback Linearization

Hyochoong Bang*, Jung-Shin Lee, Youn-Ju Eun

Division of Aerospace Engineering, KAIST

373-1, Kusong-Dong, Yousong-Gu, Daejon 305-701, Korea

Attitude control law design for spacecraft large angle maneuvers is investigated in this paper. The feedback linearization technique is applied to the design of a nonlinear tracking control law. The output function to be tracked is the quaternion attitude parameter. The designed control law turns out to be a combination of attitude and attitude rate tracking commands. The attitude-only output function, therefore, leads to a stable closed-loop system following the given reference trajectory. The principal advantage of the proposed method is that it is relatively easy to produce reference trajectories and associated controller.

Key Words  Spacecraft Attitude Control, Feedback Linearization, Quaternion Parameter,         Output Tracking Control, Singularity Avoidance Strategy, Sliding Mode Control

KSME International Journal, Vol. 18 No. 2, pp. 211-220, 2004

Three-Dimensional Contact Dynamic Model of the Human Knee Joint During Walking

Joung Hwan Mun*, Dae-Weon Lee

Department of Bio-Mechatronic Engineering, College of Life Science & Technology,

Sungkyunkwan University, 300 Chunchun, Jangan, Suwon, Kyunggi, 440-746, Korea

It is well known that the geometry of the articular surface has a major role in determining the position of articular contact and the lines of action for the contact forces. The contact force calculation of the knee joint under the effect of sliding and rolling is one of the most challenging issues in this field. We present a 3-D human knee joint model including sliding and rolling motions and major ligaments to calculate the lateral and medial condyle contact forces from the recovered total internal reaction force using inverse dynamic contact modeling and the Least-Square method. As results, it is believed that the patella, muscles and tendon affect a lot for the internal reaction forces at the initial heel contact stage. With increasing flexion angles during gait, the decreasing contact area is progressively shifted to the posterior direction on the tibia plateau. In addition, the medial side contact force is larger than the lateral side contact force in the knee joint during normal human walking. The total internal forces of the knee joint are reasonabe compared to previous studies.

Key Words  Digital Human Model, Gait analysis, Human Motion, Kinetics, Biomechanics

KSME International Journal, Vol. 18 No. 2, pp. 221-229, 2004

An Elastic-Plastic Stress Analysis in Silicon Carbide Fiber Reinforced Magnesium Metal Matrix Composite Beam Having Rectangular Cross Section Under Transverse Loading

Fuat OKUMUS

, Mamak, Ankara, Turkey

In this work, an elastic-plastic stress analysis has been conducted for silicon carbide fiber reinforced magnesium metal matrix composite beam. The composite beam has a rectangular cross section. The beam is cantilevered and is loaded by a single force at its free end. In solution, the composite beam is assumed perfectly plastic to simplify the investigation. An analytical solution is presented for the elastic-plastic regions. In order to verify the analytic solution results were compared with the finite element method. An rectangular element with nine nodes has been choosen. Composite plate is meshed into 48 elements and 228 nodes with simply supported and in-plane loading condations. Predictions of the stress distributions of the beam using finite elements were overall in good agreement with analytic values. Stress distributions of the composite beam are calculated with respect to its fiber orientation. Orientation angles of the fiber are chosen as 0 o , 30 o, 45 o, 60 o and 90 o. The plastic zone expands more at the upper side of the composite beam than at the lower side for 30 o, 45 o and 60 o orientation angles. Residual stress components of _x and _xy are also found in the section of the composite beam.

Key Words  Composite Beam, Elasto-Plastic Analysis, Orientation Angle, Stress Analysis

KSME International Journal, Vol. 18 No. 2, pp. 230-239, 2004

Evaluation of Thermal Deformation Model for BGA Packages Using Moire# Interferometry

Jinwon Joo*

School of Mechanical Engineering, Chungbuk National University,

Cheongju, Chungbuk, 361-763, Korea

Seungmin Cho

Department of Mechanical Engineering, University of Maryland

College Park, MD 20742, USA

A compact model approach of a network of spring elements for elastic loading is presented for the thermal deformation analysis of BGA package assembly. High-sensitivity moire inter-          ferometry is applied to evaluate and calibrated the model quantitatively. Two ball grid array (BGA) package assemblies are employed for moire experiments. For a package assembly with a small global bending, the spring model can predict the boundary conditions of the critical solder ball excellently well. For a package assembly with a large global bending, however, the relative displacements determined by spring model agree well with that by experiment after accounting for the rigid-body rotation. The shear strain results of the FEM with the input from the calibrated compact spring model agree reasonably well with the experimental data. The results imply that the combined approach of the compact spring model and the local FE analysis is an effective way to predict strains and stresses and to determine solder damage of the critical solder ball.

Key Words  Moire# Interferometry, BGA Package, Solder Ball, Compact Spring Model,

Thermomechanical Behavior, On Board Reliability

KSME International Journal, Vol. 18 No. 2, pp. 240-245, 2004

Flapwise Bending Vibration Analysis of Rotating Composite Cantilever Beams

Seung Hyun Lee, Sang Ha Shin, Hong Hee Yoo*

School of Mechanical Engineering, Hanyang University,

Haengdang-dong 17, Sungdong-gu, Seoul 133-791, Korea

A modeling method for the modal analysis of a rotating composite cantilever beam is presented in this paper. Linear differential equations of motion are derived using the assumed mode method. For the modeling, hybrid deformation variables are employed and approximated to derive the equations of motion. Symmetrical laminated composite beams are considered to obtain the numerical results. The effects of the dimensionless angular velocity, the hub radius and the fiber orientation angle on the variations of modal characteristics are investigated.

Key Words  Flapwise Bending Vibration, Composite, Fiber Angle, Rotating Contilever Beam, Natural Frequency Variation, Mode Shape Variation

KSME International Journal, Vol. 18 No. 2, pp. 246-252, 2004

Shape Optimization of Rotating Cantilever Beams Considering Their Varied Modal Characteristics

Jung Eun Cho, Hong Hee Yoo*

School of Mechanical Engineering, Hanyang University,

Haengdang-Dong 17, Sungdong-Gu, Seoul 133-791, Korea

The modal characteristics of rotating structures vary with the rotating speed. The material and the geometric properties of the structures as well as the rotating speed influence the variations of their modal characteristics. Very often, the modal characteristics of rotating structures need to be specified at some rotating speeds to meet their design requirements. In this paper, rotating cantilever beam is chosen as a design target structure. Optimization problems are formulated and solved to find the optimal shapes of rotating beams with rectangular cross section.

Key Words  Shape Optimization, Rotating Cantilever Beam, Modal Characteristics

KSME International Journal, Vol. 18 No. 2, pp. 253-261, 2004

Filtering Technique to Control Member Size in Topology Design Optimization

Tae Soo Kim, Jae Eun Kim, Je Hyun Jeong, Yoon Young Kim*

School of Mechanical and Aerospace Engineering, Seoul National University,

Shinlim-Dong, San 56-1, Kwanak-Gu, Seoul 151-742, Korea

A simple and effective filtering method to control the member size of an optimized structure is proposed for topology optimization. In the present approach, the original objective sensitivities are replaced with their relative values evaluated within a filtering area. By adjusting the size of the filtering area, the member size of an optimized structure or the level of its topological complexity can be controlled even within a given finite element mesh. In contrast to the checkerboard-free filter, the present filter focuses on high-frequency components of the sensitivities. Since the present filtering method does not add a penalty term to the objective function nor require additional constraints, it is not only efficient but also simple to implement. Mean compliance minimization and eigenfrequency maximization problems are considered to verify the effectiveness of the present approach.

Key Words  Member Size, Topology Optimization, Filter, Design Sensitivity

KSME International Journal, Vol. 18 No. 2, pp. 262-271, 2004

Study on Damping Characteristics of Hydropneumatic Suspension Unit of Tracked Vehicle

Jin-Rae Cho*, Hong-Woo Lee, Wan-Suk Yoo

School of Mechanical Engineering, Pusan National University,

Jangjeon-Dong, Kumjung-Ku, Pusan 609-735, Korea

Jin-Kyu Lee

Tong Myung Heavy Industries Co., Changwon, Kyungnam 641-050, Korea

Hydropneumatic suspension unit is an important part of tracked vehicles to absorb external impact load exerted from the non-paved road and the cannon discharge. Its absorption performance is strongly influenced by both damping and spring forces of the unit. In this paper, we numerically analyze the damping characteristics of the in-arm-type hydropneumatic suspension unit (ISU) by considering four distinct dynamic modes of the ISU damper  jounce-

loading, jounce-unloading, rebound-loading and rebound-unloading. The flow rate coefficients determining the oil flow rate through the damper orifice are decided with the help of in-             dependent experiments. The wheel reaction force, the flow rate at cracking and the damping energy are parametrically investigated with respect to the orifice diameter and the wheel motion frequency.

Key Words  ISU, Damping Characteristics, Damper Dynamic Mode, Damper Orifice, Flow Rate Coefficients, Flow Rate at Cracking, Damping Energy

KSME International Journal, Vol. 18 No. 2, pp. 272-285, 2004

Computation of Turbulent Flows and Radiated Sound From Axial Compressor Cascade

Seungbae Lee*, Hooi-Joong Kim

Department of Mechanical Engineering, Inha University, Incheon 402-751, Korea

Jin-Hwa Kim, Seung Jin Song

Department of Mechanical Engineering, Seoul National University, Seoul 151-742, Korea

The losses at off-design points from a compressor cascade occur due to the deviation from a design incidence angle at the inlet of the cascade. The self-noise from the blade cascade at off-design points comes from a separated boundary layer and vortex sheddings. If the incidence angle to the cascade increases, stalling in blades may occur and the noise level increases significantly. This study applied Large-Eddy Simulations (LES) using deductive and deductive dynamic SGS models to low Mach-number, turbulent flow with each incidence angle to the cascade ranging from -40 o to +20 o, and compared numerical predictions with measured data. It was observed that the oscillating separation bubbles attached to the suction surface do not modify wake flows dynamically for cases of negative incidence angles. However, an incidence angle greater than 8 o caused a separated vortex near the leading edge to be shed downstream and created stalling. The computed performance parameters such as drag coefficient and total pressure loss coefficient showed good agreement with experimental results. Noise from the cascade of the compressor is summarized as sound generated by a structure interacting with unsteady, turbulent flows. The hybrid method using acoustic analogy was observed to closely predict the measured overall sound powers and directivity patterns at design and off-design points of blade cascade.

Key Words  Cascade, LES, Subgrid-Scale, Aero-Acoustics, Compressor

KSME International Journal, Vol. 18 No. 2, pp. 286-293, 2004

Sensitivity of Hot Film Flow Meter in Four Stroke Gasoline Engine

Gangyoung Lee, Cha-Lee Myung, Simsoo Park*

Department of Mechanical Engineering, Korea University,

1, 5-Ka, Anam-Dong, Sungbuk-Ku, Seoul 136-701, Korea

Youngjin Cho

Daewoo Heavy Industries & Machinery LTD

The air fuel ratios of current gasoline engines are almost controlled by several air flow meters. When CVVT (Continuous Variable Valve Timing) is applied to a gasoline engine for higher engine performance, the MAP (Manifold Absolute Pressure) sensor is difficult to follow the instantaneous air fuel ratio due to the valve timing effect. Therefore, a HFM (Hot Film Flow Meter) is widely used for measuring intake air flow in this case. However, the HFMs are incapable of indicating to reverse flow, the oscillation of intake air flow has an negative effect on the precision of the HFM. Consequently, the various duct configurations in front of the air flow sensor affect the precision of HFM sensitivity. This paper mainly focused on the analysis of the reverse flow, flow fluctuation in throttle upstream and the geometry of intake system which influence the HFM measurement.

Key Words  HFM (Hot Film Flow Meter), Reverse Flow, Flow Oscillation, CVVT (Continuous Variable Valve Timing), MAP (Manifold Absolute Pressure), USFM (Ultra Sonic Flow Meter), Intake Air Duct

KSME International Journal, Vol. 18 No. 2, pp. 294-301, 2004

Study on Natural Convection in a Rectangular Enclosure With a Heating Source

Kang-Youl Bae, Hyo-Min Jeong, Han-Shik Chung*

School of Mechanical & Aerospace Engineering, Institute of Marine Industry, Gyeongsang National University, Gyeongnam 650-160, Korea

The natural convective heat transfer in a rectangular enclosure with a heating source has been studied by experiment and numerical analysis. The governing equations were solved by a finite volume method, a SIMPLE algorithm was adopted to solve a pressure term. The parameters for the numerical study are positions and surface temperatures of a heating source i.e., Y/H=0.25, 0.5, 0.75 and 11℃≤∆T≤59℃. The results of isotherms and velocity vectors have been represented, and the numerical results showed a good agreement with experimental values. Based on the numerical results, the mean Nusselt number of the rectangular enclosure wall could be expressed as a function of Grashof number.

Key Words  Heating source, Low Reynolds Number, Turbulence Model, Nusselt Number, Grashof Number

KSME International Journal, Vol. 18 No. 2, pp. 302-312, 2004

Three-Dimensional Flow Analysis and Improvement of Slip Factor Model for Forward-Curved Blades Centrifugal Fan

En-Min GUO, Kwang-Yong KIM*

Department of Mechanical Engineering, Inha University

Incheon 402-751, Korea

This work developed improved slip factor model and correction method to predict flow through impeller in forward-curved centrifugal fan. Both steady and unsteady three-dimen-sional CFD analyses were performed to validate the slip factor model and the correction method. The results show that the improved slip factor model presented in this paper could provide more accurate predictions for forward-curved centrifugal impeller than the other slip factor models since the present model takes into account the effect of blade curvature. The correction method is provided to predict mass-averaged absolute circumferential velocity at the exit of impeller by taking account of blockage effects induced by the large-scale backflow near the front plate and flow separation within blade passage. The comparison with CFD results also shows that the improved slip factor model coupled with the present correction method provides accurate predictions for mass-averaged absolute circumferential velocity at the exit of impeller near and above the flow rate of peak total pressure coefficient.

Key Words  Forward-Curved Blades Centrifugal Fan, Slip Factor, Three-Dimensional CFD, Blade Curvature, Blockage Effect

KSME International Journal, Vol. 18 No. 2, pp. 313-324, 2004

Numerical Study on the Motion of Azimuthal Vortices in Axisymmetric Rotating Flows

Yong Kweon Suh*

Division of Mechanical and Industrial System Engineering, Dong-A University,

840 Hadan-dong, Saha-gu, Busan 604-714, Korea

A rich phenomenon in the dynamics of azimuthal vortices in a circular cylinder caused by the inertial oscillation is investigated numerically at high Reynolds numbers and moderate Rossby numbers. In the actual spin-up flow where both the Ekman circulation and the bottom friction effects are included, the first appearance of a seed vortex is generated by the Ekman boun-dary-layer on the bottom wall and the subsequent roll-up near the corner bounded by the side wall. The existence of the small vortex then rapidly propagates toward the inviscid region and induces a complicated pattern in the distribution of azimuthal vorticity, i.e. inertial oscillation. The inertial oscillation however does not deteriorate the classical Ekman-pumping model in the time scale larger than that of the oscillatory motion. Motions of single vortex and a pair of vortices are further investigated under a slip boundary-condition on the solid walls. For the case of single vortex, repeated change of the vorticity sign is observed together with typical propagation of inertial waves. For the case of a pair of vortices with a two-step profile in the initial azimuthal velocity, the vortices movement toward the outer region is resisted by the crescent-

shape vortices surrounding the pair. After touching the border between the core and outer regions, the pair vortices weaken very fast.

Key Words  Rotating Flows, Inertial Oscillation, Spin-up, Circular Cylinder, Azimuthal Vortex

KSME International Journal, Vol. 18 No. 2, pp. 325-334, 2004

Dynamic Properties of Outwardly Propagating Spherical Hydrogen-Air Flames at High Temperatures and Pressures

Oh Chae Kwon*

School of Mechanical Engineering, Sungkyunkwan University,

300 Chunchun-dong, Jangan-gu, Suwon, Kyunggi-do 440-746, Korea

Computational experiments on fundamental unstretched laminar burning velocities and flame response to stretch (represented by the Markstein number) of hydrogen-air flames at high temperatures and pressures were conducted in order to understand the dynamics of the flames including hydrogen as an attractive energy carrier in conditions encountered in practical applications such as internal combustion engines. Outwardly propagating spherical premixed flames were considered for a fuel-equivalence ratio of 0.6, pressures of 5 to 50 atm, and temperatures of 298 to 1000 K. For these conditions, ratios of unstretched-to-stretched laminar burning velocities varied linearly with flame stretch (represented by the Karlovitz number), similar to the flames at normal temperature and normal to moderately elevated pressures, implying that the "local conditions" hypothesis can be extended to the practical conditions. Increasing temperatures tended to reduce tendencies toward preferential-diffusion instability behavior (increasing the Markstein number) whereas increasing pressures tended to increase tendencies toward preferential-diffusion instability behavior (decreasing the Markstein number).

Key Words  Hydrogen Flames, High Temperature and Pressure, Markstein Numbers, Laminar Burning Velocities, Preferential Diffusion, Stretch

KSME International Journal, Vol. 18 No. 3, pp. 337-346, 2004

Adaptive Model Reference Control Based on Takagi-Sugeno Fuzzy Models with Applications to Flexible Joint Manipulators

Jongbae Lee, Joon-hong Lim

School of Electrical Engineering and Computer Science, Hanyang University,

1271, Sa-1 dong, Sanglok-gu, Ansan-si, Kyunggi-do, Korea

Chang-Woo Park

Precision Machinery Research Center, Korea Electronics Technology Institute,

203-103 B/D 192, Yakdae-Dong, Wonmi-Gu, Puchon-Si, Kyunggi-Do, 420-140, Korea

Seungho Kim*

Advanced Robot Lab., Korea Atomic Energy Research Institute,

P.O.Box 105, Yuseong, Daejeon, 305-353, Korea

The control scheme using fuzzy modeling and Parallel Distributed Compensation (PDC) concept is proposed to provide asymptotic tracking of a reference signal for the flexible joint manipulators with uncertain parameters. From Lyapunov stability analysis and simulation results, the developed control law and adaptive law guarantee the boundedness of all signals in the closed-loop multi-input/multi-output system. In addition, the plant state tracks the state of the reference model asymptotically with time for any bounded reference input signal.

Key Words  Adaptive Control, Fuzzy Control, Flexible Joint Manipulator, Model Reference Control

KSME International Journal, Vol. 18 No. 3, pp. 347-356, 2004

Flexural Vibration Analysis of a Sandwich Beam Specimen with a Partially Inserted Viscoelastic Layer

Jin-Tack Park

Department of Mechanical Design and Production, Graduate School, Hanyang University,

17 Haengdang-Dong, Seongdong-ku, Seoul 133-791, Korea

Nak-Sam Choi*

Department of Mechanical Engineering, Hanyang University,

1271 Sa-1 dong, Ansan-si, Kyunggi-do 425-791, Korea

The flexural vibration characteristics of a sandwich beam system with a partially inserted viscoelastic layer were quantitatively studied using the finite element analysis in combination with the sine-sweep experiment. Asymmetric mode shapes of the flexural vibration were visualized by holographic interferometry, which agreed with those obtained by the finite element simulation. Effects of the length and the thickness of the partial viscoelastic layer on the system loss factor (ηs) and resonant frequency (fr) were significantly large for both the symmetric and asymmetric modes of the beam system.

Key Words  Sandwich Beam Specimen, Viscoelastic Layer, Sine-Sweep Test, Flexural Vibration Damping, Resonant Frequency, Modal Strain Energy Method

KSME International Journal, Vol. 18 No. 3, pp. 357-369, 2004

Fracture Analysis of Electronic IC Package in Reflow Soldering Process

Ji Hyuck Yang

Currently, Hyundai Motor Company,

772-1, Jangduk-Dong, Whasung-Si, Gyunggi-Do, 445-706, Korea

Kang Yong Lee*

School of Mechanical Engineering, Yonsei University,

SinchonDong, SeodaemoonGu, Seoul 120-749, Korea

Taek Sung Lee

Department of Mechanical Design Engineering, Korea Polytechnic University,

Shiheung City, Kyungki-do, 429-450, Korea

She-Xu Zhao

Department of Engineering Mechanics, Shanghai Jiaotong University,

Shanghai 200240, China

The purposes of the paper are to analyze the fracture phenomenon by delamination and cracking when the encapsulant of plastic IC package with polyimide coating shows viscoelastic behavior under hygrothermal loading in the IR soldering process and to suggest more reliable design conditions by the approaches of stress analysis and fracture mechanics. The model is the plastic SOJ package with the polyimide coating surrounding chip and dimpled diepad. On the package without cracks, the optimum position and thickness of polyimide coating to decrease the maximum differences of strains at the bonding surfaces of parts of the package are studied. For the model delaminated fully between the chip and the dimpled diepad, C(t)-integral values are calculated for the various design variables. Finally, the optimal values of design variables to depress the delamination and crack growth in the plastic IC package are obtained.

Key Words  Plastic IC Package, Polyimide Coating, Viscoelastic Analysis, C(t)-integral Value, Hygrothermal Loading

KSME International Journal, Vol. 18 No. 3, pp. 370-378, 2004

Development of Inspection Gauge System for Gas Pipeline

Hyung Seok Han*

Associate Professor, Div. Electronic and Electrical Information Engineering, Kyungwon University,

Sungnam, Kyunggido 461-701, Korea

Jae Jong Yu

Doctoral Student, School of Electrical Engineering and Computer Science,

Seoul National University, Seoul 151-742, Korea

Chan Gook Park

Associate Professor, School of Mechanical and Aerospace Engineering,

Seoul National University, Seoul 151-742, Korea

Jang Gyu Lee

Professor, School of Electrical Engineering and Computer Science,

Seoul National University, Seoul 151-742, Korea

An autonomous pipeline inspection gauge system has been developed for determining posi-              tion, orientation, curvature, and deformations such as dents and wrinkles of operating pipelines by Korea Gas Company and Seoul National University. The most important part of several subsystems is the Strapdown Inertial Measurement Unit (SIMU), which is integrated with velocity and distance sensors, weld detection system, and digital recording device. The Geometry Pipeline Inspection Gauge (GeoPIG) is designed to operate continuously and autonomously for a week or longer in operating gas pipelines. In this paper, the design concepts, system integration, and data processing/analysis method for the PIG will be presented. Results from the recent experiment for a 58 kilometer gas pipeline will be discussed.

Key Words  Pipeline Inspection Gauge (PIG), Navigation, Extended Kalman Filter (EKF)

KSME International Journal, Vol. 18 No. 3, pp. 379-387, 2004

A Self-Tuning PI Control System Design for the Flatness of Hot Strip in Finishing Mill Processes

Jeong Ju Choi

Department of Mechanical and Intelligent Systems Engineering, Pusan National University,

Busan 609-735, Korea

Wan Kee Hong

Research Institute of Industrial Science & Technology, Pohang 790-330, Korea

Jong Shik Kim*

School of Mechanical Engineering and RIMT, Pusan National University,

Busan 609-735, Korea

A novel flatness sensing system which is called the Flatness Sensing Inter-stand Looper (FlatSIL) system is suggested and a self-tuning PI control system using the FlatSIL is designed for improving the flatness of hot strip in finishing mill processes. The FlatSIL system measures the tension along the direction of the strip width by using segmented rolls, and the tension profile is approximated through the tension of each segmented roll. The flatness control system is operated by using the tension profile. The proposed flatness control system as far as the tension profile-measuring device works for the full strip length during the strip rolling in finishing mills. The generalized minimum variance self-tuning (GMV S-T) PI control method is applied to control the flatness of hot strip which has a design parameter as weighting factor for updating the PI gains. Optimizing the design parameter in the GMV S-T PI controller, the Robbins-Monro algorithm is used. It is shown by the computer simulation and experiment that the proposed GMV S-T PI flatness control system has better performance than the fixed PI flatness control system.

Key Words  Flatness, Hot Rolling Process, Generalized Minimum Variance Self-Tuning PI Control

KSME International Journal, Vol. 18 No. 3, pp. 388-394, 2004

Cutting Performance of Si3N4 Based SiC Ceramic Cutting Tools

Won Tae Kwon*

Department of Mechanical and Information Engineering, University of Seoul,

Seoul 130-743, Korea

Young-Wook Kim

Department of Materials Science and Engineering, University of Seoul,

Seoul 130-743, Korea

Composites of Si3N4-SiC containing up to 30 wt% of dispersed SiC particles were fabricated via hot-pressing with an oxynitride glass. To determine the effect of sintering time and SiC content on the mechanical properties and the cutting performance, the composites with fixed 8 hr-sintering time and 20 wt% SiC content were fabricated and tested. Fracture toughness of the composites increased with increasing sintering time, while the hardness increased as the SiC content increased up to 20 wt%. The hardness of the composites was relatively independent of the grain size and the sintered density. For machining heat-treated AISI4140, the insert with 20 wt% SiC sintered for 8 hr showed the longest tool life while the insert with 20 wt% SiC sintered for 12 hr showed the longest tool life for machining gray cast iron. An effort was made to relate the mechanical properties, such as hardness, fracture toughness and wear resistance coefficient with the tool life. However, no apparent relationship was found between them. It may be stated that tool life is affected by not only the mechanical properties but also other properties such as surface roughness, density, grian size and the number of the inherent defects in the inserts.

Key Words  Si3N4, SiC, cutting Tool, Mechanical Properties

KSME International Journal, Vol. 18 No. 3, pp. 395-406, 2004

Dynamics of an Axially Moving Bernoulli-Euler Beam Spectral Element Modeling and Analysis

Hyungmi Oh

Graduate School, Department of Mechanical Engineering, Inha University,

Incheon 402-751, Korea

Usik Lee*

Professor, Department of Mechanical Engineering, Inha University,

253 Yonghyun-Dong, Nam-Ku, Incheon 402-751, Korea

Dong-Hyun Park

Associate Professor, Department of Industrial Engineering, Inha University,

Incheon 402-751, Korea

The spectral element model is known to provide very accurate structural dynamic charac-             teristics, while reducing the number of degree-of-freedom to resolve the computational and cost problems. Thus, the spectral element model for an axially moving Bernoulli-Euler beam subjected to axial tension is developed in the present paper. The high accuracy of the spectral element model is then verified by comparing its solutions with the conventional finite element solutions and exact analytical solutions. The effects of the moving speed and axial tension on the vibration characteristics, wave characteristics, and the static and dynamic stabilities of a moving beam are investigated.

Key Words  Moving Beam, Vibration, Spectral Element Model, Natural Frequency,

Critical Moving Speed, Divergence, Flutter

KSME International Journal, Vol. 18 No. 3, pp. 407-418, 2004

Passive Prandtl-Meyer Expansion Flow with Homogeneous Condensation

Seung-Cheol Baek, Soon-Bum Kwon

Department of Mechanical Engineering, Kyungpook National University,

1370, Sankyuk-dong, Daegu 702-701, Korea

Heuy-Dong Kim*

School of Mechanical Engineering, Andong National University,

Songchun-dong, Andong 760-749, Korea

Prandtl-Meyer expansion flow with homogeneous condensation is investigated experiment-            ally and by numerical computations. The steady and unsteady periodic behaviors of the diabatic shock wave due to the latent heat released by condensation are considered with a view of technical application to the condensing flow through steam turbine blade passages. A passive control method using a porous wall and cavity underneath is applied to control the diabatic shock wave. Two-dimensional, compressible Navier-Stokes with the nucleation rate equation are numerically solved using a third-order TVD (Total Variation Diminishing) finite difference scheme. The computational results reproduce the measured static pressure distributions in passive and no passive Prandtl-Meyer expansion flows with condensation. From both the experimental and computational results, it is found that the magnitude of steady diabatic shock wave can be considerably reduced by the present passive control method. For no passive control, it is found that the diabatic shock wave due to the heat released by condensation oscillates periodically with a frequency of 2.40 kHz. This unsteady periodic motion of the diabatic shock wave can be completely suppressed using the present passive control method.

Key Words  Compressible Flow, Condensation, Diabatic Shock Wave, Passive Control

Prandtl-Meyer Flow

KSME International Journal, Vol. 18 No. 3, pp. 419-431, 2004

Dynamic Response of an Anti-plane Shear Crack in a Functionally Graded Piezoelectric Strip

Soon Man Kwon

Department of Mechanical Design & Manufacturing, Changwon National University,

9 Sarim-dong, Changwon, Kyongnam 641-773, Korea

Kang Yong Lee*

Department of Mechanical Engineering, Yonsei University, Seoul 120-749, Korea

The dynamic response of a cracked functionally graded piezoelectric material (FGPM) under transient anti-plane shear mechanical and in-plane electrical loads is investigated in the present paper. It is assumed that the electroelastic material properties of the FGPM vary smoothly in the form of an exponential function along the thickness of the strip. The analysis is conducted on the basis of the unified (or natural) crack boundary condition which is related to the ellipsoidal crack parameters. By using the Laplace and Fourier transforms, the problem is reduced to the solutions of Fredholm integral equations of the second kind. Numerical results for the stress intensity factor and crack sliding displacement are presented to show the influences of the elliptic crack parameters, the electric field, FGPM gradation, crack length, and electromechanical coupling coefficient.

Key Words  Transient Loads, Functionally Graded Piezoelectric Material, Permeable Crack, Impermeable Crack, Unified Crack Condition, Field Intensity Factors

KSME International Journal, Vol. 18 No. 3, pp. 432-442, 2004

Analysis of Effects of Sizes of Orifice and Pockets on the Rigidity of Hydrostatic Bearing Using Neural Network Predictor System

Fazl Canbulut, Cem Sinanoglu, Sahin Yildirim

Erciyes University, Faculty of Eng., Mechanical Engineering Department,

Kayseri, 38039, Turkey

This paper presents a neural network predictor for analysing rigidity variations of hydrostatic bearing system. The designed neural network has feedforward structure with three layers . The layers are input layer, hidden layer and output layer. Two main parameter could be considered for hydrostatic bearing system. These parameters are the size of bearing pocket and the orifice dimension. Due to importancy of these parameters, it is necessary to analyse with a suitable optimisation method such as neural network. As depicted from the results, the proposed neural predictor exactly follows experimental desired results.

Key Words  Hydrostatic Bearing, Orifice Dimension, Neural Predictor

KSME International Journal, Vol. 18 No. 3, pp. 443-452, 2004

Determination of Process Parameters in Stereolithography Using Neural Network

Eun-Dok Lee*, Jae-Hyung Sim

Department of Mechanical and Intelligent Systems Engineering, Graduate School, Pusan National University, 30 Jangjeon-dong, Geumjeong-gu, Busan 609-735, Korea

Hyeog-Jun Kweon

School of Automobile and Machine, Sorabol College, Gyeongju 780-711, Korea

In-Hwan Paik

Department of Mechanical Engineering, Pusan National University, Busan 609-735, Korea

For stereolithography process, accuracy of prototypes is related to laser power, scan speed, scan width, scan pattern, layer thickness, resin characteristics and etc. An accurate prototype is obtained by using appropriate process parameters. In order to determine these parameters, the stereolithography (SLA) machine using neural network was developed and efficiency of the developed SLA machine was compared with that of the traditional SLA. Optimum values for scan speed, hatching spacing and layer thickness improved the surface roughness and build time for the developed SLA.

Key Words  Stereolithography, Process Parameter, Neural Network, Surface Roughness, Build Time

KSME International Journal, Vol. 18 No. 3, pp. 453-459, 2004

Fabrication and AE Characteristics of TiNi/Al6061 Shape Memory Alloy Composite

Young-Chul Park*

Department of Mechanical Engineering, Donga University, Pusan 604-714, Korea

Jin-Kyung Lee

Department of Mechanical Engineering, Dongeui University, Pusan 614-714, Korea

TiNi/Al6061 shape memory alloy (SMA) composite was fabricated by hot press method to investigate the microstructure and mechanical properties. Interface bonding between TiNi reinforcement and Al matrix was observed by using SEM and EDS. Pre-strain was imposed to generate compressive residual stress inside composite. A tensile test for specimen, which underwent pre-strain, was performed at high temperature to evaluate the variation of strength and the effect of pre-strain. It was shown that interfacial reactions occurred at the bonding between matrix and fiber, creating two inter-metallic layers. And yield stress increased with the amount of pre-strain. Acoustic Emission technique was also used to nondestructively clarify the microscopic damage behavior at high temperature and the effect of pre-strain of TiNi/Al6061 SMA composite.

Key Words  Pre-Strain, Shape Memory Alloy (SMA), TiNi, Hot Press, Acoustic Emission

KSME International Journal, Vol. 18 No. 3, pp. 460-470, 2004

An ALE Finite Element Method for Baffled Fuel Container in Yawing Motion

Jin-Rae Cho*, Hong-Woo Lee, Wan-Suk Yoo, Min-Jeong Kim

School of Mechanical Engineering, Pusan National University,

Pusan 609-735, Korea

A computational analysis of engineering problems with moving domain or/and boundary according to either Lagrangian or Eulerian approach may encounter inherent numerical difficulties, the extreme mesh distortion in the former and the material boundary indistinctness in the latter. In order to overcome such defects in classical numerical approaches, the ALE (arbitrary Lagrangian Eulerian) method is widely being adopted in which the finite element mesh moves with arbitrary velocity. This paper is concerned with the ALE finite element formulation, aiming at the dynamic response analysis of baffled fuel-storage container in yawing motion, for which the coupled time integration scheme, the remeshing and smoothing algorithm and the mesh velocity determination are addressed. Numerical simulation illustrating theoretical works is also presented.

Key Words  ALE Finite Element Method, Coupled Iterative Time Integration, Remeshing and Smoothing, Newmark and Fractional Methods, Baffled Fuel Container

KSME International Journal, Vol. 18 No. 3, pp. 471-480, 2004

Statistical Simulation of Shift Force for a Manual Transmission

Joohyung Kim

Engineer, Samaung Data System,

Maetan-dong, Paldal-gu, Suwon 443-370, Korea

Sangjoon Park

Graduate Student, School of Mechanical Engineering, Sungkyunkwan University,

Chunchun-dong, Jangan-gu, Suwon 440-746, Korea

Hanlim Song

Assistant Professor, Dept. of Computer Applied Mechanical Engineering,

Ansan College of Technology, Choji-dong, Ansan 425-792, Korea

Chaehong Lim

Senior Research Engineer, Manual Transmission Engineering Team,

Hyundai Motor Company, Hwaseong-gun, Gyeonggi-do 445-855, Korea

Hyunsoo Kim*

Professor, School of Mechanical Engineering, Sungkyunkwan University,

Chunchun-dong, Jangan-gu, Suwon 440-746, Korea

Statistical simulation approaches are proposed to evaluate the shift feeling for a manual transmission. First, shift force simulator for the manual transmission is developed by considering the dynamic models of the external and internal linkage, synchronizer, and drivetrain. It is found that the shift force by the simulator shows a good correlation with the test results. Using the simulator, two kinds of statistical simulation approaches are proposed and the objective parameters that can be used to evaluate the shift feeling quantitatively are obtained. It is expected that the shift force simulator with the statistical approaches, developed in this study can be used as a useful design tool to evaluate the shift feeling in the initial design stage.

Key Words  Manual Transmission, Shift Feeling, Probability

KSME International Journal, Vol. 18 No. 3, pp. 481-490, 2004

Numerical Evaluation of Flow and Performance of Turbo Pump Inducers

Chang-Yeul Shim

Seoul National University, Turbo and Power Machinery Research Center,

Shillim-dong, Kwanak-gu, Seoul 151-742, Korea

Shin-Hyoung Kang*

School of Mechanical and Aerospace Engineering Seoul National University,

Shillim-dong, Kwanak-gu, Seoul 151-742, Korea

Steady state flow calculations are executed for turbo-pump inducers of modern design to validate the performance of Tascflow code. Hydrodynamic performance of inducers is evaluated and structure of the passage flow and leading edge recirculation are also investigated. Calculated results show good coincidence with experimental data of static pressure performance and velocity profiles over the leading edge. Upstream recirculation, tip leakage and vortex flow at the blade tip and near leading edge are main sources of pressure loss. Amount of pressure loss from the upstream to the leading edge corresponds to that of whole pressure loss through the blade passage. The viscous loss is considerably large due to the strong secondary flow. There appears more stronger leading edge recirculation for the backswept inducer, and this increases the pressure loss. However, blade loading near the leading edge is considerably reduced and cavitation inception delayed.

Key Words  Turbo Pump, Inducer, Pressure Loss, Secondary Flow, Recirculation

KSME International Journal, Vol. 18 No. 3, pp. 491-498, 2004

A Study on the Plane Couette Flow Using Micropolar Fluid Theory

Youn-Jea Kim*, Tae-An Kim

School of Mechanical Engineering, SungKyunKwan University,

300 CheonCheon-dong, Suwon 440-746, Korea

An analysis of the plane Couette flow between two parallel plates of a viscous, incompressible, micropolar fluid is presented. Especially, the effects of non-zero values of the micro-gyration boundary condition coefficient and pressure gradient on the flow fields are studied. Numerical results show that the micropolar parameter was found to have much more of an impact on the flow behaviors. It is also observed that the micro-gyration boundary condition coefficient influenced on the coefficients of skin friction and couple stress due to its different effect on the surface stress.

Key Words  Couette Flow, Micropolar Fluid, Micro-Gyration, Skin Friction, Couple Stress

KSME International Journal, Vol. 18 No. 3, pp. 499-512, 2004

Effects of a Swirling and Recirculating Flow on the Combustion Characteristics in Non-Premixed Flat Flames

Yong Ki Jeong

School of Mechanical Engineering, Pusan National University,

30 JangJeon-Dong, KumJung-Ku, Pusan 609-735, Korea

Chung Hwan Jeon

Research Institute of Mechanical Technology,

30 JangJeon-Dong, KumJung-Ku, Pusan 609-735, Korea

Young June Chang*

School of Mechanical Engineering, Pusan National University,

30 JangJeon-Dong, KumJung-Ku, Pusan 609-735, Korea

The effects of swirl intensity on non-reacting and reacting flow characteristics in a flat flame burner (FFB) with four types of swirlers were investigated. Experiments using the PIV method were conducted for several flow conditions with four swirl numbers of 0, 0.26, 0.6 and 1.24 in non-reacting flow. The results show that the strong swirling flow causes a recirculation, which has the toroidal structures, and spreads above the burner exit plane. Reacting flow characteristics such as temperature and the NO concentrations were also investigated in comparison with non-reacting flow characteristics. The mean flame temperature was measured as the function of radial distance, and the results show that the strong swirl intensity causes the mean temperature distributions to be uniform. However the mean temperature distributions at the swirl number of 0 show the typical distribution of long flames. NO concentration measurements show that the central toroidal recirculation zone caused by the strong swirl intensity results in much greater reduction in NO emissions, compared to the non-swirl condition. For classification into the flame structure interiorly, the turbulence Reynolds number and the Damkohler number have been examined at each condition. The interrelation between reacting and non-

reacting flows shows that flame structures with swirl intensity belong to a wrinkled laminar-

flame regime.

Key Words  CTRZ (Central Toroidal Recirculation Zone), Damkohler Number, FFB (Flat Flame Burner), PIV (Particle Image Velocimetry), Swirl, and Turbulence Reynolds Number

KSME International Journal, Vol. 18 No. 3, pp. 513-525, 2004

An Experimental Investigation of Heat Transfer in Forced Convective Boiling of R134a, R123 and R134a/R123 in a Horizontal Tube

Tae Woo Lim*

School of Mechanical Engineering, Pukyong National University,

San 100, Yongdang-Dong, Nam-Gu, Busan 608-739, Korea

Jun Hyo Kim

Division of Marine Engineering, Mokpo National Maritime University,

Mokpo 530-729, Korea

This paper reports an experimental study on flow boiling of pure refrigerants R134a and R123 and their mixtures in a uniformly heated horizontal tube. The flow pattern was observed through tubular sight glasses with an internal diameter of 10 mm located at the inlet and outlet of the test section. Tests were run at a pressure of 0.6 MPa in the heat flux ranges of 5-50 kW/m^2, vapor quality 0-100 percent and mass velocity of 150-600 kg/m^2s. Both in the nucleate boiling-dominant region at low quality and in the two-phase convective evaporation region at higher quality where nucleation is supposed to be fully suppressed, the heat transfer coefficient for the mixture was lower than that for an equivalent pure component with the same physical properties as the mixture. The reduction of the heat transfer coefficient in mixture is explained by such mechanisms as mass transfer resistance and non-linear variation in physical properties etc. In this study, the contribution of convective evaporation, which is obtained for pure refrigerants under the suppression of nucleate boiling, is multiplied by the composition factor by Singal et al.(1984). On the basis of Chens superposition model, a new correlation is presented for heat transfer coefficients of mixture.

Key Words  Convective Boiling, Flow Pattern, Heat Transfer, Horizontal Tube, Mixture

KSME International Journal, Vol. 18 No. 3, pp. 526-532, 2004

Pressure Drop in Motionless Mixers

Hei Cheon Yang*, Sang Kyoo Park

School of Applied Engineering, Yosu National University,

Dundeok-dong, Yeosu-si, Jeonnam 550-749, Korea

A motionless mixer consists of a straight pipe or transfer tube containing the mixing elements that are used to cut, fold, twist, and re-combine the mixing fluid. The number of elements and their shape required in any application depend on the complexity of the mixing process. The objectives of this study are to develop new motionless mixers and to perform the experimental investigation of pressure drop in order to evaluate the performance of the new ones. Glycerin is used as a mixing fluid. Pressure drop is measured using a hydraulic manometer and correlations of friction factor are proposed as a function of Re. The friction factors of Sulzer SMX mixer are in qualitative good agreement with the published data. On the average, the friction factors of SSC and YNU mixers are about 36% lower than and 6% higher than that of the Sulzer one.

Key Words  Motionless Mixer, Mixing Element, Pressure Drop, Friction Factor, Laminar Regime

KSME International Journal, Vol. 18 No. 4, pp. 535-549, 2004

Sliding Mode Control with Fuzzy Adaptive Perturbation Compensator for 6-DOF Parallel Manipulator

Min Kyu Park

Graduate School of Intelligent Mechanical Engineering, Pusan National University,

Gumjeong-ku, Busan 609-735, Korea

Min Cheol Lee*, Wan Suk Yoo

School of Mechanical Engineering, Pusan National University,

Gumjeong-ku, Busan 609-735, Korea

This paper proposes a sliding mode controller with fuzzy adaptive perturbation compensator (FAPC) to get a good control performance and reduce the chatter. The proposed algorithm can reduce the chattering because the proposed fuzzy adaptive perturbation compensator compensates the perturbation terms. The compensator computes the control input for compensating unmodeled dynamic terms and disturbance by using the observer-based fuzzy adaptive network (FAN). The weighting parameters of the compensator are updated by on-line adaptive scheme in order to minimize the estimation error and the estimation velocity error of each actuator. Therefore, the combination of sliding mode control and fuzzy adaptive network gives the robust and intelligent routine to get a good control performance. To evaluate the control performance of the proposed approach, tracking control is experimentally carried out for the hydraulic motion platform which consists of a 6-DOF parallel manipulator.

Key Words  6-DOF Parallel Manipulator, Sliding Mode Control, Fuzzy Adaptive

Perturbation Compensator, Observer-Based Fuzzy Adaptive Network

KSME International Journal, Vol. 18 No. 4, pp. 550-559, 2004

A Recursive Algorithm for Generating the Equations of Motion of Spatial Mechanical Systems with Application to the Five-Point Suspension

Hazem Ali Attia*

Department of Mathematics, College of Science, King Saud University,

(Al-Qasseem Branch), P.O.Box 237, Buraidah 81999, KSA

In this paper, a recursive formulation for generating the equations of motion of spatial mechanical systems is presented. The rigid bodies are replaced by a dynamically equivalent constrained system of particles which avoids introducing any rotational coordinates. For the open-chain system, the equations of motion are generated recursively along the serial chains using the concepts of linear and angular momenta. Closed-chain systems are transformed to open-chain systems by cutting suitable kinematic joints and introducing cut-joint constraints. The formulation is used to carry out the dynamic analysis of multi-link five-point suspension. The results of the simulation demonstrate the generality and simplicity of the proposed dynamic formulation.

Key Words  Multibody System Dynamics, Equations of Motion, System of Rigid Bodies,

Mechanisms, Machine Theory

KSME International Journal, Vol. 18 No. 4, pp. 560-572, 2004

Aeroelastic Response of an Airfoil-Flap System Exposed to Time-Dependent Disturbances

Jae-Hong Shim

Assistant Professor, Department of Control and Measurement Engineering Korea Polytechnic University,

Kyungi-do, Korea

Sungsoo Na*

Associate Professor, Corresponding Author, Department of Mechanical Engineering, Korea University,

Anam-dong, Sungbuk-ku, Seoul 136-701, Korea

Chan-Hun Chung

Department of Mechanical Engineering, Korea University,

Anam-dong, Sungbuk-ku, Seoul 136-701, Korea

Aeroelastic response and control of airfoil-flap system exposed to sonic-boom, blast and gust loads in an incompressible subsonic flowfield are addressed. Analytical analysis and pertinent numerical simulations of the aeroelastic response of 3-DOF airfoil featuring plunging-pitching-flapping coupled motion subjected to gust and explosive pressures in terms of important characteristic parameters specifying configuration envelope are presented. The comparisons of uncontrolled aeroelastic response with controlled one of the wing obtained by feedback control methodology are supplied, which is implemented through the flap torque to suppress the flutter instability and enhance the subcritical aeroelastic response to time-dependent excitations.

Key Words  Aeroelastic Response, Blast Load, Sonic-Boom, Flap, LQG

KSME International Journal, Vol. 18 No. 4, pp. 573-581, 2004

A Self-contained Wall Climbing Robot with Closed Link Mechanism

Hyoukryeol Choi*, Jaejun Park, Taehun Kang

School of Mechanical Engineering, Sungkyunkwan University,

300, Chonchon-dong, Jangan-gu, Suwon, Kyonggi-do, Korea

A self-contained wall climbing robot, called MRWALLSPECT (Multi-functional Robot for WALL inSPECTion) II, is developed. It is designed for scanning external surfaces of gas or oil tanks with small curvature in order to find defects. The robot contains all the components for navigation in itself without any external tether cable. Although it takes the basic structure of the sliding body mechanism, the robot has its original characteristic features in the kinematic design with closed link mechanism, which is enabled by adopting a simple and robust gait pattern mimicking a biological system. By employing the proposed link mechanism, the number of actuators is reduced and high force-to-weight ratio is achieved. This paper describes its mechanism design and the overall features including hardware and software components. Also, the preliminary results of experiments are given for evaluating its performances.

Key Words  Self-Contained, Wall-Climbing, MRWALLSPECT II

KSME International Journal, Vol. 18 No. 4, pp. 582-591, 2004

The Effects of Elbow Joint Angle on the Mechanical Properties of the Common Extensor Tendon of the Humeral Epicondyle

Jung Soo Han*

Department of Mechanical and System Engineering, Center for Safety and Science Technology,

Hansung University, Seoul 136-792, Korea

The purpose of this study was to determine the effects of elbow joint angle on mechanical properties, as represented by ultimate load, failure strain and elastic modulus, of bone-tendon specimens of common extensor tendon of the humeral epicondyle. Eight pairs of specimens were equally divided into two groups of 8 each, which selected arbitrarily from left or right side of each pair, positioned at 45 and 90 of elbow flexion and subjected to tension to failure in the physiological direction of the common extensor tendon. For comparison of the differences in the failure and elastic modulus between tendon and the bone-junction, data for both were evaluated individually. Significant reduction in ultimate load of bone-tendon specimens was shown to occur at 45. The values obtained from the bone-tendon junctions with regard to the failure strain were significant higher than those from tendon in both loading directions, but the largest failure strain at the bone-tendon junction was found at 45. The elastic modulus was found to decrease significantly at the bone-tendon junction when the loading direction switched from 90 to 45. Histological observation, after mechanical tensile tests, in both loading directions showed that failure occurred at the interface between tendon and uncalcified fibrocartilage in the thinnest fibrocartilage zone of the bone-tendon junction. We concluded that differences in measured mechanical properties are a consequence of varying the loading direction of the tendon across the bone-tendon specimen.

Key Words  Mechanical Properties, Common Extensor Tendon, Histological Observation, Fibrocartilage

KSME International Journal, Vol. 18 No. 4, pp. 592-596, 2004

A New Protection Strategy of Impressed Current Cathodic Protection for Ship

Jin-Seok Oh*

Division of Mechatronics Engineering, Korea Maritime University,

Dongsam-dong, Yeongdo-gu, Busan 606-791, Korea

Jong-Do Kim

Division of Marine System Engineering, Korea Maritime University,

Dongsam-dong, Yeongdo-gu, Busan 606-791, Korea

Corrosion is never avoided in the use of materials with various environments. The underwater hull is normally protected against rusting by several coatings of anti-corrosive paint. The purpose of ICCP (Impressed Current Cathodic Protection) system is to eliminate the rusting or corrosion, which occurs on metal immersed in seawater. The anode of ICCP system is controlled by an external DC source with converter. The function of anode is to conduct the protective current into seawater. The proposed algorithm includes the harmonic suppression control strategy and the optimum protection strategy and has tried to test the requirement current density for protection, the influence of voltage, the protection potential. This paper was studied the variation of potential and current density with environment factors, time and velocity, and the experimental results will be explained.

Key Words  Anode, ICCP, Corrosion, Control Strategy, Cathodic Protection

KSME International Journal, Vol. 18 No. 4, pp. 597-605, 2004

Direct Numerical Simulation of Turbulent Scalar Transport in a Channel with Wall Injection

Yang Na*

Center for Aerospace System Integration Technology, Department of Mechanical Engineering,

Konkuk University, Hwayang-dong 1, Gwangjin-gu, Seoul 143-701, Korea

Turbulent temperature field in a channel subject to strong wall injection has been investigated via direct numerical simulation technique. These flows are pertinent to internal flows inside hybrid rocket motors. A simplified model proble m where a regression process at the propellant surface is idealized by wall injection has been investigated to understand how the temperature field is modified. The effect of strong wall injection displaces thermal boundary layer away from the wall and this causes a sharp drop of friction temperature. Turbulent diffusivity and dissipation time scale for temperature field are found to show large variations in the streamwise direction under application of wall blowing. It is, thus, expected that more sophisticated turbulence models would be required to predict the disturbed temperature field accurately.

Key Words  Temperature Field, Wall Injection, Direct Numerical Simulation, Turbulent Diffusivity

KSME International Journal, Vol. 18 No. 4, pp. 606-621, 2004

Influence of Manufacturing Errors on the Dynamic Characteristics of Planetary Gear Systems

Gill-Jeong Cheon*

Division of Mechanical Engineering, Wonkwang University,

Iksan City, Jeon-Buk, 570-749, Korea

Robert G. Parker

Department fo Mechanical Engineering, The Ohio State University,

Columbus, OH 43220-1107, USA

A dynamic analysis using a hybrid finite element method was performed to characterize the effects of a number of manufacturing errors on bearing forces and critical tooth stress in the elements of a planetary gear system. Some tolerance control guidelines for managing bearing forces and critical stress are deduced from the results. The carrier indexing error for the planet assembly and planet runout error are the most critical factors in reducing the planet bearing force and maximizing load sharing, as well as in reducing the critical stress.

Key Words  Planetary Gear, Manufacturing Error, Thickness Error, Runout Error, Position Error

KSME International Journal, Vol. 18 No. 4, pp. 622-629, 2004

Effects of Elastic Energy of Thin Films on Bending of a Cantilevered Magnetostrictive Film-Substrate System

Ho-Mun Si, Chongdu Cho*, Chang-Boo Kim

Department of Mechanical Engineering, Inha University,

253 Yonghyun-Dong, Nam-Ku, Inchon, 402-751, Korea

In this paper, effects of elastic energy of magnetostrictive film on the deflection of a cantile-        vered film-substrate system are investigated. The total energy including the elastic energy of magnetostrictive film is formulated. And it is minimized to give the curvatures and the position of neutral axis of the cantilevered system. To discuss the effects of the elastic energy of film in a measured system, three magnetostrictive unimorph cantilevers and a bimorph cantilever reported elsewhere are reviewed. It is shown that the assumption, since the thickness of film is much smaller than that of substrate the film elastic energy is negligible, can cause considerable error in evaluating magnetostrictive coefficients. Not the ratio of thicknesses but elastic energies between film and substrate is also shown to play important role in making decision whether the assumption is valid or not.

Key Words  Magnetostrictive Film, Magnetostriction, Magnetostrictive Coefficient, Cantilever Actuator

KSME International Journal, Vol. 18 No. 4, pp. 630-639, 2004

Sliding Mode Controller with Sliding Perturbation Observer Based on Gain Optimization using Genetic Algorithm

Ki Sung You

Graduate School, Department of Mechanical and Intelligent Systems Engineering,

Pusan National University, Busan 609-735, Korea

Min Cheol Lee*, Wan Suk Yoo

School of Mechanical Engineering and Research Institute of Mechanical Technology,

Pusan National University, San 30, Changjeon-dong, Keumjeong-gu, Busan 609-735, Korea

The Stewart platform manipulator is a closed-kinematics chain robot manipulator that is capable of providing high structural rigidity and positional accuracy. However, this is a complex and nonlinear system, so the control performance of the system is not so good. In this paper, a new robust motion control algorithm is proposed. The algorithm uses partial state feedback for a class of nonlinear systems with modeling uncertainties and external disturbances. The major contribution is the design of a robust observer for the state and the perturbation of the Stewart platform, which is combined with a variable structure controller (VSC). The combination of controller and observer provides the robust routine called sliding mode control with sliding perturbation observer (SMCSPO). The optimal gains of SMCSPO, which is determined by nominal eigenvalues, are easily obtained by genetic algorithm. The proposed fitness function that evaluates the gain optimization is to put sliding function. The control performance of the proposed algorithm is evaluated by the simulation and experiment to apply to the Stewart platform. The results showed high accuracy and good performance.

Key Words  Sliding Perturbation Observer, Sliding Mode Control, Genetic Algorithm, Gain Optimization

KSME International Journal, Vol. 18 No. 4, pp. 640-648, 2004

Theoretical Consideration of Nondestructive Testing by use of Vertical Magnetization and Magneto-Optical Sensor

Jinyi Lee*

Division of Information & Control Measurement Engineering, Chosun University,

375 Seosuk-dong, Dong-gu, Gwangju 501-759, Korea

Tetsuo Shoji

Fracture Research Institute, Tohoku University,

Aoba-01, Aramaki-Aza, Aoba-ku, Sendai 980-8579, Japan

Dowon Seo

Department of Mechanical Design, Chonbuk University,

Duckjin 1-664-14, Chonju 561-756, Korea

This paper describes a new magnetization method for non-destructive testing with magneto-optical sensor (denoted as MO sensor) which have the following characteristic  high observation sensitivity, independence of the crack orientation, and precise imaging of a complex crack geometry such as multiple cracks. When a magnetic field is applied normally to the surface of a specimen which is significantly larger than its defects, approximately the same magnetic charge per unit area occurs on the surface of the specimen. If there is a crack in the specimen, magnetic charge per unit area has the same value at the bottom of the crack. The distribution of the vertical component of the magnetic flux density, B_Z, is almost uniform over the no-crack area (denoted as B_Z,BASE), while the magnetic flux density is smaller in the surroundings of the crack (denoted as B_Z,CRACK). If B_Z,BASE is a bit larger than the saturated magnetic flux density of the MO sensor (B_S), then small magnetic domains occur over the crack area and a large domain over the non-crack area because B_Z,CRACK is smaller than B.

Key Words  NDT (Non-Destructive Testing), MO Sensor (Magneto-Optical Sensor), Leakage Magnetic Flux (LMF), Lift-off, Faraday Effect, Vertical Magnetization, Dipole Model

KSME International Journal, Vol. 18 No. 4, pp. 649-663, 2004

Underlying Control Strategy of Human Leg Posture and Movement

Shinsuk Park*

Department of Mechanical Engineering, Keio University,

3-14-1 Hiyoshi, Kohoku-ku, Yokohama, Japan 223-8522

While a great number of studies on human motor control have provided a wide variety of viewpoints concerning the strategy of the central nervous system (CNS) in controlling limb movement, none were able to reveal the exact methods how the movement command from CNS is mapped onto the neuromuscular activity. As a preliminary study of human-machine interface design, the characteristics of human leg motion and its underlying motor control scheme are studied through experiments and simulations in this paper. The findings in this study suggest a simple open-loop motor control scheme in leg motion. As a possible candidate, an equilibrium point control model appears consistent in recreating the experimental data in numerical simulations. Based on the general leg motion analysis, the braking motion by the drivers leg is modeled.

Key Words  Human Motor Control, Equilibrium Point Control Hypothesis, Braking Motion

KSME International Journal, Vol. 18 No. 4, pp. 664-670, 2004

Successive Interactions of a Shock Wave with Serially Arranged Vortices

Se-Myong Chang*

School of Mechanical Engineering, College of Engineering, Kunsan National University,

San 68 Miryong-dong, Kunsan-shi, Chonbuk 573-701, Korea

Keun-Shik Chang

Department of Aerospace Engineering, Korea Advanced Institute of Science and Technology,

373-1 Kusong-dong, Yusong-gu, Taejon 305-701, Korea

Navier-Stokes computation based on a new simplified model is proposed to investigate the interactions of a moving shock wave with multiple vortices arranged in the serial manner. This model problem simulates shock-vortexlet interactions at the shear layer of a compressible vortex often observed in the experiment. Applying the Foppls idea, we extended the Rankins model generally used for the description of a single vortex to the multi-vortex version. The acoustic pulses accelerated and decelerated are successively generated and propagated from each shock-vortex interaction, which simply explains the genesis of eccentrically diverging acoustic waves appearing in the experimental photograph.

Key Words  Shock-Vortex Interaction, Navier-Stokes Equations, Foppls Idea, Rankin Vortex Model

KSME International Journal, Vol. 18 No. 4, pp. 671-680, 2004

Study on the Periodic Flows in a Rectangular Container Under a Background Rotation

Yong Kweon Suh*, Jae Hyun Park

School of Mechanical and Industrial System Engineering, Dong-A University,

840 Hadan-dong, Saha-gu, Pusan 604-714, Korea

Sung Kyun Kim, Young Rak Son

School of Mechanical Engineering, KunKook University,

Whayang-dong, Kwangjin-gu, Seoul 143-701, Korea

We present numerical and experimental results of the periodic flows inside a rectangular container under a background rotation. In numerical computation, a parallel-computation technique with MPI is implemented. Flow visualization and PIV measurement are also performed to obtain velocity fields at the free surface. Through a series of numerical and experi-mental works, we aim to clarify the fundamental reasons of discrepancy between the two-dimensional computation and the experimental measurement, which was detected in the previous study for the same flow model. Specifically, we check if the various assumptions prerequisite for the validity of the classical Ekman pumping law are satisfied for periodic flows under a background rotation.

Key Words  Periodic Flows, Background Rotation, Ekman Pumping, Rectangular Container

KSME International Journal, Vol. 18 No. 4, pp. 681-688, 2004

An Isothermal Temperature Source with a Large Surface Area using the Metal-Etched Microwick-Inserted Vapor Chamber Heat Spreader

Jeung Sang Go*, Kyung Chun Kim

School of Mechanical Engineering, Pusan National University,

30 Jangjeon-dong, Geumjeong-gu, Busan 609-735, Korea

For use of the thermal cycle of the biochemical fluid sample, the isothermal temperature source with a large surface area was designed, fabricated and its thermal characterization was experimentally evaluated. The comprehensive overview of the technology trend on the temperature control devices was detailed. The large surface area isothermal temperature source was realized by using the vapor chamber heat spreader. The cost-effectiveness and simple manu-facturing process were achieved by using the metal-etched wick structure. The temperature distribution was quantitatively investigated by using IR temperature imaging system at equivalent temperatures to the PCR thermal cycle. The standard deviation was measured to be within 0.7 oC for each temperature cycle. This concludes that the presented isothermal temperature source enables no temperature gradient inside bio-sample fluid. Furthormore it can be applied to the cooling of the electronic devices due to its slimness and low thermal spreading resistance.

Key Words  Isothermal Temperature, Vapor Chamber, Heat Spreader, Metal-Etched Wick

KSME International Journal, Vol. 18 No. 4, pp. 689-698, 2004

A Study on the Propagation of Measurement Uncertainties into the Result on a Turbine Performance Test

Soo-Yong Cho*, Chanwoo Park

Department of Mechanical and Aerospace Engineering Gyeongsang National University,

Jinju, Gajoa-dong 900, Gyeongnam 660-701, Korea

Uncertainties generated from the individual measured variables have an influence on the uncertainty of the experimental result through a data reduction equation. In this study, a performance test of a single stage axial type turbine is conducted, and total-to-total efficiencies are measured at the various off-design points in the low pressure and cold state. Based on an experimental apparatus, a data reduction equation for turbine efficiency is formulated and six measured variables are selected. Codes are written to calculate the efficiency, the uncertainty of the efficiency, and the sensitivity of the efficiency uncertainty by each of the measured quantities. The influence of each measured variable on the experimental result is figured out. Results show that the largest uncertainty magnification factor (UMF) value is obtained by the inlet total pressure among the six measured variables, and its value is always greater than one. The UMF values of the inlet total temperature, the torque, and the RPM are always one. The uncertainty percentage contribution (UPC) of the RPM shows the lowest influence on the uncertainty of the turbine efficiency, but the UPC of the torque has the largest influence to the result among the measured variables. These results are applied to find the correct direction for meeting an uncertainty requirement of the experimental result in the planning or development phase of experiment, and also to offer ideas for preparing a measurement system in the planning phase.

Key Words  Uncertainty, Axial Type Turbine, Uncertainty Magnification Factor, Uncertainty Percentage Contribution, Turbine Performance Test

KSME International Journal, Vol. 18 No. 4, pp. 699-708, 2004

Study on Gas Hydrates for the Solid Transportation of Natural Gas

Nam-Jin Kim

Mechanical Engineering Research Institute, Inha University,

Incheon 402-751, Korea

Chong-Bo Kim*

Department of Mechanical Engineering, Inha University,

Incheon 402-751, Korea

Natural gas hydrate typically contains 85 wt.% water and 15 wt.% natural gas, and commonly belongs to cubic structure I and II. When referred to standard conditions, 1 m^3 solid hydrate contains up to 200 m^3 of natural gas depending on pressure and temperature. Such the large volume of natural gas hydrate can be utilized to store and transport a large quantity of natural gas in a stable condition. In the present investigation, experiments were carried out for the formation of natural gas hydrate governed by pressure, temperature, gas compositions, etc. The results show that the equilibrium pressure of structure II is approximately 65% lower and the solubility is approximately 3 times higher than structure I. It is also found that for the subcooling of structure I and II of more than 9 and 11 K respectively, the hydrates are rapidly being formed. It is noted that utilizing nozzles for spraying water in the form of droplets into the natural gas dramatically reduces the hydrate formation time and increases its solubility at the same time.

Key Words  Gas Hydrates, Natural Gas, Induction Time, Cavity, Subcooling Nucleation

KSME International Journal, Vol. 18 No. 4, pp. 709-717, 2004

Combustion Characteristics of an Agricultural Diesel Engine using Biodiesel Fuel

Kyunghyun Ryu*, Youngtaig Oh

Department of Mechanical Engineering, Chonbuk National University,

Duckjin-Dong 1-664-14, Jeonju, Chonbuk 561-756, Korea

Biodiesel has great potential as an alternative fuel for diesel engines that would reduce air pollution. It is a domestically produced, renewable fuel that can be manufactured from fresh or used vegetable oils, or from animal fats. In this study, a biodiesel fuel derived from rice bran oil was tested as an alternative fuel for agricultural diesel engines. The emissions were characterized for both neat and blended biodiesel fuels, and for conventional diesel fuel. Since this biodiesel fuel contained 11% oxygen, it strongly influenced the combustion process. The use of biodiesel fuel resulted in lower carbon monoxide, carbon dioxide, and smoke emissions, without any increase in nitrous oxide emissions. The study demonstrated that biodiesel fuel could be effectively used as a renewable and environmentally innocuous fuel for agricultural diesel engines.

Key Words  Alternative Fuel, Biodiesel Fuel, Smoke, Exhaust Gas Emission, Oxygenated Fuel

KSME International Journal, Vol. 18 No. 4, pp. 718-730, 2004

Numerical Simulation of Natural Convection in Annuli with Internal Fins

Man Yeong Ha*, Joo Goo Kim

School of Mechanical Engineering, Pusan National University,

San 30, Chang Jeon Dong, Kuem Jeong Gu, Pusan 609-735, Korea

The solution for the natural convection in internally finned horizontal annuli is obtained           by using a numerical simulation of time-dependent and two-dimensional governing equations. The fins existing in annuli influence the flow pattern, temperature distribution and heat transfer rate. The variations of the fin configuration suppress or accelerate the free convective effects compared to those of the smooth tubes. The effects of fin configuration, number of fins and ratio of annulus gap width to the inner cylinder radius on the fluid flow and heat transfer in annuli are demonstrated by the distribution of the velocity vector, isotherms and streamlines. The governing equations are solved efficiently by using a parallel implementation. The technique is adopted for reduction of the computation cost. The parallelization is performed with the domain decomposition technique and message passing between sub-domains on the basis of the MPI library. The results from parallel computation reveal in consistency with those of the sequential program. Moreover, the speed-up ratio shows linearity with the number of processor.

Key Words  Natural Convection, Finned Annuli, Parallel Computing

KSME International Journal, Vol. 18 No. 5, pp. 733-741, 2004

Vibration of Initially Stressed Beam with Discretely Spaced Multiple Elastic Supports

Nam-Gyu Park*, Seong-Ki Lee, Hyeong-Koo Kim, Ki-Sung Choi

Nuclear Fuel Design Dep., KEPCO Nuclear Fuel Co. LTD.

493, Deokjin-dong, Yuseong-gu, Daejeon 305-353, Korea

Vibration behavior of an initially stressed beam on discretely spaced multiple elastic supports has been studied and a theoretical formulation of the system is derived using the variational principle. Unlike beams on an elastic foundation, discretely spaced supports can distort the beam mode shapes when the supports have rather large stiffness, i.e. usually expected beam modes cannot be obtained, but rather irregular mode shapes are observed. Conversely, irregular modes can be recovered by changing initial stress. Since support location is closely associated with the dynamic characteristics, this work also discusses eigenvalue sensitivity with respect to the support position and some numerical examples are investigated to illustrate the above findings.

Key Words  Vibration, Initial Stress, Multiple Elastic Supports

KSME International Journal, Vol. 18 No. 5, pp. 742-752, 2004

Matching of Physical Experiments and Multibody Dynamic Simulation for Large Deformation Problems

Wan-Suk Yoo*, Jeong-Han Lee, Jeong-Hyun Sohn, Su-Jin Park

CAELab, NRL, Pusan National University, Kumjung-Ku, Busan 609-735, South Korea

Oleg Dmitrochenko, Dmitri Pogorelov

Bryansk State Technical University, Bryansk 241035, Russia

Many papers have studied computer simulations of elastic bodies undergoing large deflections and large deformations. But there have not been many attempts to check the validity of the numerical formulations because the simulation results could not be matched without correct input data such as material properties and damping effects. In this paper, these values are obtained from real experiment with a high-speed camera and a data acquisition system. The simulation results with the absolute nodal coordinate formulation (ANCF) are compared with the results of real experiments. Two examples, a thin cantilever beam and a thin plate, are studied to verify whether the simulation results are well matched to experimental results.

Key Words  Large Displacements, Experiments, Simulation, Absolute Nodal Coordinate Formulation

KSME International Journal, Vol. 18 No. 5, pp. 753-761, 2004

Automatic NC-Data Generation Method for 5-axis Cutting of Turbine-Blades by Finding Safe Heel-Angles and Adaptive Path-Intervals

Cheng-Dao Piao

Graduate Student, Department of Mechanical Engineering at Chonnam National University,

300, Yongbong-Dong, Buk-Gu, Kwangju 500-757, Korea

Cheol-Soo Lee

Professor, Department of Industrial Engineering, Chonnam National University,

300, Yongbong-Dong, Buk-Gu, Kwangju 500-757, Korea

Kyu-Zong Cho

Reseacher, Department of Mechanical Engineering, Chonnam National University,

300, Yongbong-Dong, Buk-Gu, Kwangju 500-757, Korea

Gwang-Ryeol Park*

Reseacher, CSCAM Research Institute Gwangju 500-757, Korea

In this paper, an efficient method for generating 5-axis cutting data for a turbine blade is presented. The interference elimination of 5-axis cutting currently is very complicated, and it takes up a lot of time. The proposed method can generate an interference-free tool path, within an allowance range. Generating the cutting data just point to the cutting process and using it to obtain NC data by calculating the feed rate, allows us to maintain the proper feed rate of the 5-axis machine. This paper includes the algorithms for  (1) CL data generation by detecting an interference-free heel angle, (2) finding the optimal tool path interval considering the cusp-height, (3) finding the adaptive feed rate values for each cutter path, and (4) the inverse kinematics depending on the structure of the 5-axis machine, for generating the NC data.

Key Words  5-axis Cutting, Turbine Blade, Heel Angle, Interference Avoidance, Cusp-height, Tool Path Interval

KSME International Journal, Vol. 18 No. 5, pp. 762-769, 2004

Analysis of Billet Rolling in a Continuous Mill using Idle Vertical Stands

Laila S. Bayoumi

Department of Mechanical Design and Production, Cairo University, Egypt

Youngseog Lee*

Department of Mechanical Engineering, Chung Ang University,

Heuksuk-Dong, Dongjak-Gu, Seoul 156-756, Korea

An analytical approach is presented to investigate the deformation characteristics of billets in a continuous billet mill using power driven horizontal stands and idle vertical stands. The analysis is validated by comparison to the experimental results in a previously published work. The analytical results have shown that, apart from the problems of slip and buckling of billet, there are some shortcomings involved in this method. Compared to conventional rolling with all driven stands, the roll load for idle vertical stands and the rolling torque for horizontal stands are almost doubled. The billet is severely stressed within the roll-bite of idle vertical stands and the overall rolling power has increased by one third of that for conventional rolling. These shortcomings impair the feasibility of industrial application of idle vertical stand rolling method.

Key Words  Metal Hot Working, Billet Rolling, Idle Stands, Roll Pass Design

KSME International Journal, Vol. 18 No. 5, pp. 770-779, 2004

Micro Cutting of Tungsten Carbides with SEM Direct Observation Method

Heo Sung-jung*

Department of Mechanical Engineering, Doowon Technical College

678 Changwon-ri, Chuksan-myon, Ansong-si, Gyonggi-do 456-890, Korea

This paper describes the micro cutting of wear resistant tungsten carbides using PCD (Poly-Crystalline Diamond) cutting tools in performance with SEM (Scanning Electron Microscope) direct observation method. Turning experiments were also carried out on this alloy (V50) using a PCD cutting tool. One of the purposes of this study is to describe clearly the cutting mechanism of tungsten carbides and the behavior of WC particles in the deformation zone in orthogonal micro cutting. Other purposes are to achieve a systematic understanding of machining characteristics and the effects of machining parameters on cutting force, machined surface and tool wear rates by the outer turning of this alloy carried out using the PCD cutting tool during these various cutting conditions. A summary of the results are as follows  (1) From the SEM direct observation in cutting the tungsten carbide, WC particles are broken and come into contact with the tool edge directly. This causes tool wear in which portions scrape the tool in a strong manner. (2) There are two chip formation types. One is where the shear angle is comparatively small and the crack of the shear plane becomes wide. The other is a type where the shear angle is above 45 degrees and the crack of the shear plane does not widen. These differences are caused by the stress condition which gives rise to the friction at the shear plane. (3) The thrust cutting forces tend to increase more rapidly than the principal forces, as the depth of cut and the cutting speed are increased preferably in the orthogonal micro cutting. (4) The tool wear on the flank face was larger than that on the rake face in the orthogonal micro cutting. (5) Three components of cutting force in the conventional turning experiments were different in balance from ordinary cutting such as the cutting of steel or cast iron. Those expressed a large value of thrust force, principal force, and feed force. (6) From the viewpoint of high efficient cutting found within this research, a proper cutting speed was 15 m/min and a proper feed rate was 0.1 mm/rev. In this case, it was found that the tool life of a PCD tool was limited to a distance of approximately 230 m. (7) When the depth of cut was 0.1 mm, there was no influence of the feed rate on the feed force. The feed force tended to decrease, as the cutting distance was long, because the tool was worn and the tool edge retreated. (8) The main tool wear of a PCD tool in this research was due to the flank wear within the maximum value of V_max being about 260 m.

Key Words  PCD Cutting Tools, WC-Co, SEM (Scanning Electron Microscope), Micro Cutting, Direct Observation Method, Tool Wear, Cutting Force, Machined Surface

KSME International Journal, Vol. 18 No. 5, pp. 780-788, 2004

Force Transmission Analyses with Dimensionally Homogeneous Jacobian Matrices for Parallel Manipulators

Sung-Gaun Kim

Department of Mechatronics, Gwangju Institute of Science and Technology,

Gwangju 500-712, Korea

Jeha Ryu*

Department of Mechatronics, Gwangju Institute of Science and Technology,

Gwangju 500-712, Korea

To avoid the unit inconsistency problem in the conventional Jacobian matrix, new for-          mulation of a dimensionally homogeneous inverse Jacobian matrix for parallel manipulators with a planar mobile platform by using three end-effector points was presented (Kim and Ryu, 2003). This paper presents force relationships between joint forces and Cartesian forces at the three End-Effector points. The derived force relationships can then be used for analyses of the input/output force transmission. These analyses, forward and inverse force transmission analyses, depend on the singular values of the derived unit consistent Jacobian matrix. Using the proposed force relationship, a numerical example is presented for actuator size design of a 3-RRR planar parallel manipulator.

Key Words  Jacobian, Force Transmission Analysis, Parallel Manipulator

KSME International Journal, Vol. 18 No. 5, pp. 789-797, 2004

Implementation of a Piezoresistive MEMS Cantilever for Nanoscale Force Measurement in Micro/Nano Robotic Applications

Deok-Ho Kim, Byungkyu Kim*, Jong-Oh Park

Microsystem Research Center, Korea Institute of Science and Technology,

P.O.BOX 131, Cheongryang, Seoul 130-650, Korea

The nanoscale sensing and manipulation have become a challenging issue in micro/nano-robotic applications. In particular, a feedback sensor-based manipulation is necessary for realizing an efficient and reliable handling of particles under uncertain environment in a micro/nano scale. This paper presents a piezoresistive MEMS cantilever for nanoscale force measure-ment in microrobotics. A piezoresistive MEMS cantilever enables sensing of gripping and contact forces in nanonewton resolution by measuring changes in the stress-induced electrical resistances. The calibration of a piezoresistive MEMS cantilever is experimentally carried out. In addition, as part of the work on nanomanipulation with a piezoresistive MEMS cantilever, the analysis on the interaction forces between a tip and a material, and the associated mani-pulation strategies are investigated. Experiments and simulations show that a piezoresistive MEMS cantilever integrated into a microrobotic system can be effectively used in nanoscale force measurements and a sensor-based manipulation.

Key Words  Piezoresistive MEMS Cantilever, Atomic Force Microscope (AFM),

Microrobotics, Micro Force Sensing, Van der Waals Force,

Micro/Nano-manipulation

KSME International Journal, Vol. 18 No. 5, pp. 798-807, 2004

Fatigue Test of MEMS Device  a Monolithic Inkjet Print

Jun-Hyub Park*

Department of Mechatronics Engineering, College of Engineering,

Tongmyong University of Information Technology,

535 Yongdang-dong, Nam-gu, Busan 608-711, Korea

Yong Soo Oh

MEMS Lab, Samsung Advanced Institute of Technology,

P.O.Box 111, Suwon, Kyongki-Do, 440-600, Korea

A testing system was developed to improve the reliability of printhead and several printheads were tested. We developed a thermally driven monolithic inkjet printhead comprising dome-

shaped ink chambers, thin film nozzle guides, and omega-shaped heaters integrated on the top surface of each chamber. To perform a fatigue test of an inkjet printhead, the testing system automatically detects a heating failure using a Wheatstone bridge circuit. Various models were designed and tested to develop a more reliable printhead. Two design parameters of the width of reinforcing layer and heater were investigated in the test. Specially, the reinforcing layer was introduced to improve the fatigue life of printhead. The life-span of heater with a reinforcing layer was longer than that without a reinforcing layer. The wider the heater was, the longer the life of printhead was.

Key Words  Micro-Electro Mechanical Systems (MEMS), Print Head, Fatigue Test, Heater

KSME International Journal, Vol. 18 No. 5, pp. 808-813, 2004

A Study on Stress Analysis of Orthotropic Composite Cylindrical Shells with a Circular or an Elliptical Cutout

Chung-Hyun Ryu

Korea Atomic Energy Research Insitute,

150 Dukjin-dong, Yuseong-Gu, Daejeon 305-353, Korea

Young-Shin Lee*

Prof., Department of Mechanical Design Engineering, Chungnam National University,

220 Kung-dong, Youseong-Gu, Daejeon 305-764, Korea

Myoung-Hwan Choi

Department of Utilization Technology for HANARO, Korea Atomic Energy Research Insitute,

150 Dukjin-dong, Yuseong-Gu, Daejeon 305-353, Korea

Young-Wann Kim

Prof., Department of Mechanical Engineering, Yosu National University,

Yosu, Chonnam 550-749, Korea

The stress analysis on orthotropic composite cylindrical shells with one circular or one elliptical cutout subjected to an axial force is carried out by using an analytical and experimental method. The composite cylindrical shell governing equation of the Donnells type is applied to this study and all results are presented by the stress concentration factor. The stress concentration factor is defined as the ratio of the stress on the region around a cutout to the nominal stress of the shell. The stress concentration factor is classified into the circumferential stress concentration factors and the radial stress concentration factors due to the cylindrical coordinate of which the origin is the center of a cutout. The considered loading condition is only axial tension loading condition. In this study, thus, the maximum stress is induced on perpendicular region against axial direction, on the coordinate. Various cutout sizes are expressed using the radius ratio, θ=±π/2, which is the radius of a cutout over one of the cylindrical shell. Experimental results are obtained using strain gages, which are attached around a cutout of the cylindrical shell. As the result from this study, the stress concentration around a cutout can be predicted by using the analytical method for an orthotropic composite cylindrical shell having a circular or an elliptical cutout.

Key Words  Cutout, Stress Concentration Factor (SCF), Radius Ratio

KSME International Journal, Vol. 18 No. 5, pp. 814-819, 2004

Adaptive Parallel Decomposition for Multidisciplinary Design

Hyung-Wook Park

Research Engineer, R & D Division for Hyundai Motor Company,

772-1 Changduk-Dong, Hwasung-Si, Kynnggi-Do, Korea

Se J. Lee

Associate Professor, Department of Mechanical Engineering,

The University of Seoul, Seoul 130-743, Korea

Hyun-Seop Lee

Research Assistant, the Center of Innovative Design Optimization Technology, Hanyang University,

17 Haengdang-Dong, Sungdong-Gu, Seoul 133-791, Korea

Dong-Hoon Choi*

Director, the Center of Innovative Design Optimization Technology Hanyang University,

17 Haengdang-Dong, Sungdong-Gu, Seoul 133-791, Korea

The conceptual design of a rotorcraft system involves many different analysis disciplines. The decomposition of such a system into several subsystems can make analysis and design more efficient in terms of the total computation time. Adaptive parallel decomposition makes the structure of the overall design problem suitable to apply the multidisciplinary design optimization methodologies and it can exploit parallel computing. This study proposes a decomposition method which adaptively determines the number and sequence of analyses in each sub-problem corresponding to the available number of processors in parallel. A rotorcraft design problem is solved and as a result, the adaptive parallel decomposition method shows better performance than other previous methods for the selected design problem.

Key Words  Parallel Decomposition, Scheduling, Rotorcraft Design, Multidisciplinary Design Optimization (MDO)

KSME International Journal, Vol. 18 No. 5, pp. 820-829, 2004

An Experimental Study on the Temperature Distribution in IRWST

Sang-Nyung Kim*

Department of Nuclear Engineering, Kyunghee University Seocheon-ri #1,

Kiheung-up, Youngin-city, Kyung-ggi-do 449-701, Korea

The In-Containment Refueling Water Storage Tank (IRWST), one of the design improve-           ments applied to the APR-1400, has a function to condense the high enthalpy fluid discharged from the Reactor Coolant System (RCS). The condensation of discharged fluid by the tank water drives the tank temperature high and causes oscillatory condensation. Also if the tank cooling water temperature approaches the saturated state, the steam bubble may escape from the water uncondensed. These oscillatory condensation and bubble escape would burden the undue load to the tank structure, pressurize the tank, and degrade its intended function. For these reasons simple analytical modeling and experimental works were performed in order to predict exact tank temperature distribution and to find the effective cooling method to keep the tank temperature below the bubble escape limit (93.3 ℃), which was experimentally proven by other researchers. Both the analytical model and experimental results show that the temperature distributions are horizontally stratified. Particularly, the hot liquid produced by the condensation around the sparger holes goes up straight like a thermal plume. Also, the momentum of the discharged fluid is not so strong to interrupt this horizontal thermal stratification significantly. Therefore the layout and shape of sparger is not so important as long as the location of the sparger hole is sufficiently close to the bottom of the tank. Finally, for the effective tank cooling it is recommended that the locations of the discharge and intake lines of the cooling system be cautiously selected considering the temperature distribution, the water level change, and the cooling effectiveness.

Key Words  APR-1400, SDS, IRWST Temperature Distribution, Bubble Escape Temperature, Thermal Stratification

KSME International Journal, Vol. 18 No. 5, pp. 830-837, 2004

Rotordynamic Coefficients in Staggered Labyrinth Seals

Dursun Eser*, Ylmaz Dereli

Mathematics Department, Science and Art Faculty, Osmangazi University,

26480 Eskisehir Turkey

In this paper, the flow properties of staggered labyrinth seals are investigated. Leakage flowrates and pressure distributions are calculated for this seal. Then the dynamic stiffness and damping coefficients are calculated. The results are compared to the results of the some other papers.

Key Words  Staggered Labyrinth Seal, Rotordynamic Coefficient, Perturbation Analysis

KSME International Journal, Vol. 18 No. 5, pp. 838-846, 2004

Numerical Calculation of Minimum Ignition Energy for Hydrogen and Methane Fuels

Hong Jip Kim

Korea Aerospace Research Institute, P.O.Box 113, Yusung, Daejeon 305-600, Korea

Suk Ho Chung

School of Mechanical and Aerospace Engineering, Seoul National University,

Seoul 151-742, Korea

Chae Hoon Sohn*

Department of Aerospace Engineering, Chosun University, Gwangju 501-759, Korea

Minimum ignition energies of hydrogen/air and methane/air mixtures have been investigated numerically by solving unsteady one-dimensional conservation equations with detailed chemical kinetic mechanisms. Initial kernel size needed for numerical calculation is a sensitive function of initial pressure of a mixture and should be estimated properly to obtain quantitative agreement with experimental results. A simple macroscopic model to determine minimum ignition energy has been proposed, where the initial kernel size is correlated with the quenching distance of a mixture and evaluated from the quenching distance determined from experiment. The simulation predicts minimum ignition energies of two sample mixtures successfully which are in a good agreement with the experimental data for the ranges of pressure and equivalence ratio.

Key Words  Minimum Ignition Energy, Initial Kernel Size, Quenching Distance

KSME International Journal, Vol. 18 No. 5, pp. 847-856, 2004

Thermal Analysis of Spacecraft Propulsion System and its Validation

Cho Young Han*, Joon-Min Choi

Satellite Core Technology Department, Satellite Technology Division,

Korea Aerospace Research Institute, P.O.Box 113, Yusung, Taejon 305-600, Korea

Heaters for the spacecraft propulsion system are sized to prevent propellant from catastrophic freezing. For this purpose, thermal mathematical model (TMM) of the propulsion system is developed. Calculation output is compared with the results obtained from thermal vacuum test in order to check the validity of TMM. Despite a little discrepancy between the two types of results, both of them are qualitatively compatible. It is concluded that the propulsion system heaters are correctly sized and TMM can be used as a thermal design tool for the spacecraft propulsion system.

Key Words  Spacecraft, Propulsion System, Thermal Analysis, Heater Sizing, Thermal Vacuum Test

KSME International Journal, Vol. 18 No. 5, pp. 857-864, 2004

The Influence of a Vortex on a Freely Propagating Laminar Methane-Air Flame

Ki Yong Lee*

Andong National University, School of Mechanical Engineering,

388 Songchun-dong, Andong, Kyoungbuk 760-749, Korea

The change in the NO emission indices (EINO) in a two-dimensional plane has been investigated, which is due to the interaction between a vortex and methane-air flames established at different equivalence ratios, by solving the field equation. After solving the field equation, the spatial distribution of G-values is obtained. The NO emission index is calculated after applying the appropriate relation between the G-values and the NO production rate or the mass fraction of methane obtained from the library of freely propagating flames created from detailed simulations. When a vortex exists in a reacting flow field, in general EINO slightly increases, whereas EINO is lowered in the vicinity of the vortex regardless of flow direction. A change in vortex size has negligible impact on EINO_T but increasing the vortex strength slightly increases EINOT in the domain of this study.

Key Words  Vortex, Equivalence, NO Emission Index, Field Equation, Flame Thickness

KSME International Journal, Vol. 18 No. 5, pp. 865-876, 2004

Reduced Quasi-Dimensional Combustion Model of the Direct Injection Diesel Engine for Performance and Emissions Predictions

Dohoy Jung*

Department of Mechanical Engineering, The University of Michigan,

Ann Arbor, MI 48109-2121, USA

Dennis N. Assanis

Department of Mechanical Engineering, The University of Michigan,

Ann Arbor, MI 48109-2121, USA

A new concept of reduced quasi-dimensional combustion model for a direct injection diesel engine is developed based on the previously developed quasi-dimensional multi-zone model to improve the computational efficiency. In the reduced model, spray penetration and air entrainment are calculated for a number of zones within the spray while three zones with aggregated spray zone concept are used for the calculation of spray combustion and emission formation processes. It is also assumed that liquid phase fuel appears only near the nozzle exit during the breakup period and that spray vaporization is immediate in order to reduce the computational time. Validation of the reduced model with experimental data demonstrated that the new model can predict engine performance and NO and soot emissions reasonably well compared to the original model. With the new concept of reduced model, computational efficiency is significantly improved as much as 200 times compared to the original model.

Key Words  Diesel, Emissions, Quasi-dimensional, Multi-zone, Combustion model,

Simulation

KSME International Journal, Vol. 18 No. 6, pp. 879-894, 2004

<Invited Review Article> Sizing of Spray Particles Using Image Processing Technique

Sang Yong Lee*, Yu Dong Kim

Department of Mechanical Engineering, Korea Advanced Institute of Science and Technology,

Science Town, Daejeon 305-701, Korea

The image processing technique is simple and, in principle, can handle particles with various shapes since it is based on direct visualization. Moreover, a wide measurement area can be covered with appropriate optical arrangement. In the present paper, various techniques of image processing for sizing and counting particles are reviewed and recent developments are introduced. Two major subjects are discussed in detail  identification of particles (i.e., boundary detection and pattern recognition) and determination of in-focus criteria. Finally, an overall procedure for image processing of spray particles is suggested.

Key Words  Image Processing, Particle Size Measurement, Spray

KSME International Journal, Vol. 18 No. 6, pp. 895-903, 2004

LP Compressor Blade Vibration Characteristics at Starting Conditions of a 100 MW Heavy-duty Gas Turbine

An Sung Lee*

Rotor Dynamics Group, Korea Institute of Machinery and Materials,

Daejeon 305-600, Korea

Alexandre F. Vedichtchev

Gas Turbine Department, Leningradsky Metallichesky Zavod

Baskov 26, 191914, St. Petersburg, Russia

In this paper are presented the blade vibration characteristics at the starting conditions of the low pressure multistage axial compressor of heavy-duty 100 MW gas turbine. Vibration data have been collected through strain gauges during aerodynamic tests of the model compressor. The influences of operating modes at the starting conditions are investigated upon the compressor blade vibrations. The exciting mechanisms and features of blade vibrations are investigated at the surge, rotating stall, and buffeting flutter. The influences of operating modes upon blade dynamic stresses are investigated for the first and second stages. It is shown that a high dynamic stress peak of 120 MPa can occur in the first stage blades due to resonances with stall cell excitations or with inlet strut wake excitations at the stalled conditions.

Key Words  Compressor Blade Vibrations, Starting Conditions, Heavy-Duty Gas Turbine, Blade Dynamic Stresses, Surge, Rotating Stall, Buffeting Flutter, Stalled Oscillations

KSME International Journal, Vol. 18 No. 6, pp. 904-914, 2004

An Integrated CAD/CAM System for CNG Pressure Vessel Manufactured by Deep Drawing and Ironing Operation

Joon-Hong Park, Chul Kim*

Research Institute of Mechanical Technology, Pusan National University,

Jangjun-Dong, Kumjung-Ku, Busan 609-735, Korea

Jae-Chan Choi

School of Mechanical Engineering, Pusan National University,

Jangjun-Dong, Kumjung-Ku, Busan 609-735, Korea

The fiber reinforced composite material is widely used in the multi-industrial field because of their high specific modulus and specific strength. It has two main merits which are to cut down energy by reducing weight and to prevent explosive damage proceeding to the sudden bursting which is generated by the pressure leakage condition. Therefore, Pressure vessels using this composite material can be applied in the field such as defence industry and aerospace industry. In this paper, for nonlinear finite element analysis of E-glass/epoxy filament winding of composite vessel subjected to internal pressure, the standard interpretation model is developed by using the ANSYS with AutoLISP and ANSYS APDL languages, general commercial software, which is verified as useful characteristic of the solution. Among the modules of the system, both the process planning module for carrying out the process planning of filament wound composite pressure vessel and the autofrettage process module for obtaining higher residual stress will minimize trial and error and reduce the period for developing new products. The system can serve as a valuable system for experts and as a dependable training aid for beginners.

Key Words  ANSYS APDL, Autofrettage, Composite Material, Filament Winding Process

KSME International Journal, Vol. 18 No. 6, pp. 915-923, 2004

Effects of Carbon Black on the Fatigue Life, Critical J-Value and Fracture Morphology and a New Estimated Equation for Natural Rubber

Kim Jae-Hoon*

Korea Railroad Research Institute 360-1,

Woulam-Dong, Uiwang-City Kyounggi-Do 437-050, Korea

Jeong Hyun-Yong

Department of Mechanical Engineering, Sogang University

1 Shinsoo-Dong, Mapo-Gu, Seoul 121-742, Korea

This study investigated the fatigue lives and mechanical properties of the carbon black filled natural rubber for the vibration-proof parts of the railway vehicle and automobile. The carbon blacks were one of the sources of crack nucleation and crack propagation in the rubber matrix, like the cementite and the maganese sulfide in iron matrix. Different kinds of carbon blacks resulted in different fatigue lives, critical J-values, and fracture morphologies. It was noticed that the critical J-value remained almost the same regardless of the length of a pre-crack. In addition, different kinds of carbon blacks generated different fracture morphologies, and microscopic and macroscopic roughnesses. The critical J-value has linear relations to the roughness, and it seemed related to the size distribution of carbon black particles. By reviewing all the experimental data, we found the factors that were related to the fatigue lives, and the logarithmic value of the fatigue life could be linearly expressed by the combination of the critical J-value and the macroscopic roughness. We also proposed a new estimative equation of fatigue life.

Key Words  Fatigue Life, Carbon Black, Natural Rubber, Fracture Morphology, Critical             J-value

KSME International Journal, Vol. 18 No. 6, pp. 924-932, 2004

An Experimental Study on the Axial Collapse Characteristics of Hat and Double Hat Shaped Section Members at Various Velocities

Cheon Seok Cha*, Jin Oh Chung

Division of Mechanical and Automotive Engineering, Sunchon National University,

Suncheon, Jeonnam 540-742, Korea

In Young Yang

Division of Mechanical Engineering, Chosun University,

Kwang-ju 501-759, Korea

In this study, the axial collapse tests were performed under either static (or quasi-static) or impact loads with several collapse velocities based on the expectation that para-closed sections of the front-end side members (spot welded hat and double hat shaped section members) would show quite different collapse characteristics from those for seamless section. The test results showed that both of the hat and double hat shaped section members failed in the stable sequential collapse mode in the static or quasi-static collapse tests, while the double hat shaped section members underwent the unstable collapse mode especially when the impact velocity is high. The mean collapse loads in the hat shaped section members increase with collapse velocity for all the cases of the static, quasi-static, and impact collapse tests. In the double hat shaped section members, however, the mean collapse loads decrease with increase in collapse velocity in the impact tests.

Key Words  Hat and Double Hat Shaped Section Members, Spot Welded, Axial Collapse, Collapse Characteristics, Mean Collapse Load

KSME International Journal, Vol. 18 No. 6, pp. 933-945, 2004

Eigenstructure Assignment for Linear Systems with Probabilistic Uncertainties

Young Bong Seo, Jae Weon Choi*

School of Mechanical Engineering and RIMT, Pusan National University,

Pusan 609-735, Korea

Dal Ho Lee

Department of Electronics Engineering,

Kyungwon University, Kyungwon 461-701, Korea

In this paper, S(stochastic)-eigenvalue concept and its S-eigenvector for linear continuous-time systems with probabilistic uncertainties is proposed. The proposed concept is concerned with the perturbation of eigenvalues due to the probabilistic variable parameters in the dynamic model of a plant. S-eigenstructure assignment scheme via the Sylvester equation approach based on the S-eigenvalue concept is also proposed. The proposed design schemes are illustrated by numerical examples, and applied to the longitudinal dynamics of open-loop-unstable aircraft with possible uncertainties in aerodynamic and thrust effects as well as separate dynamic pressure. These results explicitly characterize how S-eigenvalues in the complex plane may impose stability on S-eigenstructure assignment.

Key Words  Probabilistic Parameter Variation, Gaussian Distribution, S-Eigenvalue,

S-Eigenvector, S-Stability, S-Eigenstructure Assignment

KSME International Journal, Vol. 18 No. 6, pp. 946-954, 2004

Bearing Load Distribution Studies in a Multi Bearing Rotor System and a Remote Computing Method Based on the Internet

Zhao Jian Yang*, Ze Jun Peng

College of Mechanical Engineering, Taiyuan University of Technology,

Taiyuan, 030024, China

Seock Sam Kim

School of Mechanical Engineering, Kyungpook National University,

Daegu, 702-701, Korea

A model in the form of a Bearing Load Distribution (BLD) matrix in the Multi Bearing Rotor System (MBRS) is established by a transfer matrix equation with the consideration of a bearing load, elevation and uniform load distribution. The concept of Bearing Load Sensitivity (BLS) is proposed and matrices for load and elevation sensitivity are obtained. In order to share MBRS design resources on the Internet with remote customers, the basic principle of Remote Computing (RC) based on the Internet is introduced  the RC of the BLD and BLS is achieved by Microsoft Active Server Pages (ASP) technology.

Key Words  Multi Bearing Rotor System, Bearing Load, Sensitivity, Internet, ASP, Remote Computing

KSME International Journal, Vol. 18 No. 6, pp. 955-960, 2004

Characteristics of the Eigenvalue Sensitivities to the Change of Element Correction Factors for Beams

Gun-Myung Lee*, Young-Hyo Park

School of Mechanical and Aerospace Engineering, Gyeongsang National University,

Jinju, Gyeongnam 660-701, Korea

Some characteristics of the eigenvalue sensitivities have been found for beams in the paper. For cantilever beams and simply supported beams, the sensitivities of the eigenvalues to the stiffness correction factor of one element are equal and opposite to the sensitivities to the mass correction factor of the symmetrically positioned element. For beams with other boundary conditions, however, the relationship does not hold. The relationship has been proven analytically for simply supported beams.

Key Words  Eigenvalue Sensitivity, Beam, Element Correction Factor

KSME International Journal, Vol. 18 No. 6, pp. 961-971, 2004

A Comparative Evaluation of Kop Determination and ∆Keff Estimation Methods

Jae-Youn Kang*

Korea Institute of Machinery & Materials,

171 Jang-dong, Yusong, Taejon 305-343, Korea

Ji-Ho Song, Ja-Suk Koo

Department of Automation and Design Engineering,

Korea Advanced Institute of Science and Technology, Seoul 130-012, Korea

Byung-Ik Choi

Korea Institute of Machinery & Materials,

171 Jang-dong, Yusong, Taejon 305-343, Korea

Methods for determination of the crack opening stress intensity factor (Kop) and for estimation of the effective stress intensity factor range (∆Keff) are evaluated for crack growth test data of aluminum alloys. Three methods of determining Kop, visual measurement, ASTM offset compliance method, and the neural network method proposed by Kang and Song, and three methods of estimating ∆Keff, conventional, the 2/PI0 and 2/PI methods proposed by Donald and Paris, are compared in a quantitative manner by using evaluation criteria. For all Kop determination methods discussed, the 2/PI method of estimating ∆Keff provides good results. The neural network method of determining Kop provides good correlation of crack growth data. It is recommended to use 2/PI estimation with the neural Kop determination method. The ASTM offset method used in conjunction with 2/PI estimation shows a possibility of successful application. It is desired to improve the ASTM method.

Key Words  Crack Closure, Effective Stress Intensity Factor Range, Evaluation Criteria, Fatigue Crack Growth, Opening Load

KSME International Journal, Vol. 18 No. 6, pp. 972-978, 2004

Control Scheme Using Forward Slip for a Multi-stand Hot Strip Rolling Mill

Young Hoon Moon*, I Seok Jo

School of Mechanical Engineering/Engineering Research Center for Net Shape and Die Manufacturing, Pusan National University, Pusan 609-735, Korea

Chester J. Van Tyne

Department of Metallurgical and Materials Engineering,

Colorado School of Mines, Golden, CO 80401, USA

Forward slip is an important parameter often used in rolling-speed control models for tandem hot strip rolling mills. In a hot strip mill, on-line measurement of strip speed is inherently very difficult. Therefore, for the set-up of the finishing mill, a forward slip model is used to calculate the strip speed from roll circumferential velocity at each mill stand. Due to its complexity, most previous researches have used semi-empirical methods in determining values for the forward slip. Although these investigations may be useful in process design and control, they do not have a theoretical basis. In the present study, a better forward slip model has been developed, which provides for a better set-up and more precise control of the mill. Factors such as neutral point, friction coefficient, width spread, shape of deformation zone in the roll bite are incorporated into the model. Implementation of the new forward slip model for the control of a 7-stand hot strip tandem rolling mill shows significant improvement in roll speed set-up accuracy.

Key Words  Finishing Mill, Forward Slip, Hot Strip Mill, Neutral Point, Coefficient of Friction

KSME International Journal, Vol. 18 No. 6, pp. 979-989, 2004

Tip Clearance Effect on Through-Flow and Performance of a Centrifugal Compressor

Hark-Jin Eum*, Young-Seok Kang, Shin-Hyoung Kang

Turbo System & Control Laboratory, School of Mechanical and Aerospace engineering,

Seoul National University, Seoul 151-742, Korea

Numerical simulations have been performed to investigate tip clearance effect on through-flow and performance of a centrifugal compressor which has the same configuration of impeller with six different tip clearances. Secondary flow and loss distribution have been surveyed to understand the flow mechanism due to the tip clearance. Tip leakage flow strongly interacts with mainstream flow and considerably changes the secondary flow and the loss distribution inside the impeller passage. A method has been described to quantitatively estimate the tip clearance effect on the performance drop and the efficiency drop. The tip clearance has caused specific work reduction and additional entropy generation. The former, which is called inviscid loss, is independent of any internal loss and the latter, which is called viscous loss, is dependent on every loss in the flow passage. Two components equally affected the performance drop as the tip clearances were small, while the efficiency drop was influenced by the viscous component alone. The additional entropy generation was modeled with all the kinetic energy of the tip leakage flow. Therefore, the present paper can provide how to quantitatively estimate the tip clearance effect on the performance and efficiency.

Key Words  Tip Clearance, Through-Flow, Performance, Centrifugal Compressor, Secondary Flow, Loss Distribution, Tip Leakage Flow, Performance Drop, Efficiency Drop, Specific Work Reduction, Additional Entropy Generation, Kinetic Energy

KSME International Journal, Vol. 18 No. 6, pp. 990-1001, 2004

Computational Study of the Mixed Cooling Effects on the In-Vessel Retention of a Molten Pool in a Nuclear Reactor

Byung Seok, Kim

School of Mechanical Engineering, Kyungpook National University,

1370, Sankyuk-dong, Daegu 702-701, Korea

Kwang Il, Ahn

Integrated Safety Assessment, Korea Atomic Energy Research Institute,

150, Dukjin-dong, Daejon 305-353, Korea

Chang Hyun, Sohn*

School of Mechanical Engineering, Kyungpook National University,

1370, Sankyuk-dong, Daegu 702-701, Korea

The retention of a molten pool vessel cooled by internal vessel reflooding and/or external vessel reactor cavity flooding has been considered as one of severe accident management strategies. The present numerical study investigates the effect of both internal and external vessel mixed cooling on an internally heated molten pool. The molten pool is confined in a hemispherical vessel with reference to the thermal behavior of the vessel wall. In this study, our numerical model used a scaled-down reactor vessel of a KSNP (Korea Standard Nuclear Power) reactor design of 1000 MWe (a Pressurized Water Reactor with a large and dry containment). Well-known temperature-dependent boiling heat transfer curves are applied to the internal and external vessel cooling boundaries. Radiative heat transfer has been considered in the case of dry internal vessel boundary condition. Computational results show that the external cooling vessel boundary conditions have better effectiveness than internal vessel cooling in the retention of the melt pool vessel failure.

Key Words  Nuclear Severe Accidents, In-Vessel Retention (IVR), Internal and External Vessel, Mixed Cooling, Computational Fluid Dynamics (CFD)

KSME International Journal, Vol. 18 No. 6, pp. 1002-1009, 2004

An Experimental Study on the Performance of Air/Water Direct Contact Air Conditioning System

Seong-Yeon Yoo*

Department of Mechanical Design Engineering, Chungnam National University,

Daejeon 305-764, Korea

Hwa-Kil Kwon

Graduate School, Chungnam National University,

Daejeon 305-764, Korea

Direct contact air conditioning systems, in which heat and mass are transferred directly between air and water droplets, have many advantages over conventional indirect contact systems. The purpose of this research is to investigate the cooling and heating performances of direct contact air conditioning system for various inlet parameters such as air velocity, air temperature, water flow rate and water temperature. The experimental apparatus comprises a wind tunnel, water spray system, scrubber, demister, heater, refrigerator, flow and temperature controller, and data acquisition system. The inlet and outlet conditions of air and water are measured when the air contacts directly with water droplets as a counter flow in the spray section of the wind tunnel, and the heat and mass transfer rates between air and water are calculated. The droplet size of the water sprays is also measured using a Malvern Particle Analyzer. In the cooling conditions, the outlet air temperature and humidity ratio decrease as the water flow rate increases and as the water temperature, air velocity and temperature decrease. On the contrary, the outlet air temperature and humidity ratio increase in the heating conditions as the water flow rate and temperature increase and as the air velocity decreases.

Key Words  Air Conditioning System, Direct Contact, Cooling, Heating, Humidification, Dehumidification

KSME International Journal, Vol. 18 No. 6, pp. 1010-1018, 2004

On the Method for Hot-Fire Modeling of High-Frequency Combustion Instability in Liquid Rocket Engines

Chae Hoon Sohn*

Department of Aerospace Engineering, Chosun University, Gwangju 501-759, Korea

Woo-Seok Seol

Rocket Engine Department, Korea Aerospace Research Institute,

P.O.Box 113, Yusung, Daejeon 305-600, Korea

Alexander A. Shibanov, Valery P. Pikalov

Research Institute of Chemical Machine Building (NIICHIMMASH), Sergiev Posad, Russia

This study presents the methodological aspects of combustion instability modeling and pro-        vides the numerical results of the model (sub-scale) combustion chamber, regarding geometrical dimensions and operating conditions, which are for determining the combustion stability boundaries using the model chamber. An approach to determine the stability limits and acoustic characteristics of injectors is described intensively. Procedures for extrapolation of the model operating parameters to the actual conditions are presented, which allow the hot-fire test data to be presented by parameters of the combustion chamber pressure and mixture (oxidizer/fuel) ratio, which are customary for designers. Tests with the model chamber, based on the suggested scaling method, are far more cost-effective than with the actual (full-scale) chamber and useful for injector screening at the initial stage of the combustor development in a viewpoint of combustion instabilities.

Key Words  Scaling, Combustion Instability Modeling, Stability Boundary, Injector Screening, Model Combustion Chamber

KSME International Journal, Vol. 18 No. 6, pp. 1019-1025, 2004

Relation between Pressure Variations and Noise in Axial Type Oil Piston Pumps

Jong-Ki Kim*, Hyoung-Eui Kim

Korea Institute of Machinery & Materials,

171 Jang-dong, Yuseong-Gu, Daejeon 305-600, Korea

Jae-Youn Jung

Faculty of Mechanical & Aerospace System Engineering, Chonbuk National University,

Jeonju, Jeonbuk 561-756, Korea

Seok-Hyung Oh

Faculty of mechanical Engineering, Kunsan National University,

Kunsan, Jeonbuk 573-701, Korea

Seok-Hoon Jung

Department of Automobile, Byuksung College, Kimje, Jeonbuk 576-711, Korea

Pressure variation is one of the major sources on noise emission in the axial type oil piston pumps. Therefore, it is necessary that the pressure variation characteristics of the oil hydraulic piston pumps be clarified to reduce the pump noise. Pressure variations in a cylinder at the discharge region and the pump noise were simultaneously measured with discharge pressures and rotational speeds during the pump working. To investigate the effects of the pre-compression and the V-notch in the valve plate, we used the three types of valve plates. In this research, it is clear that the pressure variation characteristics of axial type oil piston pumps is deeply related to the pre-compression and to the V-notch design in valve plate. Therefore, we could reduce the pump noise by using the appropriate pre-compression angle and the notch design that are between the suction port and the discharge port in valve plate.

Key Words  Pressure Variation, Noise, Piston Pump, Valve Plate

KSME International Journal, Vol. 18 No. 6, pp. 1026-1035, 2004

An Immersed-Boundary Finite-Volume Method for Simulation of Heat Transfer in Complex Geometries

Jungwoo Kim, Haecheon Choi*

School of Mechanical and Aerospace Engineering, Seoul National University,

Seoul 151-744, Korea

An immersed boundary method for solving the Navier-Stokes and thermal energy equations is developed to compute the heat transfer over or inside the complex geometries in the Cartesian or cylindrical coordinates by introducing the momentum forcing, mass source/sink, and heat source/sink. The present method is based on the finite volume approach on a staggered mesh together with a fractional step method. The method of applying the momentum forcing and mass source/sink to satisfy the no-slip condition on the body surface is explained in detail in Kim, Kim and Choi (2001, Journal of Computational Physics). In this paper, the heat source/sink is introduced on the body surface or inside the body to satisfy the iso-thermal or iso-heat-flux condition on the immersed boundary. The present method is applied to three different problems  forced convection around a circular cylinder, mixed convection around a pair of circular cylinders, and forced convection around a main cylinder with a secondary small cylinder. The results show good agreements with those obtained by previous experiments and numerical simulations, verifying the accuracy of the present method.

Key Words  Immersed Boundary Method, Heat Transfer, Finite Volume Method, Complex Geometry

KSME International Journal, Vol. 18 No. 6, pp. 1036-1041, 2004

Measurements of Blood Viscosity Using a Pressure-Scanning Slit Viscometer

Sehyun Shin*, Sung-Woo Lee, Yun-Hee Ku

School of Mechanical Engineering, Kyungpook National University,

1370 Sankyuk-dong, Buk-gu, Daegu 702-701, Korea

A newly designed pressure-scanning slit viscometer is developed to combine an optical device without refraction while measuring blood viscosity over a range of shear rates. The capillary tube in a previously designed capillary viscometer was replaced with a transparent slit, which is affordable to mount optical measurement of flowing blood cells. Using a pressure transducer, we measured the change of pressure in a collecting chamber with respect to the time, (), from which the viscosity and shear rate were mathematically calculated. For water, standard oil and whole blood, excellent agreement was found between the results from the pressure-scanning slit viscometer and those from a commercially available rotating viscometer. This new viscometer overcomes the drawbacks of the previously designed capillary viscometer in the measuring whole blood viscosity. First, the pressure-scanning slit viscometer can combine an optical instrument such as a microscope. Second, this design is low cost and simple (i.e., ease of operation, no moving parts, and disposable).

Key Words  Blood, Viscosity, Pressure, Slit, Viscometer

KSME International Journal, Vol. 18 No. 6, pp. 1042-1051, 2004

Vortical Flows over a Delta Wing at High Angles of Attack

Young-Ki Lee, Heuy-Dong Kim*

School of Mechanical Engineering, Andong National University,

388 Songcheon-dong, Andong, Kyeongbuk, 760-749, Korea

The vortex flow characteristics of a sharp-edged delta wing at high angles of attack were studied using a computational technique. Three dimensional, compressible Reynolds-averaged Navier-Stokes equations were solved to understand the effects of the angle of yaw, angle of attack, and free stream velocity on the development and interaction of vortices and the relationship between suction pressure distributions and vortex flow characteristics. The present computations gave qualitatively reasonable predictions of vortical flows over a delta wing, compared with past wind tunnel measurements. With an increase in the angle of yaw, the symmetry of the pair of leading edge vortices was broken and the vortex strength was decreased on both windward and leeward sides. An increase in the free stream velocity resulted in stronger leading edge vortices with an outboard movement.

Key Words  Angle of Attack, Angle of Yaw, Delta Wing, Vortical Flow, Vortex Breakdown

KSME International Journal, Vol. 18 No. 7, pp. 1055-1061, 2004

Breakage Detection of Small-Diameter Tap Using Vision System in High-Speed Tapping Machine with Open Architecture Controller

Don Jin Lee*

Engineering Research Center/Net Shape and Die Manufacturing, Pusan National University,

Busan 609-735, Korea

Sun Ho Kim

Department of Mechatronics Engineering, Dong-Eui University,

Busan 614-714, Korea

Jung Hwan Ahn

School of Mechanical Engineering, Pusan National University, ERC/NSDM

Busan 609-735, Korea

In this research, a vision system for detecting breakages of small-diameter taps, which are rarely detected by the indirect in-process monitoring methods such as acoustic emission, cutting torque and motor current, was developed. Two HMI (Human Machine Interface) programs to embed the developed vision system into a Siemens open architecture controller, 840D, were developed. They are placed in sub-windows of the main window of the 840D and can be activated or deactivated either by a softkey on the operating panel or the M code in the NC part program. In the event that any type of tool breakage is detected, the HMI program issues a command for an automatic tool change or sends an alarm signal to the NC kernel. An evaluation test in a high-speed tapping machine showed that the developed vision system was successful in detecting breakages of small-diameter taps up to M1.

Key Words  Tool Breakage, CMOS Image Sensor, Vision System, Slit Beam Laser, Threshold Filter, Centroid

KSME International Journal, Vol. 18 No. 7, pp. 1062-1073, 2004

On the Full Stand Modeling and Tension Control for the Hot Strip Finishing Mill with PID Structure

Byoung Joon Ahn

Department of Mechanical and Intelligent Systems Engineering,

Pusan National University, JangJeon-Dong, KumJeong-Ku, Pusan 609-735, Korea

Ju Yong Choi

Department of Mechanical and Intelligent Systems Engineering,

Pusan National University, JangJeon-Dong, KumJeong-Ku, Pusan 609-735, Korea

Yu Shin Chang

Department of Mechanical and Intelligent Systems Engineering, ERC/NSDM

Pusan National University, JangJeon-Dong, KumJeong-Ku, Pusan 609-735, Korea

Man Hyung Lee*

School of Mechanical Engineering,

Pusan National University, JangJeon-Dong, KumJeong-Ku, Pusan 609-735, Korea

We describe a looper controller design for a hot strip finishing mill in steel plants. The main function of the looper system is to balance the mass flow of the strip by accumulating material in the middle of the stands. Another function is to control the strip tension which influences the width of the strip. To ensure strip quality, it is very important to control the tension of the hot strip finishing mill. However, because there is a mutual interaction between the looper angle and the strip tension, it is difficult to control the looper system. Previous researches examined only the operation of a single stand. But it is not sufficient to examine the operation and effect of whole stands because the operation is wholly interdependent. In this paper, we present a full model of the hot strip finishing mill in order to more effectively control strip tension. We propose several control methods for the full-stand hot strip finishing mill, denoted as conventional PI, PI with cross gain, and coefficient diagram method (CDM) PID control. In the real plants, there are some problems by using higher order controllers such as LQ, LQG and H#.             By comparison, the PID controller is very simple and easy to apply to all real plants. To that end, we present our findings on PID controls and their potential use in the hot strip finishing mill.

Key Words  Hot Strip Finishing Mill, Tension, Looper System, Conventional PI, Cross Control, CDM

KSME International Journal, Vol. 18 No. 7, pp. 1074-1085, 2004

Web Guide Process in Cold Rolling Mill  Modeling and PID Controller

Byoung Joon Ahn

Department of Mechanical and Intelligent Systems Engineering, Pusan National University,

JangJeon-Dong, KumJeung-Ku, Pusan 609-735, Korea

Ju Yong Choi

Department of Mechanical and Intelligent Systems Engineering, Pusan National University,

JangJeon-Dong, KumJeung-Ku, Pusan 609-735, Korea

Yu Shin Chang

Department of Mechanical and Intelligent Systems Engineering, ERC/NSDM

Pusan National University, JangJeon-Dong, KumJeung-Ku, Pusan 609-735, Korea

Man Hyung Lee*

School of Mechanical Engineering,

Pusan National University, JangJeon-Dong, KumJeung-Ku, Pusan 609-735, Korea

There are many intermediate web guides in cold rolling mills process such as CRM (cold rolling mill), CGL (continuous galvanizing line), EGL (electrical galvanizing line) and so on. The main functions of the web guides are to adjust the center line of the web (strip) to the center line of the steel process. So they are called CPC(center position control). Rapid process speed cause large deviation between the center position of the strip and the process line. Too much deviation is not desirable. So the difference between the center position of the strip and the process line should be compensated. In general, the center position control of the web is obtained by the hydraulic driver and electrical controller. In this paper, we propose modelling and several controller designs for web-guide systems. We model the web and guide by using geometrical relations of the guide ignored the mass and stiffness of the web. To control the systems, we propose PID controllers with their gains tuned by the Ziegler-Nichols method, the  controller model-matching method, and the coefficient diagram method (CDM). CDM is modified for high order systems. The results are verified by computer simulations.

Key Words  Cold Rolling Mill, Center Position Control, PID, H#, CDM

KSME International Journal, Vol. 18 No. 7, pp. 1086-1093, 2004

Modal Analysis of Constrained Multibody Systems Undergoing Constant Accelerated Motions

Dong Hwan Choi, Hong Hee Yoo*

School of Mechanical Engineering, Hanyang University, Seoul 133-791, Korea

The modal characteristics of constrained multibody systems undergoing constant accelerated motions are investigated in this paper. Relative coordinates are employed to derive the equations of motion, which are generally nonlinear in terms of the coordinates. The dynamic equilibrium position of a constrained multibody system needs to be obtained from the nonlinear equations of motion, which are then linearized at the dynamic equilibrium position. The mass and the stiffness matrices for the modal analysis can be obtained from the linearized equations of motion. To verify the effectiveness and the accuracy of the proposed method, two numerical examples are solved and the results obtained by using the proposed method are compared with those obtained by analytical and other numerical methods. The proposed method is found to be accurate as well as effective in predicting the modal characteristics of constrained multibody systems undergoing constant accelerated motions.

KSME International Journal, Vol. 18 No. 7, pp. 1094-1106, 2004

Sliding Mode Control of Two-Wheeled Welding Mobile Robot for Tracking Smooth Curved Welding Path

Tan Lam Chung, Trong Hieu Bui

Department of Mechanical Eng., College of Eng., Pukyong National University,

San 100, Yongdang-Dong, Nam-Gu, Pusan 608-739, Korea

Tan Tien Nguyen

Department of Mechanical Eng., Hochiminh City University of Technology,

268 Ly Thuong Kiet, Dist. 10, Hochiminh City, Vietnam

Sang Bong Kim*

Department of Mechanical Eng., College of Eng., Pukyong National University,

San 100, Yongdang-Dong, Nam-Gu, Pusan 608-739, Korea

In this paper, a nonlinear controller based on sliding mode control is applied to a two-wheeled Welding Mobile Robot (WMR) to track a smooth curved welding path at a constant velocity of the welding point. The mobile robot is considered in terms of dynamics model in Cartesian coordinates under the presence of external disturbance, and its parameters are exactly known. It is assumed that the disturbance satisfies the matching condition with a known boundary. To obtain the controller, the tracking errors are defined, and the two sliding surfaces are chosen to guarantee that the errors converge to zero asymptotically. Two cases are to be considered  fixed torch and controllable torch. In addition, a simple way of measuring the errors is introduced using two potentiometers. The simulation and experiment on a two-wheeled welding mobile robot are provided to show the effectiveness of the proposed controller.

Key Words  Welding Mobile Robot (WMR), Nonholonomic, Sliding Mode Control

KSME International Journal, Vol. 18 No. 7, pp. 1107-1120, 2004

Time-Discretization of Nonlinear Systems with Delayed Multi-Input Using Taylor Series

Ji Hyang Park, Kil To Chong*

Division of Electronics and Information Engineering Chonbuk National University,

Duckjin-Dong, Duckjin-Gu, Jeonju 561-756, Korea

Nikolaos Kazantzis

Department of Chemical Engineering, Worcester Polytechnic Institute Worcester,

MA 01609, U.S.A.

Alexander G. Parlos

Department of Mechanical Engineering Texas A&M University College Station,

Texas 77840, U.S.A.

This study proposes a new scheme for the sampled-data representation of nonlinear systems with time-delayed multi-input. The proposed scheme is based on the Taylor-series expansion and zero-order hold assumption. The mathematical structure of a new discretization scheme is explored. On the basis of this structure, the sampled-data representation of nonlinear systems including time-delay is derived. The new scheme is applied to nonlinear systems with two inputs and then the delayed multi-input general equation is derived. The resulting time-discretization provides a finite-dimensional representation of nonlinear control systems with time-delay enabling existing controller design techniques to be applied to them. In order to evaluate the tracking performance of the proposed scheme, an algorithm is tested for some of the examples including maneuvering of an automobile and a 2-DOF mechanical system.

Key Words  Nonlinear System, Time-Discretization, Time-Delay, Multi-Input, Taylor-Series

KSME International Journal, Vol. 18 No. 7, pp. 1121-1130, 2004

Initial Design Domain Reset Method for Genetic Algorithm with Parallel Processing

O-Kaung Lim*, Keum-Shik Hong, Hyuk-Soo Lee, Eun-Ho Choi

School of Mechanical Engineering,

Pusan National University, Kumjung Ku, Busan 609-735, Korea

The Genetic Algorithm (GA), an optimization technique based on the theory of natural selection, has proven to be a relatively robust means of searching for global optimum. It converges to the global optimum point without auxiliary information such as differentiation of function. In the case of a complex problem, the GA involves a large population number and requires a lot of computing time. To improve the process, this research used parallel processing with several personal computers. Parallel process technique is classified into two methods according to subpopulations size and number. One is the fine-grained method (FGM), and the other is the coarse-grained method (CGM). This study selected the CGM as a parallel process technique because the load is equally divided among several computers. The given design domain should be reduced according to the degree of feasibility, because mechanical system problems have constraints. The reduced domain is used as an initial design domain. It is consistent with the feasible domain and the infeasible domain around feasible domain boundary. This parallel process used the Message Passing Interface library.

Key Words  Genetic Algorithm, Parallel Processing, Message Passing Interface

KSME International Journal, Vol. 18 No. 7, pp. 1131-1139, 2004

Design and Stability Analysis of Impedance Controller for Bilateral Teleoperation under a Time Delay

Hyun Chul Cho, Jong Hyeon Park*

School of Mechanical Engineering, Hanyang University,

Haengdang-Dong, Sungdong-Ku, Seoul 133-791, Korea

A new impedance controller is proposed for bilateral teleoperation under a time delay. The proposed controller does not need to measure or estimate the time delay in the communication channel using the force loop-back. In designing a stable impedance controller, absolute stability is used as a stability analysis tool, which results in a less conservative controller than the passivity concept. Moreover, in order to remove the conservatism associated with the assumption of infinite port impedances, the boundaries of human and environment impedance are set to finite values. Based on this, this paper proposes a parameter design procedure for stable impedance controllers. The validity of the proposed control scheme is demonstrated by experiments with a 1-dof master/slave system.

Key Words  Bilateral Teleoperation, Impedance Control, Absolute Stability, Force Feedback, Time Delay

KSME International Journal, Vol. 18 No. 7, pp. 1140-1149, 2004

Coupled Heat and Mass Transfer in Absorption of Water Vapor into LiBr-H2O Solution Flowing on Finned Inclined Surfaces

Taebeom Seo*, Eunjun Cho

Department of Mechanical Engineering, Inha University,

253, Yonghyundong, Namgu, Inchon 402-751, Korea

The absorption characteristics of water vapor into a LiBr-H2O solution flowing down on finned inclined surfaces are numerically investigated in order to study the absorbing performances of different surface shapes of finned tubes as an absorber element. A three-dimensional numerical model is developed. The momentum, energy, and diffusion equations are solved simultaneously using a finite difference method. In order to obtain the temperature and concentration distributions, the Runge-Kutta and the Successive over relaxation methods are used. The flat, circular, elliptic, and parabolic shapes of the tube surfaces are considered in order to find the optimal surface shapes for absorption. In addition, the effects of the fin intervals and Reynolds numbers are studied. The results show that the absorption mainly happens near the fin tip due to the temperature and concentration gradient, and the absorbing performance of the parabolic surface is better than those of the other surfaces.

Key Words  Absorption, LiBr, Absorber, Mass Transfer, Finned Tube

KSME International Journal, Vol. 18 No. 7, pp. 1150-1158, 2004

Adaptive Observer Design for Nonlinear Systems Using Generalized Nonlinear Observer Canonical Form

Nam-Hoon Jo*

School of Electrical Engineering, Soongsil University, Seoul 156-743, Korea

Young-Ik Son

Department of Electrical Engineering, Myongji University,

Yong-In, Kyunggido 449-728, Korea

In this paper, we present an adaptive observer for nonlinear systems that include unknown constant parameters and are not necessarily observable. Sufficient conditions are given for a nonlinear system to be transformed by state-space change of coordinates into an adaptive observer canonical form. Once a nonlinear system is transformed into the proposed adaptive observer canonical form, an adaptive observer can be designed under the assumption that a certain system is strictly positive real. An illustrative example is included to show the effectiveness of the proposed method.

Key Words  Nonlinear System, Adaptive Observer, Nonlinear Observer Canonical Form, Generalized Nonlinear Observer Canonical Form, Strictly Positive Real

KSME International Journal, Vol. 18 No. 7, pp. 1159-1168, 2004

Spectral Element Analysis for an Axially Moving Viscoelastic Beam

Hyungmi Oh, Jooyong Cho, Usik Lee*

Department of Mechanical Engineering, Inha University,

253 Yonghyun-Dong, Nam-Ku, Incheon 402-751, Korea

In this paper, a spectral element model is derived for the axially moving viscoelastic beams subject to axial tension. The viscoelastic material is represented in a general form by using the one-dimensional constitutive equation of hereditary integral type. The high accuracy of the present spectral element model is verified first by comparing the eigenvalues obtained by the present spectral element model with those obtained by using the conventional finite element model as well as with the exact analytical solutions. The effects of viscoelasticity and moving speed on the dynamics of moving beams are then numerically investigated.

Key Words  Viscoelastic Beam, Moving Beam, Spectral Element Model, Vibration, Critical Moving Speed

KSME International Journal, Vol. 18 No. 7, pp. 1169-1176, 2004

Investigation of Soot Formation in a D.I. Diesel Engine by Using Laser Induced Scattering and Laser Induced Incandescence

Ki Hyung Lee*

Department of Mechanical Engineering, Hanyang University,

1271 Sa-Dong, Sangrok-Gu, Ansan-si, Gyunggi-Do 426-791, Korea

Jae Woo Chung, Byung Soo Kim

Korea Automotive Technology Institute,

74 Yongjung-Ri, Pungse-Myun, Chonan, Chungnam 330-912, Korea

Sang Kwon Kim

Hyundai Motor Company,

772-1, Jangduk-Dong, Whasung-si, Gyunggi-Do 445-706, Korea

Soot has a great effect on the formation of PM (Particulate Matter) in D.I. (Direct Injection) Diesel engines. Soot in diesel flame is formed by incomplete combustion when the fuel atomization and mixture formation were poor. Therefore, the understanding of soot formation in a D.I. diesel engine is mandatory to reduce PM in exhaust gas. To investigate soot formation in diesel combustion, various measurements have been performed with laser diagnostics. In this study, the relative soot diameter and the relative number density in a D.I. engine was measured by using LIS (Laser Induced Scattering) and LII (Laser Induced Incandescence) methods simultaneously which are planar imaging techniques. And a visualization D.I. diesel engine was used to introduce a laser beam into the combustion chamber and investigate the diffusion flame characteristics. To find the optimal condition that reduces soot formation in diesel combustion, various injection timing and the swirl flow in the cylinder using the SCV (Swirl Control Valve) were applied. From this experiment, the effects of injection timing and swirl on soot formation were established. Effective reduction of soot formation is possible through the control of these two factors.

Key Words  Spray, LII (Laser Induced Incandescence), LIS (Laser Induced Scattering), D.I. Diesel Engine, Swirl, Soot Distribution, Visualization

KSME International Journal, Vol. 18 No. 7, pp. 1177-1186, 2004

Atomization Characteristics and Prediction Accuracy of LISA-DDB Model for Gasoline Direct Injection Spray

Sung Wook Park, Hyung Jun Kim

Graduate School of Hanyang University,

17 Haengdang-dong, Sungdong-gu, Seoul 133-791, Korea

Ki Hyung Lee, Chang Sik Lee*

Department of Mechanical Engineering, Hanyang University,

17 Haengdang-dong, Sungdong-gu, Seoul 133-791, Korea

In this paper, the spray atomization characteristics of a gasoline direct-injection injector were investigated experimentally and numerically. To visualize the developing spray process, a laser sheet method with a Nd YAG laser was utilized. The microscopic atomization characteristics such as the droplet size and velocity distribution were also obtained by using a phase Doppler particle analyzer system at the 5 MPa of injection pressure. With the experiments, the calculations of spray atomization were conducted by using the KIVA code with the LISA-DDB breakup model. Based on the agreement with the experimental results, the prediction accuracy of LISA-DDB breakup model was investigated in terms of the spray shapes, spray tip penetration, SMD distribution, and axial mean velocity. The results of this study provides the macroscopic and microscopic characteristics of the spray atomization, and prediction accuracy of the LISA-DDB model.

Key Words  Hybrid Breakup Model, Atomization Characteristics, GDI (Gasoline Direct

Injection), KIVA-3 Code

KSME International Journal, Vol. 18 No. 7, pp. 1187-1195, 2004

An Experimental Study on the Spray Characteristics of a Dual-Orifice Type Swirl Injector at Low Fuel Temperatures

Byung Sung Park

Graduate School of Mechanical Engineering, Korea University,

1, 5-ka, Anam-dong, Sungbuk-ku, Seoul 136-701, Korea

Ho Young Kim*, Yongchan Kim, Jin Taek Chung

Department of Mechanical Engineering, Korea University,

1, 5-ka, Anam-dong, Sungbuk-ku, Seoul 136-701, Korea

The objective of this study is to investigate the effects of fuel temperature on the spray characteristics of a dual-orifice type swirl injector used in a gas turbine. The major parameters affecting spray characteristics are fuel temperature and injection pressure entering into the injector. In this study, the spray characteristics of a dual-orifice type swirl injector are investigated by varying fuel temperature from 30 oC to 120 oC and injection pressure from 0.29 to 0.69 MPa. Two kinds of fuel having different surface tension and viscosity are chosen as atomizing fluids. As a result, injection instability occurs in the low fuel temperature range due to icing phenomenon and fuel property change with a decrease of fuel temperature. As the injection pressure increases, the range of kinematic viscosity for stable atomization becomes wider. The properties controlling the SMD of spray is substantially different according to the fuel temperature range.

Key Words  Spray, Fuel Temperature, SMD, Equivalent Spray Angle, Injection Instability

KSME International Journal, Vol. 18 No. 7, pp. 1196-1202, 2004

A Study on the Modeling of Transitional Lateral Force Acting on the Berthing Ship by CFD

Gil-Young Kong*, Yun-Sok Lee, Sang-Min Lee

Department of Ship Operation System Engineering, Korea Maritime University,

1 Dongsam-dong, Yeongdo-gu, Busan 606-791 Korea

To evaluate the unsteady motion in laterally berthing maneuver, it is necessary to estimate clearly the magnitudes and properties of hydrodynamic forces acting on ship hull in shallow water. A numerical simulation has been performed to investigate quantitatively the hydrodynamic force according to water depth for Wigley model using the CFD (Computational Fluid Dynamics) technique. By comparing the computational results with the experimental ones, the validity of the CFD method was verified. The numerical solutions successfully captured some features of transient flow around the berthing ship. The transitional lateral force in a state ranging from the rest to the uniform motion is modeled by using the concept of circulation.

Key Words  Berthing Ships, Hydrodynamic Force, Transitional Lateral Force, SGS Model, CFD, Shallow Water

KSME International Journal, Vol. 18 No. 7, pp. 1203-1212, 2004

Composite Overlapping Meshes for the Solution of Radiation Forces on Submerged-Plate

Gil-Young Kong*, Sang-Min Lee, Yun-Sok Lee

Department of Ship Operating Systems Engineering, Korea Maritime University,

Dongsam-Dong, Youngdo-Gu, Pusan 606-791 Korea

The purpose of this study is to predict and understand the hydrodynamic forces and their nonlinear behaviors of fluid motion around the submerged plate oscillating near a free surface. To achieve this objective, we have developed a composite grid method for the solution of a radiation problem. The domain is divided into two different grids  one is a moving grid system and the other is a fixed grid system. The moving grid is employed for the body fitted coordinate system and moves with the body. This numerical method is applied to calculation of radiation forces generated by the submerged plate oscillating near a free surface. In order to investigate the characteristics of the radiation forces, the forced heaving tests have been performed with several amplitudes and different submergences near a free surface. These experimental results are compared with the numerical ones obtained by the present method and a linear potential theory. As a result, we can confirm the accuracy of the present method. Finally, the effect of nonlinear and viscous damping has been evaluated on the hydrodynamic forces acting on the submerged plate.

Key Words  Composite Grid Method, Submerged Plate, Radiation Forces, Viscous Damping, Free Surface Effect

KSME International Journal, Vol. 18 No. 7, pp. 1213-1221, 2004

Analysis of Density Distribution for Unsteady Butane Flow Using Three-Dimensional Digital Speckle Tomography

Han Seo Ko*

School of Mechanical Engineering, Sungkyunkwan University,

300 Chunchun-dong, Jangan-gu, Suwon, Kyunggi-do 440-746, Korea

Kwang-Hee Park, Yong-Jae Kim

Graduate School, Department of Mechanical Engineering, Sungkyunkwan University,

300 Chunchun-dong, Jangan-gu, Suwon, Kyunggi-do 440-746, Korea

Transient and asymmetric density distributions have been investigated by three-dimensional digital speckle tomography. Multiple CCD images captured movements of speckles in three angles of view simultaneously because the flows were asymmetric and transient. The speckle movements between no flow and downward butane flow from a circular half opening have been calculated by a cross-correlation tracking method so that those distances can be transferred to deflection angles of laser rays for density gradients. The three-dimensional density fields have been reconstructed from the deflection angles by a real-time multiplicative algebraic reconstruction technique (MART).

Key Words  Digital Speckle Tomography, Butane Flow, Multiplicative Algebraic Reconstruction Technique (MART), Cross-Correlation

KSME International Journal, Vol. 18 No. 7, pp. 1222-1235, 2004

A Study of the Relation Between Nozzle Geometry, Internal flow and Sprays Characteristics in Diesel Fuel Injection Systems

Raul Payri*, S. Molina, F. J. Salvador, J. Gimeno

CMT-Motores Termicos, Universidad Politecnica de Valencia

Camino de Vera s/n, E-46022 Spain

This study examines the influence of geometry on the internal flow and macroscopic behavior of the spray in Diesel nozzles. For this investigation, two bi-orifice nozzles were employed  one cylindrical and one conical. The first step is to use a non-destructive characterization method which is based on the production of silicone moulds so that the precise internal geometry of the two nozzles can be measured. At this stage the nozzles have been characterized dimensionally and therefore the internal flow can be studied using CFD calculations. The results gained from this experiment make it possible also to ascertain the critical cavitation conditions. Once the critical cavitation conditions have been identified, the macroscopic parameters of the spray can be studied in both cavitating and non-cavitating conditions using a test rig pressurized with nitrogen and with the help of a image acquisition system and image processing software. Consequently, research can be carried out to determine the influence that cavitation has on macroscopic spray behavior. From the point of view of the spray macroscopic behavior, the main conclusion of the paper is that cavitation leads to an increment of the spray cone angle. On the other hand, from the point of view of the internal flow, the hole outlet velocity increases when cavitation appears. This phenomenon can be explained by the reduction in the cross section of the liquid phase in the outlet section of the hole.

Key Words  CFD, Nozzle Flow, Spray, Cavitation, Diesel Injection, Nozzle Geometry

KSME International Journal, Vol. 18 No. 7, pp. 1236-1245, 2004

Extraction of Sizes and Velocities of Spray Droplets by Optical Imaging Method

Yeonjun Choo, Boseon Kang*

Department of Mechanical Engineering, Chonnam National University,

300, Yongbong-Dong, Buk-Gu, Gwangju 500-757, Korea

In this study, an optical imaging method was developed for the measurements of the sizes and velocities of droplets in sprays. Double-exposure single-frame spray images were captured by the imaging system. An image processing program was developed for the measurements of the sizes and positions of individual particles including separation of the overlapped particles and particle tracking and pairing at two time instants. To recognize and separate overlapping particles, the morphological method based on watershed segmentation as well as separation using the perimeter and convex hull of image was used consecutively. Better results in separation were obtained by utilization of both methods especially for the multiple or heavily-overlapped particles. The match probability method was adopted for particle tracking and pairing after identifying the positions of individual particles and it produced good matching results even for large particles like droplets in sprays. Therefore, the developed optical imaging method could provide a reliable way of analyzing the motion and size distribution of droplets produced by various sprays and atomization devices.

Key Words  Optical Imaging Method, Morphological Method, Spray Droplet, Particle

Tracking Algorithm

KSME International Journal, Vol. 18 No. 7, pp. 1246-1257, 2004

Investigation of Self-Excited Combustion Instabilities in Two Different Combustion Systems

Seonghyeon Seo*

Rocket Engine Department, Korea Aerospace Research Institute,

Eoeun-dong, Yuseong-gu, Daejon 305-333, Korea

The objective of this paper is to characterize dynamic pressure traces measured at self-excited combustion instabilities occurring in two combustion systems of different hardware. One system is a model lean premixed gas turbine combustor and the other a fullscale bipropellant liquid rocket thrust chamber. It is commonly observed in both systems that low frequency waves at around 300Hz are first excited at the onset of combustion instabilities and after a short duration, the instability mode becomes coupled to the resonant acoustic modes of the combustion chamber, the first longitudinal mode for the lean premixed combustor and the first tangential mode for the rocket thrust chamber. Low frequency waves seem to get excited at first since flame shows the higher heat release response on the lower frequency perturbations with the smaller phase differences between heat release and pressure fluctuations. Nonlinear time series analysis of pressure traces reveals that even stable combustion might have chaotic behavior with the positive maximum Lyapunov exponent. Also, pressure fluctuations under combustion instabili-        ties reach a limit cycle or quasi-periodic oscillations at the very similar run conditions, which manifest that a self-excited high frequency instability has strong nonlinear characteristics.

Key Words  Combustion Instability, Bifurcation, Nonlinear, Time Series Analysis, Lyapunov Exponent

KSME International Journal, Vol. 18 No. 7, pp. 1258-1266, 2004

A Naphthalene Sublimation Study on Heat/Mass Transfer for Flow over a Flat Plate

Jong-Hark Park

Korea Atomic Energy Research Institute, Dukjin-dong,

150 Yusung-gu, Taejeon 305-353, Korea

Seong-Yeon Yoo*

Department of Mechanical Design Engineering, Chungnam National University,

Guong-dong, Yusung-gu, Taejeon 305-764, Korea

It is important to completely understand heat/mass transfer from a flat plate because it is a basic element of heat/mass transfer. In the present study, local heat/mass transfer coefficient is obtained for two flow conditions to investigate the effect of boundary layer using the naphthalene sublimation technique. Obtained local heat/mass transfer coefficient is converted to dimensionless parameters such as Sherwood number, Stanton number and Colburn -factor. These also are compared with correlations of laminar and turbulent heat/mass transfer from a flat plate. According to experimental results, local Sherwood number and local Stanton number are in much better agreement with the correlation of turbulent region rather than laminar region, which means analogy between heat/mass transfer and momentum transfer is more suitable for turbulent boundary layer. But average Sherwood number and average Colburn -factor representing analogy between heat/mass transfer and momentum transfer are consistent with the correlation of laminar boundary layer as well as turbulent boundary layer.

Key Words  Naphthalene Sublimation, Heat/Mass Transfer Analogy, Flat Plate

KSME International Journal, Vol. 18 No. 8, pp. 1271-1287, 2004

<Invited Review Article> Vapor Bubble Nucleation : A Microscopic Phenomenon

Ho-Young Kwak*

Mechanical Engineering Department, Chung-Ang University,

Seoul, 156-756, Korea

In this article, vapor bubble nucleation in liquid and the evaporation process of a liquid droplet at its superheat limit were discussed from the viewpoint of molecular clustering (molecular cluster model for bubble nucleation). For the vapor bubble formation, the energy barrier against bubble nucleation was estimated by the molecular interaction due to the London dispersion force. Bubble nucleation by quantum tunneling in liquid helium under negative pressure near the absolute zero temperature and bubble nucleation on cavity free micro heaters were also presented as the homogenous nucleation processes.

Key Words  Evaporation, Molecular Cluster, Quantum Tunneling, Superheat Limit, Tensile Strength, Vapor Bubble

KSME International Journal, Vol. 18 No. 8, pp. 1288-1296, 2004

Wall-Following Control of a Two-Wheeled Mobile Robot

Tan Lam Chung*, Trong Hieu Bui, Sang Bong Kim, Myung Suck Oh

Department of Mechanical Eng., College of Eng., Pukyong National University

San 100, Yongdang-Dong, Nam-Gu, Pusan 608-739, Korea

Tan Tien Nguyen

Department of Mechanical Eng., Ho Chi Minh City University of Technology

268 Ly Thuong Kiet, Dist. 10, Ho Chi Minh City, Vietnam

Wall-following control problem for a mobile robot is to move it along a wall at a constant speed and keep a specified distance to the wall. This paper proposes wall-following controllers based on Lyapunov function candidate for a two-wheeled mobile robot (MR) to follow an unknown wall. The mobile robot is considered in terms of kinematic model in Cartesian coordinate system. Two wall-following feedback controllers are designed  full state feedback controller and observer-based controller. To design the former controller, the errors of distance and orientation of the mobile robot to the wall are defined, and the feedback controller based on Lyapunov function candidate is designed to guarantee that the errors converge to zero asymptotically. The latter controller is designed based on Busawons observer as only the distance error is measured. Additionally, the simulation and experimental results are included to illustrate the effectiveness of the proposed controllers.

Key Words  Two-Wheeled Mobile Robot, Wall-Following

KSME International Journal, Vol. 18 No. 8, pp. 1297-1305, 2004

Time-Discretization of Non-Affine Nonlinear System with Delayed Input Using Taylor-Series

Ji Hyang Park, Kil To Chong*

Division of Electronics and Information Engineering

Chonbuk National University, Duckjin-Dong, Duckjin-Gu,

Jeonju 561-756, Korea

Nikolaos Kazantzis

Department of Chemical Engineering, Worcester Polytechnic Institute

Worcester, MA 01609, U.S.A.

Alexander G. Parlos

Department of Mechanical Engineering Texas A&M University

College Station, Texas 77840, U.S.A.

In this paper, we propose a new scheme for the discretization of nonlinear systems using Taylor series expansion and the zero-order hold assumption. This scheme is applied to the sampled-data representation of a non-affine nonlinear system with constant input time-delay. The mathematical expressions of the discretization scheme are presented and the ability of the algorithm is tested for some of the examples. The proposed scheme provides a finite-dimensional representation for nonlinear systems with time-delay enabling existing controller design techniques to be applied to them. For all the case studies, various sampling rates and time-delay values are considered.

Key Words  Non-Affine, Nonlinear, Taylor-Series, Time-Delay, Time-Discretization

KSME International Journal, Vol. 18 No. 8, pp. 1306-1311, 2004

A New Approach to Anti-Sway System Design Problem

Young-Bok Kim*

Pukyong National University, San100, Yongdang-Dong, Namku, Pusan 608-739, Korea

We suggest a new type of swing motion control system for a crane system in which a small auxiliary mass is installed on the spreader. The actuator reacting against the auxiliary mass applies inertial control forces to the spreader of the container crane to reduce the swing motion in the desired manner. In this paper, as the basic and first step, we apply the  control approach to anti-sway control system design problem. And, it will be shown that the proposed control strategy is useful and it can be easily applicable to the real world. So, in this study, we investigate usefulness of the proposed anti-sway system and evaluate system performance through simulation and experimental studies.

Key Words  Swing Motion Control, Crane, Auxiliary Mass, Spreader, Anti-Sway System

KSME International Journal, Vol. 18 No. 8, p. 1312-1318, 2004

A Study on an Anti-Rolling System Design of a Ship with the Flaps

Young-Bok Kim*

Pukyong National University, San100, Yongdang-Dong, Namku, Pusan 608-739, Korea

Roll stabilization systems for ships are employed to increase comfort for passengers, maintain full working capabilities for members of the crew and prevent cargo damage. In this paper, we have investigated the usefulness of active stabilizing system to reduce ship rolling under disturbances, using varied reaction of the flaps. In the proposed anti-rolling system for a ship, the flaps as the actuator are installed on the stern to reject rolling motion induced by disturbances such as wave. The action induced by flaps depends on power of disturbances and can take the ship balance. Especially, in this study we define the system parameters under the given system structure and design the controller to evaluate the usefulness of the proposed system.

Key Words  Ship Rolling, Flap, Anti-Rolling System, Stern, Wave, Disturbance

KSME International Journal, Vol. 18 No. 8, pp. 1319-1326, 2004

Transient EHL Analysis on Spur Gear Teeth with Consideration of Gear Kinematics

Young-Pil Koo*

School of Mechanical Engineering, Pukyong National University, Busan,

608-739, Korea

Transient 3-dimensional elasto-hydrodynamic lubrication (EHL) analysis is performed on the contacting teeth surfaces of involute spur gears. Kinematics of the gear and the pinion are taken into account to get accurate geometric clearance around the EHL region of the contacting teeth. The surface pressure and film thickness distribution for the whole contact faces in a lubricated condition at several time steps are obtained through the analysis. Besides the pressure spike at the outlet region, a representative phenomenon in EHL regime, the pressure at the inlet region is slightly higher than that of the center region. The film thickness of transient condition is thicker than that of steady condition.

Key Words  Elasto-Hydrodynamic Lubrication, Spur Gear, Kinematics, Transient

KSME International Journal, Vol. 18 No. 8, p. 1327-1337, 2004

Optimum Tire Contour Design Using Systematic STOM and Neural Network

Jin-Rae Cho*, Hyun-Sung Jeong, Wan-Suk Yoo, Sung-Woo Shin

School of Mechanical Engineering, Pusan National University,

Busan 609-735, Korea

An efficient multi-objective optimization method is presented making use of neural network and a systematic satisficing trade-off method (STOM), in order to simultaneously improve both maneuverability and durability of tire. Objective functions are defined as follows  the sidewall-

carcass tension distribution for the former performance while the belt-edge strain energy density for the latter. A back-propagation neural network model approximates the objective functions to reduce the total CPU time required for the sensitivity analysis using finite difference scheme. The satisficing trade-off process between the objective functions showing the remarkably conflicting trends each other is systematically carried out according to our aspiration-level adjustment procedure. The optimization procedure presented is illustrated through the optimum design simulation of a representative automobile tire. The assessment of its numerical merit as well as the optimization results is also presented.

Key Words  Multi-Objective Optimization, Tire Sidewall Contour, Maneuverability and Durability, Systematic STOM, Back-Propagation Neural Network, CPU Time

KSME International Journal, Vol. 18 No. 8, pp. 1338-1348, 2004

Simplified Modeling of Deflagration in Vessels

Joon Hyun Kim, Joo-Hyun Kim*

School of Mechanical and Automotive Engineering, Kookmin University,

861-1, Chongnung-dong, Songbuk-gu, Seoul 136-702, Korea

A simplified method that models the deflagration process occurring in closed or vented vessels is described. When combustion occurs within the spherical or cylindrical vessels, the flame moves spherically or segmentally to the vessel periphery. The volume and area of each element along the propagating flame front are calculated by using simple geometrical rules. For instabilities and turbulence resulting in enhanced burning rates, a simple analysis results in reasonable agreement with the experimental pressure transients when two burning rates (a laminar burning rate prior to the onset of instability and an enhanced burning rate) were used. Pressure reduction caused by a vent opening at predetermined pressure was modeled. Parameters examined in the modeling include ignition location, mixture concentration, vented area, and vent opening pressure. It was found that venting was effective in reducing the peak pressure experienced in vessels. The model can be expected to estimate reasonable peak pressures and flame front distances by modeling the enhanced burning rates, that is, turbulent enhancement factor.

Key Words  Deflagration, Explosions, Flame, Gas Dynamics

KSME International Journal, Vol. 18 No. 8, pp. 1349-1357, 2004

A Computer-Aided Inspection Planning System for On-Machine Measurement - Part I  Global Inspection Planning -

Honghee Lee, Myeong-Woo Cho*, Gil-Sang Yoon, Jin-Hwa Choi

Division of Mechanical Engineering, Inha University

253 Yonghyun-dong, Nam-gu, Incheon 402-751, Korea

Computer-Aided Inspection Planning (CAIP) is the integration bridge between CAD/CAM and Computer Aided Inspection (CAI). A CAIP system for On-Machine Measurement (OMM) is proposed to inspect the complicated mechanical parts efficiently during machining or after machining. The inspection planning consists of Global Inspection Planning (GIP) and Local Inspection Planning (LIP). In the GIP, the system creates the optimal inspection sequence of the features in a part by analyzing the various feature information such as the relationship of the features, Probe Approach Directions (PAD), etc. Feature groups are formed for effective planning, and special feature groups are determined for sequencing. The integrated process and inspection plan is generated based on the sequences of the feature groups and the features in a feature group. A series of heuristic rules are developed to accomplish it. In the LIP of Part II, the system generates inspection parameters. The integrated inspection planning is able to determine optimum manufacturing sequence for inspection and machining processes. Finally, the results are simulated and analyzed to verify the effectiveness of the proposed CAIP.

Key Words  Computer-Aided Inspection Planning (CAIP), Geometric Feature, Feature Group, On Machine Measurement (OMM)

KSME International Journal, Vol. 18 No. 8, pp. 1358-1367, 2004

A Computer-Aided Inspection Planning System for On-Machine Measurement - Part II  Local Inspection Planning -

Myeong-Woo Cho*, Honghee Lee, Gil-Sang Yoon, Jin-Hwa Choi

Division of Mechanical Engineering, Inha University

253 Yonghyun-dong, Nam-gu, Incheon 402-751, Korea

As a part II of theis research, new local inspection planning strategy is proposed in this paper based on the proposed inspection feature extraction method. In the local inspection planning stage, each feature is decomposed into its constituent geometric elements for more effective inspection planning. The local inspection planning for the decomposed features are performed to determine  (1) the suitable number of measuring points, (2) their locations, and (3) the optimum probing paths to minimize measuring errors and times. The fuzzy set theory, the Hammersleys algorithm and the TSP method are applied for the local inspection planning. Also, a new collision checking algorithm is proposed for the probe and/or probe holder based on the Z-map concept. Finally, the results are simulated and analyzed to verify the effectiveness of the proposed methods.

Key Words  Computer-Aided Inspection Planning (CAIP), Geometric Feature, Collision

Avoidance, On-Machine Measurement (OMM)

KSME International Journal, Vol. 18 No. 8, pp. 1368-1374, 2004

DC Potential Drop Method for Evaluating Material Degradation

Chang-Sung Seok*

School of Mechanical Engineering, Sungkyunkwan University,

300 Chunchun-dong, Jangan-gu, Suwon, Kyonggi-do 440-746, Korea

Bong-Kook Bae

Graduate School, School of Mechanical Engineering, Sungkyunkwan University,

300 Chunchun-dong, Jangan-gu, Suwon, Kyonggi-do 440-746, Korea

Jae-Mean Koo

School of Mechanical Engineering, Sungkyunkwan University,

300 Chunchun-dong, Jangan-gu, Suwon, Kyonggi-do 440-746, Korea

The remaining life estimation for the aged components in power plants as well as chemical plants are very important because mechanical properties of the components are degraded with in-service exposure time in high temperatures. Since it is difficult to take specimens from the operating components to evaluate mechanical properties of components, nondestructive techniques are needed to evaluate the degradation. In this study, test materials with several different degradation levels were prepared by isothermal aging heat treatment at 630 oC. The DC potential drop method and destructive methods such as tensile and fracture toughness were used in order to evaluate the degradation of 1Cr-1Mo-0.25V steels. In this result, we can see that tensile strength and fracture toughness can be calculated from resistivity and it is possible to evaluate material degradation using DC potential drop method, non-destructive method.

Key Words  DC Potential Drop Method, Resistivity, Degradation, Four-Point Probe, Fracture Toughness, Tensile Strength

KSME International Journal, Vol. 18 No. 8, pp. 1375-1387, 2004

Elastodynamic Response of a Crack Perpendicular to the Graded Interfacial Zone in Bonded Dissimilar Materials Under Antiplane Shear Impact

Sungho Kim, Hyung Jip Choi*

School of Mechanical and Automotive Engineering, Kookmin University,

Seoul 136-702, Korea

A solution is given for the elastodynamic problem of a crack perpendicular to the graded interfacial zone in bonded materials under the action of antiplane shear impact. The interfacial zone is modeled as a nonhomogeneous interlayer with the power-law variations of its shear modulus and mass density between the two dissimilar, homogeneous half-planes. Laplace and Fourier integral transforms are employed to reduce the transient problem to the solution of a Cauchy-type singular integral equation in the Laplace transform domain. Via the numerical inversion of the Laplace transforms, the values of the dynamic stress intensity factors are obtained as a function of time. As a result, the influences of material and geometric parameters of the bonded media on the overshoot characteristics of the dynamic stress intensities are discussed. A comparison is also made with the corresponding elastostatic solutions, addressing the inertia effect on the dynamic load transfer to the crack tips for various combinations of the physical properties.

Key Words  Bonded Dissimilar Materials, Functionally Graded Materials, Interfacial Zone, Mode III Dynamic Stress Intensity Factors

KSME International Journal, Vol. 18 No. 8, pp. 1388-1400, 2004

Improvement of the Control Performance of Pneumatic Artificial Muscle Manipulators Using an Intelligent Switching Control Method

KyoungKwan AHN*, TU Diep Cong Thanh

School of Mechanical and Automotive Engineering, University of Ulsan,

San 29, Muger 2dong, Nam-gu, Ulsan, 680-764, Korea

Problems with the control, oscillatory motion and compliance of pneumatic systems have prevented their widespread use in advanced robotics. However, their compactness, power/weight ratio, ease of maintenance and inherent safety are factors that could be potentially exploited in sophisticated dexterous manipulator designs. These advantages have led to the development of novel actuators such as the McKibben Muscle, Rubber Actuator and Pneumatic Artificial Muscle Manipulators. However, some limitations still exist, such as a deterioration of the performance of transient response due to the changes in the external inertia load in the pneumatic artificial muscle manipulator.

To overcome this problem, a switching algorithm of the control parameter using a learning vector quantization neural network (LVQNN) is newly proposed. This estimates the external inertia load of the pneumatic artificial muscle manipulator. The effectiveness of the proposed control algorithm is demonstrated through experiments with different external inertia loads.

Key Words  Pneumatic Artificial Muscle, Neural Network, Switching Control, Intelligent Control

KSME International Journal, Vol. 18 No. 8, pp. 1401-1417, 2004

Experimental and Computational Studies on Flow Behavior Around Counter Rotating Blades in a Double-Spindle Deck

Woochong Chon*

Nuclear Safety Analysis Department, Korea Nuclear Fuel Co. Ltd,

493 Deokjin-dong, Yuseong-gu, Daejeon 305-353, Korea

Ryoichi S. Amano

Dept. of Mechanical Engineering, University of Wisconsin-Milwaukee,

PO Box 784, Milwaukee, WI 53201, U.S.A.

Experimental and computational studies were performed to determine the effects of different blade designs on a flow pattern inside a double-spindle counter rotating mower deck. In the experimental study, two different blade models were tested by measuring air velocities using a forward-scatter LDV system. The velocity measurements were taken at several different azimuth and axial sections inside the deck. The measured velocity distributions clarified the air flow pattern caused by the rotating blades and demonstrated the effects of deck and blade designs. A high-speed video camera and a sound level meter were used for flow visualization and noise level measurement. In the computational works, two-dimensional blade shapes at several arbitrary radial sections have been selected for flow computations around the blade model. For three-dimensional computation applied a non-inertia coordinate system, a flow field around the entire three-dimensional blade shape is used to evaluate flow patterns in order to take radial flow interactions into account. The computational results were compared with the experimental results.

Key Words  Experimental Investigation, Computational Fluid Dynamics (CFD), Laser Doppler Velocimetry (LDV), Lawn Mower, Rotating Blades, Flow Behavior

KSME International Journal, Vol. 18 No. 8, pp. 1418-1427, 2004

Simulation of Biocube-Fluid Mixture Using Combined Formulation

Hyoung-gwon Choi*

Corresponding Author, Full-time Lecturer, Department of Mechanical Engineering,

Seoul National University of Technology, Seoul 139-743, Korea

Myeong-ho Lee, Ho Taek Yong

Department of Mechanical Engineering, Seoul National University of Technology,

Seoul 139-743, Korea

Combined formulation developed for the fluid-particle mixture is introduced to simulate the biocube-fluid mixture flow, which is utilized for sewage disposal. Some tricky boundary conditions are introduced in order to simulate the effect of screen wall and air bubble, which is injected from the bottom of sewage reservoir. It has been shown that a circulated flow pattern, which was observed in experiment, is reproduced from the present numerical simulation. Furthermore, the effect of biocube density on the distribution pattern of biocube is also studied. It has been shown that a biocube whose density is slightly smaller than that of surrounding fluid or neutrally buoyant one are optimal for the uniform distribution of biocube.

Key Words  Combined Formulation, Biocube-Fluid Mixture, Boundary Conditions

KSME International Journal, Vol. 18 No. 8, pp. 1428-1434, 2004

Mean Streamline Analysis for Performance Prediction of Cross-Flow Fans

Jae Won Kim*

Department of Mechanical Engineering, Sunmoon University,

Asan City, Chung Nam, Korea

Hyoung Woo Oh

Department of Mechanical Engineering, Chungju National University,

Chungju, Chungbuk, Korea

This paper presents the mean streamline analysis using the empirical loss correlations for performance prediction of cross-flow fans. Comparison of overall performance predictions with test data of a cross-flow fan system with a simplified vortex wall scroll casing and with the published experimental characteristics for a cross-flow fan has been carried out to demonstrate the accuracy of the proposed method. Predicted performance curves by the present mean streamline analysis agree well with experimental data for two different cross-flow fans over the normal operating conditions. The prediction method presented herein can be used efficiently as a tool for the preliminary design and performance analysis of general-purpose cross-flow fans.

Key Words  Cross-Flow Fan, Mean Streamline Analysis, Loss Correlation, Performance Prediction

KSME International Journal, Vol. 18 No. 8, pp. 1435-1450, 2004

Effects of Combustor-Level High Inlet Turbulence on the Endwall Flow and Heat/Mass Transfer of a High-Turning Turbine Rotor Cascade

Sang Woo Lee*, Sang Bae Jun

School of Mechanical Engineering Kumoh National Institute of Technology

188 Shinpyong, Gumi, Gyongbook 730-701, Korea

Byung-Kyu Park, Joon Sik Lee

School of Mechanical and Aerospace Engineering Seoul National University

Seoul 151-742, Korea

Experimental data are presented which describe the effects of a combustor-level high free-stream turbulence on the near-wall flow structure and heat/mass transfer on the endwall of a linear high-turning turbine rotor cascade. The endwall flow structure is visualized by employing the partial- and total-coverage oil-film technique, and heat/mass transfer rate is measured by the naphthalene sublimation method. A turbulence generator is designed to provide a highly-turbulent flow which has free-stream turbulence intensity and integral length scale of 14.7% and 80mm, respectively, at the cascade entrance. The surface flow visualizations show that the high free-stream turbulence has little effect on the attachment line, but alters the separation line noticeably. Under high free-stream turbulence, the incoming near-wall flow upstream of the adjacent separation lines collides more obliquely with the suction surface. A weaker lift-up force arising from this more oblique collision results in the narrower suction-side corner vortex area in the high turbulence case. The high free-stream turbulence enhances the heat/mass transfer in the central area of the turbine passage, but only a slight augmentation is found in the endwall regions adjacent to the leading and trailing edges. Therefore, the high free-stream turbulence makes the endwall heat load more uniform. It is also observed that the heat/mass transfers along the locus of the pressure-side leg of the leading-edge horseshoe vortex and along the suction-side corner are influenced most strongly by the high free-stream turbulence. In this study, the endwall surface is classified into seven different regions based on the local heat/mass transfer distribution, and the effects of the high free-stream turbulence on the local heat/mass transfer in each region are discussed in detail.

Key Words  Gas Turbine, Turbine Rotor, Endwall, Combustor-Level Turbulence, Turbulence Intensity, Integral Length Scale, Near-Wall Flow, Heat/Mass Transfer

KSME International Journal, Vol. 18 No. 8, pp. 1451-1460, 2004

Analysis of Compression Ignition Combustion in a Schnurle-Type Gasoline Engine - Comparison of performance between direct injection and port injection systems -

Seok Woo Kim*

Graduate School of Science and Technology, Chiba University

1-33 Yayoi-cho, Inage-ku, Chiba, 263-8522, Japan

Yasuo Moriyoshi

Dept. of Electronics and Mechanical Engineering, Chiba University,

1-33 Yayoi-cho, Inage-ku, Chiba, 263-8522, Japan

A two-stroke Schnurle-type gasoline engine was modified to enable compression-ignition in both the port fuel injection and the in-cylinder direct injection. Using the engine, examinations of compression-ignition operation and engine performance tests were carried out. The amount of the residual gas and the in-cylinder mixture conditions were controlled by varying the valve angle rate of the exhaust valve (VAR) and the injection timing for direct injection conditions. It was found that the direct injection system is superior to the port injection system in terms of exhaust gas emissions and thermal efficiency, and that almost the same operational region of compression-ignition at medium speeds and loads was attained. Some interesting combustion characteristics, such as a shorter combustion period in higher engine speed conditions, and factors for the onset of compression-ignition were also examined.

Key Words  Gasoline Engine, Compression-Ignition Engine, Two-Stroke Engine,

Fuel Injection, Homogeneous Charge Compression Ignition

KSME International Journal, Vol. 18 No. 8, pp. 1461-1469, 2004

Numerical Analysis of Acoustic Characteristics in Gas Turbine Combustor with Spatial Non-homogeneity

Chae Hoon Sohn*

Department of Aerospace Engineering, Chosun University,

Gwangju 501-759, Korea

Han Chang Cho

Research Institute of Industrial Science and Technology, San 32 Hyoja-dong,

Nam-gu, Pohang 790-600, Korea

Acoustic characteristics in an industrial gas-turbine combustor are numerically investigated by a linear acoustic analysis. Spatially non-homogeneous temperature field in the combustor is considered in the numerical calculation and the characteristics are analyzed in view of acoustic instability. Acoustic analyses are conducted in the combustors without and with acoustic resonator, which is one of the acoustic-damping devices or combustion stabilization devices. It has been reported that severe pressure fluctuation frequently occurs in the adopted combustor, and the measured signal of pressure oscillation is compared with the acoustic-pressure response from the numerical calculation. The numerical results are in good agreement with the measurement data. In this regard, the phenomenon of pressure fluctuation in the combustor could be caused by acoustic instability. From the numerical results for the combustor with present acoustic resonators installed, the acoustic effects of the resonators are analyzed in the viewpoints of both the frequency tuning and the damping capacity. It is found that the resonators with present specifications are not optimized and thus, the improved specification or design is required.

Key Words  Acoustic Characteristics, Acoustic Instability, Gas Turbine Combustor, Acoustic Resonators

KSME International Journal, Vol. 18 No. 8, pp. 1470-1478, 2004

A Lagrangian Based Scalar PDF Method for Turbulent Combustion Models

Hee-Jang Moon*

School of Aerospace and Mechanical Engineering, Hankuk Aviation University

200-1 Hwajeon-dong, Duckyang-gu, Koyang-shi, Kyungki-do 412-791, Korea

Roland Borghi

IRPHE-UMR 6594 CNRS, ESM2 Technopole de Chateau Gombert,

13451 Marseille Cedex 20, France

In this paper, a new "presumed" Probability Density Function (PDF) approach coupled with a Lagrangian tracking method is proposed for turbulent combustion modeling. The test and the investigation of the model are conducted by comparing the model results with DNS data for a premixed flame subjected in a decaying turbulent field. The newly constructed PDF, which incorporates the instantaneous chemical reaction term, demonstrates consistent improvement over conventional assumed PDF models. It has been found that the time evolution of the mean scalar, the variance and the mean reaction rate are strongly influenced by a parameter deduced by a Lagrangian equation which takes into account explicitly the local reaction rate. Tests have been performed for a moderate Damkohler number, and it is expected the model may cover a broader range of Damkohler number. The comparison with the DNS data demonstrates that the proposed model may be promising and affordable for implementation in a moment-equation solver.

Key Words  Turbulent Premixed Flame, Lagrangian Trajectory, Presumed PDF Method, Turbulent Combustion Modeling

KSME International Journal, Vol. 18 No. 8, pp. 1479-1489, 2004

A Modeling Study of Local Equivalence Ratio Fluctuation in Imperfectly Premixed Turbulent Flames

Hee-Jang Moon*

School of Aerospace and Mechanical Engineering, Hankuk Aviation University

200-1 Hwajeon-dong, Duckyang-gu, Koyang-shi, Kyungki-do 412-791, Korea

The effect of fluctuation of Equivalence Ratio (ER) in a turbulent reactive field has been studied in order to check the global combustion characteristics induced by the local fluctuation. When the flow is premixed on a large scale, closer examination on a small scale reveals that local fluctuations of ER exist in an imperfectly premixed mixture, and that these fluctuations must be considered to correctly estimate the mean reaction rate. The fluctuation effect is analyzed with DNS by considering the joint PDF of reactive scalar and ER, followed by modeling study where an extension of stochastic mixing models accounting for the ER fluctuation is reviewed and tested. It was found that models prediction capability as well as its potential is in favor to this case accounting the local ER fluctuation. However, the effect of local fluctuation did not show any notable changes on the mean global characteristics of combustion when statistical inde-pendence between the reactive scalar and ER field is imposed, though it greatly influenced the joint PDF distribution. The importance of taking into account the statistical dependency between ER and combustible at the initial phase is demonstrated by testing the modeled reaction rate.

Key Words  Equivalence Ratio Fluctuation, PDF Balance Method, Small Scale Mixing Model, Turbulent Combustion

KSME International Journal, Vol. 18 No. 9, pp. 1439-1499, 2004

Non-Destructive Evaluation of Separation and Void Defect of a Pneumatic Tire by Speckle Shearing Interferometry

Koungsuk Kim

Department of Mechanical Information Engineering, Chosun University

375 Seosuk-dong Dong-gu, Gwangju, 501-759 South Korea

Kisoo Kang, Hyunchul Jung

Graduate school, Chosun University,

375 Seosuk-dong Dong-gu, Gwangju, 501-759 South Korea

Nakyong Ko

Department of Information and Control Engineering, Chosun University

375 Seosuk-dong Dong-gu, Gwangju, 501-759 South Korea

This paper describes the speckle shearing interferometry, a non-destructive optical method, for quantitative estimation of void defect and monitoring separation defect inside of a pneumatic tire. Previous shearing interferometry has not supplied quantitative result of inside defect, due to effective factors. In the study, factors related to the details of an inside defect are classified and optimized with pipeline simulator. The size and the shape of defect can be estimated accurately to find a critical point and was closely related with shearing direction. The technique is applied for quantitative estimation of defects inside of a pneumatic tire. The actual traveling tire is monitored to reveal the cause of separation and the starting points. And also unknown void defects on tread is inspected and the size and shape of defects is estimated which has good agreement with the result of visual inspection.

Key words: Speckle Shearing Interferometry, Pneumatic Tire, Quantitative Estimation, Separation Defect, Void Defect, Effective Factor, Amount of Shearing

KSME International Journal, Vol. 18 No. 9, pp. 1500-1511, 2004

Transient Response of a Permeable Crack Normal to a Piezoelectric-elastic Interface: Anti-plane Problem

Soon Man Kwona

Department of Mechanical Design & Manufacturing, Changwon National University,

9 Sarim-dong, Changwon, Kyongnam 641-773, Korea

Kang Yong Lee

School of Mechanical Engineering, Yonsei University, Seoul 120-749, Korea

In this paper, the anti-plane transient response of a central crack normal to the interface between a piezoelectric ceramics and two same elastic materials is considered. The assumed crack surfaces are permeable. By virtue of integral transform methods, the electroelastic mixed boundary problems are formulated as two set of dual integral equations, which, in turn, are reduced to a Fredholm integral equation of the second kind in the Laplace transform domain. Time domain solutions are obtained by inverting Laplace domain solutions using a numerical scheme. Numerical values on the quasi-static stress intensity factor and the dynamic energy release rate are presented to show the dependences upon the geometry, material combination, electromechanical coupling coefficient and electric field.

Key Words : Anti-plane Shear Impact, Piezoelectric-elastic Composites, Permeable Crack,             Intensity Factors, Electromechanical Coupling Coefficient

KSME International Journal, Vol. 18 No. 9, pp. 1512-1518, 2004

##### Optimal Design of Truss Structures by Rescaled Simulated Annealing

Jungsun Park, Miran Ryu

School of Aerospace and Mechanical Engineering, Hankuk Aviation University,

200-1, Hwajon-dong, Deokyang-gu, Koyang-si, Kyonggi-do, 412-791, Korea.

Rescaled Simulated Annealing (RSA) has been adapted to solve combinatorial optimization problems in which the available computational resources are limited. Simulated Annealing (SA) is one of the most popular combinatorial optimization algorithms because of its convenience of use and because of the good asymptotic results of convergence to optimal solutions. However, SA is too slow to converge in many problems. RSA was introduced by extending the Metropolis procedure in SA. The extension rescales the state’s energy candidate for a transition before applying the Metropolis criterion. The rescaling process accelerates convergence to the optimal solutions by reducing transitions from high energy local minima. In this paper, structural optimization examples using RSA are provided. Truss structures of which design variables are discrete or continuous are optimized with stress and displacement constraints. The optimization results by RSA are compared with the results from classical SA. The comparison shows that the numbers of optimization iterations can be effectively reduced using RSA.

key words: Optimization, Rescaled Simulated Annealing, Truss Structure

KSME International Journal, Vol. 18 No. 9, pp. 1519-1528, 2004

##### Re-Entry Trajectory Tracking Via an Inverse Dynamics Method

Dae-Woo Lee, Kyeum-Rae Cho

Department of Aerospace Engineering Pusan National University,

Jangjun-Dong, Kumjung-Ku, Pusan, #609-735, Korea

Hui Yan

Department of Mathematics, Texas A&M, #77843, USA

Atmospheric Re-Entry guidance is divided as longitudinal and lateral. This paper proposes a longitudinal reference trajectory and control law using the inverse dynamics method with pseudospectral Legendre method. Application of this method into Re-Entry problem forces a power of calculation time-reduction due to unnecessary of integration or any iteration as well as sufficient accuracy convergence. The used guidance scheme is time-to-go.

Key words : Atmospheric Re-Entry(RE), Reference Trajectory, Tracking, Pseudospectral Legendre Method, Inverse Dynamic Method, Linear Algebraic Equations

KSME International Journal, Vol. 18 No. 9, pp. 1529-1536, 2004

##### An Analytical Approach for Structural Synthesis of Substructures

Hee-Chang Eun

Division of Architectural Engineering, Kangwon National University, Chuncheon, Korea

Sang-Yeol Park

Division of Civil and Environmental  Engineering, Cheju National University, Jeju, Korea

Eun-Taik Lee

Division of Architectural Engineering, Chung-Ang University, Seoul, Korea

A structure is broken down into a number of substructures by means of the finite element method and the substructures are synthesized for the complete structure.  The divided substructures take two types: fixed-free and free-free elements.  The flexibility and stiffness matrices of the free-free elements are the Moore-Penrose inverse of each other.  Thus, it is not easy to determine the equilibrium equations of the complete structure composed of two mixed types of substructures.  This study provides the general form of equilibrium equation of the entire structure through the process of assembling the equilibrium equations of substructures with end conditions of mixed types.  Applications demonstrate that the proposed method is effective in the structural analysis of geometrically complicated structures.

Key words: substructuring, compatibility, equilibrium equation, constraint, synthesis method

KSME International Journal, Vol. 18 No. 9, pp. 1537-1548, 2004

Diagnostics and prognostics based on adaptive time-frequency feature discrimination

Jae Hyuk Oh, Chang Gu Kim, Young Man Cho

School of Mechanical and Aerospace Engineering, Seoul National University, Seoul 151-742, Korea

This paper presents a novel diagnostic technique for monitoring the system conditions and detecting failure modes and precursors based on wavelet-packet analysis of external noise/vibration measurements. The capability is based on extracting relevant features of noise/vibration data that best discriminate systems with different noise/vibration signatures by analyzing external measurements of noise/vibration in the time-frequency domain. By virtue of their localized nature both in time and frequency, the identified features help to reveal faults at the level of components in a mechanical system in addition to the existence of certain faults. A prima-facie case is made via application of the proposed approach to fault detection in scroll and rotary compressors, although the methods and algorithms are very general in nature. The proposed technique has successfully identified the existence of specific faults in the scroll and rotary compressors. In addition, its capability of tracking the severity of specific faults in the rotary compressors indicates that the technique has a potential to be used as a prognostic tool.

Keywords: diagnostic, wavelet packet, time-frequency analysis, noise and vibration, rotary compressor, scroll compressor

KSME International Journal, Vol. 18 No. 9, pp. 1549-1558, 2004

Central Crack in a Piezoelectric Disc

Jong Ho Kwon

Department of Automotive Engineering, ShinHeung College, 117 Howon-dong, Uijeongbu, Gyeonggi 480-701, Korea

This study is concerned with the general solution of the field intensity factors and energy release rate for a Griffith crack in a piezoelectric ceramic of finite radius under combined anti-plane mechanical and in-plane electrical loading.  Both electrically continuous and impermeable crack surface conditions are considered.  Employing Mellin transforms and Fourier series, the problem is reduced to dual integral forms.  The solution to the resulting expressions is expressed in terms of Fredholm integral equation of the second kind.  The solutions are provided to study the influence of the crack length, the crack surface boundary conditions on the intensity factors and the energy release rate.

Keywords: Piezoelectric disc, central crack, crack boundary condition, intensity factors, energy release rate, integral transform

KSME International Journal, Vol. 18 No. 9, pp. 1559-1564, 2004

Process Design for the Hot Forging of Asymmetric Rail to Symmetric Rail

Hae Yong Cho*, Yong Yun Kim

Department of Mechanical Engineering, Chungbuk National University, San 48, Gaesin-Dong, Heungduk-Gu, Cheongju, Chungbuk 361-763, Korea

Ki Joung Lee, Sung Ho Lee

LG Industrial Systems Co., Ltd., Songjung-Dong, Heungduk-Gu, Cheongju, Chungbuk  361-720, Korea

Byung Ki Oh and Gi Jung Nam

Graduate School of Mechanical Engineering, Chungbuk National University, San 48, Gaesin-Dong, Heungduk-Gu, Cheongju, Chungbuk 361-763, Korea

The process design of hot forging, asymmetric to symmetric rib-web shaped steel, which is used for the turnout of express rails has been studied. Owing to the great difference in shape between the initial billet and the final forged product, it is impossible to hot forge the rail in a single stage operation. The numerical simulation for hot forging of asymmetric shape to symmetric shape was carried out by using commercial FEM code, DEFORMTM-2D. For comparison with the simulation results, a experiment of flow analysis using plasticine was also carried out. The results of the flow experiment showed good agreement with those of the simulation.

Key Words: Asymmetric, High Speed Rail, Hot Forging, Symmetric, Process Design

KSME International Journal, Vol. 18 No. 9, pp. 1565-1571, 2004

Non-Stationary Response of a Vehicle Obtained From a Series of Stationary Responses

Tuncay KARACAY*, Nizami AKTURK, Mehmet EROGLU, BA

Gazi University, Faculty of Engineering and Architecture, Department of Mechanical Engineering

Maltepe, Ankara, Turkey

Ride characteristics of a vehicle moving on a rough ground with changing travel velocity are analyzed in this paper. The solution is difficult due to the non-stationary characteristics of the problem. Hence a new technique has been proposed to overcome this difficulty. This new technique is employed in the analysis of ride characteristics of a vehicle with changing velocity in the time/frequency domain. It is found that the proposed technique gives successful results in modelling non-stationary responses in terms of a series of stationary responses.

Keywords: Ride characteristics, random vibrations, nonstationary processes

KSME International Journal, Vol. 18 No. 9, pp. 1572-1581, 2004

Application of the Axiomatic Design Methodology on the Design of PBGA Package with Polyimide Coating Layer

Ji Hyuck Yang

Hyundai Motor Company, 772-1, Jangduk-Dong, Whasung-Si, Gyunggi-Do, 445-706, Korea

Kang Yong Lee*, C. Y. Dong

School of Mechanical Engineering, Yonsei University, SinchonDong, SeodaemoonGu, Seoul 120-749, Korea

The purposes of the paper are to apply the axiomatic design methodology on the design of PBGA package with polyimide coating under hygrothermal loading in the IR soldering process and to suggest more reliable design conditions by the approaches of stress analysis. The model for analysis is the 256-pin perimeter Plastic Ball Grid Array (PBGA) package with the polyimide coating surrounding chip and above surface of BT-substrate. The polyimide coating is suggested to depress the maximum stresses on the stress concentration positions. The axiomatic design methodology is proved to be useful to find the more reliable design conditions of PBGA package. Finally, the optimal values of design variables to depress the stress in the PBGA package are obtained.

Key word : BGA Package, IR soldering, Axiomatic design, polyimide coating, stress

KSME International Journal, Vol. 18 No. 9, pp. 1582-1589, 2004

Dynamic Characteristics of an Eccentric Crack in a Functionally Graded Piezoelectric Ceramic Strip

Jeong Woo Shin*

Korea Aerospace Research Institute, 45 Eoeun-Dong, YouSeong-Gu, Daejeon, 305-333, Korea.

Tae-Uk Kim

Korea Aerospace Research Institute, 45 Eoeun-Dong, YouSeong-Gu, Daejeon, 305-333, Korea.

Sung Chan Kim

Korea Aerospace Research Institute, 45 Eoeun-Dong, YouSeong-Gu, Daejeon, 305-333, Korea.

The dynamic response of an eccentric Griffith crack in functionally graded piezoelectric ceramic strip under anti-plane shear impact loading is analysed using integral transform method. Laplace transform and Fourier transform are used to reduce the problem to two pairs of dual integral equations, which are then expressed to Fredholm integral equations of the second kind. We assume that the properties of the functionally graded piezoelectric material vary continuously along the thickness. The impermeable crack boundary condition is adopted. Numerical values on the dynamic stress intensity factors are presented for the functionally graded piezoelectric material to show the dependence of the gradient of material properties and electric loadings.

Keywords : Piezoelectric / Eccentric Crack / FGM(functionally graded material) / DSIF(dynamic stress intensity factor)

KSME International Journal, Vol. 18 No. 9, pp. 1590-1603, 2004

Shape Optimization of a Plate-Fin Type Heat Sink with Triangular-Shaped Vortex Generator

Kyoungwoo Park*, Dong-Hoon Choi

The Center of Innovative Design Optimization Technology, Hanyang University (HIT Rm # 312), 17 Haengdang-dong, Sungdong-gu, Seoul 133-791, Korea

In this study the optimization of plate-fin type heat sink with vortex generator for the thermal stability is performed numerically. The optimum solutions in the heat sink are obtained when the temperature rise and the pressure drop are minimized simultaneously. Thermal performance of heat sink is influenced by the heat sink shape such as the base-part fin width, lower-part fin width, and basement thickness. To acquire the optimal design variables automatically, the CFD and mathematical optimization are integrated. The flow and thermal fields are predicted using the finite volume method. The optimization is carried out by means of the sequential quadratic programming (SQP) method which is widely used in the constrained nonlinear optimization problem. The results show that when the temperature rise is less than 40 K, the optimal design variables are as follows; B1 = 2.584 mm, B2 = 1.741 mm, and t = 7.914 mm. Comparing with the initial design, the temperature rise is reduced by 4.2 K, while the pressure drop is increased by 9.43 Pa. The relationship between the pressure drop and the temperature rise is also presented to select the heat sink shape for the designers.

Keywords : Design Optimization, Plate-Fin Heat Sink, Vortex Generator, CFD, SQP Method

KSME International Journal, Vol. 18 No. 9, pp. 1604-1613, 2004

Evaluation of Fracture Strength and Material Degradation for Weldment of High Temperature Service Steel Using Advanced Small Punch Test

Dong-Hwan Lee*

Division of Mechanical & Aerospace System Engineering,

Chonbuk National University, Chonju, Chonbuk, Korea, 561-756

This paper presents an effective and reliable evaluation method for fracture strength and material degradation of the micro-structure of high temperature service steel weldment using advanced small punch (ASP) test developed from conventional small punch (CSP) test. For the purpose of the ASP test, a lower die with a minimized φ1.5mm diameter loading ball and an optimized deformation guide hole of φ3mm diameter were designed. The behaviors of fracture energy (ESP), ductile-brittle transition temperature (DBTT) and material degradation from the ASP test showed a definite dependency on the micro-structure of weldment. Results obtained from ASP test were compared and reviewed with results from CSP test, Charpy impact test, and hardness test. The utility and reliability of the proposed ASP test were verified by investigating fracture strength, behavior of DBTT, and fracture location of each micro-structure of steel weldment for test specimen in ASP test. It was observed that the fracture toughness in the micro-structure of FL+CGHAZ and ICHAZ decreased remarkably with increasing aging time. From studies of all micro-structures, it was observed that FGHAZ microstructure has the most excellent fracture toughness, and it showed absence of material degradation.

Key Words : Advanced Small Punch (ASP) Test, Conventional Small Punch (CSP) Test, Material Degradation, Heat Affected Zone (HAZ), Ductile-Brittle Transition Temperature (DBTT)

KSME International Journal, Vol. 18 No. 9, pp. 1614-1622, 2004

Wind Pressure Transients in the Tunnel inside a Station Caused by a Passing High Speed Train

Nahmkeon Hur

Department of Mechanical Engineering, Sogang University Sinsoo 1, Mapo, Seoul 121-742, Korea

Sa-Ryang Kim*

Department of Precision Mechanical Engineering, Kangnung National University, Chibyun 123, Gangneung, Gangwon-Do, 210-702, Korea

Wook Kim, Sangyeul Lee

Department of Mechanical Engineering, Graduate School, Sogang University Sinsoo 1, Mapo,

Seoul 121-742, Korea

When a High Speed Train (HST) passes through a station with no stop, effects of wind pressure transients caused by this passing train have to be considered for the safety of passengers on the platform and for the possible structural safety problems as well.  In Gwangmyeong and Daejeon stations of the Korean high speed railroad, tunnels inside stations for the passing train are proposed to reduce the noise and wind pressure transients to the passengers on the platform.  In the present study, transient 3-D full Navier-Stokes solutions with moving mesh to implement train movement are obtained and compared with the results obtained by the towing tank experiment.  Investigations on flow phenomena for various train speeds and design modifications are also performed.

KEYWORDS : Pressure Transient, High Speed Train, Station, Moving Mesh

KSME International Journal, Vol. 18 No. 9, pp. 1623-1629, 2004

A Study on the Rapid Bulk Combustion of Premixture Using the Radical Seeding

Myung-Jun Lee*, Jong-Youl Kim

Department of Automotive Engineering, Yangsan College, Kyeongnam 626-740, Korea

Jong-Sang Park

Graduate school, Donga University,  Busan, 604-714, Korea

Jeong-Kuk Yeom, Sung-Sik Chung

Department of Mechanical Engineering, Donga University, Busan 604-714, Korea

The objective of this study is the rapid bulk combustion of mixture in a constant volume chamber with a tiny sub-chamber. Some narrow passage holes were arranged to induce simultaneous multi-point ignition in the main chamber by jet of burned and unburned gases including radicals from the sub-chamber, and the equivalence ratios of pre-mixture in the main chamber and the sub-chamber were the same. The principal factors of the Radical Induced Auto-Ignition (RIAI) method are the diameter of the passage holes and the volume of sub-chamber. The relationship between the sub-chamber and diameter of passage hole was represented by the ratios of sub-chamber volume to passage hole volume. The ratios are non-dimensional coefficients for sub-chamber characteristics. As a result, the RIAI method reduced the combustion period, which expanded the lean limit in comparison with SI method.

Key Words : Rapid Bulk Combustion, Constant Volume Chamber, Sub-Chamber, Radical Induced Auto-Ignition method(RIAI), Lean Limit

KSME International Journal, Vol. 18 No. 9, pp. 1630-1639, 2004

A Study on Correlation between Pressure Variations and Augmentation of Heat Transfer in Acoustic Fields

Yool Kwon Oh*

Department of Mechatronics Engineering, Chosun University, 375 Seosuk-dong, Dong-gu,

Gwangju 501-759, Korea

Ho Dong Yang

Department of Precision Mechanical Engineering, Chosun University, 375 Seosuk-dong, Dong-gu,

Gwangju 501-759, Korea

The present paper investigated the correlation between the acoustic pressure variations and the augmentation of heat transfer in the ultrasonic induced acoustic fields. The augmentation ratios of heat transfer coefficient were experimentally measured and were compared with the profile of the pressure distribution in the acoustic fields predicted by numerical analysis. For numerical analysis, a coupled finite element-boundary element method (coupled FE-BEM) was applied. The results of the present study reveal that the acoustic pressure is higher near two ultrasonic transducers than other points where no ultrasonic transducer was installed. The augmentation trend of heat transfer is similar with the profile of the acoustic pressure distribution. In other words, as the acoustic pressure increases, the higher augmentation ratio of heat transfer is obtained. Numerical and experimental studies clearly show that the acoustic pressure variations are closely related to the augmentation of heat transfer in the acoustic fields.

Key Words : Acoustic Pressure, A Coupled FE-BEM, Ultrasonic vibrations, Acoustic Fields, Acoustic   Streaming, Ultrasonic wave, Wave Speed

KSME International Journal, Vol. 18 No. 9, pp. 1640-1647, 2004

A Effect of Water Induction on the Performance and Exhaust Emissions in Diesel Engine (Ⅱ)

Kyunghyun Ryu* , Youngtaig Oh

Department of Mechanical Engineering, Chonbuk National University,

1-664-14, Duckjin-Dong, Duckjin-gu, Jeonju, Chonbuk, 561-756, Korea

This study was to investigate the effects of water induction through the air intake system on the characteristics of combustion and exhaust emissions in an IDI diesel engine. The fuel injection timing was also controlled to investigate a method for the simultaneous reduction of smoke and NOx when water was injected into the combustion chamber.

The formation of NOx was significantly suppressed by decreasing the gas peak temperature during the initial combustion process because the water played a role as a heat sink during evaporating in the combustion chamber, while the smoke was slightly increased with increased water amount. Also, NOx emission was significantly decreased with increase in water amount.

A simultaneous reduction in smoke and NOx emissions was obtained when water was injected into the combustion chamber by retarding more 2 ℃A of the fuel injection timing than without water injection.

Key Words : Water Injection, Fuel Injection Timing, Diesel Engine, Intake Port, Smoke, Nox

KSME International Journal, Vol. 18 No. 9, pp. 1648-1660, 2004

Effect of Suction Nozzle Modification on the Performance and Aero-acoustic Noise of a Vacuum Cleaner

Cheol-Woo Park

School of Mechanical Engineering, Kyungpook National University, Daegu, 702-701, Korea

Sang-Ik Lee, Sang-Joon Lee*

Department of Mechanical Engineering, Pohang University of Science and Technology, Pohang, 790-784, Korea

The suction nozzle of a vacuum cleaner was modified to enhance the power performance and to reduce the airflow-induced acoustic noise. The suction power efficiencies of the vacuum cleaner were measured for various nozzles: (1) original nozzle, (2) original nozzle with modified trench height, (3) original nozzle with modified connecting chamber, and (4) a combination of (2) and (3). In addition, the suction pressure and sound pressure level around the suction nozzle were measured to validate the reduction of acoustic noise. The power efficiency and mean suction pressure increased when the trench height of the suction nozzle was increased. This was attributed to the suppression of the flow separation in the suction channel. Modification of the connecting chamber in the original nozzle, which had an abrupt contraction from a rectangular chamber into a circular pipe, into a smooth converging contraction substantially improved the suction flow into the connecting pipe. When both modifications were applied simultaneously, the resulting suction nozzle was more effective from the viewpoints of aerodynamic power increase and sound pressure level reduction.

Key Word : Vacuum Cleaner, Suction Nozzle, Aerodynamic Power, Suction Pressure, Sound Pressure Level

KSME International Journal, Vol. 18 No. 9, pp. 1661-1667, 2004

Microscopic Spray Characteristics in the Effervescent Atomizer with Two Aerator Tubes

Hyung Gon Kim*

Graduate School, Department of Mechanical Engineering, Kagoshima University, 1-21-40, Korimoto, Kagoshimasi, 890-0065, Japan

Toshiaki Yano

Department of Mechanical Engineering, Kagoshima University, Japan

Kyu Keun Song

RCIT, Chonbuk National University, Korea

Torii Shuichi

Department of Mechanical Engineering and Materials Science, Kumamoto University, Japan

An experimental study is performed on atomization characteristics and stable operating conditions for the injection of high viscous waste vegetable oil using an effervescent atomizer with 2 aerator tubes.  Consideration is given to the effects of ALR and liquid viscosity on the velocity and mean diameter of the injected droplet.  It is found that (i) as ALR increases, the axial velocity of the droplet is increased, while half-velocity width and SMD are decreased regardless of the change in liquid viscosities, (ii) the rate of fine drop distribution occupied in the total spray field is increased with an increase in ALR, and (iii) the effect of viscosity on the atomization characteristics is minor. Consequently, it is expected that the effervescent atomizer will exhibit an excellent atomization performance at the high ALR condition, regardless of liquid viscosities.

Key Words : SMD, PDPA, Effervescent atomizer, ALR

KSME International Journal, Vol. 18 No. 9, pp. 1668-1679, 2004

Analysis on the friction losses of a bent-axis type hydraulic piston pump

Yeh-Sun Hong*, Yoon-Ho Doh,

Hankuk Aviation University, School of Aeronautical & Mechanical Engineering, Hwajeon-dong, Duckyang-ku, Goyang-city, Gyeonggi-do, 412-791 Korea

The design of an axial piston pump for electro-hydrostatic transmission systems requires accurate information where and how much the internal friction and flow losses are produced. This study is particularly focused on the friction losses of a bent-axis type hydraulic piston pump, aiming at finding out which design factors influence its torque efficiency most significantly. To this end, the friction coefficients of the pump parts such as piston heads, spherical joints, shaft bearings, and valve plate were experimentally identified by a specially constructed tribometer. Applying the experimental data to the equations of motion for pistons as well as to the theoretical friction models for the pump parts, the friction torques produced by them were computed. The accuracy of the computed results was confirmed by the comparison with the practical input torque of the pump. In this paper, it is shown that the viscous friction forces on the valve plate and input shaft bearing are the primary source of the friction losses of the bent-axis type pump, while the friction forces and moments on the piston are of little significance.

Key Words : Bent-axis type hydraulic piston pump, Kinematics analysis, Dynamic analysis, Friction loss, Measurement of friction coefficients, Tribometer

KSME International Journal, Vol. 18 No. 9, pp. 1680-1688, 2004

Temperature Analysis for the Point-Cell Source in the Vapor Deposition Process

Jongwook Choi*, Sungcho Kim

School of Mechanical and Automotive Engineering, Sunchon National University, Suncheon, Jeonnam, 540-742, Korea

Hun Jung

Graduate School, Department of Mechanical Engineering, Chonnam National University,

Gwangju, 500-757, Korea

The information indicating device plays an important part in the information times. Recently, the classical CRT(Cathod Ray Tube) display is getting transferred to the LCD(Liquid Crystal Display) one which is a kind of the FPDs(Flat Panel Displays). The OLED(Organic Light Emitting Diodes) display of the FPDs has many advantages for the low power consumption, the luminescence in itself, the light weight, the thin thickness, the wide view angle, the fast response and so on as compared with the LCD one. The OLED has lately attracted considerable attention as the next generation device for the information indicators. And also it has already been applied for the outside panel of a mobile phone, and its demand will be gradually increased in the various fields. It is manufactured by the vapor deposition method in the vacuum state, and the uniformity of thin film on the substrate depends on the temperature distribution in the point-cell source. This paper describes the basic concepts that are obtained to design the point-cell source using the computational temperature analysis. The grids are generated using the module of AUTOHEXA in the ICEM CFD program and the temperature distributions are numerically obtained using the STAR-CD program. The temperature profiles are calculated for four cases, i.e., the charge rate for the source in the crucible, the ratio of diameter to height of the crucible, the ratio of interval to height of the heating bands, and the geometry modification for the basic crucible. As a result, the blowout phenomenon can be shown when the charge rate for the source increases. The temperature variation in the radial direction is decreased as the ratio of diameter to height is decreased and it is suggested that the thin film thickness can be uniformed. In case of using one heating band, the blowout can be shown as the higher temperature distribution in the center part of the source, and the clogging can appear in the top end of the crucible in the lower temperature. The phenomena of both the blowout and the clogging in the modified crucible with the nozzle-diffuser can be prevented because the temperature in the upper part of the crucible is higher than that of other parts and the temperature variation in the radial direction becomes small.

Key Words : OLED(Organic Light Emitting Diodes), Point-Cell Source, Radiative Heat Transfer, Conductive Heat Transfer, Vapor Deposition

KSME International Journal, Vol. 18 No. 10, pp. 1691-1699, 2004

Analytical Method for Constrained Mechanical & Structural Systems

Hee-Chang Eun*

Department of Architectural Engineering, Kangwon National University, Hyoja 2 Dong

Chuncheon, Korea

Sang-Yeol Park

Cheju National University

Eun-Taik Lee, Heon-Soo Chung

Department of Architectural Engineering, Chung-Ang University, Seoul, Korea

The objective of this study is to present an accurate and simple method to describe the motion of constrained mechanical or structural systems.  The proposed method is an elimination method to require less effort in computing Moore-Penrose inverse matrix than the generalized inverse method provided by Udwadia and Kalaba.  Considering that the results by numerical integration of the derived second-order differential equation to describe constrained motion veer away the constrained trajectories, this study presents a numerical integration scheme to obtain more accurate results.  Applications of holonomically or nonholonomically constrained systems illustrate the validity and effectiveness of the proposed method.

Key words: constraint, control force, minimization, robot, end-effector, generalized inverse matrix

KSME International Journal, Vol. 18 No. 10, pp. 1700-1711, 2004

On the Instantaneous and Average Piston Friction of Swash Plate Type Hydraulic Axial Piston Machines

Heon-Sul Jeong*,

School of Mechanical Engineering, Kunsan National Univ., Kunsan, Chonbuk 573-701, KOREA

Hyoung-Eui Kim

Hydraulic Power Transmission Research Lab.,

Korea Institute of Machinery & Materials, Yusung P.O Box 101, Taejun, 305-600, Korea

Piston friction is one of the important but complicated sources of energy loss of a hydraulic axial piston machine. In this paper, two formulas are derived for estimating instantaneous piston friction force and average piston friction moment loss. The derived formula can be applicable for piston guides with or without bushing as well as for axial piston machines of motoring and pumping operations. Through the formula derivation, a typical curve shape of friction force found from several experimental measurements during one revolution of a machine is clearly explained in this paper that it is mainly due to the equivalent friction coefficient dependent on its angular position. Stribeck curve effect can easily be incorporated into the formula by replacing outer and inner friction coefficients at both edges of a piston with the coefficient given by Manring [1] considering mixed/boundary lubrication effects. Novel feature of the derived formula is that it is represented only by physical dimensions of a machine, hence it allows to estimate the piston friction force and loss moment of a machine without hardworking experimental test.

Key words : Hydraulic axial piston machine, Swash plate type design, Piston guide bushing, Piston friction force and moment, Instantaneous and average loss moment

KSME International Journal, Vol. 18 No. 10, pp. 1712-1721, 2004

The Theoretical Study of the Measuring Thermal Diffusivity of Semi-Infinite Solid Using the Photothermal Displacement

Pilsoo Jeon, Kwangjai Lee*

Department of Mechanical Engineering, Graduate School, Ajou University, San 5, Wonchun-Dong, Yeongtong-Gu, Suwon, Kyunggi-do, 442-749, Korea

Jaisuk Yoo, Youngmoo Park, Jonghwa Lee

Division of Mechanical Engineering, Ajou University, San 5, Wonchun-Dong, Yeongtong-Gu, Suwon, Kyunggi-do, 442-749, Korea

A method of measuring the thermal diffusivity of semi-infinite solid material at room temperature using photothermal displacement is proposed. In previous works, within the constant thickness of material, the thermal diffusivity was determined by the magnitude and phase of deformation gradient as the relative position between the pump and probe beams. In this study, however, a complete theoretical treatment of the photothermal displacement technique has been performed for thermal diffusivity measurement in semi-infinite solid materials. The influence of parameters, such as, radius and modulation frequency of the pump beam and the thermal diffusivity, was studied. We propose a simple analysis method based on the zero-crossing position of real part of deformation gradient and the minimum position of phase as the relative position between two beams. It is independent of parameters such as power of pump beam, absorption coefficient, reflectivity, Poisson's ratio, and thermal expansion coefficient.

Key Words : Photothermal displacement, Deformation gradient, Phase, Thermal diffusivity, Thermal diffusion length, Zero-crossing position, Minimum position

KSME International Journal, Vol. 18 No. 10, pp. 1722-1729, 2004

Reliability-Based Design Optimization of Slider Air Bearings

Sang-Joon Yoon, Dong-Hoon Choi*

Center of Innovative Design Optimization Technology, Hanyang University, Seoul 133-791, Korea

This paper presents a design methodology for determining configurations of slider air bearings considering the randomness of the air-bearing surface (ABS) geometry by using the iSIGHT. A reliability-based design optimization (RBDO) problem is formulated to minimize the variations in the mean values of the flying heights from a target value while satisfying the desired probabilistic constraints keeping the pitch and roll angles within a suitable range. The reliability analysis is employed to estimate how the fabrication tolerances of individual slider parameters affect the final flying attitude tolerances. The proposed approach first solves the deterministic optimization problem. Then, beginning with this solution, the RBDO is continued with the reliability constraints affected by the random variables. Reliability constraints overriding the constraints of the deterministic optimization attempt to drive the design to a reliability solution with minimum increase in the objective. The simulation results of the RBDO are listed in comparison with the values of the initial design and the results of the deterministic optimization, respectively. To show the effectiveness of the proposed approach, the reliability analyses are simply carried out by using the mean value first-order second-moment (MVFO) method. The Monte Carlo simulation of the RBDO’s results is also performed to estimate the efficiency of the proposed approach. Those results are demonstrated to satisfy all the desired probabilistic constraints, where the target reliability level for constraints is defined as 0.8.

KSME International Journal, Vol. 18 No. 10, pp. 1730-1737, 2004

Evaluation of Material Degradation of 1Cr-1Mo-0.25V steel using Ball Indentation Method

Chang-Sung Seok*

School of Mechanical Engineering, Sungkyunkwan University,300 Chunchun-dong, Jangan-gu,

Suwon, Kyonggi-do, 440-746, Korea

Jeong-Pyo Kim

Digital Module Division, Sound Solution Team(R & D), SamSung Electro-Mechanics Co., LTD.,

314 Maetan 3-Dong, Yeongtong-Gu, Suwon, Kyunggi-Do, 442-743, Korea

Jae-Mean Koo

School of Mechanical Engineering, Sungkyunkwan University,300 Chunchun-dong, Jangan-gu,

Suwon, Kyonggi-do, 440-746, Korea

The BI(Ball Indentation) method has the potential to assess the mechanical properties and to replace conventional fracture tests. In this study, the effect of aging on mechanical behavior of 1Cr-1Mo-0.25V steels procured by isothermal aging heat-treatment at four different aging times in the range of 0~1820 hours at 630℃, were investigated using BI system.

Keywords: Material Properties, Ball Indentation, Degradation, Fracture Toughness, 1Cr-1Mo-0.25V

KSME International Journal, Vol. 18 No. 10, pp. 1738-1746, 2004

Enhancing Nearfield Acoustic Holography using Wavelet Transform

Byeongsik Ko

Director, Korea simulation technology Inc.

When there are low signal to noise relationships or low coherences between measured pressure and a reference sensor, a pressure field measured and estimated by NAH (Nearfield Acoustic Holography) becomes noisy on the hologram and source planes. This paper proposes a method to obtain the high coherent de-noised pressure signals from low coherent noisy ones by combining a wavelet algorithm with NAH. The proposed method obtains the de-noised field from acoustic fields on a noise source plane reconstructed through backward propagation of NAH. Thus this method does not need high coherent pressure signals on the hologram surface while the conventional nearfield acoustic holography requires high-coherent signals. The proposed method was verified by numerical simulation using noisy signals, composed of original signals and imposed noises distributed on the hologram surface.

KSME International Journal, Vol. 18 No. 10, pp. 1747-1754, 2004

Harmonic Axisymmetric Thick Shell Element for Static and Vibration Analyses

Jin-Gon Kim

School of Mechanical and Automotive Engineering, Catholic University of Daegu, Hayang-up, Kyungsan-si, Kyongbuk, 712-702, Korea

In this study, a new harmonic axisymmetric thick shell element for static and dynamic analyses is proposed. The newly proposed element considering shear strain is based on a modified Hellinger-Reissner variational principle, and introduces additional nodeless degrees for displacement field interpolation in order to enhance numerical performance. The stress parameters selected via the field-consistency concept are very important in formulating a trouble-free hybrid-mixed elements. For computational efficiency, the stress parameters are eliminated by the stationary condition and then the nodeless degrees are condensed out by the dynamic reduction. Several numerical examples confirm that the present element shows improved efficiency and yields very accurate results for static and vibration analyses.

Key Words: Harmonic axisymmetric shell element, Hybrid-mixed formulation, Static and vibration analyses

KSME International Journal, Vol. 18 No. 10, pp. 1755-1762, 2004

Pre-Sliding Friction Control Using the Sliding Mode Controller with Hysteresis Friction Compensator

Jeong Ju Choi

Department of Mechanical and Intelligent Systems Engineering, Pusan National University

Jong Shik Kim

School of Mechanical Engineering and RIMT, Pusan National University

Seong Ik Han*

Dept. of Mechatronics, Suncheon First College

Friction phenomenon can be described as two parts, which are the pre-sliding and sliding regions. In the motion of the sliding region, the friction force depends on the velocity of the system and consists of the Coulomb, stick-slip, Streibeck effect and viscous frictions. The friction force in the pre-sliding region, which occurs before the breakaway, depends on the position of the system. In the case of the motion of the friction in the sliding region, the LuGre model describes well the friction phenomenon and is used widely to identify the friction model, but the motion of the friction in the pre-sliding such as hysteresis phenomenon cannot be expressed well. In this paper, a modified friction model for the motion of the friction in the pre-sliding region is suggested which can consider the hysteresis phenomenon as the Preisach model. In order to show the effectiveness of the proposed friction model, the sliding mode controller(SMC) with hysteresis friction compensator is synthesized for a ball-screw servo system.

Key words: Friction, Preisach hysteresis model, Sliding mode control, Feedforward hysteresis friction compensator

KSME International Journal, Vol. 18 No. 10, pp. 1763-1771, 2004

An Experimental Study on Flow Characteristics of ERF Between Two Parallel-Plate Electrodes by Using PIV Technique

Tae-Hyun Chang*

Division of Mechanical and Automation Engineering, Kyungnam University,

449 Wolyoung Dong, Masan, Kyungnam 631-701, Korea

Sung-Cheol Jang

Department of Mechanical Engineering, Kyungnam University Graduate School,

449 Wolyoung Dong, Masan, Kyungnam 631-701, Korea

An experimental investigation was performed to study the characteristics of ER(Electro-Rheological) fluid flow in a horizontal rectangular tube with or without D.C voltage. To determine some characteristics of the ER flow, 2D PIV(Particle Image Velocimetry) technique was employed for velocity measurements. This research found the mean velocity distributions with 0kV/mm, 1.0kV/mm and 1.5kV/mm for Re = 0, 0.62, 1.29 and 2.26. When the strength of the electric field increased, the cluster of ERF was clearly strong along the test tube and the flow rate decreased. The present results will contribute to the economical and compact design of ER fluids system.

Key Words : Electro-Rheological Fluids, Cluster, Particle Image Velocimetry

KSME International Journal, Vol. 18 No. 10, pp. 1772-1781, 2004

Nano-Mechanical and Tribological Characteristics of Ultra-Thin Amorphous Carbon Film Investigated by AFM

Koo-Hyun Chung, Jae-Won Lee, and Dae-Eun Kim*

School of Mechanical Engineering, Yonsei University, Seoul 120-749, Korea

The mechanical as well as tribological characteristics of coating films as thin as a few nm become more crucial as applications in micro-systems grow.  Especially, the amorphous carbon film has a potential to be used as a protective layer for micro-systems.  In this work, quantitative evaluation of nano-indentation, scratching, and wear tests were performed on the 7 nm thick amorphous carbon film using an Atomic Force Microscope (AFM).  It was shown that AFM-based nano-indentation using a diamond coated tip can be feasibly utilized for mechanical characterization of ultra-thin films.  Also, it was found that the critical load where the failure of the carbon film occurred was about 18 μN by the ramp load scratch test.  Finally, the wear experimental results showed that the quantitative wear rate of the carbon film ranged 10-9~10-8 mm3/N cycle.  These experimental methods can be effectively utilized for a better understanding the mechanical and tribological characteristics at the nano-scale.

Keywords: Atomic Force Microscope (AFM), Diamond coated tip, Nano-indentation, Nano-wear rate, Scratch test

KSME International Journal, Vol. 18 No. 10, pp. 1782-1798, 2004

Computation of a Turbulent Natural Convection in a Rectangular Cavity with the Low-Reynolds-Number Differential Stress and Flux Model

Seok-Ki Choi , Eui-Kwang Kim. Myung-Hwan Wi and Seong-O Kim

Korea Atomic Energy Research Institute, Fluid System Engineering Division, 150 Deokjin-dong, Yuseong-gu, Daejeon, 305-353, Korea

A numerical study of a natural convection in a rectangular cavity with the low-Reynolds-number differential stress and flux model is presented.  The primary emphasis of the study is placed on the investigation of the accuracy and numerical stability of the low-Reynolds-number differential stress and flux model for a natural convection problem.  The turbulence model considered in the study is that developed by Peeters and Henkes (1992) and further refined by Dol and Hanjalic (2001), and this model is applied to the prediction of a natural convection in a rectangular cavity together with the two-layer model, the shear stress transport model and the time-scale bound  model, all with an algebraic heat flux model.  The computed results are compared with the experimental data commonly used for the validation of the turbulence models.  It is shown that the low-Reynolds-number differential stress and flux model predicts well the mean velocity and temperature, the vertical velocity fluctuation, the Reynolds shear stress, the horizontal turbulent heat flux, the local Nusselt number and the wall shear stress, but slightly under-predicts the vertical turbulent heat flux.  The performance of the model is comparable to that of the low-Reynolds-number differential stress and flux model except for the over-prediction of the horizontal turbulent heat flux.  The two-layer model predicts poorly the mean vertical velocity component and under-predicts the wall shear stress and the local Nusselt number.  The shear stress transport model predicts well the mean velocity, but the general performance of the shear stress transport model is nearly the same as that of the two-layer model, under-predicting the local Nusselt number and the turbulent quantities.

Key Words : Turbulent Natural Convection, Two-layer model, Shear stress transport model,   model, Low-Reynolds-number differential stress and flux model

KSME International Journal, Vol. 18 No. 10, pp. 1799-1808, 2004

Investigation on Airflows in Abnormal Nasal Cavity with Adenoid Vegetation by Particle Image Velocimetry

Sung Kyun Kim*

Department of Mechanical Engineering, Konkuk University, #1 Whayang-dong   Kwanggin-gu Seoul, 143-701, Korea

Young Rak Son

GraduateSchool of Mechanical Engineering, Konkuk University, Seoul, Korea

Knowledgeof airflow characteristics in nasal cavity is essential to understand the physiological and pathological aspects of nasal breathing. Several studies have utilizedphysical models of the healthy nasal cavity to investigate the relationship between nasal anatomy and airflow. Since the final goal of these works is their contribution to the diagnosisand treatment of nasal diseases, the next step on this topic is naturally studies for disordered nasal cavities. In this paper, as the first application, airflows in the normal and abnormal nasal cavities with adenoid vegetation are investigated experimentally by PIV, and comparisons of both cases are appreciated. Dense CT data and careful treatment of model surface under the ENT doctor's advice provide more sophisticatedcavity model. The CBC PIV algorithm with window offset is used for PIV flow analysis. Average and RMS distributions are obtained for inspirational and expirational nasal airflows. Airflow characteristics that are related with the abnormalities in nasal cavity are presented.

Key Words : Nasal Airflow, Adenoid vegetation, PIV(Particle Image Velocimetry),  Computed Tomogram (CT)

KSME International Journal, Vol. 18 No. 10, pp. 1809-1818, 2004

An Investigation of The Effect of Changes in Engine Operating Conditions on Ignition in an HCCI Engine

Kyung-Hwan Lee*

Automotive Engineering Department, Sunchon National University, Sunchonsi, Chonnam 540-742, Korea

Venkatesh Gopalakrishnan and John Abraham

School of Mechanical Engineering, Purdue University, West Lafayette, IN 47907, USA

The dependence of the ignition timing in an HCCI engine on intake temperature and pressure, equivalence ratio, and fuel species is investigated with a zero-dimensional model combined with a detailed chemical kinetics.  The accuracy of the model is evaluated by comparing measured and computed results in a propane-fueled HCCI engine.  It is shown that the peak pressure values are reproduced within 10% and ignition timing within 5( CA.  The heat loss through the walls is found to affect significantly on the ignition timing for different inlet conditions.   It is also shown that for the propane-fueled engine, the tolerance in intake temperatures is 20-25 K and the tolerance in intake pressure is about 1 bar for stable operation without misfire or too early ignition.  Comparison of propane and heptane fuels indicates that the tendency to misfire when heptane is employed as the fuel is less than that when propane is employed with the same wall temperature conditions.  However, the heptane-fueled engine may have a lower compression ratio to avoid too early ignition and hence lower efficiency.  For the selected set of engine parameters, stable operations might be achieved for the heptane-fueled engine with twice as much tolerance in intake temperatures as for the propane-fueled engine.

Key Words : Ignition, HCCI Engine, Fuel

KSME International Journal, Vol. 18 No. 10, pp. 1819-1828, 2004

Experimental Investigation on the Turbulence Augmentation of a Gun-type Gas Burner by Slits and Swirl Vanes

Jang-kweon Kim

Power Mechanical System Engineering Major, Kunsan National University,

San 68, Miryong-Dong, Kunsan, Chonbuk 573-701, Korea

The purpose of this paper is to investigate the effects of slits and swirl vanes on the turbulence augmentation in the flow fields of a gun-type gas burner using an X-type hot-wire probe. The gun-type gas burner adopted in this study is composed of eight slits and swirl vanes located on the surface of an inclined baffle plate. Experiment was carried out at a flow rate of 450 ℓ/min in burner model installed in the test section of subsonic wind tunnel. Swirl vanes play a role diffusing main flow more remarkably toward the radial direction than axial one, but slits show a reverse feature. Consequently, both slits and swirl vanes remarkably increase turbulence intensity in the whole range of a gun-type gas burner with a cone-type baffle plate.

Key Words : Gun-Type Gas Burner, Hot-Wire Anemometer, Slit, Subsonic Wind                 Tunnel, Swirl Flow, Swirl Vane, Turbulence Augmentation, X-probe

KSME International Journal, Vol. 18 No. 10, pp. 1829-1836, 2004

Performance Optimization of Hypervelocity Launcher System using Experimental Data

Choul-Jun Huh, Jin-Ho Lee, Ki-Joon Bae, Kwon-Su Jeon,

Yung-Hwan Byun, Jae-Woo Lee, Chang-Jin Lee

CASIT Konkuk University, Seoul 143-701, Korea

This study presents the performance optimization of hypervelocity launcher system by using the experimentall data. During the optimization, the RSM (Response Surface Method) is adopted to find the operating parameters that could maximize the projectile speed. To construct a reliable response surface model, 3 full factorial method is used with the selected design variables, such as piston mass and 2 driver fill pressure. Nine test data could successfully construct the reasonable response surface, which used to yield the optimal operational conditions of the system using the genetic algorithm. The optimization results are confirmed by the experimental test with a good accuracy. Thus, the optimization can improve the performance of the facility.

Key Words : Hypervelocity Launcher System, Numerical Optimization Response Surface Method, Genetic Algorithm

KSME International Journal, Vol. 18 No. 10, pp. 1837-1848, 2004

Interaction of High–Speed Compressible Viscous Flow and Structure by Adaptive Finite Element Method

Wiroj Limtrakarn

Mechanical Engineering Department, Thammasat University, Bangkok 12120, Thailand

Pramote Dechaumphai*

Mechanical Engineering Department, Chulalongkorn University, Bangkok 10330, Thailand

Interaction behaviors of high–speed compressible viscous flow and thermal–structural response of structure are presented. The compressible viscous laminar flow behavior based on the Navier–Stokes equations is predicted by using an adaptive cell-centered finite-element method.  The energy equation and the quasi-static structural equations for aerodynamically heated structures are solved by applying the Galerkin finite-element method.  The finite-element formulation and computational procedure are described.  The performance of the combined method is evaluated by solving Mach 4 flow past a flat plate and comparing with the solution from the finite different method.  To demonstrate their interaction, the high-speed flow, structural heat transfer, and deformation phenomena are studied by applying the present method to Mach 10 flow past a flat plate.

Keywords: flow-structure interaction, aerodynamic heating rate, adaptive mesh

KSME International Journal, Vol. 18 No. 10, pp. 1849-1858, 2004

Test Results of Friction Factor for Round-Hole Roughness Surfaces in Closely Spaced Channel Flow of Water

Tae Woong Ha

Associate professor, Mechanical Engineering Department,  Kyung-won University, Sungnam 461-701, Korea,

For examining friction-factor characteristics of round-hole pattern surfaces which are usually applied on damper seals, flat plate test apparatus is designed and fabricated. The measurement method of leakage and pressure distribution along round-hole pattern specimen with different hole area is described and a method for determining the Fanning friction factor is discussed. Results show that the round-hole pattern surfaces provide a much larger friction factor than smooth surface, and the friction factor vs. clearance behavior yields that the friction factor generally decreases as the clearance increases unlike the results of Nava's flat plate test. As the hole depth is decreased, the friction factor is increased, and maximum friction factor is obtained for 50% of hole area. Since the present experimental friction factor results show coincident characteristics with Moody's friction factor model, empirical friction factors for round-hole pattern surfaces are obtained by using the Moody's formula based on curve-fit of the experimental data. Results of Villasmil's 2D CFD simulation support the present experimental test result.

Key Words: Friction Factor, Flat Plate Tester, Round-Hole Pattern Surface, Moody Friction Factor Model, Damper Seal

KSME International Journal, Vol. 18 No. 10, pp. 1859-1868, 2004

Symptoms of Self-excited Combustion Oscillation and their Detection

Young-Joon Yang, Fumiteru Akamatsu, Masashi Katsuki

Department of Mechanical Engineering, Osaka University, 2-1 Yamadaoka, Suita, Osaka 565-0871, Japan

Suk-Tae Bae

Department of Mechatronics, Tongmyong College, 505 Yongdang-dong, Nam-gu, Busan 608-740, Korea

Si-Pom Kim

Department of Mechanical Engineering, Dong-A University, 840 Hadan2-dong, Saha-gu,

Busan 604-714, Korea

Monitoring of OH chemiluminescence through an optical fiber was demonstrated to be a useful method in detecting self-excited combustion oscillations.  OH chemiluminescence intensity detected by the optical fiber showed mostly excellent agreement with those obtained by high speed CCD camera measurements when combustion oscillations were strong.  Symptoms of self-excited combustion oscillation were also studied in order to predict the onset of combustion oscillation before it proceeded to a catastrophic failure.  For the purpose, we have found and proposed unique measures to tell the onset of self-excited combustion oscillations based on the careful statistics of fluctuating properties in flames, such as pressure or emission of OH radicals.

Key Words: Flame, Combustion Oscillation, Unsteady Combustion, Premixed Combustion, Oscillation Control, Symptom of Combustion Oscillation, Detection.

KSME International Journal, Vol. 18 No. 10, pp. 1869-1879, 2004

Numerical Study on Laminar Flow over Three Side-by-Side Cylinders

Sangmo Kang

Department of Mechanical Engineering, Dong-A University, Busan 604-714, Korea

The present study has numerically investigated two-dimensional flow over three circular cylinders in an equidistant side-by-side arrangement at a low Reynolds number. For the study, numerical simulations are performed, using the immersed boundary method, in the range of ????, where ??? is the spacing between two adjacent cylinder surfaces divided by the cylinder diameter. Results show that the flow characteristics significantly depend on the gap spacing and a total of five kinds of wake patterns are observed over the range: modulation-synchronized (????), inphase-synchronized (???), flip-flopping (???), deflected (???), and single bluff-body patterns (???). Moreover, the parallel and symmetric modes are also observed depending on ??? in the regime of the flip-flopping pattern. The corresponding flow fields and statistics are presented to verify the observations.

KSME International Journal, Vol. 18 No. 11, pp. 1883-1890, 2004

Analysis of a Clutch Damper using a Discrete Model

Kukhyun Ahn, Jang Moo Lee

Seoul National University

Wonsik Lim, Yeong-il Park*

Seoul National University of Technology

It is important to have a precise model for the clutch damper in order to simulate the entire powertrain of a vehicle and predict the responses of the system. In this research, we developed a new model in which the spring used in the clutch damper is divided into a finite number of elements. The model takes many unique properties of arc-shaped springs into consideration and is anticipated to be more precise than conventional simple models. With the model, two meaningful results were presented which can be utilized afterwards. One is a simulation concerning the peak torque transmitted via the clutch damper. The other is a simulation that shows the hysteretic characteristics of the clutch damper.

KEY WORDS: Vehicle powertrain, Clutch damper, Multi-d.o.f. discrete model, Transient torque, Hysteresis

KSME International Journal, Vol. 18 No. 11, pp. 1891-1899, 2004

Structural and Mechanical Systems Subjected to Constraints

Hee-Chang Eun

Department of Architectural Engineering, Kangwon National University, Hyoja 2 Dong, Chuncheon, Korea

Eun-Taik Lee, Heon-Soo Chung

Department of Architectural Engineering, Chung-Ang University, Seoul, Korea

Sang-Yeol Park

Cheju National University, Jeju 690-756, Korea

The characteristics of dynamic systems subjected to multiple linear constraints are determined by considering the constrained effects.  Although there have been many researches to investigate the dynamic characteristics of constrained systems, most of them depend on numerical analysis like Lagrange multipliers method.  In 1992, Udwadia and Kalaba presented an explicit form to describe the motion for constrained discrete systems.  Starting from the method, this study determines the dynamic characteristics of the systems to have positive semidefinite mass matrix and the continuous systems.  And this study presents a closed form to calculate frequency response matrix for constrained systems subjected to harmonic forces.  The proposed methods that do not depend on any numerical schemes take more generalized forms than other research results.

Key words; generalized inverse, constraint, continuous system, substructure

KSME International Journal, Vol. 18 No. 11, pp. 1900-1908, 2004

A Human Robot Interactive System “RoJi”

Joongsun Yoon

School of Mechanical Engineering, Pusan National University, Pusan 609-735, Korea

A human-friendly interactive system that is based on the harmonious symbiotic coexistence of human and robots is explored. Based on interactive technology paradigm, a robotic cane is proposed for blind or visually impaired travelers to navigate safely and quickly through obstacles and other hazards faced by blind pedestrians. Robotic aids, such as robotic canes, require cooperation between human and robots. Various methods for implementing the appropriate cooperative recognition, planning, and acting, have been investigated. The issues discussed include the interaction between humans and robots, design issues of an interactive robotic cane, and behavior arbitration methodologies for navigation planning.

Key Words : Human-Robot Interaction, Interactive Technology, Robotic Cane, Shared Behavior Control

KSME International Journal, Vol. 18 No. 11, pp. 1909-1915, 2004

Transmission Path Analysis of Noise and Vibration in a Rotary Compressor by Statistical Energy Analysis

Seon-Woong Hwang,

Digital Appliance Lab., LG Electronics, Seoul 153-802, Korea

Weui-Bong Jeong*, Wan-Suk Yoo and Kyu-Hwan Kim

Department of Mechanical Engineering, Pusan National University, Busan 609-735, Korea

The hermetic rotary compressor is one of the most important components of an air conditioning system since it has a great effect on both the performance and the noise and vibration of the system. Noise and vibration occurs due to gas pulsation during the compression process and to unbalanced dynamic force. In order to reduce noise and vibration, it is necessary to identify their sources and transmission path and effectively control them. Many approaches have been tried in order to identify the noise transmission path of a compressor. However, identification has proven to be difficult since the characteristics of compressor noise are complicated due to the interaction of the compressor parts and gas pulsation. In this study, the statistical energy analysis has been used to trace the energy flow in the compressor and to identify the transmission paths from the noise source to the exterior sound field.

Key Words : Rotary Compressor,  SEA,  Modal Density,  Damping Loss Factor,  Coupling Loss Factor, Power Spectrum, Point Mobility

KSME International Journal, Vol. 18 No. 11, pp. 1916-1922, 2004

A Robust Control with a Neural Network Structure for Uncertain Robot Manipulator

In-Chul Ha*

Center for Robot Technology & Manufacturing of Institute for Advanced Engineering

Yongin P.O.Box 25, Kyonggi Do, 449-863, Korea

Myoung-Chul Han

Department of Mechanical Engineering, Pusan University,

San 30, Jangjun Dong, Kumjung Ku, Pusan, 609-735, Korea

A robust position control with the bound function of neural network structure is proposed for uncertain robot manipulators. The uncertain factors come from imperfect knowledge of system parameters, payload change, friction, external disturbance, and etc. Therefore, uncertainties are often nonlinear and time-varying. The neural network structure presents the bound function and does not need the concave property of the bound function. The robust approach is to solve this problem as uncertainties are included in a model and the controller can achieve the desired properties in spite of the imperfect modeling. Simulation is performed to validate this law for four-axis SCARA type robot manipulator.

Keywords : Robot manipulator, Robust Control, NN(Neural Network), Lyapunov stability,              Bound Function

KSME International Journal, Vol. 18 No. 11, pp. 1923-1931, 2004

Optimum Design of Ship Design System Using Neural Network Method in Initial Design of Hull Plate

Soo-Young Kim, Byung-Young Moon*

Pusan National University, Busan 609-735, Korea

Duk-Eun Kim

Pusan National University, Busan 609-735, Korea

Manufacturing the complex surface plates in stern and stem is a major factor in cost of a preliminary ship design by computing process. If these hull plate parts are effectively classified, it helps to compute the processing cost and find the way of cut-down the processing cost. This paper presents a new method to classify surface plates effectively in preliminary ship design using neural network. A neural network based ship hull plate classification program developed and tested for the automatic classification of ship design. The input variables are regarded as Gaussian curvature distributions on the plate. Various applicable rules of network topology are applied in ship design. In automation of hull plate classification, two different numbers of input variables are used. By observing the results of the proposed method, the effectiveness of the proposed method are discussed. As a result, high prediction rate was achieved in ship design. Accordingly, in the initial design stage, the ship hull plate classification program can be used to predict the ship production cost. And the proposed method will contribute to reduce the production cost of ship.

Key Words ; Ship Design, Optimum Design, Neural Network, Hull Plate, Artificial Intelligence,

Automatic Classification

KSME International Journal, Vol. 18 No. 11, pp. 1932-1940, 2004

Development of the Delamination Evaluation Parameters - The Delamination Aspect Ratio and the Delamination Shape Factors -

Cheol-Woong Kim*

Mechanical System, Induk Institute of Technology, San 76 Wolgye-dong Nowon-gu, Seoul, 139-749 Korea

Sam-Hong Song

Department of Mechanical Engineering, Korea University, 1, 5ga, Anam-dong, Sungbuk-gu, Seoul 136-701, Korea

Dong-Joon Oh

Department of Mechanical Education, Andong National University,  388 Songchun-dong, Andong, Kyoungbuk, 760-749, Korea

Although the previous researches evaluated the fatigue behavior of Al/GFRP laminates using the traditional fracture mechanism, their researches were not sufficient to do it : the damage zone of Al/GFRP laminates was occurred at the delamination zone instead of the crack-metallic damages. Thus, previous researches were not applicable to the fatigue behavior of Al/GFRP laminates. The major purpose of this study was to evaluate delamination behavior using the relationship between crack length (a) and delamination width (b) in Al/GFRP laminate. The details of investigation were as follows : 1) Relationship between crack length (a) and delamination width (b), 2) Relationship between delamination aspect ratio (b/a) and delamination area rate ((AD)N/(AD)All), 3) The effect of delamination aspect ratio (b/a) on the delamination shape factor (fS) and the delamination growth rate (dAD/da). As results, it was known that the delamination aspect ratio (b/a) was decreased and the delamination area rate ((AD)N/(AD)All) was increased as the normalized crack size (a/W) was increased. And, the delamination shape factors (fS) of the ellipse-II (fS3) was greater than of the ellipse-I (fS2) but that of the triangle (fS1) was less than of the ellipse-I (fS2).

Key Words: Delamination Width (b), Delamination Aspect Ratio (b/a), Delamination Shape Factor (fS), Delamination Growth Rate (dAD/da), Delamination Area Rate ((AD)N/(AD)All), Al/GFRP Laminates, Cyclic Bending Moment

KSME International Journal, Vol. 18 No. 11, pp. 1941-1948, 2004

Wheeled Blimp : Hybrid Structured Airship with Passive Wheel Mechanism for Tele-guidance Applications

Sungchul Kang*

Advanced Robotics Research Center, Korea Institute of Science and Technology, Hawolgok-dong 39-1,

Sungbook-ku, Seoul 136-791, Korea

Mi-Hee Nam

Department of Mechanical Engineering Graduate school, Yonsei University

Bong-Seok Kim

Department of Mechanical Engineering Graduate school, Korea University

This paper presents a novel design of indoor airship having a passive wheeled mechanism and its stationary position control. This wheeled blimp can work both on the ground using wheeled vehicle part and in the air using the floating capability of the blimp part. The wheeled blimp stands on the floor keeping its balance using a caster-like passive wheel mechanism. In tele-guidance application, stationary position control is required to make the wheeled blimp naturally communicate with people in standing phase since the stationary blimp system responds sensitively to air flow even in indoor environments. To control the desired stationary position, a computed torque control method is adopted. By performing a controller design through dynamic analysis, the control characteristics of the wheeled blimp system have been found and finally the stable control system has been successfully developed. The effectiveness of the controller is verified by experiment for the real wheeled blimp system.

Key Words : blimp, wheeled vehicle, tele-presence, stationary position control, computed torque control method

KSME International Journal, Vol. 18 No. 11, pp. 1949-1960, 2004

A Feasibility Study on a Robotic Exercise System for MDOF Physical Rehabilitation Therapy

Hyung Joon Sim*

Deptartment of Mechatronics Engineering, Hanyang University, 1271, Sa 1-dong Sangrok-gu, Ansan, Kyunggi, 426-791, Korea

Joo Yeon Won

Samsung Electronics Co., Ltd., San24, Nongseo-ri, Kihung-eop, Yongin, Kyunggi, 449-711

Chang Soo Han

Deptartment of Mechanical Engineering, Hanyang University, 1271, Sa 1-dong Sangrok-gu, Ansan, Kyunggi, 426-791, Korea

This paper presents a robot system developed for medical purpose. A 6-degree-of-freedom robot was introduced for physical exercise and rehabilitation. This system was proposed for stroke patients or patients who cannot use one of their arms or legs. The robot system exercises the hemiplegic part based on the motion of normal part of a patient. Kinematic studies on the human body and robot were applied to develop the robotic rehabilitation exercise system. A clamp which acts as an end effector of the robot to hold a patient was designed and applied to the robot to guarantee the safety of patients. The proposed robotic rehabilitation system was verified by simulations and experiments on arm (elbow and shoulder) motion. Patients are expected to be able to exercise various motions by themselves with the proposed robotic rehabilitation system.

Key words: rehabilitation therapy, physical exercise, medical robot, symmetry operator

KSME International Journal, Vol. 18 No. 11, pp. 1961-1968, 2004

Motion Sensor Fault Detection and Failsafe Logic for Vehicle Stability Control Systems (VSCs)

Kyongsu Yi*

School of Mechanical Engineering, Hanyang University, Seoul, 133-791, KOREA

Kyongchan Min

Department of Automotive Engineering, Hanyang University, Seoul, 133-791, KOREA

The design of a reliable and failsafe control system requires that sensor failures be detected and identified within acceptable time limit so that system malfunction can be prevented. This paper presents a model-based approach to sensor fault detection with applications to vehicle stability control systems. The effectiveness of the proposed method is illustrated through test data-based evaluation. Vehicle test data-based evaluation results show that the proposed fault management scheme can be used for the design of a failsafe VSCs.

Keywords: fault detection, vehicle control system, stability control, sensor

KSME International Journal, Vol. 18 No. 11, pp. 1969-1977, 2004

Nonlinear Parameter Identification of Partial Rotor Rub based on Experiment

Yeon-Sun Choi

School of Mechanical Engineering, Sungkyunkwan University, Kyunggi-do 440-746, Korea

To model and understand the physics of partial rub, a nonlinear rotor model is sought by applying a nonlinear parameter identification technique to the experimental data. The results show that the nonlinear terms of damping and stiffness should be included to model partial rotor rub. Especially, the impact and friction during the contact between rotor and stator are tried to explain with a nonlinear model on the basis of experimental data. The estimated nonlinear model shows good agreements between the numerical and the experimental results in its orbit. Also, the estimated nonlinear model could explain the backward whirling orbit and jump phenomenon, which are the typical phenomena of partial rub.

Key Words  Partial rotor rub, Nonlinear system identification, Impact, Friction

KSME International Journal, Vol. 18 No. 11, pp. 1978-1988, 2004

Influence of Bearing Stiffness on the Static Properties of a Planetary Gear System with Manufacturing Errors

Cheon Gill-Jeong*

Division of Mechanical Engineering, Wonkwang University, Iksan City, Jeon-Buk, 570-749, Korea

Robert G.. Parker

Department of Mechanical Engineering, The Ohio State University, Columbus, OH 43220-1107, USA

Hybrid finite element analysis was used to analyze the influence of bearing stiffness on the static properties of a planetary gear system with manufacturing errors. The effects of changes in stiffness were similar for most of the manufacturing errors. State variables were most affected by the stiffness of the planet bearings. Floating either the sun or carrier helps to equal load sharing and minimizes the critical tooth stress. The effects of a floating sun and carrier are similar, but it is not recommended that both float, because this can induce greater critical tooth stress. Planet bearing stiffness should be optimized. Both load sharing and critical tooth stress should be considered to determine optimal bearing stiffness.

Key Words: Planetary Gear, Manufacturing Error, Bearing Stiffness, Load Sharing, Gear

KSME International Journal, Vol. 18 No. 11, pp. 1989-1995, 2004

Numerical Analysis for Prediction of Fatigue Crack Opening Level

Hyeon Chang Choi*

Department of Mechatronics Engineering, College of Engineering, TongMyong University of Information Technology, 535 Yongdang-dong, Nam-gu, Busan,  608-711, Korea

Finite element analysis(FEA) is the most popular numerical method to simulate plasticity-induced fatigue crack closure and can predict fatigue crack closure behavior. Finite element analysis under plane stress state using 4-node isoparametric elements  is performed to investigate the detailed closure behavior of fatigue cracks and the numerical results are compared with experimental results. The  mesh of constant size elements on the crack surface can not correctly predict the opening level for fatigue crack as shown in the previous works.  The crack opening behavior for the size mesh with a linear change shows almost flat stress level after a crack tip  has passed by the monotonic plastic zone. The prediction of crack opening level presents a good agreement with published experimental data regardless of stress ratios, which are using the  mesh of the elements  that are in proportion to the reversed plastic zone size considering the opening stress intensity factors.  Numerical interpolation results of finite element analysis can precisely predict the crack opening level. This method shows a good agreement with the experimental data regardless of the stress ratios and kinds of materials.

Key Words: Fatigue  Crack Growth, Finite Element Analysis, Crack Closure Behavior, Prediction of Opening Level, Reversed Plastic Zone Size

KSME International Journal, Vol. 18 No. 11, pp. 1996-2008, 2004

Numerical Calculation of Energy Release Rates by Virtual Crack Closure Technique

Yoon-Suk Chang*, Jae-Boong Choi, Young-Jin Kim

SAFE Research Centre, School of Mechanical Engineering, Sungkyunkwan University,

300 Chunchun-dong, Jangan-gu, Suwon, Kyonggi-do 440-746, Korea

Genki Yagawa

Department of Quantum Engineering & System Science, University of Tokyo,

7-3-1 Hongo, Bunkyo-ku, Tokyo, 113-8656, Japan

A seamless analysis of material behavior incorporating complex geometry and crack- tip modeling is one of greatly interesting topics in engineering and computational fracture mechanics fields. However, there are still large gaps between the industrial applications and fundamental academic studies due to a time consuming detailed modeling. In order to resolve this problem, a numerical method to calculate an energy release rate by virtual crack closure technique was proposed in this paper. Both free mesh method and finite element method have been utilized and, thereafter, robust local and global elements for various geometries and boundary conditions were generated. A validity of the proposed method has been demonstrated through a series of fracture mechanics analyses without tedious crack-tip meshing.

Key Words: Free Mesh Method, Finite Element Method, Energy Release Rate, Stress Intensity Factor, Virtual Crack Closure Technique

KSME International Journal, Vol. 18 No. 11, pp. 2009-2020, 2004

A Parameter Study for Static and Dynamic Denting

Dong-Won Jung*

Department of Mechanical Engineering, Cheju National University, 1, Ara 1(il)-dong,

Jeju-do 690-756, Korea,

M. J. Worswick

Department of Mechanical Engineering, University of Waterloo, Waterloo, Ontario, N2L 3G1, Canada

A parametric study of the factors controlling static and dynamic denting, as well as local stiffness, has been made on simplified panels of different sizes, curvatures, thicknesses and strengths.  Analyses have been performed using the finite element method to predict dent resistance and panel stiffness.

A parametric approach is used with finite element models of simplified panels.   Two sizes of panels with square plan dimensions and a wide range of curvatures are analysed for several combinations of material thickness and strength, all representative of automotive closure panels. Analysis was performed using the implicit finite element code, LS-NIKE, and the explicit dynamic code, LS-DYNA for the static and dynamic cases, respectively.

Panel dent resistance and stiffness behaviour are shown to be complex phenomena and strongly inter-related.  Factors favouring improved dent resistance include increased yield strength and panel thickness.  Panel stiffness also increases with thickness and with higher curvatures but decreases with size and very low curvatures.  Conditions for best dynamic and static dent performance are shown to be inherently in conflict; that is, panels with low stiffness tend to perform well under impact loading but demonstrate inferior static dent performance.  Stiffer panels are prone to larger dynamic dents due to higher contact forces but exhibit good static performance through increased resistance to oil canning.

Key Words : Static Denting, Dynamic Denting, Parameter Study, Finite Element Method, Panel Stiffness

KSME International Journal, Vol. 18 No. 11, pp. 2021-2031, 2004

Windmilling Characteristics of Centrifugal-Flow Turbojets

Yoo, Il Su*

School of Mechanical Engineering, Korea Advanced Institute of Science and Technology

Guseong-Dong, Yuseong-Gu, Daejon, 305-701, Korea

Song, Seung Jin

School of Mechanical and Aerospace Engineering, Seoul National University, San 56-1, Sillim- Dong,

Gwanak-Gu, Seoul, 151-742, Korea

Lim, Jin Shik

Agency for Defense Development, P.O. Box35, Yuseong-Gu, Daejon, Korea

A new nondimensional method for predicting the windmilling performance of centrifugal-flow turbojet engines in flight has been developed. The method incorporates loss correlations to estimate the performance of major engine components. Given basic engine geometry, flight Mach number, and ambient conditions, this method predicts transient and steady-state windmilling performance. Thus, this method can be used during the preliminary design stage when detailed hardware geometry and component performance data are not yet available. A nondimensional time parameter is newly defined, and using this parameter, the transient performance of different types of turbojets (e.g. centrifugal vs. axial) is compared. In addition, the predictions’ sensitivity to loss correlations, slip factors, and inlet ambient temperatures are analyzed.

KSME International Journal, Vol. 18 No. 11, pp. 2032-2041, 2004

LDV Measurement, Flow Visualization and Numerical Analysis of Flow Distribution in a Close-Coupled Catalytic Converter

Duk-Sang.Kim*, Yong-Seok,Cho

Graduate School of Automotive Engineering, Kookmin University, Seoul, Korea

Results from an experimental study of flow distribution in a close-coupled catalytic converter (CCC) are presented. The experiments were carried out with a flow measurement system specially designed for this study under steady and transient flow conditions. A pitot tube was a tool for measuring flow distribution at the exit of the first monolith. The flow distribution of the CCC was also measured by LDV system and flow visualization. Results from numerical analysis are also presented. Experimental results showed that the flow uniformity index decreases as flow Reynolds number increases. In steady flow conditions, the flow through each exhaust pipe made some flow concentrations on a specific region of the CCC inlet. The transient test results showed that the flow through each exhaust pipe in the engine firing order, interacted with each other to ensure that the flow distribution was uniform. The results of numerical analysis were qualitatively accepted with experimental results. They supported and helped explain the flow in the entry region of CCC.

Key World : Close-coupled catalytic converter, Exhaust gas after-treatment, Exhaust gas flow distribution, Flow visualization, LDV(Laser Doffler Velocimetry), Numerical analysis

KSME International Journal, Vol. 18 No. 11, pp. 2042-2048, 2004

Molecular Dynamics Study on External Field Induced Crystallization of Amorphous Argon Structure

Seungho Park*, Sung San Cho

Department of Mechanical and System Design Engineering, Hongik University, Seoul, Korea

Joon Sik Lee

School of Mechanical and Aerospace Engineering, Seoul National University, Seoul, Korea

Young Ki Choi

School of Mechanical Engineering, Chung-Ang University, Seoul, Korea

Ohmyoung Kwon

School of Mechanical Engineering, Korea University, Seoul, Korea

A molecular dynamics study has been conducted on an external-force-field-induced isothermal crystallization process of amorphous structures as a new low-temperature athermal crystallization process. An external cyclic-force field with a dc bias is imposed on molecules selected randomly in an amorphous-phase of argon. Multiple peaks smoothed out in the radial distribution functions for amorphous states appear very clearly during the crystallization process that cannot be achieved otherwise. When the amorphous material is locally exposed to an external force field, crystallization starts and propagates from the interfacial region and crystallization growth rates can be estimated.

KSME International Journal, Vol. 18 No. 11, pp. 2049-2057, 2004

The Effect of Water Emulsified Fuel on a Motorway-Bus Diesel Engine

Kweonha Park*, Inseok Kwak

Department of Mechanical Engineering, Korea Maritime University, 1, Dongsam-dong, Yeongdo-gu, Pusan, 606-791, Korea

Seungmook Oh

Department of Engine and Enviromment, KIMM, 171, Jang-dong, Yuseong-gu, Daejeon, 305-343, Korea

Abstract: This study is carried out to investigate the combustion characteristics and durability of a diesel engine using emulsified fuel. The test uses water in oil type emulsified fuel. In order to understand the effect of emulsified fuel in a wide range of engine running conditions, D-13 mode is selected as a test condition, and a durability test is included to understand the long-term effect of water. Combustion pressure in cylinder, exhaust emissions, specific fuel consumption, sound level and maximum torque are measured. NOx and PM are reduced simultaneously and the specific fuel consumption is increased and decreased at low and high loads, respectively. There is no trouble and any damage on the parts of the cylinder during a 500 hour durability test.

Key Words : Emulsified Fuel, Micro-Explosion, D-13 Mode Test, NOx, Particulate Matter

KSME International Journal, Vol. 18 No. 11, pp. 2058-2065, 2004

Application of Light Collecting Probe with High Spatial Resolution to Spark-Ignited Spherical Spray Flames

Young-Joon Yang*, Fumiteru Akamatsu, Masashi Katsuki

Department of Mechanical Engineering, Osaka University, 2-1 Yamadaoka, Suita, Osaka 565-0871, Japan

A light collecting probe named Multi-color Integrated Cassegrain Receiving Optics (MICRO) is applied to spark-ignited spherical spray flames to obtain the flame propagation speed in freely falling droplet suspension produced by an ultrasonic atomizer.  Two MICRO probes are used to monitor time-series signals of OH chemiluminescence from two different locations in the flame.  By detecting the arrival time difference of the propagating flame front, the flame propagation speed is calculated with a two-point delay-time method.  In addition, time-series images of OH chemiluminescence are simultaneously obtained by a high-speed digital CCD camera to ensure the validity of the two-point delay-time method by the MICRO system.  Furthermore, the relationship between the spray properties measured by phase Doppler anemometer (PDA) and the flame propagation speed are discussed with three different experimental conditions by changing the fuel injection rate.  It was confirmed that the two-point delay-time method with two MICRO probes was very useful and convenient to obtain the flame propagation speed and that the flame propagation speed was different depending on the spray properties.

Keywords: Light Collecting Probe, Chemiluminescence, Spray Combustion, Flame Propagation Speed

KSME International Journal, Vol. 18 No. 12, pp. 2069-2079, 2004

Modeling and Numerical Investigation of the Biomechanical Interaction for Human-Rifle System

Je-Wook Chae*

Senior Researcher, Department of Ground System Development Center, Agency for Defence Development, 215 Sunam-dong, Yuseong-gu, Daejeon, 305-600, Korea

Young-Shin Lee

Professor, Department of Mechanical Design Engineering, Chungnam National University, 220 Gung-dong, Yuseong-gu, Daejeon, 305-764, Korea

This paper represents the description of a complex mathematical model of biomechanical interaction for human-rifle system during shooting. The model is developed by finite element method using bar elements. And three typical shooting positions, i.e. standing, kneeling and prone are used. Characteristics of interior/exterior ballistics and behaviors of human-rifle system are evaluated by this model, which takes into account the influence of environment, bullet, powder, barrel geometry parameters and anthropological parameters. The results of this study can be applied to anthropology, biomechanics, medical science, gait analysis, interior ballistics and exterior ballistics.

KEY WORDS : Human-Rifle System, Small Arms, Standing Position, Kneeling Position, Prone Position, Ballistics, Dispersion Characteristics

KSME International Journal, Vol. 18 No. 12, pp. 2080-2094, 2004

Design of a Nuclear Reactor Controller Using a Model Predictive Control Method

Man Gyun Na*, Dong Won Jung, Sun Ho Shin, Sun Mi Lee

Chosun University, Department of Nuclear Engineering,

375 Seosuk-dong, Dong-gu, Gwangju 501-759, Korea

Yoon Joon Lee

Cheju National University, Department of Nuclear and Energy Engineering,

1 Ara-il-dong, Jeju-do 690-756, Republic of Korea

Jin Wook Jang, Ki Bog Lee

Korean Atomic Energy Research Institute, P.O. Box 105, Yuseong, Daejon 305-600, Republic of Korea

A model predictive controller is designed to control thermal power in a nuclear reactor. The basic concept of the model predictive control is to solve an optimization problem for finite future time steps at current time, to implement only the first optimal control input among the solved control inputs, and to repeat the procedure at each subsequent instant. A controller design model used for designing the model predictive controller is estimated every time step by applying a recursive parameter estimation algorithm. A 3-dimensional nuclear reactor analysis code, MASTER that was developed by Korea Atomic Energy Research Institute (KAERI), was used to verify the proposed controller for a nuclear reactor. It was known that the nuclear power controlled by the proposed controller well tracks the desired power level and the desired axial power distribution.

Key Words: Nuclear Reactor Control, Model Predictive Control, Load-following Operation, Nuclear Power Level Control, Axial Shape Index (ASI) Control, Recursive Parameter Estimation

KSME International Journal, Vol. 18 No. 12, pp. 2095-2103, 2004

Rule-Based Process Planning by Grouping Features

Honghee Lee*

Division of Mechanical Engineering, Inha University,

253 Yonghyun-dong, Nam-gu, Inchon 402-751, Korea

A macro-level CAPP system is proposed to plan the complicated mechanical prismatic parts efficiently. The system creates the efficient machining sequence of the features in a part by analyzing the feature information. Because the planning with the individual features is very complicated, feature groups are formed for effective planning using the nested relations of the features of a part, and special feature groups are determined for sequencing. The process plan is generated based on the sequences of the feature groups and features. When multiple machines are required, efficient machine assignment is performed. A series of heuristic rules are developed to accomplish it.

Keywords: Computer-Aided Process Planning (CAPP), Geometric Feature, Feature Group

KSME International Journal, Vol. 18 No. 12, pp. 2104-2113, 2004

Molecular Dynamics Study on Evaporation Process of Adherent Molecules on Surface by High Temperature Gas

Young-Joon Yang, Osamu Kadosaka, Masahiko Shibahara, Masashi Katsuki

Department of Mechanical Engineering, Osaka University,

2-1 Yamadaoka, Suita, Osaka 565-0871, Japan

Si-Pom Kim*

Department of Mechanical Engineering, Dong-A University,

840 Hadan2-dong, Saha-gu, Busan 604-714, Korea

Surface degreasing method with premixed flame is proposed as the removal method of adherent impurities on materials.  Effects of adherent molecular thickness and surface potential energy on evaporation rate of adherent molecules and molecular evaporation mechanism were investigated and discussed in the present study.  Evaporation processes of adherent molecules on surface molecules were simulated by the molecular dynamics method to understand thermal phenomena on evaporation processes of adherent molecules by using high temperature gas like burnt gas.  The calculation system was composed of a high temperature gas region, an adherent molecular region and a surface molecular region.  Both the thickness of adherent molecules and potential parameters affected the evaporation rate of adherent molecules and evaporation mechanism in molecular scale.

Keywords : Molecular Dynamics Method, Evaporation, Surface Treatment, Adherent Molecules, Thin Film, Burnt Gas

KSME International Journal, Vol. 18 No. 12, pp. 2114-2124, 2004

A Frequency Response Function-Based Damage Identification Method for Cylindrical Shell Structures

Usik Lee*, Wonhee Jeong, Jooyong Cho

Department of Mechanical Engineering, Inha University

253 Yonghyun-Dong, Nam-Ku, Incheon 402-751, Korea

In this paper, a structural damage identification method (SDIM) is developed for cylindrical shells and the numerically simulated damage identification tests are conducted to study the feasibility of the proposed SDIM. The SDIM is derived from the frequency response function solved from the structural dynamic equations of damaged cylindrical shells. A damage distribution function is used to represent the distribution and magnitudes of the local damages within a cylindrical shell. In contrast with most existing modal parameters-based SDIMs which require the modal parameters measured in both intact and damaged states, the present SDIM requires only the FRF-data measured in the damaged state. By virtue of utilizing FRF-data, one is able to make the inverse problem of damage identification well-posed by choosing as many sets of excitation frequency and FRF measurement point as needed to obtain a sufficient number of equations.

Key Words : Structural Damage, Damage Identification, Cylindrical Shell, Frequency Response Function, Vibration

KSME International Journal, Vol. 18 No. 12, pp. 2125-2136, 2004

Fluid Effects on the Core Seismic Behavior of a Liquid Metal Reactor

Gyeong-Hoi Koo*, Jae Han Lee

Korea Atomic Energy Research Institute,P.O. Box 105, Yusong,

Taejon, 305-600, Korea.

In this paper, a numerical application algorithm for applying the CFAM(Consistent Fluid Added Mass) matrix for a core seismic analysis is developed and applied to the 7-ducts core system to investigate the fluid effects on the dynamic characteristics and the seismic time history responses. To this end, three cases such as the in-air condition, the in-water condition without the fluid coupling terms, and the in-water condition with the fluid coupling terms are considered in this paper. From modal analysis, the core duct assemblies revealed strongly coupled out-of-phase vibration modes unlike the other cases with the fluid coupling terms considered. From the results of the seismic time history analysis, it was also verified that the fluid coupling terms in the CFAM matrix can significantly affect the impact responses and the seismic displacement responses of the ducts.

Key Words : Core Seismic Analysis, Fluid-Structure Interaction, Consistent Fluid Added Mass Matrix, FAMD(Fluid Added Mass and Damping) Code, Liquid Metal Reactor

KSME International Journal, Vol. 18 No. 12, pp. 2137-2147, 2004

Adaptive Clustering Algorithm for Recycling Cell Formation : An Application of Fuzzy ART Neural Networks

Kwang-Kyu Seo*

Department of Industrial Information and Systems Engineering, Sangmyng University,

San 98-20, Anso-Dong, Chonan, Chungnam 330-720, Korea.

Ji-Hyung Park

CAD/CAM Research Center, Korea Institute of Science and Technology,

P.O. Box 131, Cheongryang, Seoul, Korea.

The recycling cell formation problem means that disposal products are classified into recycling part families using group technology in their end-of-life phase. Disposal products have the uncertainties of product status by usage influences during product use phase, and recycling cells are formed design, process and usage attributes. In order to deal with the uncertainties, fuzzy set theory and fuzzy logic-based neural network model are applied to recycling cell formation problem for disposal products. Fuzzy C-mean algorithm and a heuristic approach based on fuzzy ART neural network is suggested. Especially, the modified Fuzzy ART neural network is shown that it has a good clustering results and gives an extension for systematically generating alternative solutions in the recycling cell formation problem. Disposal refrigerators are shown as examples.

Key Words : Fuzzy Theory, Fuzzy C-Mean Algorithm, Fuzzy ART neural network, Recycling Cell  Formation

KSME International Journal, Vol. 18 No. 12, pp. 2148-2157, 2004

Vibration and Dynamic Stability of Pipes Conveying Fluid on Elastic Foundations

Bong-Jo Ryu*

Department of Mechanical Design Engineering, Hanbat National University,

San 16-1, Duckmyoung-dong, Yuseong-gu, Daejon 305-764, Korea

Si-Ung Ryu, Geon-Hee Kim

Operation & Research Division, Korea Basic Science Institute,

52, Yeoeun-dong, Yuseong-gu, Daejon 305-333, Korea

Kyung-Bin Yim

Department of Mechanical Engineering, Dongyang Technical College

62-160, Gocheok-dong, Guro-gu, Seoul 152-714, Korea

The paper deals with the vibration and dynamic stability of cantilevered pipes conveying fluid on elastic foundations. The relationship between the eigenvalue branches and corresponding unstable modes associated with the flutter of the pipe is thoroughly investigated. Governing equations of motion are derived from the extended Hamilton's principle, and a numerical scheme using finite element methods is applied to obtain the discretized equations. The critical flow velocity and stability maps of the pipe are obtained for various elastic foundation parameters, mass ratios of the pipe, and structural damping coefficients. Especially critical mass ratios, at which the transference of the eigenvalue branches related to flutter takes place, are precisely determined. Finally, the flutter configuration of the pipe at the critical flow velocities is drawn graphically at every twelfth period to define the order of the quasi-mode of flutter configuration.

Key words ; Elastic foundations, Pipe conveying fluid, Eigenvalue branches, Flutter configuration, Structural damping

KSME International Journal, Vol. 18 No. 12, pp. 2158-2173, 2004

Development of Cleavage Fracture Toughness Locus Considering Constraint Effects

Yoon-Suk Chang*, Young-Jin Kim

SAFE Research Centre, School of Mechanical Engineering, Sungkyunkwan University

300 Chunchun-dong, Jangan-gu, Suwon, Kyonggi-do 440-746, Korea

Ludwig Stumpfrock

Staatliche Materialprüfungsanstalt, Universität Stuttgart, Pfaffenwaldring 32,

D-70569 Stuttgart, Germany

In this paper, the higher order terms in the crack tip stress fields are investigated macroscopically for more realistic assessment of structural material behaviors. For reactor pressure vessel material of A533B ferritic steel, effects of crack size and temperature have been evaluated using 3-point SENB specimens through a series of finite element analyses, tensile tests and fracture toughness tests. The T-stress, Q-parameter and q-parameter as well as the K and J-integral are calculated and mutual relationships are investigated also. Based on the evaluation, it has proven that the effect of crack size from standard length(a/W=0.53) to shallow length (a/W=0.11) is remarkable whilst the effect of temperature from -20°C to -60°C is negligible. Finally, the cleavage fracture toughness loci as a function of the promising Q-parameter or q-parameter are developed using specific test results as well as finite element analysis results, which can be applicable for structural integrity evaluation considering constraint effects.

Key Words: Constraint Effect, Two-parameter Approach, Modified Boundary Layer Formulation, T-stress, Q-parameter, q-parameter, Biaxiality Ratio, Cleavage Fracture Toughness Locus

KSME International Journal, Vol. 18 No. 12, pp. 2174-2181, 2004

A Study on the Fault Diagnosis of the 3-D Roll Shape in Cold Rolling

Chang Woo Lee

Department of Mechanical Engineering, Konkuk University, 1 Hwayang-Dong,

Gwangjin-Gu, Seoul 143-701, Korea

Hyun Kyoo Kang

Department of Mechanical Engineering, Konkuk University, 1 Hwayang-Dong,

Gwangjin-Gu, Seoul 143-701, Korea

Kee Hyun Shin*

Department of Mechanical and Aerospace Engineering, Konkuk University, 1 Hwayang-Dong,

Gwangjin-Gu, Seoul 143-701, Korea

The metal processing system usually consists of various components such as motors, work rolls, backup rolls, idle rolls, sensors, etc. Even a simple fault in a single component in the system may cause a serious damage on the final product. It is, therefore, necessary to diagnose the faults of the components to detect and prevent a system failure. Especially, the defects in a work roll are critical to the quality of strip. In this study, a new 3-D diagnosis method was developed for roll shape defects in rolling processes. The new method was induced from analyzing the rolling mechanism by using a rolling force model, a tension model, the Hitchcock’s equation, and measurement of the strip thickness, etc. Computer simulation shows that the proposed method is very useful in the diagnosis of the 3-D roll shape.

Keywords: 3-D Roll Shape Fault, Deformed Roll Radius, Diagnosis, Parameters Sensitive Analysis, Rolling Force, Transverse Strip Tension, Work Roll

KSME International Journal, Vol. 18 No. 12, pp. 2182-2189, 2004

Analysis of cutting properties with reference to amount of coolant used in an environment-conscious turning process

Seung-Han Yang*

School of Mechanical Engineering, Kyungpook National University, Daegu-702-701, Korea

Young-Moon Lee

School of Mechanical Engineering, Kyungpook National University, Daegu-702-701, Korea

Young-Suk Kim

School of Mechanical Engineering, Kyungpook National University, Daegu-702-701, Korea

In the recent years, environmentally conscious design and manufacturing technologies have attracted considerable attention. The coolants, lubricants, solvents, metallic chips and discarded tools from manufacturing operations will harm our environment and the earth’s ecosystem. In the present work, the Tukey method of multiple comparisons is used to select the minimum level of coolant required in a turning process.  The amount of coolant is varied in 270 designed experiments and the parameters cutting temperature, surface roughness, and specific cutting energy are carefully evaluated.  The effects of coolant mix ratio as well as the amount of coolant on the turning process are studied in the present work.  The cutting temperature and surface roughness for different quantity of coolant are investigated by analysis of variance (ANOVA)-test and a multiple comparison method.  ANOVA-test results signify that the average tool temperature and surface roughness depend on the amount of coolant.  Based on Tukey’s Honestly Significant Difference (HSD) method, one of the multiple comparison methods, the minimum level of coolant is 1.0 L/min with 2% mix ratio in the aspect of controlling tool temperature.  F-test concludes that the amount of coolant used does not have any significant effect on specific cutting energy.  Finally, Tukey method ascertains that 0.5 L/min with 6% mix ratio is the minimum level of coolant required in turning process without any serious degradation of the surface finish.  Considering all aspects of cutting, the minimum coolant required is 1.0 L/min with 6% mix ratio.  It is merely half the coolant currently used i.e. 2.0 L/min with 10% mix ratio.  Minimal use of coolant not only economically desirable for reducing manufacturing cost but also it imparts fewer hazards to human health.  Also, sparing use of coolant will eventually transform the turning process into a more environment-conscious manufacturing process.

Key Word: Cutting temperature, Surface roughness, Analysis of variance (ANOVA), Tukey method of multiple comparisons, Honestly Significant Difference (HSD)

KSME International Journal, Vol. 18 No. 12, pp. 2190-2203, 2004

Two-dimensional adaptive mesh generation algorithm and its application with higher-order compressible flow solver

Sutthisak Phongthanapanich, Pramote Dechaumphai*

Mechanical Engineering Department, Chulalongkorn University, Bangkok 10330, Thailand

A combined procedure for two-dimensional Delaunay mesh generation algorithm and an adaptive remeshing technique with higher-order compressible flow solver is presented.  A pseudo-code procedure is described for the adaptive remeshing technique.  The flux-difference splitting scheme with a modified multidimensional dissipation for high-speed compressible flow analysis on unstructured meshes is proposed.  The scheme eliminates nonphysical flow solutions such as the spurious bump of the carbuncle phenomenon observed from the bow shock of the flow over a blunt body and the oscillation in the odd-even grid perturbation in a straight duct for the Quirk's odd-even decoupling test.  The proposed scheme is further extended to achieve higher-order spatial and temporal solution accuracy.  The performance of the combined procedure is evaluated on unstructured triangular meshes by solving several steady-state and transient high-speed compressible flow problems.

Keywords:  Adaptive mesh; Delaunay triangulation; carbuncle phenomenon; H-correction entropy fix

KSME International Journal, Vol. 18 No. 12, pp. 2204-2208, 2004

A STUDY ON THE MECHANICAL PROPERTIES OF Ti-8Ta-3Nb Alloy for BIOMATERIALS

Kyung Won Lee, Jae Sam Ban, Yeong Seon Yu and Kyu Zong Cho

Department of Mechanical Engineering, Chonnam National University,

Gwangju 500-757, Korea

Ti-8Ta-3Nb has been developed as a new biomaterial. The experimental specimens are as-cast and forged Ti-8Ta-3Nb alloys. Treatment in a solution, ranging from 760 to 960℃ has carried out. The microstructural research has carried out after the solution treatment and the hardness was measured. The specific heat and the length variations of Ti-8Ta-3Nb were also measured. The optimum temperature for the solution heat treatment of Ti-8Ta-3Nb was found to be 880℃. This was based on the mechanical properties and the volume fraction of α phase and their phases shown from the results of the solution heat treatment. From the results, the β transition temperature of Ti-8Ta-3Nb was found to be between 860℃ and 880℃.

Key words: Specific heat, β-transition temperature(Tβ), Ti alloy, Hardness, Heat treatment solution

KSME International Journal, Vol. 18 No. 12, pp. 2209-2215, 2004

Development of machine vision system and dimensional analysis of the automobile front-chassis-module

Dong-Mok Lee

Graduate school of Mechanical Engineering, Kyungpook National University, Daegu, South Korea

Seung-Han Yang*, Sang-Ryong Lee, and Young-Moon Lee

School of Mechanical Engineering, Kyungpook National University, Daegu, South Korea

In the present research work, an automated machine vision system and a new algorithm to interpret the inspection data has been developed. In the past, the control of tolerance of front-chassis-module was done manually. In the present work a machine vision system and required algorithm was developed to carryout dimensional evaluation automatically. The present system is used to verify whether the automobile frontchassis-module is within the tolerance limit or not. The directional ability parameters related with front-chassis-module such as camber, caster, toe and king-pin angle are also determined using the present algorithm. The above mentioned parameters are evaluated by the pose of interlinks in the assembly of an automobile front-chassis-module. The location of ball-joint center is important factor to determine these parameters. A method to determine the location of ball-joint center using geometric features is also suggested in this paper. In the present work a 3-D best fitting method is used for determining the relationship between nominal design coordinate system and the corresponding feature coordinate system.

Key words: Machine Vision, Front-Chassis-Module, Ball-Joint Center, Dimensional Analysis, Least Squares, Best Fitting

KSME International Journal, Vol. 18 No. 12, pp. 2216-2224, 2004

Dynamic Behavior of Cracked Pipe Conveying Fluid with Moving Mass Based on Timoshenko Beam Theory

Han-Ik Yoon *

Mechanical Engineering, University of Dong-eui, San 24, Gaya3-dogn Busanjin-gu,

Busan 614-714, Korea

In-Soo Son

Department of Mechanical Engineering, Graduate School of Dong-eui University, Busan 614-714, Korea

In this paper we studied about the effect of the open crack and the moving mass on the dynamic behavior of simply supported pipe conveying fluid. The equation of motion is derived by using Lagrange’s equation and analyzed by numerical method. The crack section is represented by a local flexibility matrix connecting two undamaged pipe segments i.e. the crack is modeled as a rotational spring. The influences of the crack severity, the position of the crack, the moving mass and its velocity, the velocity of fluid, and the coupling of these factors on the vibration mode, the frequency, and the mid-span displacement of the simply supported pipe are depicted.

Key Words : Dynamic Behavior, Open Crack, Moving Mass, Pipe Conveying Fluid, Timoshenko  Beam Theory, Flexibility Matrix, Crack Severity

KSME International Journal, Vol. 18 No. 12, pp. 2225-2235, 2004

Dynamic Characteristic Identification on Steel Column bases Installed in Pendulum-type Earthquake

Response Observatory

Choi, Jae-hyouk*, Ohi, Kenichi

Department of Architecture and Civil Engineering, Kobe University, 1-1Rokodai- cho, Nada-ku, Kobe,  657-8501, JAPAN

An observatory termed ‘Steel Swing’ has been developed, where a 15000 kg pendulum is hanged from a stiff steel frame. A building element can be tested after inserted between the pendulum and the frame. Free vibration, forced vibration tests and earthquake monitoring were performed on an exposed box-type steel column base. The response records monitored during natural earthquakes were used to identify the vibration property of the specimen. Identified system gain was approximated by a theoretical gain of linear SDOF system, and the response calculated based on such a linear system agrees with the monitored response fairly well. This research technique can be applied to check the behaviors of new materials and new details of connections and the safety of non-structural elements as well.

Keyword: Dynamic Characteristic, Free vibrations, Forced vibration, System gain,

Single Degree of Freedom viscous damped system (SDOF)

KSME International Journal, Vol. 18 No. 12, pp. 2236-2249, 2004

A Numerical Study for the Three-Dimensional Fluid Flow Past Tube Banks and Comparison with PIV Experimental Data

Man Yeong Ha*, Seung-Hyeon Kim, Kyung Chun Kim,

School of Mechanical Engineering, Pusan National University, Pusan 609-735, Korea

Young Chul Son

LG Electronic, Digital Appliance Co., Gyeongnam 641-711, Korea

The analysis for the three-dimensional fluid flow past tube banks arranged in equilateral-triangular form at = 4,000 is carried out using a large eddy simulation technique. The governing equations for the mass and momentum conservation are discretized using the finite volume method. Parallel computational techniques using MPI (Message Passing Interface) are implemented in the present computer code. The computation time decreases linearly proportional to the number of used CPUs in the present parallel computation. We obtained the time-averaged streamwise and cross-streamwise velocities and turbulent intensities. The present numerical results are compared with the PIV experimental data and agree generally well with the experimental data.

Keywords : Tube Bundle, Fluid Flow, LES, Parallel Computing

KSME International Journal, Vol. 18 No. 12, pp. 2250-2257, 2004

Site Calibration for the Wind Turbine Performance Evaluation

Yoonsu Nam*, Neungsoo Yoo, Jungwan Lee

Division of Mechanical and Mechatrontics Eningeering, Kangwon National University,

192-1 Hyoja 2 dong, Chunchon city, Kangwon-do, 200-701, Korea

The accurate wind speed information at the hub height of a wind turbine is very essential to the exact estimation of the wind turbine power performance testing. Several methods on the site calibration, which is a technique to estimate the wind speed at the wind turbine’s hub height based on the measured wind data using a reference meteorological mast, are introduced. A site calibration result and the wind resource assessment for the TaeKwanRyung test site are presented using three-month wind data from a reference meteorological mast and the other mast temporarily installed at the site of wind turbine. Besides, an analysis on the uncertainty allocation for the wind speed correction using site calibration is performed.

Keywords : Site Calibration, Wind Turbine, Flow Distortion Correction Factor, Wind Direction Sector

KSME International Journal, Vol. 18 No. 12, pp. 2258-2264, 2004

Comparison of Shear-Thinning Blood Flow Characteristics between Longitudinal and Transverse Vibration

Sung-Ho Choi, Sehyun Shin*

School of Mechanical Engineering, Kyungpook National University

1370 Sangyeok-dong Buk-gu Daegu, 702-701 Republic of Korea

Kyung-Tae Lee

Department of Aerospace Engineering, Sejong University
98 Gunja-Dong, Gwangjin-Gu, Seoul, 143-747, Korea

This article described the numerical investigation of shear-thinning blood flow characteristics when subjected to longitudinal and transverse vibrations and delineated the underlying mechanisms of the flow rate enhancements, respectively. In order to fully consider the mechanical vibrations of the capillary, a moving wall boundary condition was adopted. The present numerical results showed that the longitudinal vibration caused a significant increase of wall shear rates, which resulted in a decrease of viscosity and the subsequent increase of flow rates. However, the shear rate for the transverse vibration was slightly increased and the calculated flow rate was underestimated comparing with the previous experimental results.

Keywords : shear-thinning, vibration, flow rate, vibration-induced shear, viscosity

KSME International Journal, Vol. 18 No. 12, pp. 2265-2272, 2004

Fluid Flow Characteristics in the Aquaculture Tank for a Breeding Fish

Hyo Min Jeong, Han Shik Chung*

School of Mechanical & Aerospace Engineering, Institute of Marine Industry,

Gyeongsang National University, Gyeongnam 650-160, Korea

Se-Hyun Kim, Seuk-Cheun Choi

Graduate School, Department of Mechanical and Precision Engineering,

Gyeongsang National University, Gyeongnam 650-160, Korea

Kang-Youl Bae

Boo Kang Plant Co., Ltd., 6 Floor, Hwoiwon Credit Union B/D, 670-6, Hwoiwon-Dong, Masan, Gyeongnam, Korea

The aquaculture tank is used for breeding fish in sea water which was pumped up to land. The flow characteristics in the aquaculture were investigated with varying the tank geometry and flow rate. The numerical analysis has been employed for calculating the velocity and temperature distributions in a water tank of rectangular type. The finite volume method and SIMPLE algorithm with 3-dimensional standard k-ε turbulence model were used for the numerical analysis. For comparison with experimental results, the PIV system was applied to visualize the flow patterns quantitatively. The numerical results showed good agreements with the experimental results. The mean velocity and temperature versus aquarium depth were represented for various circulating flow rates. Especially, the aquaculture environment is recommended that the aquarium depth has to be d=0.5m, and this case is the condition of higher velocity and temperature in winter season.

Keywords : PIV (Particle Image Velocimetry), Circulating flow rate, Flow characteristics,

Standard k-εturbulence model, FVM(Finite Volume Method)

KSME International Journal, Vol. 18 No. 12, pp. 2273-2283, 2004

Vortical Flows over a LEX-Delta Wing at High Angles of Attack

Young-Ki Lee, Heuy-Dong Kim(

School of Mechanical Engineering, Andong National University, 388 Songcheon-dong, Andong, 
Kyeongbuk, 760-749, Korea

The vortical flows over sharp-edged delta wings with and without a leading edge extension have been investigated using a computational method. Three-dimensional compressible Reynolds-averaged Navier-Stokes equations are solved to provide an understanding of the effects of the angle of attack and the angle of yaw on the development and interaction of vortices and the aerodynamic characteristics of the delta wing at a freestream velocity of 20 m/s. The present computations provide qualitatively reasonable predictions of vortical flow characteristics, compared with past wind tunnel measurements. In the presence of a leading edge extension, a significant change in the suction pressure peak in the chordwise direction is much reduced at a given angle of attack. The leading edge extension can also stabilize the wing vortex on the windward side at angles of yaw, which dominates the vortical flows over yawed delta wings.

Key Words: Angle of Attack, Angle of Yaw, Delta Wing, Leading Edge Extension, Vortical Flow, Vortex Breakdown

KSME International Journal, Vol. 18 No. 12, pp. 2284-2293, 2004

Evaporation Heat Transfer and Pressure Drop Characteristics of R-134a in the Oblong Shell and Plate Heat Exchanger

Jae-Hong Park*

Department of Refrigeration & Air-Conditioning Engineering, PuKyong National University,

San 100, Yong-dang dong, Namgu, Busan, 608-739, Korea

Young-Soo Kim

College of Engineering School of Mechanical Engineering, PuKyong National University,

San 100, Yong-dang dong, Namgu, Busan, 608-739, Korea

The evaporation heat transfer coefficient hr and frictional pressure drop Δpf of refrigerant R-134a flowing in the oblong shell and plate heat exchanger were investigated experimentally in this study. Four vertical counterflow channels were formed in the oblong shell and plate heat exchanger by four plates of geometry with a corrugated sinusoid shape of a 45° chevron angle. Upflow of refrigerant R-134a boils in two channels receiving heat from downflow of hot water in other channels. The effects of the refrigerant mass flux, average heat flux, refrigerant saturation temperature and vapor quality of R-134a were explored in detail. Similar to the case of a plate heat exchanger, even at a very low Reynolds number, the flow in the oblong shell and plate heat exchanger remains turbulent. The results indicate that the evaporation heat transfer coefficient hr and pressure drop Δpf increase with the vapor quality. A rise in the refrigerant mass flux causes an increase in the hr and Δpf. But the effect of the average heat flux does not show significant effect on the hr and Δpf. Finally, at a higher saturation temperature, both the hr and Δpf are found to be lower. The empirical correlations are also provided for the measured heat transfer coefficient and pressure drop in terms of the Nusselt number and friction factor.

Key Words: Oblong Shell and Plate Heat Exchanger, Evaporation, Heat Transfer Coefficient, Pressure Drop

KSME International Journal, Vol. 18 No. 12, pp. 2294-2302, 2004

Experimental Study on Spray Etching Process in Micro Fabrication of Lead Frame

Ji-Won Jung

Research Institute of Mechanical Technology, Pusan National University, 30, Jangjeon-dong, Geumjeong-gu, Busan 609-735, Korea

Gyung-Min Choi, Duck-Jool Kim*

School of Mechanical Engineering, Pusan National University, 30, Jangjeon-dong, Geumjeong-gu, Busan 609-735, Korea

The objective of this study is to obtain detailed information for the micro fabrication of lead frames by applying spray technology to wet etching process. Wet etching experiments were performed with different etching parameters such as injection pressure, distance from nozzle tip to etched substrate, nozzle pitch and etchant temperature. The characteristics of single and twin spray were measured to investigate the correlation between the spray characteristics and the etching characteristics. Drop size and velocity were measured by Phase-Doppler Anemometer (PDA). Four liquids of different viscosity were used to reveal the effects of viscosity on the spray characteristics. The results indicated that the shorter the distance from nozzle tip and the nozzle pitch, the larger etching factor became. The average etching factor had good positive correlation with average axial velocity and impact force. It was found that the etching characteristics depended strongly on the spray characteristics.

Key Words : Wet Etching, Lead Frame, Spray Characteristics, Etching Factor, Impact Force

KSME International Journal, Vol. 18 No. 12, pp. 2303-2309, 2004

Characteristics of NOx Emission with Flue Gas Dilution in Air and Fuel Sides

Eun-Seong Cho and Suk Ho Chung*

School of Mechanical and Aerospace Engineering, Seoul National University

Seoul 151-742, Korea

Flue gas recirculation (FGR) is a method widely adopted to control NOx in combustion system.  The recirculated flue gas decreases flame temperature and reaction rate, resulting in the decrease in thermal NO production.  Recently, it has been demonstrated that the recirculated flue gas in fuel stream, that is, the fuel induced recirculation (FIR), could enhance a much improved reduction in NOx per unit mass of recirculated gas, as compared to the conventional FGR in air.  In the present study, the effect of FGR/FIR methods on NOx reduction in turbulent swirl flames by using N2 and CO2 as diluent gases to simulate flue gases.  Results show that CO2 dilution is more effective in NO reduction because of large temperature drop due to the larger specific heat of CO2 compared to N2 and FIR is more effective to reduce NO emission than FGR when the same recirculation ratio of dilution gas is used.

Key Words : Flue Gas Recirculation (FGR), Fuel Induced Recirculation (FIR), Nitric Oxides

KSME International Journal, Vol. 18 No. 12, pp. 2303-2309, 2004

A Study on the Behavior of Evaporating Diesel Spray Using LIEF Measurement and KIVA Code

Jeongkuk Yeom*, Sungsik Chung, Jongyul Ha

Department of Mechanical Engineering, Dong-A University, Busan 604-714, Korea

Yongrae Kim

School of Mechanical and Aerospace Engineering, Seoul National University, Seoul 151-742, Korea

Kyoungdoug Min

School of Mechanical and Aerospace Engineering, Seoul National University, Seoul 151-742, Korea

The effects of change in injection pressure on spray structure in high temperature and pressure field have been investigated. The analysis of liquid and vapor phases of injected fuel is important for emissions control of diesel engines. Therefore, this work examines the evaporating spray structure using a constant volume vessel. The injection pressure is selected as the experimental parameter, is changed from 400 bar to 800 bar by using a common rail injection system. Also, we conducted simulation study by modified KIVA-II code. The results of simulation study are compared with experimental results. The images of liquid and vapor phase for free spray were simultaneously taken by exciplex fluorescence method. As experimental results, the vapor concentration of injected fuel is leaner due to the increase of atomization in the case of the high injection pressure than in that of the low injection pressure. The calculated results obtained by modified KIVA-II code show good agreements with experimental results.

Key Words: Exciplex Fluorescence Method, KIVA-II Code, Diesel Spray, Mie Scattering, Common Rail

Journal of Mechanicl Science and Technology(KSME I. J.), Vol. 19, No. 1, pp. 1-14, 2005

A Robust Real Time Adaptive Controller Design for Robot Manipulator with Eight-Joints based on DSPs

Sung Hyun Han*

Division of Mechanical and Automation Eng., Kyungnam Univ., Masan, 631-701, Korea.

## Hideki Hashimoto

Institute of Industrial science Univ. of Tokyo, 7-22-1, Roppongi, Minato Tokyo 106 Japan.

In this paper we propose a new technique to the design and real-time control of an adaptive controller for robotic manipulator based on digital signal processors. The Texas Instruments DSPs(TMS320C80) chips are used in implementing real-time adaptive control algorithms to provide  enhanced motion control performance for robotic manipulators. In the proposed scheme, adaptation laws are derived from model reference adaptive control principle based on the improved Lyapunov second method. The proposed adaptive controller consists of an adaptive feed-forward and feedback controller and time-varying auxiliary controller elements. The proposed control scheme is simple in structure, fast in computation, and suitable for real-time control. Moreover, this scheme does not require any accurate dynamic modeling, nor values of manipulator parameters and payload. Performance of the proposed adaptive controller is illustrated by simulation and experimental results for robot manipulator with eight joints at the joint space and cartesian space.

Key Words : Model Reference Adaptive Control, DSP(TMS320C80), Eight Joints  Robot, Real Time Control, Implementation, Lyapunov stability

Journal of Mechanicl Science and Technology(KSME I. J.), Vol. 19, No. 1, pp. 15-27, 2005

A Smart Memory Type of Data Acquisition System for Shaft Misalignment Maintenance

Seung Min Kim

Korea Plant Service & Engineering Company, 196, Geumgok-dong, Bundang-dong, Seongnam, Gyeonggi-do, Korea

Jin Ho Suh

Research Center for Ocean Industrial Development, Pukyong National University,

599-1, Daeyon-dong, Nam-gu, Busan, 608-737, Korea

Jae Sung Im

Department of Mechanical Engineering, College of Engineering, Pukyong National University,

San 100, Yongdang-dong, Nam-gu, Busan, 608-739, Korea

Seong Bong Kim

Korea Plant Service & Engineering Company, 196, Geumgok-dong, Bundang-dong, Seongnam, Gyeonggi-do, Korea

Sang Bong Kim*

Department of Mechanical Engineering, College of Engineering, Pukyong National University, San 100, Yongdang-dong, Nam-gu, Busan, 608-739, Korea

This paper presents the development results of a smart memory module for data acquisition system to examine the characteristics of shaft misalignment. The smart memory module is a standalone type with high capacity, and it can communicate with computer via RS-232 interface in off-line after data acquisition. In the process of shaft misalignment maintenance, the misalignment data achieved by strain gauges on the turbine rotor are synchronized with the angle data gathered by 4 angular sensors boarded on the smart memory system. The real time data are acquisitioned in the manner of self operation during testing; then the data saved in smart memory are translated into a computer for data processing and analysis via RS-232C. For the better precision, the system uses two types of filters: a low pass filter on interface circuit and a transfer average filter in software. Also, the effectiveness of data acquisition operation using the developed smart memory module is proved through the experimental results using mock-up system.

Keywords: Strain Gauge, Smart Media Memory Card (SMC), Alignment, Turbine Rotor, One-Chip Computer, Strain Gauge Data Acquisition (SA)

Journal of Mechanicl Science and Technology(KSME I. J.), Vol. 19, No. 1, pp. 28-39, 2005

An Adaptive Control of an Autonomous Guided Vehicle System Using Cell-Mediated Immune Algorithm Controller and Vision Sensor

Young Jin Lee

Department  of Electrical Instrument and Control, Korea Aviation Polytechnic College,

438 Egeum-dong, Sachon City, Kyungnam, 664-180, Korea

Jin Ho Suh, Jin Woo Lee

Department of Electrical Engineering, Dong-A University, 840, Hadan-dong,

Saha-gu, Busan, 604-714, Korea

Kwon Soon Lee*

Division of Electrical, Electronic, and Computer Eng., Dong-A University, 840,

Hadan-dong, Saha-gu, Busan, 604-714, Korea

In this paper, we proposed an adaptive control method which is named CMIA (cell-mediated immune algorithm) controller with PID scheme. It is based on specific immune response of the biological immune system which is the cell-mediated immune response. It is also applied for the autonomous guided vehicle (AGV) system which is manufactured in this paper. The AGV is used for the port automation to carry container without human and to overcome uncertainty and nonlinearity because of running in the outdoor. To verify the performance of the proposed CMIA controller, some experiments for the AGV system are performed. Finally, the experimental results for the control of steering and speed of an AGV system illustrate the effectiveness of the proposed control scheme. These results for the proposed method also show that it has better performance than other conventional controller design methods.

Key words: Port automation, Autonomous guided vehicle (AGV), Adaptive control, Cell-mediated immune algorithm (CMIA) controller, Vision sensor, Neural network identifier (NNI)

Journal of Mechanicl Science and Technology(KSME I. J.), Vol. 19, No. 1, pp. 40-50, 2005

Boundary Control of an Axially Moving String: Actuator Dynamics Included

### Chang Won Kim

## Department of Mechanical and Intelligent Systems Engineering, Pusan National

### University, San 30 Jangjeon-dong Gumjeong-gu, Busan, 609-735, Korea.

### Keum-Shik Hong*

### School of Mechanical Engineering, Pusan National University,

### San 30 Jangjeon-dong Gumjeong-gu, Busan, 609-735, Korea

### Hahn Park

## Department of Mechanical and Intelligent Systems Engineering, Pusan National University,

San 30 Jangjeon-dong Gumjeong-gu, Busan, 609-735, Korea.

In this paper, an active vibration control of a translating tensioned string with the use of an electro-hydraulic servo mechanism at the right boundary is investigated. The equations of motion of the string are derived by using Hamilton’s principle for the systems with changing mass. The control objective is to suppress the transverse vibrations of the string via a right-boundary control. An energy-based right-boundary control law, generating a specific current input to the servo-valve, is derived. It is revealed that a time-varying boundary force, as a function of the slope of the string at the right end and a suitably chosen damping coefficient of the actuator, can successfully suppress the transverse vibrations. The exponential stability of the closed loop system is proved. The effectiveness of the proposed control law is demonstrated via simulations.

Key Words: Axially Moving System, Exponential Stability, Boundary Control, Hyperbolic Partial Differential Equation, Lyapunov Method

Journal of Mechanicl Science and Technology(KSME I. J.), Vol. 19, No. 1, pp. 51-60, 2005

KSNP+ Reactor Vessel Head Drop Analysis for a 5.5M Free Fall

Ihn Namgung

Daejeon Intelligent Robot Center, Daejeon Hightech Industry, Promotion Foundation

Jang-dong 48, Yuseong-gu, Daejeon 305-715, Korea,

Seung Ha Jeong

Korea Power Engineering Co., Deokjin-dong 150,

Yuseong-gu, Daejeon 305-600, South Korea

Dae Hee Lee*

Korea Power Engineering Co., Deokjin-dong 150,

Yuseong-gu, Daejeon 305-600, Korea

Taek Sang Choi

Korea Power Engineering Co., Deokjin-dong 150,

Yuseong-gu, Daejeon 305-600, Korea

The KSNP+ RV closure head drop analysis was carried out to assess the reactor core coolability in case of the RV closure head drop accident during the refueling operation. The analysis consists of a number of different RV head drop scenarios as the postulated accident events during refueling that include a concentric head drop case and three different cases of laterally offset head drop cases. The analysis was initiated due to the adoption of the IHA (Integrated Head Assembly) in the KSNP+ reactor design, which increases the weight of the RV closure head assembly.

Four different analysis models were developed that correspond to the RV head drop analysis scenarios. An in-house dynamic analysis code was used for the RV head drop analysis. The entire reactor internals and fuel assemblies are modeled by using lumped masses and spring elements. Because of the extreme load exerted by RV head drop, most members experience stresses that are beyond the elastic limits. A separate elastic-plastic analysis for some members was carried out and the resulting load-deflection curve was used as the stiffness of the element. The effect of water above the reactor vessel in the refueling pool was ignored for the conservative estimation of the analysis.

The analysis shows that the concentric head drop is the most severe case of loading condition. It also reveals that the local deformation of some reactor internals and the fuel assemblies is occurred; however the primary membrane stresses are within the bound of allowable stress limits. Consequently the reactor core remains in coolable state.

Key words : Impact analysis, Elastic-plastic analysis, Non-linear stress analysis, RV (Reactor Vessel) head drop analysis, KSNP+ (Korean Standard Nuclear Power Plant Plus)

Journal of Mechanicl Science and Technology(KSME I. J.), Vol. 19, No. 1, pp. 61-71, 2005

Finite Element Analysis of Transient Dynamic Viscoelastic Problems in Time Domain

Woo-Jin Sim*, Sung-Hee Lee

School of Mechanical Engineering, Kum-Oh National Institute of Technology,

188 Shinpyung-dong, Gumi, Gyungbuk, 730-701, Korea

In this paper, the simplified and stable finite element method is presented  for the time domain analysis of the transient dynamic viscoelastic problems, for which the weak form is obtained by applying the Galerkin's method to the equations of motion in time integral which do not contain the inertia terms explicitly, but the inertia effect is taken into account, and discretized spatially to obtain the semidiscrete equations in time integral. In the temporal approximation, only the time interpolation functions are used for approximating the dependent variables on the divided time axis, while the time integration schemes such as the Newmark and Houbolt methods are not necessary in contrary to the conventional approach. To show the validity and applicability, two-dimensional examples are given and solved for the displacements and stresses, especially for the dynamic stress concentrations by the wave diffraction, which are discussed in detail at the aspect of the viscoelastic damping. To the authors’ knowledge, no previous results except for the test example exist in the literature.

Key Words : Viscoelastic, Dynamic Stress Concentration, Wave Propagation, Finite Element

Journal of Mechanicl Science and Technology(KSME I. J.), Vol. 19, No. 1, pp. 72-86, 2005

A Tracking Algorithm for Autonomous Navigation of AGVs in an Automated Container Terminal

Yong-Shik Kim

Department of Mechanical and Intelligent Systems Engineering, Pusan National University,

San 30 Jangjeon-dong Gumjeong-gu, Busan 609-735, Korea.

Keum-Shik Hong*

School of Mechanical Engineering, Pusan National University,

San 30 Jangjeon-dong Gumjeong-gu, Busan 609-735, Korea

Abstract: In this paper, a tracking algorithm for the autonomous navigation of the automated guided vehicles (AGVs) operated in a container terminal is investigated. The navigation system is based on sensors that detect range and bearing. The navigation algorithm used is an interacting multiple model algorithm to detect other AGVs and avoid obstacles using information obtained from the multiple sensors. In order to detect other AGVs (or obstacles), two kinematic models are derived: A constant velocity model for linear motion and a constant-speed turn model for curvilinear motion. For the constant-speed turn model, an unscented Kalman filter is used because of the drawbacks of the extended Kalman filter in nonlinear systems. The suggested algorithm reduces the root mean squares error for linear motions and rapidly detects possible turning motions.

Keywords: Automated Guided Vehicle, Hybrid, Interacting Multiple Model, Nonlinear Filtering, Extended Kalman Filter, Unscented Filter, Navigation

Journal of Mechanicl Science and Technology(KSME I. J.), Vol. 19, No. 1, pp. 87-96, 2005

An Approach for Pattern Recognition of Hand Activities Based on EEG and Fuzzy Neural Network

Xiaodong Zhang

School of Mechanical Engineering, Xi’an Jiaotong University,

Xi’an, Shaanxi Province 710049, China

Taehun Kang, Hyoukryeol Choi*

School of Mechanical Engineering, SungKyunKwan University,

300 Chunchun-Dong, Jangan-Gu, Suwon 440-746, Korea

Electroencephalography (EEG) is another interesting bio-electrical signal to differ from EMG (Electromyography). In order to pursue its application in the control of the multi-fingered robot hand or the prosthetic hand, the pattern recognition technology of the human hand activities based on EEG should be investigated as a very important and elementary research objective at first. After discussing our research strategy about EEG applied in the control of the robot hand, the recognition model named as Fuzzy Neural Network (FNN) is set up in this paper, and then its related algorithms, such as the fundamental knowledge produced, the learning samples set, the features extracted, and the patterns recognized with the artificial neural network (ANN), are deeply discussed for achieving the classification of some basic mental tasks. In addition, the experimental research has also been done using a two-channel system of measuring EEG signal, and the result shows the new recognition model using FNN can extract not only the effective spectral features of the hand movements and the other usual accompanying mental tasks, such as blinking eyes, watching red color and listening music, so as to achieve the fundamental knowledge production and the feature extraction, but also has the good capability of the pattern recognition about the human hand activities through the fuzzy setting of the learning samples and the training of its ANN.

Key Words: Electroencephalography, Pattern recognition, Artificial Neural Network

Journal of Mechanicl Science and Technology(KSME I. J.), Vol. 19, No. 1, pp. 97-105, 2005

A Scheme for an Internet-based Checking Method of Machine-Tools with Variant CNC Architecture

Dong-Hoon Kim*

Department of Intelligence and Precision Machines, Korea Institute of Machinery and Materials, Daejeon, 305-343, Korea

Sun-Ho Kim

Mechatronics Engineering Major, College of Eng., Dong-Eui University, Busan, 614-714, Korea

Kwang-Sik Koh

School of Electrical Engineering and Computer Science, Kyungpook National University,

Daegu, 702-701, Korea

This paper proposes an Internet-based checking technique for machine-tools with variant Computerized Numerical Controller (CNC). According to its architecture, CNC is classified into one of two types: Closed Architecture Controller (CAC), which is the conventional CNC, or Open Architecture Controller (OAC), which is a recently introduced PC-based controller. Since CAC has a closed architecture, it is dependent on CNC vender specification. Because of this, it has been very difficult for users to implement application programs in the CNC domain. Recently, the conventional CNC of machine-tools has been replaced by a PC-based open architecture CNC. However, now many conventional CAC machines are being operated together with OAC machines in inadequately equipped shop floors. For Internet-based checking for variant CNC machines with CAC and OAC, a suitable systematic environment is necessary. Through this research, for the global management of variant CNC machines both a CAC and an OAC in the manufacturing system, a suitable environment for Internet-based checking of variant CNC machines was designed, and the checking methods for CAC and OAC machines were compared. The results of this research may serve as a base model for global monitoring and remote control in an integrated manufacturing system with variant CNC machines. Checking points defined in this research are classified into two categories:  structured point and operational point. The former includes the vibration of bearing, temperature of spindle unit, and  other points of periodical management, while the latter includes oil checking, clamp locking/unlocking, and machining on/off status.

Key Words: Internet-based checking method, variant CNC, CAC, OAC

Journal of Mechanicl Science and Technology(KSME I. J.), Vol. 19, No. 1, pp. 106-115, 2005

Nonlinear PID Control to Improve the Control Performance of the Pneumatic Artificial Muscle Manipulator Using Neural Network

Kyoung Kwan Ahn*

School of Mechanical and Automotive Engineering, University of Ulsan,

San 29, Muger 2dong, Nam-gu, Ulsan 680-749, Korea

TU Diep Cong Thanh

Graduate School of Mechanical and Automotive Engineering, University of Ulsan,

San 29, Muger 2dong, Nam-gu, Ulsan 680-749, Korea

A novel actuator system which has achieved increased popularity to provide these advantages such as high strength and power/weight ratio, low cost, compactness, ease of maintenance, cleanliness, readily available, cheap power source, inherent safety and mobility assistance to humans performing tasks has been the utilization of the pneumatic artificial muscle (PAM) manipulator, in recent times. However, the complex nonlinear dynamics of the PAM manipulator makes it a challenging and appealing system for modeling and control design. The problems with the time variance, compliance, high hysteresis and nonlinearity of pneumatic systems have made it difficult to realize precise position control with high speed. In order to realize satisfactory control performance, the effect of nonlinear factors contained in the PAM manipulator must be considered.

The purpose of this study is to improve the control performance of the PAM manipulator using a nonlinear PID controller. Superb mixture of conventional PID controller and the neural network, which has powerful capability of learning, adaptation and tackling nonlinearity, brings us a novel nonlinear PID controller using neural network. This proposed controller is appropriate for a kind of plants with nonlinearity uncertainties and disturbances. The experiments were carried out in practical PAM manipulator and the effectiveness of the proposed control algorithm was demonstrated through the experiments, which suggests its superior performance and disturbance rejection.

Key Words: pneumatic artificial muscle, neural network, nonlinear PID control

Journal of Mechanicl Science and Technology(KSME I. J.), Vol. 19, No. 1, pp. 116-126, 2005

Optimization of a Driver-Side Airbag Using Kriging Based Approximation Model

Kwon-Hee Lee*

Department of Mechanical Engineering, Dong-A University,

840 Hadan2-Dong, Saha-Gu, Busan 604-714, Korea

The performance of an occupant protection system in the proto-design stage of a new car is often evaluated by CAE (Computer Aided Engineering) instead of the real test.  CAE predicts and recommends the appropriate design values; hence reducing a number of the real tests.  In this research, the optimization procedure of a protection system, such as airbag and load limiter, is suggested for frontal collisions. The DACE modeling, known as one of the kriging interpolations, is introduced to obtain the surrogate approximation model of the system, followed by the tabu search method to determine the global optimum. A mathematical problem is solved to check the usefulness of the suggested method.  To overcome the limitation of existing CAE method having uncertainties of parameters, a distribution of combined injury probability is investigated using the Monte-Carlo simulation on the optimum design obtained from the suggested method.

Key Words : Optimization, Airbag, DACE(design and analysis of computer experiments), Kriging, Tabu Search, Global Optimum, Monte-Carlo Simulation

Journal of Mechanicl Science and Technology(KSME I. J.), Vol. 19, No. 1, pp. 127-135, 2005

Modeling of a Hybrid Passive Damping System

Chul Hue Park*, Sang Jun Ahn, Hyun Chul Park

Department of Mechanical Engineering, Pohang University of Science and Technology (POSTECH),

Pohang, KyungBuk, 790-784, Korea

Sungsoo Na

Department of Mechanical Engineering, Korea University,

1, 5-ga, Anam-dong, Sungbuk-gu, 136-701, Korea

The modeling of a hybrid passive damping system is presented for suppressing the multiple vibration modes of beams in this paper.  This hybrid passive damping system consists of a constrained layer damping and a resonant shunt circuit.  In a passive mechanical constrained layer damping, a viscoelastic layer, which is sandwiched between a host structure and a cover layer, is used to suppress vibration amplitudes in the high frequency range. A passive electrical damping is designed for targeting the vibration amplitude in the low frequency range.  The governing equations of motion of the hybrid passive damping system are derived through the Hamilton's principle. The obtained mathematical model is validated experimentally. The theoretical and experimental techniques presented provide an invaluable tool in controlling the multiple vibration modes across a wide frequency band.

Key word: Vibration Control, Shunt Circuit, Viscoelastic Material, Passive Damping

Journal of Mechanicl Science and Technology(KSME I. J.), Vol. 19, No. 1, pp. 136-143, 2005

Precision Measurements of Reaction Wheel Disturbances with Frequency Compensation Process

Hwa-Suk Oh*, Dong-Ik Cheon

Hankuk Aviation University, Hwajun, Goyang, 412-791, Korea

The reaction wheel, an actuator for satellite attitude control, produces disturbance torque and force as well as axial control torque. The disturbances are so crucial to the pointing stability of this high precision satellite that a measurement of disturbances is necessary for such a satellite. The measurement table that is equipped with several load cells is one of the favorite types of measurement devices. The disturbance force and torque caused by the wheel’s rotation, however, stimulate the elasticity of the loadcells from the measurement table and induce the vibration of the table. This then causes the measurement error, which is especially large near the resonance frequencies of the table. In order to reduce this type of error, a calibration process with frequency compensation is suggested in this paper. The “filtered” disturbance spectrum is obtained from the raw data and the degradation of data accuracy caused by the table vibration is alleviated. Since the exact measurement is made possible by this compensation process even in the resonance area, the measurement range can be expanded up to the frequency area including the resonance frequencies. The compensation method has been adopted for the HAU measurement table where three uni-directional loadcells are used. The validity of the use of uni-directional loadcells is also tested theoretically.

Key word: Reaction Wheel, Torgue Disturbance, Frequency Compensation, Measurement Table

Journal of Mechanicl Science and Technology(KSME I. J.), Vol. 19, No. 1, pp. 144-155, 2005

Determination of Fabrication Direction to Minimize Post-machining in FDM by Prediction of Non-linear Roughness Characteristics

Dae Keon Ahn

Department of Mechanical and Intelligent Systems Engineering, Pusan National University,

Busan 609-735, Korea

Ho Chan Kim

School of Mechanical Engineering, Youngnam University, Kyung-San, Kyung-Puk 712-749, Korea

Seok Hee Lee*

School of Mechanical Engineering, Pusan National University, Busan 609-735, Korea

Rapid Prototyping (RP) is a technology that generates physical objects directly from CAD data. As a prototype can be rapidly built by using this technology, the product cycle is remarkably reduced in manufacturing. However, the surface quality of RP processed parts is not sufficient for general mechanical parts because of the use of the layered manufacturing process. Therefore, additional post-machining processes are required such as grinding and coating. But, these processes are time-consuming and detrimental to the original part’s geometry. In this paper, a methodology for determining fabrication direction which aims to minimize the post-machining process in FDM (Fused Deposition Modeling) is proposed. In order to enhance the accuracy and the computational speed in determining the fabrication direction, a surface roughness model that is considered even non-linear surface roughness characteristics is presented. And, a required post-machining volume is newly introduced as a objective function. Also, a genetic algorithm is applied to obtain a reliable solution. Finally, it is verified that the proposed approach can be very efficient with the developed system.

Key Words : Fused Deposition Modeling, Fabrication Direction, Post-Machining, Surface Roughness

Journal of Mechanicl Science and Technology(KSME I. J.), Vol. 19, No. 1, pp. 156-163, 2005

Effect on Boiling Heat Transfer of Horizontal Smooth Microchannel for R-410A and R-407C

Kwang-Il Choi, A.S. Pamitran

Graduate School, Yosu National University, San 96-1, Dunduck-Dong, Yeosu, Chonnam 550-749, Korea

Jong-Taek Oh*

Department of Refrigeration Eng., Yosu National University,

San 96-1, Dunduck-Dong, Yeosu, Chonnam 550-749, Korea

Hoo-Kyu Oh

Department of Refrigeration and AC Engineering, Pukyong National University, Busan 608-739, Korea

An experimental study of boiling heat transfer with refrigerants R-410A and R-407C is presented. The present paper is focused on pressure drop and boiling heat transfer coefficient of the refrigerants inside a horizontal smooth microchannel. To evaluate the diameter size effect on pressure and heat transfer characteristics, microchannels with inner diameters of 1.5mm and 3.0mm and with lengths of 1500mm and 3000mm respectively are used. The pressure drop increases with mass flux and heat flux for both inner tube diameters and for both the refrigerants. The pressure drop of R-407C is higher than that of R-410A, but the heat transfer coefficient of R-410A is higher than of R-407C at the low quality region. The heat transfer coefficient in the tube with an inner diameter of 1.5mm is higher than that of 3.0mm diameter tube at the low quality region. The comparison of present heat transfer coefficient with the predictions of some previous correlations shows a large deviation. Therefore, there is a necessity to develop a new correlation.

Key Words: R-410A, R-407C, pressure drop, heat transfer coefficient, microchannel

Journal of Mechanicl Science and Technology(KSME I. J.), Vol. 19, No. 1, pp. 164-172, 2005

Water Cooling Characteristics in an Enclosed Vacuum Tank by Water Driven Ejector

Hyo Min Jeong, Han Shik Chung*

School of Mechanical & Aerospace Engineering, Institute of Marine Industry,

Gyeongsang National University, Gyeongnam 650-160, Korea

Kang Youl Bae

Boo Kang Plant Co., Ltd., 6 Floor, Hwoiwon Credit Union B/D,

670-6, Hwoiwon-Dong, Masan, Gyeongnam, Korea

Se Hyun Kim, You Sik Shin

Graduate School, Department of Mechanical and Precision Engineering,

Gyeongsang National University, Gyeongnam 650-160, Korea

The general cooling tower is a device for cooling water in industrial condensers or heat exchangers. The present cooling towers have defects with noises, complicated structures and environmental problems.  This paper focuses on a new water cooling system using the latent heat of evaporation in an enclosed vacuum tank and a water driven ejector system. Several experiments were carried out to improve high vacuum pressure and water cooling characteristics. The ejector performance was tested with various   water temperatures. Based on the vacuum pressure of the water driven ejector, the water cooling characteristics were investigated for the condensed and vaporized air and the effect of increased evaporating surface area in an enclosed tank.

Key Words: Cooling Tower, Water Driven Ejector, Vacuum Pressure, Latent Heat of Evaporation

Journal of Mechanicl Science and Technology(KSME I. J.), Vol. 19, No. 1, pp. 173-180, 2005

Fluid Mixing Analysis for Predicting Shell Wall Thinning of a Feedwater Heater

Kyung Hoon Kim*

Dept. of Mechanical Engineering, New Clear Power Plant Technology Research Center, KyungHee University, 1, Seocheon-Ri, Gihung-Eup, Yongin-Shi, Gyunggi-Do, Korea

Kyeong Mo Hwang

Korea Power Engineering Company, 360-9, Mabuk-Ri, Gusong-Eup, Yongin-Shi, Gyunggi-Do, Korea

Tae Eun Jin

Korea Power Engineering Company, 360-9, Mabuk-Ri, Gusong-Eup, Yongin-Shi, Gyunggi-Do, Korea

Feedwater flowing in the tube side of the number 5 high pressure feedwater heaters is heated by extraction steam from the high pressure turbine and drain water from the moisture separators and the number 6 high pressure feedwater heaters and supplied into the steam generators. Because the extraction steam from the high pressure turbine is a two phase fluid of high temperature, high pressure, and high speed and changes direction after colliding with the impingement baffle, the shell wall of the number 5 high pressure feedwater heaters may be subjected to flow-accelerated corrosion. Wall thinning damage caused by the flow-accelerated corrosion has primarily occurred in carbon and low alloy steel piping. Components, such as feedwater heaters, condensers, etc., however, have recently experienced severe wall thinning damage, which will increase as operating time progresses. This paper describes the fluid mixing analysis study using PHOENICS code in order to determine root cause of the shell wall thinning of the feedwater heaters. To identify the relation between the wall thinning and the fluid behavior, the local velocity components in the x-, y-, and z-direction were compared with the wall thickness data by ultrasonic test.

Key Words: Fluid Mixing Analysis, Wall Thinning, Flow-Accelerated Corrosion, Extraction Nozzle, Impingement Baffle

Journal of Mechanicl Science and Technology(KSME I. J.), Vol. 19, No. 1, pp. 181-188, 2005

Numerical Study on the Low Density Gas Flows in a Plasma Etch Reactor

Joong-Sik Heo

Researcher, Institute of Advanced Machinery and Technology, Sungkyunkwan University,

300 Chunchun-dong, Jangan-ku, Suwon 440-746, S. Korea

Young-Kyu Hwang*

Professor, School of Mechanical Engineering, Sungkyunkwan University,

300 Chunchun-dong, Jangan-ku, Suwon 440-746, S. Korea

The direct simulation Monte Carlo method is employed to predict the etch rate distribution on Al wafer for a chlorine feed gas flow. The etching process of an Al wafer in a plasma etch reactor is examined by simulating molecular collisions of reactant and product. The surface reaction on the Al wafer is simply modelled by one-step reaction: 3Cl2 + 2Al ( 2AlCl3. The gas flow inside the reactor is compared for six different nozzle locations. The present numerical results show that the etch rate increases with the mass flow rate of source gas Cl2. It is also shown that the flow field inside the reactor is significantly affected by the nozzle locations.

Key Words: Plasma Etching, Etch Rate, DSMC Method, Rarefied Gas Flow, Knudsen Number

Journal of Mechanicl Science and Technology(KSME I. J.), Vol. 19, No. 1, pp. 189-198, 2005

An Experimental Study of a Two-Phase Closed Loop

Thermosyphon with Dual Evaporator in Parallel Arrangement

Chul Ju Kim*

School of Mechanical Engineering, Sungkyunkwan University,

Chunchun-Dong 300, Jangan-Gu, Suwon 440-746, Korea

Byoung Ok Yoo, Yong Joo Park

Graduate School of Mechanical Engineering, Sungkyunkwan University,

Chunchun-dong 300, Jangan-Gu, Suwon 440-746, Korea

A Two-phase Closed Loop Thermosyphon (TCLT) has been applied to many industrial fields as a waste heat recovery system, a telecommunication cooling system and other heat transport devices for the last 2 decades. It is common to design a TCLT to consist of one evaporator, one condenser and 2 separated lines of condensate liquid and vapor of working fluid. The present study was conducted in search of the new possibility of connecting multiple evaporators in parallel to the evaporator section. There has been little information about this so far. It is expected that a TCLT with multi-evaporator would provide a new solution to designing a compact telecommunication cooling system where lots of heat generating circuit boards are connected in parallel arrangement. In the present study a TCLT with two evaporators was prepared and given to a series of operational performance tests. The study was focused on investigating its operational problems and collecting information about its performances.

Some important findings are as follows.

The main source of operational instability was an occurrence of a hot dried patch on the heated surface when the rate of heat input was raised to a certain limit. For a single evaporator mode of the present TCLT model, the maximum allowable heat transport rate was about 650 W. For dual evaporator mode of operation, this instability problem was found to be closely related not only to the quantity of heat flux but also the difference in heat input rate to each evaporator. For all those problems, it was found that a TCLT with multi-evaporator could operate in a proper way when the thermal loads were evenly distributed to all the evaporator or the maximum power gap were contained under about ±5 ~ 7% of the average power input.

Key words : Two-phase Closed Loop Thermosyphon (TCLT), Dual Evaporator, Heat Transfer Coefficient, Fill Charge Ratio

Journal of Mechanicl Science and Technology(KSME I. J.), Vol. 19, No. 1, pp. 189-198, 2005

An Experimental Study of a Two-Phase Closed Loop Thermosyphon with Dual Evaporator in Parallel Arrangement

Chul Ju Kim*

School of Mechanical Engineering, Sungkyunkwan University,

Chunchun-Dong 300, Jangan-Gu, Suwon 440-746, Korea

Byoung Ok Yoo, Yong Joo Park

Graduate School of Mechanical Engineering, Sungkyunkwan University,

Chunchun-dong 300, Jangan-Gu, Suwon 440-746, Korea

A Two-phase Closed Loop Thermosyphon (TCLT) has been applied to many industrial fields as a waste heat recovery system, a telecommunication cooling system and other heat transport devices for the last 2 decades. It is common to design a TCLT to consist of one evaporator, one condenser and 2 separated lines of condensate liquid and vapor of working fluid. The present study was conducted in search of the new possibility of connecting multiple evaporators in parallel to the evaporator section. There has been little information about this so far. It is expected that a TCLT with multi-evaporator would provide a new solution to designing a compact telecommunication cooling system where lots of heat generating circuit boards are connected in parallel arrangement. In the present study a TCLT with two evaporators was prepared and given to a series of operational performance tests. The study was focused on investigating its operational problems and collecting information about its performances. Some important findings are as follows. The main source of operational instability was an occurrence of a hot dried patch on the heated surface when the rate of heat input was raised to a certain limit. For a single evaporator mode of the present TCLT model, the maximum allowable heat transport rate was about 650 W. For dual evaporator mode of operation, this instability problem was found to be closely related not only to the quantity of heat flux but also the difference in heat input rate to each evaporator. For all those problems, it was found that a TCLT with multi-evaporator could operate in a proper way when the thermal loads were evenly distributed to all the evaporator or the maximum power gap were contained under about ±5 ~ 7% of the average power input.

Key words : Two-phase Closed Loop Thermosyphon (TCLT), Dual Evaporator, Heat Transfer Coefficient, Fill Charge Ratio.

Journal of Mechanicl Science and Technology(KSME I. J.), Vol. 19, No. 1, pp. 199-208, 2005

Enhancement of Stirring in a Straight Channel

at Low Reynolds-Numbers with various Block-Arrangement

Hyeung Seok Heo, Yong Kweon Suh*

Department of Mechanical Engineering Dong-A University,

840 Hadan-dong, Saha-gu, Busan 604-714, Korea

In this study a newly designed microchannel as an efficient fluid-mixer is proposed. This design is comprised of a channel and a series of blocks periodically attached on the bottom surface of the channel. In this configuration, the stirring is greatly enhanced at a certain range of parametric values. To characterize the flow field and the stirring effect, both numerical and experimental methods were employed. To obtain the velocity field, three-dimensional numerical computation to the Navier Stokes equations was performed by using a commercial code, FLUENT 6.0. The fluid-flow solutions were then cast into studying the characteristics of stirring with the aid of Lyapunov exponent. In this study the Lyapunov exponents were computed manually because the commercial code does not provide the corresponding tool. In the experiment, flow visualization was performed by using pure glycerin in a tank and glycerin mixed with small amount of a fluorescent dye in the other tank. The numerical results show that the pattern of the particles’ trajectories in the microchannel heavily depends on the block arrangement. It was shown that the stirring is significantly enhanced by a larger block-height and reaches maximum when the height is 0.8 times the channel width. We also studied the effect of the block stagger angle. It was found that stirring performance is the best at the block stagger angle of 45°.

Key Words : MEMS, Micro Mixer, Lyapunov Exponent

Journal of Mechanicl Science and Technology(KSME I. J.), Vol. 19, No. 1, pp. 209-215, 2005

Simultaneous Measurement of Red Blood Cell Aggregation and Viscosity :

Light Transmission Slit Rheometry

Sehyun Shin*, Myung-Su Park, Yunhee Ku, Joo-Hee Jang

School of Mechanical Engineering, Kyungpook National University

1370 Sankyuk-dong Book-gu, Daegu, 702-701 Korea

Jang-Soo Suh

Department of Laboratory Medicine, Kyungpook National University,

Sanmduk-dong Joong-gu, Daegu, 700-721

Aggregation of red blood cells (RBCs) is a major determinant of blood viscosity. There have not been available techniques for measuring RBC aggregation and viscosity, simultaneously. A laser transmission technique has been combined with a slit rheometry, which shows significant advances in rheometer design, operation and data analysis. A laser beam traverses a blood suspension flowing through a slit and is scattered by RBCs in the volume. The transmitted light is captured by a photodiode, linked to a computer, while the differential pressure variation is measured by a pressure transducer. Both measurements of the laser-transmitted intensity and pressure with respect to time enable to determine the aggregation index and the viscosity. The advantages of this design are in its simplicity, i.e., ease of operation and no moving parts, low cost and a short operating time. In addition, the slit-flow aggregometer can be easily used in a clinical setting owing to the incorporation of a disposable element that holds the blood sample.

Keywords: aggregation, red blood cell, viscosity, light, transmission, critical shear rate

Journal of Mechanicl Science and Technology(KSME I. J.), Vol. 19, No. 1, pp. 216-223, 2005

Deformability of Red Blood Cells : A Determinant of Blood Viscosity

Sehyun Shin*, Yunhee Ku, Myung-Su Park

School of Mechanical Engineering, Kyungpook National University,

1370 Sankyuk-dong, Buk-gu, Daegu 702-701, Korea

Jang-Soo Suh

Department of Laboratory Medicine, Kyungpook National University Hospital,

Daegu 700-721, Korea

The suspension of hardened red blood cells (RBCs) differs from the suspension of normal RBCs with respect to their rheological behavior. The present study investigated the effect of deformability of RBCs on blood viscosity. RBC deformability and blood viscosity were measured with a recently developed slit-flow laser-diffractometer and the pressure-scanning capillary viscometer, respectively. At the same level of cell concentration, the viscosity of the hardened RBC suspension is higher than that of the normal RBCs suspension. An increase in cell percentage for hardened RBCs shows the significant increase in the level of blood viscosity compared to the normal RBCs. In addition, it was found that RBC deformability played an important role in reducing viscosity at low shear rates as well as high shear rates. These results present the evidence for the effect of RBC deformability on blood viscosity using newly developed methods, which can be used in early diagnosis of the cardiovascular diseases.

Keywords: RBC, Deformability; Viscosity, Blood, Diagnosis

Journal of Mechanicl Science and Technology(KSME I. J.), <Special Edition> Vol. 19, No. 1, pp. 227-236, 2005

Recent Developments in Multibody Dynamics

Werner Schiehlen*

Institute B of Mechanics, University of Stuttgart,

70550 Stuttgart, GERMANY

Multibody system dynamics is based on classical mechanics and its engineering applications originating from mechanisms, gyroscopes, satellites and robots to biomechanics. Multibody system dynamics is characterized by algorithms or formalisms, respectively, ready for computer implementation. As a result simulation and animation are most convenient. Recent developments in multibody dynamics are identified as elastic or flexible systems, respectively, contact and impact problems, and actively controlled systems. Based on the history and recent activities in multibody dynamics, recursive algorithms are introduced and methods for dynamical analysis are presented. Linear and nonlinear engineering systems are analyzed by matrix methods, nonlinear dynamics approaches and simulation techniques.  Applications are shown from low frequency vehicles dynamics including comfort and safety requirements to high frequency structural vibrations generating noise and sound, and from controlled limit cycles of mechanisms to periodic nonlinear oscillations of biped walkers. The fields of application are steadily increasing, in particular as multibody dynamics is considered as the basis of mechatronics.

Key Words : History of Multibody Dynamics, Mechanical Modelling, Kinematics, Newton-Euler Equation, Equition of Motion, Recursive Formalisms, Linear Vinrations, Nonlinear Analysis, Vehicle Vibrations and Control, Structural Vibrations, Contact, Mechanicims, Biped Walker

Journal of Mechanicl Science and Technology(KSME I. J.), <Special Edition> Vol. 19, No. 1, pp. 237-254, 2005

Multibody Dynamics of Closed, Open, and Switching Loop Mechanical Systems

Youngil Youm*

Department of Mechanical Engineering,

Pohang University of Science & Technology, Pohang 790-784, Korea

The vast mechanical systems could be classified as closed loop system, open loop system and open & closed(switching) system. In the closed loop system, the kinematics and dynamics of 3-D mechanisms will be reviewed and closed form solutions using the direction cosine matrix method and reflection transformation method by Youm will be introduced. In the open loop system, kinematic & dynamic analysis methods regarding to redundant system which has more degrees of freedom in joint space than that of task space are reviewed and discussed. Finally, switching system which changes its phase between closed and open loop motion is investigated with the principle of dynamical balance. Among switching systems, human gait in biomechanics and humanoid in robotics are presented.

Key Words : Closed Loop System, Open Loop System, Multibody Dynamics

Journal of Mechanicl Science and Technology(KSME I. J.), <Special Edition> Vol. 19, No. 1, pp. 255-264, 2005

Vehicle Dynamic Simulation Including an Artificial Neural Network Bushing Model

Jeong Hyun Sohn*

Department of Mechanical Engineering,

Pukyong National University, Busan 608-739, Korea

Woon Kyung Baek

Department of Mechanical Engineering,

Pukyong National University, Busan 608-739, Korea

In this paper, a practical bushing model is proposed to improve the accuracy of the vehicle dynamic analysis.  The results of the rubber bushing are used to develop an empirical bushing model with an artificial neural network. A back propagation algorithm is used to obtain the weighting factor of the neural network. Since the output for a dynamic system depends on the histories of inputs and outputs, Narendra algorithm of 'NARMAX' form is employed to consider these effects. A numerical example is carried out to verify the developed bushing model. Then, a full car dynamic model with artificial neural network bushings is simulated to show the feasibility of the proposed bushing model.

Key Words : Vehical Dynamics, Bushing, Neural Network, Simulation

Journal of Mechanicl Science and Technology(KSME I. J.), <Special Edition> Vol. 19, No. 1, pp. 265-271, 2005

Study on the Dynamic Model and Simulation of a Flexible

Mechanical Arm Considering its Random Parameters

Bai-Yan He

China Automotive Technology and Research Center, Tianjin, 300162, China

Shu-Xin Wang*

School of Mechanical Engineering, Tianjin University, Tianjin, 300072, China

Randomness exists in engineering. Tolerance, assemble-error, environment temperature and wear make the parameters of a mechanical system uncertain. So the behavior or response of the mechanical system is uncertain. In this paper, the uncertain parameters are treated as random variables. So if the probability distribution of a random parameter is known, the simulation of mechanical multibody dynamics can be made by Monte Carlo method. Thus multibody dynamics simulation results can be obtained in statistics. A new concept called functional reliability is put forward in this paper, which can be defined as the probability of the dynamic parameters (such as position, orientation, velocity, acceleration etc.) of the key parts of a mechanical multibody system belong to their tolerance values. A flexible mechanical arm with random parameters is studied in this paper. The length, width, thickness and density of the flexible arm are treated as random variables and Gaussian distribution is used with given mean and variance. Computer code is developed based on the dynamic model and Monte Carlo method to simulate the dynamic behavior of the flexible arm. At the same time the end effector’s locating reliability is calculated with circular tolerance area. The theory and method presented in this paper are applicable on the dynamics modeling of general multibody systems.

Key Words : Multibody System, Flexible Body, Dynamics, Rondom Parameters, Monte-Carlo Method, Reliability, Flexible Mechanical Arm, Kane`s Equation, Simulition, Matlab

Journal of Mechanicl Science and Technology(KSME I. J.), <Special Edition> Vol. 19, No. 1, pp. 272-282, 2005

Development of a Washout Algorithm for a Vehicle Driving Simulator

Using New Tilt Coordination and Return Mode

Ki Sung You

Research Institute of Industrial Science & Technology,

San, 32, Hyoja-Dong, Nam-Ku, Pohang City, 790-330, Korea

Min Cheol Lee*

School of Mechanical Engineering, Pusan National University

San, 30, Jangjeon-dong, Kumjeong-gu, Busan 609-735, Korea

Eugene Kang

Advanced Engineering Center, Samsung SDI

575, Sin-dong, Paldal-gu, Suwon-si, Gyeonggi-do 442-731, Korea

Wan Suk Yoo

School of Mechanical Engineering, Pusan National University

San, 30, Jangjeon-dong, Kumjeong-gu, Busan 609-735, Korea

A vehicle driving simulator is a virtual reality device which makes a man feel as if he drove an actual vehicle. Unlike actual vehicles, the simulator has limited kinematical workspace and bounded dynamic characteristics. So it is difficult to simulate dynamic motions of a multi-body vehicle model. In order to overcome these problems, a washout algorithm which controls the workspace of the simulator within the kinematical limitation is needed. However, a classical washout algorithm contains several problems such as generation of wrong sensation of motions by filters in tilt coordination, requirement of trial and error method in selecting the proper cut-off frequencies and difficulty in returning the simulator to its origin using only high pass filters. This paper proposes as a washout algorithm with new tilt coordination method which gives more accurate sensations to drivers. To reduce the time in returning the simulator to its origin, an algorithm that applies selectively onset mode from high pass filters and return mode from error functions is proposed. As a result of this study, the results of the proposed algorithm are compared with the results of classical washout algorithm through the human perception models. Also, the performance of the suggested algorithm is evaluated by using human perception and sensibility of some drivers through experiments.

Key Words: Vehicle Driving Simulator, Washout Algorithm, New Tilt Coordination, Return Mode

Journal of Mechanicl Science and Technology(KSME I. J.), <Special Edition> Vol. 19, No. 1, pp. 283-291, 2005

Study on the Frame Structure Modeling of the Beam Element Formulated by Absolute Nodal Coordinate Approach

Yoshitaka Takahashi*

Department of Mechanical Engineering, Iwaki Meisei University,

Iwaki, Fukushima,970-8551, Japan

Nobuyuki Shimizu

Department of Mechanical Engineering, Iwaki Meisei University,

Iwaki, Fukushima,970-8551, Japan

Kohei Suzuki

Department of Mechanical Engineering, Tokyo Metropolitan University,

Hachioji, Tokyo, 192-0397, Japan

Accurate seismic analyses of large deformable moving structures are still unsolved problems in the .eld of earthquake engineering. In order to analyze these problems, the nonlinear finite element method formulated by the absolute nodal coordinate approach is noticed. Because, this formulation has several advantages over the standard procedures on mass matrix, elastic forces and damping forces in the case of large displacement problems. But, it has not been fully studied to build frame structure models by using beam elements in the absolute nodal coordinate formulation. In this paper, we propose the connecting method of the beam elements formulated by the absolute nodal coordinate. The coordinate transformation matrix of this element is introduced into the frame structure. This beam element has the characteristic that the mass matrix and bending sti.ness matrix are constant even if in the case of large displacement problems, and this characteristic is being kept after the transformation. In order to verify the proposed method, we show the numerical simulation results of frame structures for a vibration problem and a large displacement problem.

Keywords: Finite Element Method, Beam, Absolute Nodal Coordinate Approach, Frame Structure, Seismic Analysis

Journal of Mechanicl Science and Technology(KSME I. J.), <Special Edition> Vol. 19, No. 1, pp. 292-304, 2005

Benchmark Results on the Linearized Equations of Motion of an Uncontrolled Bicycle

- L. Schwab*

Laboratory for Engineering Mechanics, Delft University of Technology,

Mekelweg 2, NL-2628 CD Delft, The Netherlands

J. P. Meijaard

School of MMME, The University of Nottingham, University Park,

Nottingham NG7 2RD, United Kingdom

J. M. Papadopoulos

The Paper Converting Machine Company, Green Bay, Wisconsin, USA

In this paper we present the linearized equations of motion for a bicycle as a benchmark. The results obtained by pencil-and-paper and two programs are compared. The bicycle model we consider here con-sists of four rigid bodies, viz. a rear frame, a front frame being the front fork and handlebar assembly, a rear wheel and a front wheel, which are connected by revolute joints. The contact between the knife-edge

wheels and the flat level surface is modelled by holonomic constraints in the normal direction and by non-holonomic constraints in the lon-gitudinal and lateral direction. The rider is rigidly attached to the rear frame with hands free from the handlebar. This system has three degrees of freedom, the roll, the steer, and the forward speed. For the benchmark we consider the linearized equations for small perturba-tions of the upright steady forward motion. The entries of the matrices of these equations form the basis for comparison. Three diffrent kinds of methods to obtain the results are compared: pencil-and-paper, the numeric multibody dynamics program SPACAR, and the symbolic software system AutoSim. Because the results of the three methods are the same within the machine round-o?error, we assume that the results are correct and can be used as a bicycle dynamics benchmark.

Key Words: Vehicle Dynamics, Non-Holonomic Constraints, Dynamic Stability

Journal of Mechanicl Science and Technology(KSME I. J.), <Special Edition> Vol. 19, No. 1, pp. 305-311, 2005

Simulation and Experimental Methods for Media Transport System: Part I, Three-Dimensional Sheet Modeling Using Relative Coordinate

Heui Je Cho*, Dea Sung Bae

Department of Mechanical Engineering, Hanyang University,

Sadong, Sangrokku, Ansan 425-791, Korea

Jin Hwan Choi, Soon Geul Lee, Sung Soo Rhim

Department of Mechanical Engineering, Kyunghee University,

Yongin, Kyungki 449-791, Korea

This research presents a three-dimensional modeling technique for a flexible sheet. A relative coordinate formulation is used to represent the kinematics of the sheet. The three-dimensional flexible sheet is modeled by multi-rigid bodies interconnected by out-of-plane joints and plate force elements. A parent node is designated as a master body and is connected to the ground by a floating joint to cover the rigid motion of the flexible sheet in space. Since the in-plane deformation of a sheet such as a paper and a film is relatively small, compared to out-of-plane deformation, only the out-of-plane deformation is accounted for in this research. The recursive formulation has been adopted to solve the equations of motion efficiently. An example is presented to show the validity of the proposed method.

Key Words: Media Transport System, Three-Dimensional Flexible Sheet Model, Floating Joint, Out-Of-Plane Joint, Plate Force, Nodal Body, Parent Node, Child Node, Relative Coordinate, Recursive Formula

Journal of Mechanicl Science and Technology(KSME I. J.), <Special Edition> Vol. 19, No. 1, pp. 312-319, 2005

Subsystem Synthesis Methods with Independent Coordinates

for Real-Time Multibody Dynamics

Sung-Soo Kim*

Department of Mechatronics Engineering, Chungnam National University,

220 Kung-dong, Yusong-ku, Daejeon 305-764, Korea

Ji-Hyeun Wang

Agency for Defense Development,

Yusong P. O. Box 35-1, Daejeon 305-600, Korea

For real time dynamic simulation, two different subsystem synthesis methods with independent generalized coordinates have been developed and compared.  In each formulation, the subsystem equations of motion are generated in terms of independent generalized coordinates.  The first formulation is based on the relative Cartesian coordinates with respect to moving subsystem base body.  The second formulation is based on the relative joint coordinates using recursive formulation.  Computational efficiency of the formulations has been compared theoretically by the arithmetic operational counts.  In order to verify real-time capability of the formulations, bump run simulations of a quarter car model with SLA suspension subsystem have been carried out to measure the actual CPU time.

Key Words : Realtime Dynamic Simulation, Subsystem Synthesis Method

Journal of Mechanicl Science and Technology(KSME I. J.), <Special Edition> Vol. 19, No. 1, pp. 320-327, 2005

Hyper Redundant Manipulator Using Compound Three-Bar Linkages

Koichi Koganezawa*

Department of Mechanical Engineering, TOKAI University

1117 Kitakaname, Hiratsuka, Kanagawa 259-1292, Japan

A new mechanism for hyper redundant manipulator (HRM) is presented, which comprises of serially assembled compound three-bar linkages (CTL). The CTL mechanism has some unique properties. This paper presents the forward and inverse kinematics of this mechanism and shows the simulation of the HRM havig 9 CTL units. The recursive algorithm of the inverse kinematics that the author originally developed is employed. It is fast and stable; moreover, it enables us to obtain a solution in which the end-point of the HRM is controlled by a portion of joints. It also presents the method of the dynamical analysis. There exist kinematical constraints in the proposed closed linkage mechanism. In the dynamic analysis  constraints are sufficiently sustained by the constraint stabilization method that the author developed. The mechanical structure of the HRM having some CTL units that is under construction is shown.

Key Words : Hyper-Redundant Manipulator, Inverse Kinematics, Constraint Stabilization

Journal of Mechanicl Science and Technology(KSME I. J.), <Special Edition> Vol. 19, No. 1, pp. 328-335, 2005

Dynamics of Track／Wheel Systems on High－Speed Vehicles

Isamu Kato

Department of Mechanical Engineering, Sophia University,

7-1 Kioi-cho, Chiyoda-ku, Tokyo 102-8554, Japan

Yoshiaki Terumichi*

Department of Mechanical Engineering, Sophia University,

7-1 Kioi-cho, Chiyoda-ku, Tokyo 102-8554, Japan

Masahito Adachi

Technology Research and Development Departmen, Central Japan Railway Company,

1545-33, Oyama, Komaki-shi, Aichi 485-0801, Japan

Kiyoshi Sogabe

Department of Mechanical Engineering, Sophia University,

7-1 Kioi-cho, Chiyoda-ku, Tokyo 102-8554, Japan

For high speed railway vehicles, we consider a vibration of flexible track/wheel system. It is very important to deal with the complex phenomena of high-speed vehicles that can be occurred in the vertical vibration of the system. From a viewpoint of multibody dynamics, this kind of problem needs accurate analysis because the system includes mutual dynamic behaviors of rigid body and flexible body. The simulation technique for the complex problems is also discussed. We consider the high-speed translation, rail elasticity, elastic supports under the rail and contact rigidity. Eigen value analysis is also completed to verify the mechanism of the coupled vertical vibration of the system.

Key Words : Contact, Flexible Multibody Dynamics, Absolute Nodal Coordinate Formulation, Railroad System

Journal of Mechanicl Science and Technology(KSME I. J.), <Special Edition> Vol. 19, No. 1, pp. 336-342, 2005

The Noise Reduction of a DC Motor Using Multi-body Dynamics

Il-Ho Jung, Jong-Hwi Seo

Graduate School of Mechanical Engineering, Ajou University,

Wonchun-dong, Youngtong-gu, Suwon-city, 442-749, Korea

Sung-Jin Choi

Korea Automotive Technology Institute,

74 Yongjeong-ri, Pungse-myeon, Cheonan-city, Chungcheongnam-do 330-912, Korea

Tae-Won Park*, Jang-Bom Chai

Division of Mechanical Engineering, Ajou University,

Wonchun-dong, YoungTong-gu, Suwon-city, 442-749, Korea

The DC motor of a vehicle may cause noise and vibration due to high-speed revolution, which can make a driver feel uncomfortable. There have been various studies attempting to solve these problems, mostly focusing on the causes of noise and vibration and a means of preventing them. The CAE methodology is more efficient than a real test for the purpose of looking for various design parameters to reduce the noise and vibration of the DC motor. In this study, a design process for reducing brush noise is presented with the use of a computer model, which is made by using a multi-body dynamics program (DADS). The design parameters to reduce the brush noise and vibration were proposed using a computer model. They were used to reduce the noise and vibration of the DC motor and verified by the test results of the fan DC motor in the vehicle. This method may be applicable to various DC motors.

Key Words : DC Motor, Hertz Contact, Brush Noise, Multi-body Dynamics, Durability Test

Journal of Mechanicl Science and Technology(KSME I. J.), <Special Edition> Vol. 19, No. 1, pp. 343-349, 2005

Multibody Dynamics in Aaterial System

Sang-Hoon Shin, Young-Bae Park

School of Oriental Medicine, Kyunghee University, Seoul, 130-701, Korea

Hye-Whon Rhim

Biomedical Research Center, KIST, Hawolgok-dong, Seongbuk-gu, Seoul, 136-791, Korea

Wan-Suk Yoo

Department of Mechanical Engineering, Pusan National University, Busan, 609-735, Korea

Young-Jae Park

College of Oriental Medicine, Saemyung University, Jecheon, Chungbuk, 390-711, Korea

Dae-Hun Park*

Cancer Experimental Resources Branch, National Cancel Center, Goyang, Gyeonggi, 411-769, Korea

There are many things in common between hemodynamics in arterial systems and multibody dynamics in mechanical systems. Hemodynamics is concerned with the forces generated by the heart and the resulting motion of blood through the multi-branched vascular system. The conventional hemodynamics model has been intended to show the general behavior of the body arterial system with the frequency domain based linear model. The need for detailed models to analyze the local part like coronary arterial tree and cerebral arterial tree has been required recently. Non-linear analysis techniques are well-developed in multibody dynamics. In this paper, the studies of hemodynamics are summarized from the view of multibody dynamics. Computational algorithms of arterial tree analysis is derived, and proved by experiments on animals. The flow and pressure of each branch are calculated from the measured flow data at the ascending aorta. The simulated results of the carotid artery and the iliac artery show in good accordance with the measured results.

Key Words : Multibody Dynamics, Hemodynamics Arterial Tree System, Pulsatile Blood Flow, Vascular Impedance, Input Impedance, Arterial System Model, Forward & Backward Calculation

Journal of Mechanicl Science and Technology(KSME I. J.), <Special Edition> Vol. 19, No. 1, pp. 350-356, 2005

Dynamic Analysis of Multi-body Systems Considering Probabilistic Properties

Dong Hwan Choi

School of Mechanical Engineering, Hanyang University,

Haengdang-dong, Seongdong-gu, Seoul 133-791, Korea

Se Jeong Lee

Department of Mechanical and Information Engineering, University of Seoul,

Siripdae-gil 13, Dongdaemun-gu, Seoul 130-743, Korea

Hong Hee Yoo*

School of Mechanical Engineering, Hanyang University,

Haengdang-dong, Seongdong-gu, Seoul 133-791, Korea

A method of dynamic analysis of mechanical systems considering probabilistic properties is proposed in this paper. Probabilistic properties that result from manufacturing tolerances can be represented by means and standard deviations (or variances). The probabilistic characteristics of dynamic responses of constrained multi-body systems are obtained by two ways: the proposed analytical approach and the Monte Carlo simulation. The former necessitates sensitivity information to calculate the standard deviations. In this paper, a direct differentiation method is employed to find the sensitivities of constrained multi-body systems. To verify the accuracy of the proposed method, numerical examples are solved and the results obtained by using the proposed method are compared to those obtained by Monte Carlo simulation.

Key Words : Manufacturing Tolerance, Multibody system, Probabilistic Property, Monte Carlo Method, Direct Differentiation Method (DDM)

Journal of Mechanicl Science and Technology(KSME I. J.), <Special Edition> Vol. 19, No. 1, pp. 357-363, 2005

Model-based Reference Trajectory Generation for Tip-based Learning Controller

Sungsoo Rhim, Soon-Geul Lee*

School of Mechanical and Industrial Systems Engineering, Kyung Hee University,

Yongin, 449-701, Korea

Tae Gyoon Lim

Research Institute of Industrial Science and Technology, Pohang 790-600, Korea

The non-minimum phase characteristic of a flexible manipulator makes tracking control of its tip difficult. The level of the tip tracking performance of a flexible manipulator is significantly affected by the characteristics of the tip reference trajectory as well as the characteristics of the flexible manipulator system. This paper addresses the question of how to best specify a reference trajectory for the tip of a flexible manipulator to follow in order to achieve the objectives of reducing: tip tracking error, residual tip vibration, and the required actuation effort at the manipulator joint. A novel method of tip-based learning controller for the flexible manipulator system is proposed in the paper, where a model of the flexible manipulator system with a command shaping filter is used to generate a smooth and realizable tip reference trajectory for a tip-based learning controller.

Keywords: Command Shaping, Tip Control, Flexible Link, Learning Control

Journal of Mechanicl Science and Technology(KSME I. J.), <Special Edition> Vol. 19, No. 1, pp. 364-370, 2005

Walking Pattern Generation employing DAE Integration Method

Yun-Seok Kang*

Department of Automotive Engineering, Kookmin University,

Seoul 136-702, Korea

Jung-Hun Park

Noise & Vibration Team, Center for Product Design Technology,

Institute for Advanced Engineering, Gyeonggi-do 449-863, Korea

Hong-Jae Yim

Department of Automotive Engineering, Kookmin University,

Seoul 136-702, Korea

A stable walking pattern generation method for a biped robot is presented in this paper. In general, the ZMP (zero moment point) equations, which are expressed as differential equations, are solved to obtain a stable walking pattern. However, the number of differential equations is less than that of unknown coordinates in the ZMP equations. It is impossible to integrate the ZMP equations directly since one or more constraint equations are involved in the ZMP equations. To overcome this difficulty, DAE (differential and algebraic equation) solution method is employed. The proposed method has enough flexibility for various kinematic structures. Walking simulation for a virtual biped robot is performed to demonstrate the effectiveness and validity of the proposed method. The method can be applied to the biped robot for stable walking pattern generation.

Key Words : Biped Robot, Stable Walking Pattern, ZMP(Zero Moment Point) Equation, DAE(Differential and Algebraic Equation)

Journal of Mechanicl Science and Technology(KSME I. J.), <Special Edition> Vol. 19, No. 1, pp. 371-376, 2005

Contributions of the Lower Extremity Joint on the Support Moment

in Normal Walking and in Unexpected Step-Down Walking

Young-Ho Kim

Department of Biomedical Engineering, Yonsei University,

Wonju 220-710, Korea

Han-Sung Kim, Sung-Jae Hwang, Seong-Sik Myeong, Young-Kwang Keum

Department of Biomedical Engineering, Yonsei University

Wonju 220-710, Korea

Relative contributions of lower extremity joints on the support moment were investigated in this study. Three-dimensional gait analyses were performed in normal walking and in unexpected step-down walking. For both gait studies, inverse dynamics were performed to obtain each joint moment of the lower extremity, which was applied to the forward dynamics simulation to determine the contributions on the support moment at different phases of walking. The forward dynamic simulation results showed that, in normal walking, the ankle plantar flexors contributed significantly during single-limb-support. However, the ankle plantar flexors, knee extensors and hip extensors worked together during double-limb-support. In unexpected step-down walking, the important contributors on the support of the body during single-limb-support were not only ankle plantar flexors but also knee extensors. This study, analyzing the relative contributions of the lower limb joint moments for the body support, would be helpful to understand different unexpected walking conditions and compensatory mechanisms for various pathological gaits.

Key Words : Gait Analysis, Gait Simulation, Support Moment, Normal Walking, Unexpected Step-Down Waling

Journal of Mechanicl Science and Technology(KSME I. J.), <Special Edition> Vol. 19, No. 1, pp. 377-387, 2005

Turning Dynamics and Equilibrium of Two-wheeled Vehicles

Chih-Keng Chen*, Thanh-Son Dao, Chih-Kai Yang

Department of Mechanical and Automation Engineering, Da-Yeh University, 112 Shan-Jiau Rd., Changhua, Taiwan 515 ROC

The equations of motion of two-wheeled vehicles, e.g. bicycles or motorcycles, are developed by using Lagrange’s equations for quasi-coordinates. The pure rolling constraints between the ground and the two wheels are considered in the dynamical equations of the system. For each wheel, two nonholonomic and two holonomic constraints are introduced in a set of differential-algebraic equations (DAE). The constraint Jacobian matrix is obtained by collecting all the constraint equations and converting them into the velocity form. Equilibrium, an algorithm for searching for equilibrium points of two-wheeled vehicles and the associated problems are discussed. Formulae for calculating the radii of curvatures of ground-wheel contact paths and the reference point are also given.

Key Words : Bicycle Dynamics, Two-wheeled Vehicle, Nonholonomic Constraint, Multibody

Journal of Mechanicl Science and Technology(KSME I. J.), <Special Edition> Vol. 19, No. 1, pp. 388-394, 2005

IRK vs Structural Integrators for Real-Time Applications in MBS

D. Dopico, U. Lugris, M. Gonzalez, J. Cuadrado*

Laboratory of Mechanical Engineering, University of La Coruna, Ferrol 15403, Spain

Recently, the authors have developed a method for real-time dynamics of multibody systems, which combines a semi-recursive formulation to derive the equations of motion in dependent relative coordinates, along with an augmented Lagrangian technique to impose the loop closure conditions. The following numerical integration procedures, which can be grouped into the so-called structural integrators, were tested: trapezoidal rule, Newmark dissipative schemes, HHT rule, and the Generalized-a family. It was shown that, for large multibody systems, Newmark dissipative was the best election since, provided that the adequate parameters were chosen, excellent behavior was achieved in terms of efficiency and robustness with acceptable levels of accuracy. In the present paper, the performance of the described method in combination with another group of integrators, the Implicit Runge-Kutta family (IRK), is analyzed. The purpose is to clarify which kind of IRK algorithms can be more suitable for real-time applications, and to see whether they can be competitive with the already tested structural family of integrators. The final objective of the work is to provide some practical criteria for those interested in achieving real-time performance for large and complex multibody systems.

Key Words : Multibody Systems, Dynamics, Real-Time Simulation, Numerical Integration, Structural Integrators, IRK

Journal of Mechanicl Science and Technology(KSME I. J.), <Special Edition> Vol. 19, No. 1, pp. 395-402, 2005

A Symbolic Computation Method for Automatic Generation of a Full Vehicle Model Simulation Code for a Driving Simulator

Ji-Young Lee*

S&TRI, InnoSimulation, Inc., Donggyo-dong, Mapo-gu, Seoul 121-819, Korea

Woon-Sung Lee

Graduate School of Automotive Engineering, Kookmin University, Seoul 136-702, Korea

This paper deals with modeling and computer simulation of a full multibody vehicle model for a driving simulator. The multibody vehicle model is based on the recursive formulation and a corresponding simulation code is generated automatically from AUTOCODE, which is a symbolic computation package developed by the authors using MAPLE. The paper describes a procedure for automatically generating a highly efficient simulation code for the full vehicle model, while incorporating realistically modeled components. The following issues have been accounted for in the procedure, including software design for representing a mechanical system in symbolic form as a set of computer data objects, a multibody formulation for systems with various types of connections between bodies, automatic manipulation of symbolic expressions in the multibody formulation, interface design for allowing users to describe unconventional force- and torque-producing components, and a method for accommodating external computer subroutines that may have already been developed. The effectiveness and efficiency of the proposed method have been demonstrated by the simulation code developed and implemented for driving simulation.

Key Words : Symbolic Computation, Multibody Vechicle Model, Driving Simulatior, Automatic Code Generation, Vehicle Dynamics, Real-Time Simulation

Journal of Mechanicl Science and Technology(KSME I. J.), <Special Edition> Vol. 19, No. 1, pp. 303-410, 2005

Simulation and Experimental Methods for Media Transport System: Part II, Effect of Normal Force on Slippage of Paper

Jae-Kwan Ryu, Soon-Geul Lee, Sung-Soo Rhim*, Jin-Hwan Choi

School of Mechanical and Industrial Systems Engineering, Kyung Hee University,

Yongin 449-791, Korea

In-Ho Song

FunctionBay, 601 6F, Seo-Won B/D, 1515-4, Seocho-Dong, Seocho-Gu, Seoul 131-871, Korea

Many daily appliances for examples copiers, printers and ATMs contain the media transport system (MTS) and the slippage between the medium in the MTS deteriorates the performance quality of the whole system. The slippage of the medium in the MTS is affected by many parameters including the friction coefficient between the feeding rollers and the medium, the velocity of the feeding rollers, and the normal force exerted on the medium by feeding rollers. This paper focuses on the effect of the normal force on the slippage while the medium is being fed. For this purpose, we developed a two-dimensional simulation model for a paper feeding system. Using the simulation model, we calculated the slippage of the paper for different normal forces. We have also constructed a testbed of the paper feeding system to verify the simulation results. Experimental results are compared with the simulation results.

Key Words : Media Transport System, Slippage, Normal Force, Friction Coefficients, Paper Modeling

Journal of Mechanicl Science and Technology(KSME I. J.), <Special Edition> Vol. 19, No. 1, pp. 411-421, 2005

A Computational Efficient General Wheel-Rail Contact Detection Method

Joao Pombo

IDMEC Instituto Superior Tecnico, Av. Rovisco Pais 1, 1049-001 Lisboa, PORTUGAL

Jorge Ambrosio*

IDMEC Instituto Superior Tecnico, Av. Rovisco Pais 1, 1049-001 Lisboa, PORTUGAL

The development and implementation of an appropriate methodology for the accurate geometric description of track models is proposed in the framework of multibody dynamics and it includes the representation of the track spatial geometry and its irregularities. The wheel and rail surfaces are parameterized to represent any wheel and rail profiles obtained from direct measurements or design requirements. A fully generic methodology to determine, online during the dynamic simulation, the coordinates of the contact points, even when the most general three dimensional motion of the wheelset with respect to the rails is proposed. This methodology is applied to study specific issues in railway dynamics such as the flange contact problem and lead and lag contact configurations. A formulation for the description of the normal contact forces, which result from the wheel-rail interaction, is also presented. The tangential creep forces and moments that develop in the wheel-rail contact area are evaluated using: Kalker linear theory; Heuristic force method; Polach formulation. The methodology is implemented in a general multibody code. The discussion is supported through the application of the methodology to the railway vehicle ML95, used by the Lisbon metro company.

Key Word : Railway Dynamics, Multibody Dynamics, Contact Mechanics, Rail-Wheel Contact

Journal of Mechanicl Science and Technology(KSME I. J.), <Special Edition> Vol. 19, No. 1, pp. 422-428, 2005

A Modeling of Impact Dynamics and its Application to Impact Force Prediction

Kil-Young Ahn

Electrotechnology R&D Center, LGIS Co.,Ltd., Cheong Ju Plant, #1, Songjung-dong,

Hungduk-gu, Cheong Ju, 361-290, Korea

Bong-Jo Ryu*

Department of Mechanical Design Engineering, Hanbat National University, San 16-1,

Duckmyoung-dong, Yuseong-gu, Daejeon 305-719, Korea

In this paper, the contact force between two colliding bodies is modeled by using Hertz’s force-displacement law and nonlinear damping function. In order to verify the appropriateness of the proposed contact force model, the drop type impact test is carried out for different impact velocities and different materials of the impacting body, such as rubber, plastic and steel. In the drop type impact experiment, six photo interrupters in series close to the collision location are installed to measure the velocity before impact more accurately. The characteristics of contact force model are investigated through experiments. The parameters of the contact force model are estimated using the optimization technique. Finally the estimated parameters are used to predict the impact force between two colliding bodies in opening action of the magnetic contactor, a kind of switch mechanism for switching electric circuits.

Key words ; Contact force model, Impact force prediction, Hertz’s force-displacement law, Drop type impact test

Journal of Mechanicl Science and Technology(KSME I. J.), <Special Edition> Vol. 19, No. 1, pp. 429-436, 2005

A Time Integration Method for Analysis of Dynamic Systems Using Domain Decomposition Technique

Takeshi Fujikawa*

Department of Education, Ashiya University, Ashiya 659-8511, Japan

Etsujiro Imanishi

Mechanical Engineering Research Laboratory, Kobe Steel, Kobe, 657-2272, Japan

This paper presents a precise and stable time integration method for dynamic analysis of vibration or multibody systems. A total system is divided into several subsystems and their responses are calculated separately, while the coupling effect is treated  equivalently as constant force during time steps. By using iterative procedure to improve equivalent coupling forces, a precise and stable solution is obtained. Some examples such as a seismic response and multibody analyses were carried out to demonstrate its usefulness.

Key Words : Multibody Dynamics, Time History Analysis, Substructure Method, Domain Decomposition Mothod

Journal of Mechanicl Science and Technology(KSME I. J.), <Special Edition> Vol. 19, No. 1, pp. 437-443, 2005

A Proposal of Wheel / Rail Contact Model for Friction Control

Kosuke Matsumoto*

Institute of Industrial Science, The University of Tokyo, (Tokyo Metro Co., Ltd.),

Tokyo 110-8614, JAPAN

Yoshihiro Suda

Center of Collaborative Research, & Institute of Industrial Science, The University of Tokyo,

Tokyo 153-8505, JAPAN

Hisanao Komine

Institute of Industrial Science, The University of Tokyo, Tokyo 153-8505, JAPAN

Takuji Nakai

Railway Bogie Track Manufacturing Department, Sumitomo Metal Industries, Ltd.,

Osaka, 554-0024, JAPAN

Masao Tomeoka, Kunihito Shimizu

Rolling Stock Department, Tokyo Metro Co., Ltd., Tokyo, 110-8614, JAPAN

Masuhisa Tanimoto, Yasushi Kishimoto

Railway Engineering Department, Sumitomo Metal Technology, INC., Osaka 554-0024, JAPAN

Takashi Fujii

Institute of Industrial Science, The University of Tokyo, Tokyo 153-8505, JAPAN

Controlling the friction between wheel and rail is direct and very effective measures to improve the curving performances of railway trucks, because the curving performances depend much on friction characteristics. Authors have proposed a method, “friction control”, which utilizes friction modifier (KELTRACKTM HPF) with onboard spraying system. With the method, not only friction coefficient, but also friction characteristics can be controlled as expected. In this study, MBD simulation is very valuable tool to foresee the effect of the control in advance of experiment with real car. And the creep characteristics of wheel / rail contact with the friction modifier takes very important role in the simulation. In this paper, authors propose a theoretical model of wheel/rail contact condition considering the creep characteristics of friction modifier, which is derived the application of principle tribological theories.

Key Words : Friction, Railway, Contact, Creep

Journal of Mechanicl Science and Technology(KSME I. J.), <Special Edition> Vol. 19, No. 1, pp. 444-451, 2005

Analysis of Human Arm Movement During Vehicle Steering Maneuver

Taeoh Tak*,

Professor, Kangwon National University, Department of Mechanical Engineering,

192-1 Hyoja 2 dong, Chuncheon, Kangwon-do 200-701, Korea

Kunyoung Kim, Hynung Ho Chun

Graduate students, Kangwon National University, Department of Mechanical Engineering

The analysis of human arm motion during steering maneuver is carried out for investigation of man-machine interface of driver and steering system  Each arm is modeled as interconnection of upper arm, lower arm, and hand by rotational joints that can properly represents permissible joint motion, and both arms are connected to a steering wheel through spring and damper at the contact points. The joint motion law during steering motion is determined through the measurement of each arm movement, and subsequent inverse kinematic analysis. Combining the joint motion law and inverse dynamic analysis, joint stiffness of arm is estimated. Arm dynamic analysis model for steering maneuver is setup, and is validated through the comparison with experimentally measured data, which shows relatively good agreement. To demonstrate the usefulness of the arm model, it is applied to study the effect of steering column angles on the steering motion.

Key Words : Steering Motion, Multibody Dynamics, Joint Motion Law, Muscular-Skeletal Motor Action, Man-Machine Interface

Journal of Mechanicl Science and Technology(KSME I. J.), <Special Edition> Vol. 19, No. 1, pp. 452-460, 2005

Accuracy Analysis of Optimal Trajectory Planning Methods Based on Function Approximation for a Four-DOF Biped Walking Model

Chunye Peng

Department of Mechanical Engineering and Science, Tokyo Institute of Technology,

2-12-1, Ookayama, Meguro-ku, Tokyo 152-8552, Japan

Kyosuke ONO*

Department of Mechanical Engineering and Science, Tokyo Institute of Technology,

2-12-1, Ookayama, Meguro-ku, Tokyo 152-8552, Japan

Based on an introduced optimal trajectory planning method, this paper mainly deals with the accuracy analysis during the function approximation process of the optimal trajectory planning method. The basis functions are composed of Hermit polynomials and Fourier series to improve the approximation accuracy. Since the approximation accuracy is affected by the given orders of each basis function, the accuracy of the optimal solution is examined by changing the combinations of the orders of Hermit polynomials and Fourier series as the approximation basis functions. As a result, it is found that the proper approximation basis functions are the 5th order Hermit polynomials and the 7th-10th order of Fourier series.

Key words : Optimal Trajectory Planning, Biped Walking, Accuracy Analysis, Function Approximation, Forward Dynamic Simulation

Journal of Mechanicl Science and Technology(KSME I. J.), <Special Edition> Vol. 19, No. 1, pp. 461-472, 2005

A Modular Formulation for Flexible Multibody Systems including Nonlinear Finite Elements

Lars Kubler*

Institute of Applied Mechanics, University of Erlangen-Nuremberg,

Egerlandstr. 5, 91058 Erlangen, Germany

Peter Eberhard

Institute B of Mechanics, University of Stuttgart, Pfaffenwaldring 9, 70569 Stuttgart, Germany

A formulation for flexible Multibody Systems (MBS) is investigated, where rigid MBS substructures are coupled with flexible bodies described by a nonlinear Finite Element (FE) approach. Several aspects that turned out to be crucial for the presented approach are discussed. The system describing equations are given in differential algebraic form (DAE), where many sophisticated solvers exist. In this paper the performance of several solvers is investigated regarding their suitability for the application to the usually highly stiff DAE. The substructures are connected with each other by nonlinear algebraic constraint equations. Further, partial derivatives of the constraints are required, which often leads to extensive algebraic transformations. Handcoding of analytically determined derivatives is compared to an approach utilizing algorithmic differentiation.

Key Words : Flexible Multibody System, Large Deformation, MBS, FEM, Algorithmic Differentiation, Numerical Simulation of DAE, DAE Solver

Journal of Mechanicl Science and Technology(KSME I. J.), <Special Edition> Vol. 19, No. 1, pp. 473-480, 2005

Design and Control of a Marine Satellite Antenna

Mooncheol Won*

Department of Mechatronics Engineering Chungnam National University, Daejeon 305-764, Korea

Sung-Soo Kim

Department of Mechatronics Engineering Chungnam National University, Daejeon 305-764, Korea

A three axes marine satellite antenna has been developed.  As a design step, a CAD model for the antenna has been created according to the design requirements.  Kinematic analyses are carried out to insure design specification and to check collision detection of the CAD model. Marine satellite antennas experience base motions, and a relevant control system should control the three antenna axis to point to the satellites accurately. A sensor fusion algorithm and a PIDA(Proportional, Integral, Derivative, Acceleration) control algorithm are designed and implemented to control the yaw, level, and cross-level angle of a small size satellite marine antenna. Antenna stabilization control experiments are performed using a test simulator which gives the antenna base motions. Experimental results show small pointing errors, which is less than 0.2 degree for the level, cross-level, and yaw axis.

Key Words : Marine satellite antenna, CAD modeling, Sensor Fusion, PIDA control

Journal of Mechanicl Science and Technology(KSME I. J.), <Special Edition> Vol. 19, No. 1, pp. 481-486, 2005

Solving Dynamic Equation Using Combination of Both Trigonometric and Hyperbolic Cosine Functions for Approximating Acceleration

Do Kien Quoc*

Department of Civil Engineering, Ho Chi Minh City University of Technology,

268 Ly Thuong Kiet St., Ho Chi Minh City, VIETNAM

Nguyen Trong Phuoc

Department of Civil Engineering, Ho Chi Minh City University of Technology,

268 Ly Thuong Kiet St., Ho Chi Minh City, VIETNAM

This paper introduces a numerical method for integration of the linear and nonlinear differential dynamic equation of motion. The variation of acceleration in two time steps is approximated as a combination of both trigonometric cosine and hyperbolic cosine functions with weighted coefficient. From which all necessary formulae are elaborated for the direct integration of the governing equation. A number of linear and nonlinear dynamic problems with various degrees of freedom are analysed using both the suggested method and Newmark method for the comparison. The numerical results show high advantages and effectiveness of the new method.

Key Word : Numerical Method, Approximation, Time Step, Accuracy

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 2, pp. 487-495, 2005

Studies on the Correlation between Mechanical Properties and

Ultrasonic Parameters of aging 1Cr-1Mo-0.25V Steel

Chang-Sung Seok *

School of Mechanical Engineering, Sungkyunkwan University,

300 Chunchun-dong, Jangan-gu, Suwon, Kyonggi-do 440-746, Korea

Jeong-Pyo Kim

Digital Module Division, Sound Solution Team, Samsung Electro-Mechanics Co., Ltd.,

314, Maetan 3-Dong, Paldal-Gu, Suwon, Gyunggi-Do 442-743, Korea

Mechanical properties of in-service facilities are required to evaluate the integrity of power plants and chemical plants. Non-destructive technique can be used to evaluate the mechanical properties. To investigate the mechanical properties using ultrasonic technique, the four classes of thermally aged specimens were prepared using an artificially accelerated aging method. Ultrasonic tests, tensile tests, fracture toughness tests and hardness tests were performed for the specimens. Then the mechanical properties were compared with ultrasonic parameters such as attenuation and non-linear parameter. From the investigation, we confirm that the ultrasonic parameter can be used to evaluate the mechanical properties.

Key Words: Mechanical  Properties, Ultrasonic Technique, Attenuation, Non-linear Parameter

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 2, pp. 496-504, 2005

Thermal and Mechanical Properties of Electro-Slag Cast Steel for Hot Working Tools

Young Hoon Moon*

Department of Mechanical Engineering/Engineering Research Center for Net Shape

and Die Manufacturing Technology, Pusan National University,

Jangjeon Dong, Geumjeong Gu, Pusan 609-735, Korea

Boo Hyun Kang

Department of Mechanical Engineering, Pusan National University,

Jangjeon Dong, Geumjeong Gu, Pusan 609-735, Korea

Chester J. Van Tyne

Department of Metallurgical and Materials Engineering,

Colorado School of Mines, Golden, CO 80401, USA

The thermal and mechanical properties of an electro-slag cast steel having a similar chemical composition to an AISI-6F2 steel have been investigated and compared with a forged AISI-6F2 steel.  AISI-6F2 is a hot-working tool steel.  Electro-slag casting (ESC) is a method of producing ingots in a water-cooled metal mold by the heat generated in an electrically conductive slag when current passes through a consumable electrode.  The ESC method provides the possibility of producing material for the high quality hot-working tools and ingots directly into a desirable shape.  In the present study, the thermal and mechanical properties of yield strength, tensile strength, hardness, impact toughness, wear resistance, thermal fatigue resistance, and thermal shock resistance for electro-slag cast and forged steel have been experimentally measured for both annealed and quenched and tempered heat treatment conditions.  It has been found that the electro-slag cast steel has comparable thermal and mechanical properties to the forged steel.

Key Words :  Electro-Slag Cast Steel, Tensile Test, Hardness Test, Impact Test, Wear Test, Thermal Fatigue Test, Thermal Shock Test

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 2, pp. 505-519, 2005

Anti-sway Position Control of an Automated Transfer Crane

Based on Neural Network Predictive PID Controller

Jin-Ho Suh, Jin-Woo Lee

Department of Electrical Engineering, Dong-A National University,

840, Hadan-dong, Saha-gu, Busan, 604-714, Korea

Young-Jin Lee

Dept. of Electrical Instrument and Control, Korea Aviation Polytechnic College,

438 Egeum-dong, Sachon City, Kyungnam, 664-180, Korea

Kwon-Soon Lee*

Division of Electrical, Electronic, and Computer Eng., Dong-A University,

840, Hadan-dong, Saha-gu, Busan, 604-714, Korea

In this paper, we develop an anti-sway control in proposed techniques for an ATC system. The developed algorithm is to build the optimal path of container motion and to calculate an anti-collision path for collision avoidance in its movement to the finial coordinate. Moreover, in order to show the effectiveness in this research, we compared NNP PID controller to be tuning parameters of controller using NN with 2 DOF PID controller. The simulation and experimental results show that the proposed control scheme guarantees performances, trolley position, sway angle and settling time in NNP PID controller than other controller. As the results in this paper, the application of NNP PID controller is analyzed to have robustness about disturbance which is wind of fixed pattern in the yard. Accordingly, the proposed algorithm in this study can be readily used for industrial applications.

Keywords: Automated transfer crane (ATC), Neural network predictive (NNP) control, Predictive control, NN auto tuner, Anti-sway control, Collision avoidance path

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 2, pp. 520-528, 2005

Study on the Damping Performance Characteristics Analysis

of Shock Absorber of Vehicle by Considering Fluid Force

Choon-Tae Lee

Department of Mechanical and Intelligent Systems Engineering, Busan National University,

30 Changjeon-dong, Keumjeong-ku, Busan 609-735 Korea

Byung-Young Moon*

Department of Mechanical Engineering, Miryang National University,

Samnangjin-eup, GyeongNam  627-706  Korea

In this study, a new mathematical dynamic model of displacement sensitive shock absorber(DSSA) is proposed to predict the dynamic characteristics of automotive shock absorber. The performance of shock absorber is directly related to the vehicle behaviors and performance, both for handling and ride comfort. The proposed model of the DSSA  has two modes of damping force (i.e. soft and hard) according to the position of piston. In this paper, the performance of the DSSA is analyzed by considering the transient zone for more exact dynamic characteristics. For the mathematical modeling of DSSA, flow continuity equations at the compression and rebound chamber are formulated. And the flow equations at the compression and rebound stroke are formulated, respectively. Also, the flow analysis at the reservoir chamber is carried out. Accordingly, the damping force of the shock absorber is determined by the forces acting on the both side of piston.  The analytic result of damping force characteristics are compared with the experimental results to prove the effectiveness. Especially, the effects of displacement sensitive orifice area and the effects of displacement sensitive orifice length on the damping force are observed, respectively. The results reported herein will provide a better understanding of the shock absorber.

Key Words :  Shock absorber, Damping force, Displacement sensitive orifice, Flow continuity equations, Stroke Dependent, Piston valve, Mathematical model

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 2, pp. 529-539, 2005

Intelligent Switching Control of Pneumatic Cylinders by Learning Vector Quantization Neural Network

KyoungKwan Ahn*, ByungRyong Lee

School of Mechanical and Automotive Engineering, University of Ulsan,

San 29, Muger2-dong, Nam-gu, Ulsan, 680-749, Korea

The development of a fast, accurate, and inexpensive position-controlled pneumatic actuator that may be applied to various practical positioning applications with various external loads is described in this paper. A novel modified pulse-width modulation (MPWM) valve pulsing algorithm allows on/off solenoid valves to be used in place of costly servo valves. A comparison between the system response of the standard PWM technique and that of the modified PWM technique shows that the performance of the proposed technique was significantly increased. A state-feedback controller with position, velocity and acceleration feedback was successfully implemented as a continuous controller. A switching algorithm for control parameters using a learning vector quantization neural network (LVQNN) has newly proposed, which classifies the external load of the pneumatic actuator. The effectiveness of this proposed control algorithm with smooth switching control has been demonstrated through experiments with various external loads.

Keywords : Pneumatic, Switching control, On/off solenoid valve, Pulse width modulation, Neural Network, Intelligent control

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 2, pp. 540-548, 2005

Robust State Estimation based on Sliding Mode Observer for Aeroelastic System

In-Joo Jeong

Graduate Student, Department of Mechanical Engineering, Korea University, 136-701 Seoul, Korea

Sungsoo Na*

Associate Professor, Department of Mechanical Engineering, Korea University, 136-701 Seoul, Korea

Myung-Hyun Kim

Assistant Professor, Department of Naval Architecture and Ocean Engineering, Pusan University,

609-735 Pusan, Korea

Jae-Hong Shim

Associate Professor, Department of Mechatronics Engineering, Korea Polytechnic University,

Siheung City, 429-793 Keonggi-do, Korea

Byung-Young Oh

Graduate Student, Department of Mechanical Engineering, Korea University, 136-701 Seoul, Korea

This paper concerns the application and demonstration of sliding mode observer for aeroelastic system, which is robust to model uncertainty including mass and stiffness of the system and various disturbances. The performance of a sliding mode observer is compared with that of a conventional Kalman filter to demonstrate robustness and disturbance decoupling characteristics. Aeroelastic instability may occur when an elastic structure is moving even in subcritical flow speed region. Simulation results using sliding mode observer are presented to control aeroelastic response of flapped wing system due to various external excitations as well as model uncertainty and sinusoidal disturbances in subcritical speed in an incompressible flow region.

Keywords: Sliding mode observer, Kalman filter, LQG, aeroelastic response, state estimation

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 2, pp. 549-557, 2005

Feature-Based Multi-Resolution Modeling of Solids Using History-Based Boolean Operations

- Part I:  Theory of History-Based Boolean Operations

Sang Hun Lee*,

School of Automotive Engineering, Kookmin University,

Jeongneung-Dong, Seongbuk-Gu, Seoul, 136-702, Korea

Kyu-Yeul Lee

Department of Naval Architecture and Ocean Engineering, Seoul National University,

Seoul 151-744, Korea

Yoonwhan Woo

Graduate School of Automotive Engineering, Kookmin University,

Jeongneung-Dong, Seongbuk-Gu, Seoul, 136-702, Korea

Kang-Soo Lee

School of Mechanical Engineering, Hanbat National University,

Deokmyeong-Dong, Yuseng-Gu, Daejeon, 305-719, Korea

The requirements of multi-resolution models of feature-based solids, which represent an object at many levels of feature detail, are increasing for engineering purposes, such as analysis, network-based collaborative design, virtual prototyping and manufacturing.  To provide multi-resolution models for various applications, it is essential to generate adequate solid models at varying levels of detail (LOD) after feature rearrangement, based on the LOD criteria.  However, the non-commutative property of the union and subtraction Boolean operations is a severe obstacle to arbitrary feature rearrangement.  To solve this problem we propose history-based Boolean operations that satisfy the commutative law between union and subtraction operations by considering the history of the Boolean operations.  Because these operations guarantee the same resulting shape as the original and reasonable shapes at the intermediate LODs for an arbitrary rearrangement of its features, various LOD criteria can be applied for multi-resolution modeling in different applications.

Key Words: Non-Manifold, Solid, Multi-Resolution, Feature, Boolean Operation

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 2, pp. 558-566, 2005

Feature-Based Multi-Resolution Modeling of Solids Using History-Based Boolean Operations

- Part II: Implementation Using Non-Manifold Modeling System

Sang Hun Lee*,

School of Automotive Engineering, Kookmin University,

Jeongneung-Dong, Seongbuk-Gu, Seoul, 136-702, Korea

Kyu-Yeul Lee

Department of Naval Architecture and Ocean Engineering, Seoul National University,

Seoul 151-744, Korea

Yoonwhan Woo

Graduate School of Automotive Engineering, Kookmin University,

Jeongneung-Dong, Seongbuk-Gu, Seoul, 136-702, Korea

Kang-Soo Lee

School of Mechanical Engineering, Hanbat National University,

Deokmyeong-Dong, Yuseng-Gu, Daejeon, 305-719, Korea

We propose a feature-based multi-resolution representation of B-rep solid models using history-based Boolean operations based on the merge-and-select algorithm.  Because union and subtraction are commutative in the history-based Boolean operations, the integrity of the models at various levels of detail (LOD) is guaranteed for the reordered features regardless of whether the features are subtractive or additive.  The multi-resolution solid representation proposed in this paper includes a non-manifold topological merged-set model of all feature primitives as well as a feature-modeling tree reordered consistently with a given LOD criterion.  As a result, a B-rep solid model for a given LOD can be provided quickly, because the boundary of the model is evaluated without any geometric calculation and extracted from the merged set by selecting the entities contributing to the LOD model shape.

Key Words: Non-Manifold, Solid, Multi-Resolution, Feature, Boolean Operation

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 2, pp. 567-577, 2005

Analysis of a Composite Double Cantilever Beam with Stitched

Reinforcements Under Mixed Mode Loading: Formulation (I)

Insik Jang*

Department of Mechano-Informatics and Design Engineering , Hongik University,

300 Jochiwon-eup, Yonki-gun, Chungnam-do, Korea 339-701

Bhavani. V. Sankar

Department of Mechanical and Aerospace Engineering, University of Florida,

PO Box 116250 Gainesville, FL 32611-6250, U.S.A

Several methods for improving the interlaminar strength and fracture toughness of composite materials are developed Through-the-thickness stitching is considered one of the most common ways to prevent delamination. Stitching significantly increases the Mode I fracture toughness and moderately improves the Mode II fracture toughness. An analytical model has been developed for simulating the behavior of stitched double cantilever beam specimen under various loading conditions. For z-directional load and moment about the y-axis the numerical solutions are compared with the exact solutions. The derived formulation shows good accuracy when the relative error of displacement and rotation between numerical and exact solution were calculated. Thus we can use the present model with confidence in analyzing other problems involving stitched beams.

Key Words : Composite Double Cantilever Beam, Stitched Reinforcement, Mixed Mode Loading, Analytical Modelling

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 2, pp. 578-588, 2005

A Face Robot Actuated With Artificial Muscle Based on Dielectric Elastomer

Jong Won Kwak, Ho June Chi, Kwang Mok Jung, Ja Choon Koo

School of Mechanical Engineering, Sungkyunkwan University,

Chunchun-dong, 300, Jangan-gu, Suwon, Kyunggi-do 440-746, Korea

Jae Wook Jeon

School of Information and Communication Engineering,

Chunchun-dong, 300, Jangan-gu, Suwon, Kyunggi-do 440-746, Korea

Youngkwan Lee, Jae-do Nam

School of Applied Chemistry, Sungkyunkwan University,

Chunchun-dong, 300, Jangan-gu, Suwon, Kyunggi-do 440-746, Korea

Youngsun Ryew

Robolands Co., Hanyang Business Incubator, 1271 Sa1-dong, Sangrok-gu, Ansan-si, 426-791, Korea

Hyouk Ryeol Choi*

School of Mechanical Engineering, Sungkyunkwan University,

Chunchun-dong, 300, Jangan-gu, Suwon, Kyunggi-do 440-746, Korea

Face robots capable of expressing their emotional status, can be adopted as an efficient tool for friendly communication between the human and the machine. In this paper, we present a face robot actuated with artificial muscle based on dielectric elastomer. By exploiting the properties of dielectric elastomer, it is possible to actuate the covering skin, eyes as well as provide human-like expressivity without employing complicated mechanisms. The robot is driven by seven actuator modules such eye, eyebrow, eyelid, brow, cheek, jaw and neck module corresponding to movements of facial muscles. Although they are only part of the whole set of facial motions, our approach is sufficient to generate six fundamental facial expressions such as surprise, fear, angry, disgust, sadness, and happiness. In the robot, each module communicates with the others via CAN communication protocol and according to the desired emotional expressions, the facial motions are generated by combining the motions of each actuator module. A prototype of the robot has been developed and several experiments have been conducted to validate its feasibility.

Key Words : face robot, head robot, EAP, artificial muscle, dielectric elastomer

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 2, pp. 589-604, 2005

Thin-Walled Curved Beam Theory Based on Centroid-Shear Center Formulation

Kim, Nam-Il

Post-Doctoral Fellow, Depart. of Civil and Environmental Engineering, Sungkyunkwan University,

Cheoncheon-Dong, Jangan-Ku, Suwon, 440-746, Korea

Kim, Moon-Young*

Professor, Depart. of Civil and Environmental Engineering, Sungkyunkwan University,

Cheoncheon-Dong, Jangan-Ku, Suwon, 440-746, Korea

To overcome the drawback of currently available curved beam theories having non-symmetric thin-walled cross sections, a curved beam theory based on centroid-shear center formulation is presented for the spatially coupled free vibration and elastic analysis. For this, the displacement field is expressed by introducing displacement parameters defined at the centroid and shear center axes, respectively. Next the elastic strain and kinetic energies considering the thickness-curvature effect and the rotary inertia of curved beam are rigorously derived by degenerating the energies of the elastic continuum to those of curved beam. And then the equilibrium equations and the boundary conditions are consistently derived for curved beams having non-symmetric thin-walled cross section. It is emphasized that for curved beams with L- or T-shaped sections, this thin-walled curved beam theory can be easily reduced to the solid beam theory by simply putting the sectional properties associated with warping to zero. In order to illustrate the validity and the accuracy of this study, FE solutions using the Hermitian curved beam elements are presented and compared with the results by previous research and ABAQUS’s shell elements.

Key Words : curved beam, free vibration analysis, elastic analysis, thin-walled, warping

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 2, pp. 605-617, 2005

Three-Dimensional Computations of the Impulsive Wave Discharged from a Duct

Young-Ki Lee

School of Mechanical Engineering, Andong National University,

388 Songcheon-dong, Andong, 760-749, Korea

Yong-Hun Kweon

Department of Energy and Environmental Engineering, Kyushu University,

6-1, Kasugakouen, Kasuga, Fukuoka, 816-8580, Japan

Heuy-Dong Kim*

School of Mechanical Engineering, Andong National University,

388 Songcheon-dong, Andong, 760-749, Korea

Toshiaki Setoguchi

Department of Mechanical Engineering, Saga University,1, Honjo-machi, Saga, 840-8502, Japan

A sudden discharge of mass flow from the exit of a duct can generate an impulsive wave, generally leading to undesirable noise and vibration problems. The present study develops an understanding of unsteady flow physics with regard to the impulsive wave discharged from a duct, using a numerical method. A second order total variation diminishing scheme is employed to solve three-dimensional, unsteady, compressible Euler equations. Computations are performed for several exit conditions with and without ground and wall effects under a change in the Mach number of an initial shock wave from 1.1 to 1.5. The results obtained show that the directivity and magnitude of the impulsive wave discharged from the duct are significantly influenced by the initial shock Mach number and by the presence of the ground and walls.

Keywords: Compressible Flow, Ground Effect, Impulsive Noise, Unsteady Flow, Wave Propagation, Weak Shock Wave

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 2, pp. 618-624, 2005

A New Approach to Design of a Dynamic Output Feedback Stabilizing Control Law for LTI Systems

Young-Ik Son*

NPT Center & Department of Electrical Engineering, Myongji University,

38-2 Namdong, Yong-In, Kyunggido 449-728, Korea

Hyungbo Shim

School of Electrical Engineering and Computer Science #060, Seoul National University,

Kwanak PO Box 34, Seoul, 151-600, Korea

Nam-Hoon Jo

School of Electrical Engineering, Soongsil University,

1-1 Sangdo-dong, Dongjak-gu, Seoul 156-743, Korea

Kab-Il Kim

NPT Center & Department of Electrical Engineering, Myongji University,

38-2 Namdong, Yong-In, Kyunggido 449-728, Korea

We present a new state-space approach to construct a dynamic output feedback controller which stabilizes a class of linear time invariant systems. All the states of the given system are not measurable and only the output is used to design the stabilizing control law. In the design scheme, however, we first assume that the given system can be stabilized by a feedback law composed of the output and its derivatives of a certain order. Beginning with this assumption, we systematically construct a dynamic system which removes the need of the derivatives. The main advantage of the proposed controller is regarding the controller order, which may be smaller than that of conventional output feedback controller. Using a simple numerical example, it is shown that the order of the proposed controller is indeed smaller than that of reduced-order observer based output feedback controller.

Key Words: Linear System, Stability, State Space, Output Derivatives, Dynamic Output Feedback, Recursive Design

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 2, pp. 625-633, 2005

Frequency Response Analysis of Cylindrical Shells Conveying Fluid Using Finite Element Method

Young-Soo Seo, Weui-Bong Jeong*, Wan-Suk Yoo

Department of Mechanical Engineering, Pusan National University,

Jangjeon-dong, Kumjung-ku, Pusan, 609-735, Korea

Ho-Kyeong Jeong

Structure & Materials Department KSLV Technology Division,

45 Eoeun-Dong, Yuseong-Gu, Daejeon, 305-333, Korea

A finite element vibration analysis of thin-walled cylindrical shells conveying fluid with uniform velocity is presented. The dynamic behavior of thin-walled shell is based on Sanders’ theory and the fluid in cylindrical shell is considered as inviscid and incompressible fluid so that it satisfies the Laplace’s equation. A beam-like shell element is used to reduce the number of degree-of-freedom by assuming the circumferential modes of cylindrical shell. An estimation of frequency response function of the pipe with taking into consideration of the coupled effects of the internal fluid is presented. A dynamic coupling condition of the interface between the fluid and the structure is used. The effective thickness of fluid according to circumferential modes is also discussed. The influence of fluid velocity on the frequency response function is illustrated and discussed. The results by this method are compared with published results and those by commercial tools.

Key Words: Fluid-Structure Interaction, Frequency Response Analysis, Beam-like Shell Element, Effective Thickness

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 2, pp. 634-648, 2005

Round Robin Analysis for Probabilistic Structural Integrity of Reactor Pressure Vessel under Pressurized Thermal Shock

Myung Jo Jhung*, Changheui Jang, Seok Hun Kim, Young Hwan Choi, Hho Jung Kim

Korea Institute of Nuclear Safety, 19 Guseong-dong, Yuseong-gu, Daejeon 305-338 Korea

Sunggyu Jung, Jong Min Kim, Gap Heon Sohn, Tae Eun Jin, Taek Sang Choi

Korea Power Engineering Company

Ji Ho Kim, Jong Wook Kim, Keun Bae Park

Korea Atomic Energy Research Institute

Performed here is a comparative assessment study for the probabilistic fracture mechanics approach of the pressurized thermal shock of the reactor pressure vessel. A round robin consisting of one prerequisite deterministic study and five cases for probabilistic approaches is proposed, and all organizations interested are invited. The problems are solved by the participants and their results are compared to issue some recommendation of best practices and to assure an understanding of the key parameters in this type of approach, like transient description and frequency, material properties, defect type and distribution, fracture mechanics methodology etc., which will be useful in the justification through a probabilistic approach for the case of a plant over-passing the screening criteria. Six participants from 3 organizations responded to the problem and their results are compiled and analyzed in this study.

Keywords : probabilistic analysis, pressurized thermal shock, reactor pressure vessel, stress intensity factor, fracture toughness, residual stress, Monte Carlo simulation

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 2, pp. 649-654, 2005

Fabrication and Drive Test of a Peristaltic Thermopnumatic PDMS Micropump

Ok Chan Jeong

Center for Promotion of the COE program, Ritsumeikan University,

1-1-1 Nojihigashi, Kusatsu, Shiga 525-8577, Japan

Sin Wook Park, Sang Sik Yang*

Division of Electrical and Computer Engineering, Ajou University,

San 5 Wonchun-Dong, Yeongtong-Gu, Suwon, 443-749, Korea

This paper presents fabrication and drive test of a peristaltic PDMS micropump actuated by the thermopneumatic force.  The micropump consists of the three peristaltic-type actuator chambers with microheaters on the glass substrate and a microchannel connecting the chambers and the inlet/outlet port.  The micropump is fabricated by the spin-coating process, the two-step curing process, the JSR (negative PR) molding process, and etc.  The diameter and the thickness of the actuator diaphragm are 2.5 mm and 30 μm, respectively.  The meniscus motion in the capillary tube is observed with a video camera and the flow rate of the micro pump is calculated through the frame analysis of the recorded video data.  The maximum flow rate of the micropump is about 0.36 μL/sec at 2 Hz for the zero hydraulic pressure difference when the 3-phase input voltage is 20 V.

Key Words: PDMS(Polydimethylsiloxane) micropump, peristaltic micropump, thermopneumatic force, flow rateReferences

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 2, pp. 655-663, 2005

Measurment of Fluid Film Thickness on The Valve Plate in Oil Hydraulic Axial Piston Pumps

(Part Ⅱ:Spherical Design Effects)

Jong-Ki Kim*, Hyoung-Eui Kim, Yong-Bum Lee

Korea Institute of Machinery&Materials, 171 Jang-dong, Yuseong-Gu, Daejeon, 305-600, Korea

Jae-Youn Jung

Faculty of Mechanical&Aerospace System Engineering,Chonbuk National University,

Jeonju, Jeonbuk, 561-756, Korea

Tribological characteristics in the sliding parts of oil hydraulic piston pumps are very important in increasing overall efficiency. In this study, the fluid film between the valve plate and the cylinder block was measured by using  a gap sensor and the mercury-cell slip ring unit under real working conditions. To investigate the effect of the valve shape, we designed three valve plates each having a different shape. One of the valve plates was without bearing pad, another valve plate had bearing pad and the last valve plate was a spherical valve plate. It was noted that these three valve plates observed different aspects of the fluid film characteristics between the cylinder block and the valve plate. The leakage flow rates and the shaft torque were also investigated in order to clarify the performance difference between these three types of valve plates. From the results of this study, we found that the spherical valve plate estimated good fluid film patterns and good performance more than the other valve plates in oil hydraulic axial piston pumps.

Key words : Hydraulic axial piston pump, Fluid film, Valve plate, Cylinder block

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 2, pp. 664-673, 2005

Heat Transfer in a Micro-actuator Operated by Radiometric Phenomena

Joong-Sik Heo

Researcher, Institute of Advanced Machinery and Technology, Sungkyunkwan University,

300 Chunchun-dong, Jangan-ku, Suwon 440-746, S. Korea

Young-Kyu Hwang*

Professor, School of Mechanical Engineering, Sungkyunkwan University,

300 Chunchun-dong, Jangan-ku, Suwon 440-746, S. Korea

The heat transfer characteristics of rarefied flows in a micro-actuator are studied numerically. The effect of Knudsen number ( ) on the heat transfer of the micro-actuator flows is also examined. The   based on gas density and characteristic dimension is varied from near-continuum to highly rarefied conditions. Direct simulation Monte Carlo calculations have been performed to estimate the performance of the micro-actuator. The results show that the magnitude of the temperature jump at the wall increases with  . Also, the heat transfer to the isothermal wall is found to increase significantly with  .

Key Words: Micro-actuator, Radiometric Phenomena, DSMC Method, Rarefied Gas Flow Field, Knudsen Number

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 2, pp. 674-681, 2005

Wake Shapes Behind Wings in Close Formation Flight Near the Ground

Cheolheui Han

Kyungwon Tech, Yatap-Dong, Bundang-Gu, KyungKi-Do, 463-827, Korea

Leesang Cho, Jinsoo Cho*

Hanyang University, Seoul, 133-791, Korea

The unsteady evolution of trailing vortex sheets behind wings in close formation flight near the ground is simulated using a discrete vortex method. The ground effect is included by an image method. The method is validated by comparing computed results with other numerical results. For a lifting line with an elliptic loading, the ground has an effect of moving wingtip vortices laterally outward and suppressing the development of vortex evolution. The gap between wings in close formation flight has an effect of moving up wingtip vortices facing each other. For wings flying in parallel, the ground effect causes the wingtip vortices facing each other to move up, and it makes the opposite wing tip vortices to move laterally outward. When there is a relative height between the wings in ground effect, right-hand side wingtip vortices from a mothership move laterally inward.

Key Words : Formation Flight, Ground Effect, Aircraft Wake Vortices, Discrete Vortex Method

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 2, pp. 682-691, 2005

Design, Fabrication, and Testing of a MEMS Microturbine

Byung Sun Jeon

Research Engineer, Hyundai Motor Company,

Jangduk-Dong 772-1, Whasung-Si, Gyunggi-Do, 445-706, Korea

Kun Joong Park

Graduate Student, School of Mechanical and Aerospace Engineering, Seoul National University,

Shinlim-Dong, Kwanak-Gu Seoul 151-742, Korea

Seung Jin Song*

Associate Professor, School of Mechanical and Aerospace Engineering, Seoul National University,

Shinlim-Dong, Kwanak-Gu Seoul 151-742, Korea

Young Chang Joo

Assistant Professor, School of Materials Science and Engineering, Seoul National University,

Shinlim-Dong, Kwanak-Gu Seoul 151-742, Korea

Kyoung Doug Min

Associate Professor, School of Mechanical and Aerospace Engineering, Seoul National University,

Shinlim-Dong, Kwanak-Gu Seoul 151-742, Korea

This paper describes the design, fabrication, and testing of a microturbine developed at Seoul National University. Here, the term “microturbine” refers to a radial turbine with a diameter on the order of a centimeter. Such devices can be used to transmit power for various systems. The turbine was designed using a commercial CFD code, and it has a design flow coefficient of 0.238 and work coefficient of 0.542. It has 31 stator blades and 24 rotor blades. A hydrodynamic journal bearing and hydrostatic thrust bearings counteract radial and axial forces on the rotor. The test turbine consists of a stack of five wafers and is fabricated by MEMS technology, using photolithography, DRIE, and bonding processes. The first, second, fourth, and fifth layers contain plumbing, and hydrostatic axial thrust bearings for the turbine. The third wafer contains the turbine’s stator, rotor, and hydrodynamic journal bearings. Furthermore, a turbine test facility containing a flow control system and instrumentation has been designed and constructed. In performance tests, a maximum rotation speed of 11,400 rpm and flow rate of 16,000 sccm have been achieved.

Key words: Microturbine, Micro Power System, High Aspect Ratio, DRIE, Si direct bonding

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 2, pp. 692-703, 2005

Energy and exergy analyses of drying of eggplant slices in a cyclone type dryer

E. Kavak Akpinar*

Mechanical Engineering Department, Firat University, 23279, Elazig, Turkey.

In this paper, the energy and exergy analyses of the drying process of thin layer of eggplant slices are investigated. Drying experiments were conducted at inlet temperatures of drying air of 55, 65 and 75 °C and at drying air velocities of 1 and 1.5 ms-1 in a cyclone type dryer. Using the first law of thermodynamics, energy analysis was carried to estimate the ratios of energy utilization. However, exergy analysis was accomplished to determine type and magnitude of exergy losses during the drying process by applying the second law of thermodynamics. It was deduced that eggplant slices are sufficiently dried in the ranges between 55-75 oC of drying air temperature and at 1 and 1.5 ms-1 of drying air velocity during 12000-21600 s despite the exergy losses of 0-0.739 kJs-1.

Keywords: Drying, Energy and Exergy analyses, Eggplant

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 2, pp. 704-715, 2005

A study on the characteristics of in-cylinder intake flow in spark ignition engine using the PIV

Suk-Young Lee

Department of Mechanical Engineering, Pusan National University,

30 Jangjeon-dong, Geumjeong-gu, Busan 609-735, Korea

Ku-Seob Jeong

Department of Automotive Engineering, jinju International University,

270 Sangmoonri, Moonsaneub, Jinju city, Kuyungsang-namdo, 609-735, korea

Chung-Hwan Jeon*

Department of Mechanical Engineering, Pusan National University,

30 Jangjeon-dong, Geumjeong-gu, Busan 609-735, Korea

Young-June Chang

Department of Mechanical Engineering, Pusan National University,

30 Jangjeon-dong, Geumjeong-gu, Busan 609-735, Korea

In this study, to investigate in-cylinder tumble or swirl intake flow of a gasoline engine, the flow characteristics were examined with opening control valve (OCV) and several swirl control valves (SCV) which intensify intake flow through steady flow experiment, and also turbulent characteristics of in-cylinder flow field were investigated by 2-frame cross-correlation particle image velocimetry (PIV) method. In the investigation of intake turbulent characteristics using PIV method, the different flow characteristics were showed according to OCV or SCV figures. The OCV or SCV installed engine had higher vorticity and turbulent kinetic energy than a baseline engine, especially around the wall and lower part of the cylinder. Above all, SCV B type was superior to the others. About energy dissipation and reynolds shear stress distribution, a baseline engine had larger loss than OCV or SCV installed one because flow impinged on the cylinder wall. It should be concluded, from what has been said above, as swirl component was added to existing tumble flow adequately, it was confirmed that turbulent intensity was enlarged, flow energy was conserved effectively through the experiment. In other words, there is a suggestion that flow characteristics as these affected to in-cylinder combustion positively.

Key words : Particle Image Velocimetry, Cross Correlation, Swirl Control Valve, Open Control Valve, Flow Visualization

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 2, pp. 716-727, 2005

Measurements of Temperature and Flow Fields with Sub-Millimeter Spatial Resolution Using Two-Color Laser Induced Fluorescence (LIF) and Micro-Particle Image Velocimetry (PIV)

HyunJung. Kim*

Division of Mechanical Engineering, Ajou Universtiy,

San 5 Wonchon-Dong, Yeongtong-Gu, Suwon 443-749, Korea

Comprehensive measurements for velocity and temperature fields have been conducted. A Micro PIV 2-color LIF system have been setup to measure the buoyancy driven fields in a 1-mm heated channel with low Grashof-Prandtl numbers [86 <   < 301]. Fluorescence microscopy is combined with an MPIV system to obtain enough intensity images and clear pictures from nano-scale fluorescence particles. The spatial resolution of the Micro PIV system is 75-mm by 67-mm and error due to Brownian motion is estimated 1.05%. Temperature measurements have achieved the 4.7-mm spatial resolution with relatively large data uncertainties the present experiment. The measurement uncertainties have been decreased down to less than ±1.0 C° when measurement resolution is equivalent to 76-mm. Measured velocity and temperature fields will be compared with numerical results to examine the feasibility of development as a diagnostic technique.

Key Words : Fluorescence, Laser, Micro PIV, Temperature Measurement

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 3, pp. 731-742, 2005

Fault Tolerant Control of Magnetic Bearings with Force Invariance

Uhn Joo Na*

Division of Mechanical and Automation Engineering, Kyungnam University,

Masan, Kyungnam 631-701, Korea

A magnetic bearing even with multiple coil failure can produce the same decoupled magnetic forces as those before failure if the remaining coil currents are properly redistributed. This fault-tolerant, force invariance control can be achieved with simply replacing the distribution matrix with the appropriate one shortly after coils fail, without modifying feedback control law. The distribution gain matrix that satisfies the necessary constraint conditions of decoupling linearized magnetic forces is determined with the Lagrange Multiplier optimization method.

Keywords: Magnetic Bearings, Fault Tolerance, Rotor Dynamics, Active Vibration Control

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 3, pp. 743-755, 2005

Development of a Rule-based Inference Model for Human Sensibility Engineering System

Sun-Mo Yang*,

Six-Sigma Strategic Management Consulting Co., Ltd., 635-4 Yeoksam-dong, Kangnam gu, Seoul, Korea

Beumjun Ahn, Kwang-Kyu Seo**

Department of Industrial Information and Systems Engineering, Sangmyung University,

San 98-20, Anso-Dong, Chonan, Chungnam 330-720, Korea

Human Sensibility Engineering System (HSES) has been applied to product development for customer’s satisfaction based on ergonomic technology. The system is composed of three parts such as human sensibility analysis, inference mechanism, and presentation technologies. Inference mechanism translating human sensibility into design elements plays an important role in the HSES. In this paper, we propose a rule-based inference model for HSES. The rule-based inference model is composed of five rules and two inference approaches. Each of these rules reasons the design elements for selected human sensibility words with the decision variables from regression analysis in terms of forward inference. These results are evaluated by means of backward inference. By comparing the evaluation results, the inference model decides on product design elements which are closer to the customer’s feeling and emotion. Finally, simulation results are tested statistically in order to ascertain the validity of the model.

Key Words: Human Sensibility Engineering, Rule-based Inference Model, Computer Simulation

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 3, pp. 756-767, 2005

Decentralized Control Design for Welding Mobile Manipulator

Tan Tung Phan*, Tan Lam Chung, Manh Dung Ngo, Hak Kyeong Kim, Sang Bong Kim

Department of Mechanical Eng., College of Eng., Pukyong National University,

San 100, Yongdang-Dong, Nam-Gu, Pusan 608-739, Korea

This paper presents a decentralized motion control method of welding mobile manipulators which use for welding in many industrial fields. Major requirements of welding robots are accuracy, robust, and reliability so that they can substitute for the welders in hazardous and worse environments. To do this, the manipulator has to take the torch tracking along a welding trajectory with a constant velocity and a constant heading angle, and the mobile-platform has to move to avoid the singularities of the manipulator. In this paper, we develop a kinematic model of the mobile-platform and the manipulator as two separate subsystems. With the idea that the manipulator can avoid the singularities by keeping its initial configuration in the welding process, the redundancy problem of system is solved by introducing the platform mobility to realize this idea. Two controllers for the mobile-platform and the manipulator were designed, respectively, and the relationships between two controllers are the velocities of two subsystems. Control laws are obtained based on the Lyapunov function to ensure the asymptotical stability of the system. The simulation and experimental results show the effectiveness of the proposed controllers.

Keywords: decentralized motion control method, mobile manipulator, welding reference trajectory

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 3, pp. 768-777, 2005

Optimal Design of Nonlinear Fluid Engine Mount

Young Kong Ahn

Research Center for Machine Parts and Material Processing, University of Ulsan,

San 29, Muger 2-Dong, Ulsan 680-749, KOREA

Jin Dae Song, Bo-Suk Yang*

School of Mechanical Engineering, Pukyong National University,

San 100, Yongdang-dong, Nam-gu, Busan 608-739, KOREA

Kyoung Kwan Ahn

Research Center for Machine Parts and Material Processing,

School of Mechanical & Automotive Engineering, University of Ulsan, Ulsan 680-749, KOREA

Shin Morishita

Department of Mechanical Engineering, Yokohama National University,

79-5 Tokiwadai, Hodogaya-ku, Yokohama 240-8501, JAPAN

This paper shows that the performance of a nonlinear fluid engine mount can be improved by an optimal design process. The property of a hydraulic mount with inertia track and decoupler differs according to the disturbance frequency range. Since the excitation amplitude is large at low excitation frequency range and is small at high excitation frequency range, mathematical model of the mount can be divided into two linear models. One is a low frequency model and the other is a high frequency model. The combination of the two models is very useful in the analysis of the mount and is used for the first time in the optimization of an engine mount in this paper. Normally, the design of a fluid mount is based on a trial and error approach in industry because there are many design parameters. In this study, a nonlinear mount was optimized to minimize the transmissibilities of the mount at the notch and the resonance frequencies for low and high-frequency models by a popular optimization technique of sequential quadratic programming (SQP) supported by MATLABa subroutine. The results show that the performance of the mount can be greatly improved for the low and high frequencies ranges by the optimization method.

Key Words: Fluid Mount, Nonlinear Fluid Mount, Optimal Design

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 3, pp. 778-791, 2005

Performance Improvement of Pneumatic Artificial Muscle

Manipulators using Magneto-Rheological Brake

KyoungKwan Ahn*

School of Mechanical and Automotive Engineering, University of Ulsan,

San 29, Muger 2dong, Nam-gu, Ulsan, 680-764, Korea

TU Diep Cong Thanh

Graduate School of Mechanical and Automotive Engineering, University of Ulsan,

San 29, Muger 2dong, Nam-gu, Ulsan, 680-764, Korea

Young Kong Ahn

Research Center for Machine Parts and Material Processing, University of Ulsan,

San 29, Muger 2dong, Nam-gu, Ulsan, 680-764, Korea

A novel pneumatic artificial muscle actuator (PAM actuator), which has achieved increased popularity to provide the advantages such as high strength and high power/weight ratio, low cost, compactness, ease of maintenance, cleanliness, readily available and cheap power source, inherent safety and mobility assistance to humans performing tasks, has been regarded during the recent decades as an interesting alternative to hydraulic and electric actuators. However, some limitations still exist, such as the air compressibility and the lack of damping ability of the actuator bring the dynamic delay of the pressure response and cause the oscillatory motion. Then it is not easy to realize the performance of transient response of pneumatic artificial muscle manipulator (PAM manipulator) due to the changes in the external inertia load with high speed.

In order to realize satisfactory control performance, a variable damper ? Magneto-Rheological Brake (MRB), is equipped to the joint of the manipulator. Superb mixture of conventional PID controller and a phase plane switching control method brings us a novel controller. This proposed controller is appropriate for a kind of plants with nonlinearity, uncertainties and disturbances. The experiments were carried out in practical PAM manipulator and the effectiveness of the proposed control algorithm was demonstrated through experiments, which had proved that the stability of the manipulator can be improved greatly in a high gain control by using MRB with phase plane switching control method and without regard for the changes of external inertia loads.

Key Words: Pneumatic artificial muscle, Magneto-Rheological brake, Phase plane switching control, Manipulator

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 3, pp. 792-801, 2005

Improvement of the Steering Feel of an Electric Power Steering System by Torque Map Modification

Man Hyung Lee*

School of Mechanical Engineering, Pusan National University, Busan, 609-735, Korea

Seong Ki Ha

Department of Interdisciplinary Program in Mechatronics, Pusan National University,

Busan, 609-735, Korea

Ju Yong Choi

Department of Mechanical and Intelligent Systems Engineering, Pusan National University,

Busan, 609-735, Korea

Kang Sup Yoon

School of Automative, Industrial and Mechanical Engineering, Daeku University,

Gyeongsan, 712-714, Korea

This paper discusses a dc motor equipped electric power steering (EPS) system and demonstrates its advantages over a typical hydraulic power steering (HPS) system. The tire-road interaction torque at the steering tires is calculated using the 2 d.o.f. bicycle model, in other words by using a single-track model, which was verified with the J-turn test of a real vehicle. Because the detail parameters of a steering system are not easily acquired, a simple system is modeled here. In previous EPS systems, the assisting torque for the measured driving torque is developed as a boost curve similar to that of the HPS system. To improve steering stiffness and return-ability of the steering system, a third-order polynomial as a torque map is introduced and modified within the preferred driving torques researched by Bertollini. Using the torque map modification sufficiently improves the EPS system.

Key words : Electric Power Steering, Assist Torque, Steering Feel, On-center Handling, Return-ability, Steering Stiffness

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 3, pp. 802-810, 2005

A Study of Deformation and Orientation Dependent Behavior in Single Crystals

Chulho Yang*

School of Mechanical Engineering, Andong National University,

388 Song chon-Dong, Andong, Kyungbuk 760-749, S. Korea

Deformations of single crystals were studied using finite element analysis to investigate the localized modes and the orientation dependence of plastic deformation observed in single crystals. Investigation of mechanical properties of single crystals is closely related with the understanding of deformation processes in single crystals. Localized bands such as shear and kink were studied and the material and geometric characteristics that influence the formation of such localized bands were investigated. Orientation dependence of material behavior in NiAl single crystals was studied by rotating slip directions from ‘hard’ orientation. The maximum nominal compressed stress in NiAl single crystals was widely ranged depending on the misalignment from ‘hard’ orientation. As the compression axis was set closer to ‘hard’ orientation, the maximum nominal compressed stress was rapidly increased and made <100> slips difficult to activate. Therefore, non-<100> slips will be activated instead of <100> slips for ‘hard’ orientation.

Key Words : Single Crystal, Localized Deformation, Orientation Dependence, FEA

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 3, pp. 811-819, 2005

A New Hybrid-Mixed Composite Laminated Curved Beam Element

Ho-Cheol Lee, Jin-Gon Kim*

School of Mechanical & Automotive Engineering, Catholic University of Daegu,

Hayang-up, Kyongsan-si, Kyongbuk, 712-702, Korea

In this study, we present a new efficient hybrid-mixed composite laminated curved beam element. The present element, which is based on the Hellinger-Reissner variational principle and the first-order shear deformation lamination theory, employs consistent stress parameters corresponding to cubic displacement polynomials with additional nodeless degrees in order to resolve the numerical difficulties due to the spurious constraints. The stress parameters are eliminated and the nodeless degrees are condensed out to obtain the (6x6) element stiffness matrix. The present study also incorporates the straightforward prediction of interlaminar stresses from equilibrium equations. Several numerical examples confirm the superior behavior of the present composite laminated curved beam element.

Key Words : Composite Laminated Curved Beam Element, Hybrid-Mixed Formulation, Interlaminar Stresses, First-order Shear Deformation Lamination Theory, Stress Parameters, Field Consistency

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 3, pp. 820-825, 2005

Non-Destructive Evaluation of Semiconductor Package by Electronic Speckle Pattern Interferometry

Koungsuk Kim

Department of Mechanical Design Engineering, Chosun University,

375 Seosuk-dong, Dong-gu, Gwangju 501-759, Korea

Kisoo Kang*

Department of Mechanical Design Engineering, Graduate School, Chosun University,

375 Seosuk-dong, Dong-gu, Gwangju 501-759, Korea

Seungtack Jung

Sairon Technology, Inc., 548-6 Oseon-Dong, Gwangsan-Gu, Gwangju 506-253, Korea

This paper proposes non-destructive ESPI technique to evaluate inside defects of semiconductor package quantitatively. Inspection system consists of ESPI system, thermal loading system and adiabatic chamber. The technique has high feasibility in non-destructive testing of semiconductor and gives solutions to the drawbacks in previous technique, time-consuming and the difficulty of quantitative evaluation. In result, most of defects are classified in delamination, from which it is inferred to the insufficiency of adhesive strength between layers and nonhomogeneous heat spread. The 90% of tested samples have a delamination defect started at the around of the chip which may be related to heat spread design.

Key Words: Electronic Speckle Pattern Interferometry(ESPI), Semiconductor, Non-Destructive Testing, Quantitative Evaluation

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 3, pp. 826-835, 2005

Evaluation on Interaction Surface of Plastic Resistance

for Exposed-type Steel Column Bases under Biaxial Bending

Jae-hyouk Choi*, Kenichi Ohi

Department of Architecture and Civil Engineering, Kobe University,

1-1Rokodai-cho,Nada-ku, Kobe, 657-8501, JAPAN

Exposed-type steel column bases are used widely in low-rise building construction. Numerous researchers have examined methods to identify their stiffness and strength, but those studies have heretofore been restricted to in-plane behaviors. This paper presents an experimental investigation of inelastic behaviors of square hollow section (SHS) steel column bases under biaxial bending. Two types of failure modes are considered: anchor bolt yielding and base plate yielding. Different pinching effects and interaction surfaces for biaxial bending are observed for these two modes during bi-directional quasi-static cyclic loading tests. Differences are elucidated using limit analyses based on a simple analytical model.

Keywords: Interaction surface, Biaxial bending, Limit analysis, Loading Path, Convex set

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 3, pp. 836-845, 2005

Significance of Hemodynamic Effects on the Generation of Atherosclerosis

Sang-Ho Suh*, Hyung-Woon Roh, Dong-Joo Kim

Dept. of Mech. Eng., Soongsil University, Seoul, Korea

Hyuck-Moon Kwon

Dept of Internal Medicine, College of Medicine, Yonsei Univ., Seoul, Korea

Byoung-Kwon Lee

Dept.of Internal Medicine, College of Medicine, Inje Univ., Seoul, Korea

Atherosclerosis, which is a degenerative vascular disease, is believed to occur in the blood vessels due to deposition of cholesterol or low density lipoprotein(LDL). Atherosclerotic lumen narrowing causes reduction of blood flow due to hemodynamic features. Several hypothetical theories related to the hemodynamic effects have been reported: high shear stress theory, low shear stress theory, high shear stress gradient theory, flow separation and turbulence theory, and high pressure theory. However, no one theory clearly explains the causes of atherosclerosis. The objective of the present study was to investigate the mechanism of the generation of atherosclerosis. In the study, the database of Korean carotid and coronary arteries for geometrical and hemodynamic clinical data was established. The atherosclerotic sites were predicted by the computer simulations. The results of the computer simulation were compared with the in vivo experimental results, and then the pathogenesis of atherosclerosis by using the clinical data and several hypothetical theories were investigated. From the investigation, it was concluded carefully that the mechanism of the generation of atherosclerosis was related to the hemodynamic effects such as flow separation and oscillatory wall shear stress on the vessel walls.

Key words: Atherosclerosis, Hemodynamic Hypotheses, Comparative Study, Hemodynamic characteristics, Vision technique, Computer Simulation

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 3, pp. 846-859, 2005

Fault Diagnosis of Rotating Machinery Based on Multi-Class Support Vector Machines

Bo-Suk Yang*, Tian Han, Won-Woo Hwang

School of Mechanical Engineering, Pukyong National University,

San 100, Yongdang-dong, Nam-gu, Busan 608-739, Korea

Support vector machines (SVMs) have become one of the most popular approaches to learning from examples and have many potential applications in science and engineering. However, their applications in fault diagnosis of rotating machinery are rather limited. Most of the published papers focus on some special fault diagnoses. This study covers the overall diagnosis procedures on most of the faults experienced in rotating machinery and examines the performance of different SVMs strategies. The excellent characteristics of SVMs are demonstrated by comparing the results obtained by artificial neural networks (ANNs) using vibration signals of a fault simulator.

Key Words: Fault Diagnosis, Support Vector Machine, Rotating Machinery, Multi-class Classification

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 3, pp. 860-869, 2005

Local Pool Boiling Coefficients on Horizontal Tubes

Myeong-Gie Kang*

Department of Mechanical Engineering Education, Andong National University,

388 Songchun-dong, Andong-city, Kyungbuk 760-749, Korea

Local pool boiling on the outside and inside surfaces of a 51 mm diameter tube in horizontal direction has been studied experimentally in saturated water at atmospheric pressure. Much variation in local heat transfer coefficients was observed along the tube periphery. On the outside surface the maximum and the minimum are observed at  =45° and 180°, respectively. However, on the inside surface only the minimum was observed at  =0°. Major mechanisms on the outside surface are liquid agitation and bubble coalescence while those on the inside surface are micro layer evaporation and liquid agitation. As the heat flux increases liquid agitation gets effective both on outside and inside surfaces. The local coefficients measured at  =90° can be recommended as the representative values of both outside and inside surfaces.

Key Words:  Pool Boiling, Annuli, Horizontal Tube, Heat Transfer

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 3, pp. 870-876, 2005

The Effect of Biodiesel and Ultra Low Sulfur Diesel Fuels

on Emissions in 11,000 cc Heavy-Duty Diesel Engine

Doo Sung Baik*, Young Chool Han

Graduate School of Automotive Engineering, Kookmin University,

861-1 Chongnung-dong, Songbuk-gu, Seoul, 136-702, Korea

It seems very difficult to comply with upcoming stringent emission standards in vehicles. To develop low emission engines, better quality of automotive fuels must be achieved.  Since sulfur contents in diesel fuels are transformed to sulfate-laden particulate matters as a catalyst is applied, it is necessary to provide low sulfur fuels before any Pt-based oxidation catalysts are applied. In general, flash point, distillation 90% and cetane index are improved but viscosity can be worse in the process of desulfurization of diesel fuel.  Excessive reduction of sulfur may cause to degrade viscosity of fuels and engine performance in fuel injection systems.  This research focused on the performance of  an 11,000cc diesel engine and emission characteristics by the introduction of ULSD, bio-diesel and a diesel oxidation catalyst, where the bio-diesel was used to improve viscosity of fuels in fuel injection systems as fuel additives or alternative fuels.

Key Words: ULSD (Ultra Low Sulfur Diesel), SOF (Soluble Organic Fraction), Sulfate, PM (Particulate Matter), DOC (Diesel Oxidation Catalyst), Cetane value, Distillation 90%, Pour point, Viscosity, B20 (Bio-diesel 20%), PAH (Polycle Aromatic Hydrocarbon)

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 3, pp. 877-886, 2005

Unsteady Viscous Flow over Elliptic Cylinders At Various Thickness with Different Reynolds Numbers

Moon-Sang Kim*

Associate Professor, School of Aerospace and Mechanical Engineering, Hankuk Aviation University,

Kyungki-Do, 412-791, Korea

Ayan Sengupta

Research Assistant, Department of Aerospace Engineering, Iowa State University, Ames, IA 50011, USA

Two-dimensional incompressible Navier-Stokes equations are solved using SIMPLER method in the intrinsic curvilinear coordinates system to study the unsteady viscous flow physics over two-dimensional ellipses. Unsteady viscous flows over various thickness-to-chord ratios of 0.6, 0.8, 1.0, and 1.2 elliptic cylinders are simulated at different Reynolds numbers of 200, 400, and 1,000. This study is focused on the understanding the effects of Reynolds number and elliptic cylinder thickness on the drag and lift forces. The present numerical solutions are compared with available experimental and numerical results and show a good agreement. Through this study, it is observed that the Reynolds number and the cylinder thickness affect significantly the frequencies of the force oscillations as well as the mean values and the amplitudes of the drag and lift forces.

Key Words : Unsteady Viscous Flow, Vortex Shedding, SIMPLER Method, Elliptic Cylinder, Navier-Stokes Equations

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 3, pp. 887-893, 2005

Optical Detection of Red Blood Cell Aggregation in a Disposable Microfluidic Channel

Sehyun Shin*, Ju-Hee Jang, Myung-Soo Park, Yunhee Ku

School of Mechanical Engineering, Kyungpook National University, Korea

Jnag-Soo Suh

Dept. of Laboratory Medicine, Kyungpook National University Hospital, Korea

The aggregability of red blood cells (RBCs) was determined by laser backscattering light analysis in a microfluidic channel. Available techniques for RBC aggregation often adopt a rotational Couette-flow using a bob-and-cup system for disaggregating RBCs, which causes the system to be complex and expensive. A disposable microfluidic channel and vibration generating mechanism were used in the proposed new detection system for RBC aggregation. Prior to measurement, RBC aggregates in a blood sample were completely disaggregated by the application of vibration-induced shear. With the present apparatus, the aggregation indexes of RBCs can be measured easily with small quantities of a blood sample. The measurements with the present aggregometer were compared with those of LORCA and the results showed a strong correlation between them. The aggregability of the defibrinogenated blood RBCs is markedly lower than that of the normal RBCs. The noble feature of this design is the vibration-induced disaggregation mechanism, which can incorporate the disposable element that holds the blood sample.

Keywords: aggregation, red blood cell, vibration, light, backscattering

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 3, pp. 894-904, 2005

Experimental Analysis of Flow inside Intake Heads of a Household Vacuum Cleaner

Daichin

Institute of Applied Mathematics and Mechanics, Shang Hai University, Shang Hai, 200072, China

Sang Joon Lee*

Dept. of Mechanical Engineering, Pohang University of Science and Technology,

Pohang, 790-784, Korea

The flow structure inside the intake head greatly affects the working efficiency of a vacuum cleaner such as suction power and aero-acoustic noise. In this study, the flow inside intake heads of a vacuum cleaner was investigated using qualitative flow visualization and quantitative PIV (Particle Image Velocimetry) techniques. The aerodynamic power, suction efficiency and noise level of the intake heads were also measured. In order to improve the performance of the vacuum cleaner, inner structure of the flow paths of the intake head, such as trench height and shape of connection chamber were modified. The flow structure of modified intake heads were compared with that of the original intake head. The aero-acoustic noise caused by flow separation was reduced and the suction efficiency was also changed due to flow path modification of intake head. In this paper, the variations of flow fields for different intake heads are presented and discussed together with results of aerodynamic power, suction efficiency and noise level.

Keywords: Vacuum Cleaner, Intake Head, Flow Structure, Suction Efficiency

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 3, pp. 905-912, 2005

Coronary Artery Numerical Flow Analysis for Determination of Bypass Graft Geometric Parameters

Kim, Hyung Min*

Division of Mechanical Design System Engineering, Kyonggi University,

San 94-6, Yiui-Dong, YoungTong-Ku, Suwon-Shi, Kyonggi-Do,442-760, Korea

Kim, Woong

Graduate School of Mechanical Engineering, Kyonggi University,

San 94-6, Yiui-Dong, YoungTong-Ku, Suwon-Shi, Kyonggi-Do,442-760, Korea

A computational investigation of blood flow in a coronary artery grafted by artificial bypass was performed to determine such geometric parameters as the curvature of radius, approach length, and angle of end-to-side anastomosis. Transient flow features in the host artery were computed using FVM and SIMPLE algorithms. We compared flow distributions and wall shear stresses in two simple models, planar and non-planar, and confirmed that the non-planar bypass model was more conducive to suppressing intimal hyperplasia. Our non-planar model with 60o of anastomosis and a 1.0 diameter approach length and radius of curvature predicts a relatively small, spatially-extended high-OSI (>0.01) zone, as well as an increased average wall shear stress on this zone.

Key Words: Coronary Artery, Bypass Graft, Oscillatory Shear Index, Computational Fluid Dynamics

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 3, pp. 913-923, 2005

On the Large Eddy Simulation of

Scalar Transport with Prandtl Number up to 10 Using Dynamic Mixed Model

Yang Na*

CAESIT, Department of Mechanical Engineering, Konkuk University, Seoul 143-701, Korea

The dynamic mixed model (DMM) combined with a box filter of Zang et. al. (1993) has been generalized for passive scalar transport and applied to large eddy simulation of turbulent channel flows with Prandtl number up to 10. Results from a priori test showed that DMM is capable of predicting both subgrid-scale (SGS) scalar flux and dissipation rather accurately for the Prandtl numbers considered. This would suggest that the favorable feature of DMM, originally developed for the velocity field, works equally well for scalar transport problem. The validity of the DMM has also been tested a posteriori. The results of the large eddy simulation showed that DMM is superior to the dynamic Smagorinsky model in the prediction of scalar field and the model performance of DMM depends to a lesser degree on the ratio of test to grid filter widths, unlike in the a priori test.

Key Words:  Temperature Field, Prandtl Number, Subgrid-scale Diffusivity, Large Eddy Simulation

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 4, pp. 927-935, 2005

On The Motion of the Structure Varying Multibody Systems with Two-Dimensional Dry Friction

Fujie Xia*

Faculty of Engineering and Physical Systems, Central Queensland University,

Rockhampton QLD 4702, Australia

Peter Wolfs, Colin Cole

Faculty of Engineering and Physical Systems, Central Queensland University,

Rockhampton QLD 4702, Australia

In the present paper the dynamics of the structure varying multibody systems caused by stick-slip motion with two-dimensional dry friction are analyzed. The methods to determine friction force both in stick and slip states are described. The direct method of considering the wagon bogie system as a structure varying system was used to consider two dimensional friction at the wheelset-side frame connection. The concept of friction direction angle used to determine the friction force components of two-dimensional dry friction both in the stick and slip motion states was used.  A speed depended friction coefficient was used and described approximately by hyperbolic secant function. All switch conditions were derived and friction forces both for stick and slip states. Some simulation results are provided.

Key Words : Multibody Syatem, Dry Friction, Structure Varying, Stick and Slip

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 4, pp. 936-946, 2005

Lubrication Effect of Liquid Nitrogen in Cryogenic Machining Friction on the Tool-chip Interface

Seong-Chan Jun*

Department of Mechanical Engineering, Columbia University, New York, NY 10027, USA

The liquid nitrogen as an environmentally safe coolant has been widely recognized in cryogenic machining, its function as a lubricant is plausible due to its chemical inertness, physical volatility and low viscosity. Since a reduced friction is a direct witness of the lubrication effect from a tribological viewpoint, this paper presents an evaluation of the apparent friction coefficient on the tool-chip interface in cryogenic cutting operations to prove and characterize the lubricity of LN2 in cryogenic machining. The cryogenic cutting technology used in this study is based on a cooling approach and liquid nitrogen delivery system which are intended to apply liquid nitrogen in well-controlled fine jets to selectively localized cutting zones and to penetrate liquid nitrogen to the tool-chip interface. It has been found that the apparent friction coefficient can be significantly reduced in cryogenic machining, depending on the approach of liquid nitrogen delivery.

Key Words : Tool Wear, Tool Life, Cryogenic Machining

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 4, pp. 947-957, 2005

Modelling of Low Velocity Impact Damage in Laminated Composites

Jounghwan Lee

Researcher, Graduate School of Aerospace Engineering, The University of Sheffield, U.K.

Changduk Kong*

Professor, Department of Aerospace Engineering, Chosun University, Kwangju 501-759, Korea

Costas Soutis

Professor, Aerospace Engineering, The University of Sheffield, U.K.

In this study a simple model is developed that predicts impact damage in a composite laminate avoiding the need of the time-consuming dynamic finite element method (FEM). The analytical model uses a non-linear approximation method (Rayleigh-Ritz) and the large deflection plate theory to predict the number of failed plies and damage area in a quasi-isotropic composite circular plate (axisymmetric problem) due to a point impact load at its centre. It is assumed that the deformation due to a static transverse load is similar to that occurred in a low velocity impact. It is found that the model, despite its simplicity, is in good agreement with FEM predictions and experimental data for the deflection of the composite plate and gives a good estimate of the number of failed plies due to fibre breakage. The predicted damage zone could be used with a fracture mechanics model developed by the second investigator and co-workers to calculate the compression after impact strength of such laminates. This approach could save significant running time when compared to FEM solutions.

Key Worlds: Low Velocity Impact Model, Non-linear Approximation Method, Composite Laminate, Compression After Impact Strength

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 4, pp. 958-967, 2005

Strip Tension Control Considering the temperature Change in Multi-Span Systems

Chang Woo Lee

Department of Mechanical Engineering, Konkuk University,

1 Hwayang-Dong, Gwangjin-Gu, Seoul 143-701, Korea

Kee Hyun Shin*

Department of Mechanical and Aerospace Engineering, Konkuk University,

1 Hwayang-Dong, Gwangjin-Gu, Seoul 143-701, Korea

The mathematical model for tension behaviors of a moving web by Shin (Shin, 2000) is extended to the tension model considering the thermal strain due to temperature variation in furnace. The extended model includes the terms that take into account the effect of the change of the Young’s Modulus, the thermal coefficient, and the thermal strain on the variation of strip tension. Computer simulation study proved that the extended tension model could be used to analyze tension behaviors even when the strip goes through temperature variation. By using the extended tension model, a new tension control method is suggested in this paper. The key factors of suggested tension control method include that the thermal strain of strip could be compensated by using the velocity adjustment of the helper-rollers. The computer simulation was carried out to confirm the performance of the suggested tension control method. Simulation results show that the suggested tension control logic not only overcomes the problem of the traditional tension control logic, but also improves the performance of tension control in a furnace of the CAL (Continuous Annealing Line).

Keywords: Temperature Change, Tension Control, Thermal Coefficient, Thermal Strain

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 4, pp. 968-975, 2005

Burr Control in Meso-Punching Process

Hong Gue Shin, Young Seung Shin, Byeong Hee Kim*, Heon Young Kim

Division of Mechanical Engineering and Mechatronics,

Kangwon National University, 192-1, Hyoja-dong, Chunchon, Gangwon, 200-701, Korea

The shearing process for the sheet metal is normally used in the precision elements such as semi-conductor components. In these precision elements, the burr formation brings a bad effect on the system assembly and demands the additional de-burring process, so this imposes high cost on manufacturing. In this paper, we have developed the in-situ auto-aligning precision meso-punching system to investigate the burr formation mechanism and ultimately minimize burr. Firstly, we introduced the punch-die contact sensing method to align the punch and the die at initial state prior to the punching process. Secondly, by using the low-price semi-conductor laser, burr formed on the edges is measured intermittently during the punching process. We could, finally, make burr on the sheet metal uniformized and minimized by controlling of the precision X-Y table, 1mm resolution, and measuring burr height by semiconductor laser. Experimental results show the validity of our system for pursuing the burr-free punched elements.

Key Words : Alignment, Burr, Laser Measurement, Meso-Punching

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 4, pp. 976-984, 2005

Dynamics in Carom and three cushion billiards

Inhwan Han*

Department of Mechano-Informatics & Design Engineering, Hongik University,

Jochiwon, Choongnam 339-701, Korea

This paper presents the analysis results of dynamics in the billiards game within the framework of rigid-body mechanics and a numerical simulation program. The friction exists between the ball and the table bed as well as between the ball and the rail. There are three parts in the dynamic behavior of the ball on the table bed; motion of the ball on the table bed, collision between balls, and collision between the ball and the cushion. During the development of the simulation program, the dynamics problems such as rolling motion and three-dimensional frictional impact motion have been analyzed in detail. The theoretical issues are implemented into a viable graphic simulation program and its efficacy is demonstrated through the experimental validation of the billiards game. The resulting analysis results are verified quantitatively and qualitatively using high-speed video camera. Through the experimental tests, it was found that the physical parameters such as coefficients of restitution and friction vary according to the motion variables and corresponding empirical formulations were developed. The simulation and experimental results agree well.

Key Words: Billiards, Rigid-Body Mechanics, Friction, Impact

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 4, pp. 985-992, 2005

Side Slip Angle Based Control Threshold of Vehicle Stability Control System

Taeyoung Chung

PhD Candidate, Automotive Engineering, Hanyang University,

17 Haengdang-dong, Seongdong-gu, Seoul, 133-791, Korea

Kyongsu Yi*

Professor, School of Mechanical Engineering, Hanyang University,

17 Haengdang-dong, Seongdong-gu, Seoul, 133-791, Korea.

Vehicle Stability Control (VSC) system prevents vehicle from spinning or drifting out mainly by braking intervention. Although a control threshold of conventional VSC is designed by vehicle characteristics and centered on average drivers, it can be a redundancy to expert drivers in critical driving conditions. In this study, a manual adaptation of VSC is investigated by changing the control threshold. A control threshold can be determined by phase plane analysis of side slip angle and angular velocity which is established with various vehicle speeds and steering angles. Since vehicle side slip angle is impossible to be obtained by commercially available sensors, a side slip angle is designed and evaluated with test results. By using the estimated value, phase plane analysis is applied to determine control threshold. To evaluate an effect of control threshold, we applied a 23-DOF vehicle nonlinear model with a vehicle planar motion model based sliding controller. Controller gains are tuned as the control threshold changed. A VSC with various control thresholds makes VSC more flexible with respect to individual driver characteristics.

Key words: Vehicle Stability Control (VSC) System, Control Threshold, Side Slip Angle Estimator, Phase Plane Analysis

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 4, pp. 993-1000, 2005

A Vehicle Stop-and-Go Control Strategy based on Human Drivers Driving Characteristics

Kyongsu Yi*

School of Mechanical Engineering, Hanyang University, Seoul, 133-791, KOREA

Donghoon Han

Department of Automotive Engineering, Hanyang University, Seoul, 133-791, KOREA

A vehicle cruise control strategy designed based on human drivers driving characteristics has been investigated. Human drivers driving patterns have been investigated using vehicle driving test data obtained from 125 participants. The control algorithm has been designed to incorporate the driving characteristics of the human drivers and to achieve natural vehicle behavior of the controlled vehicle that would feel comfortable to the human driver. Vehicle following characteristics of the cruise controlled vehicle have been investigated using real-world vehicle driving test data and a validated simulation package.

Keywords: Stop-and-Go, Adaptive Cruise Control, Human Driver, Clearance, Time Gap, Time to Collision, Vehicle

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 4, pp. 1001-1005, 2005

Measurement of Indoor Air Quality for Ventilation with the Existence of Occupants in Schools

Hee-Soo Shin*, Jai-Kwon Lee, Young-Chull Ahn, Chang-Shin Yeo, Sang-Hyun Byun, Jae-Keun Lee

Department of Mechanical Engineering, Pusan National University,

San 30, Jangjeon-Dong, Kumjeong-Ku, Busan, 609-735, Korea

Tae-Wook Kang, Kam-Gyu Lee

Air Conditioner Division, LG Electronics, 76, Seongsan-Dong, Changwon, 641-713, Korea

Hyo-Soon Park

Building Energy Research Team, Korea Institute of Energy Research (KIER),

71-2 Jang-Dong, Yuseong-Ku, Daejeon, 305-343, Korea

This paper evaluates the performance of ventilation for the removal of indoor pollutants as a function of ventilation rate and the number of occupants in a test room and school classroom.  An experimental apparatus consists of a test room, a tracer gas supply system, a gas detector, and a fan for ventilation air supply with a controller.  The ventilation performance is evaluated in a step-down method based on ASTM Standard E741-83 using CO2 gas as a tracer gas in the test room of 35 m3.  For the ventilation air flow rate of 1.0 ACH, a recommended ventilation flow rate of Korea school standard for acceptable indoor air quality in the case of one person, CO2 gas concentration decreases up to 55% within 50 minutes without occupancy and increases up to 75% in the case of one occupant.  Also indoor air quality at the school classroom is investigated experimentally.

Key Words: Indoor Air Quality, Ventilation, School Ventilation

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 4, pp. 1006-1017, 2005

Parallelized Unstructured-Grid Finite Volume Method for Modeling Radiative Heat Transfer

Gunhong Kim, Seokgwon Kim, Yongmo Kim*

Department of Mechanical Engineering, Hanyang University, Seoul 133-791, Korea

In this work, we developed an accurate and efficient radiative finite volume method applicable for the complex 2D planar and 3D geometries using an unstructured-grid finite volume method. The present numerical model has fully been validated by several benchmark cases including the radiative heat transfer in quadrilateral enclosure with isothermal medium, tetrahedral enclosure, a three-dimensional idealized furnace, as well as convection-coupled radiative heat transfer in a square enclosure. The numerical results for all cases are well agreed with the previous results. Special emphasis is given to the parallelization of the unstructured-grid radiative FVM using the domain decomposition approach. Numerical results indicate that the present parallel unstructured-grid FVM has the good performance in terms of accuracy, geometric flexibility, and computational efficiency.

Key Words : Radiative Heat Transfer, Unstructured-Grid Finite Volume Method, Parallel Algorithm

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 4, pp. 1018-1026, 2005

Effects of Key Operating Parameters on the Efficiency of Two Types of

PEM Fuel Cell Systems (High-Pressure and Low-Pressure Operating) for Automotive Applications

Han-Sang Kim, Dong-Hun Lee, Kyoungdoug Min*, Minsoo Kim

School of Mechanical and Aerospace Engineering, Seoul National University,

San 56-1, Shinlim-dong, Kwanak-gu, Seoul 151-742, Korea

The proton exchange membrane (PEM) fuel cell system consisting of stack and balance of plant (BOP) was modeled in a MATLAB/Simulink environment. High-pressure operating (compressor type) and low-pressure operating (air blower type) fuel cell systems were considered. The effects of two main operating parameters (humidity and the pressure of the supplied gas) on the power distribution characteristics of BOP and the net system efficiency of the two systems mentioned above were compared and discussed. The simulation determines an optimum condition regarding parameters such as the cathode air pressure and the relative humidity for maximum net system efficiency for the operating fuel cell systems. This study contributes to get a basic insight into the fuel cell stack and BOP component sizing. Further research using multi-object variable optimization packages and the approach developed by this study can effectively contribute to an operating strategy for the practical use of fuel cell systems for vehicles.

Keywords : PEM fuel cell, Fuel cell system, BOP, High-pressure operating, Low-pressure operating, Net system efficiency, Component sizing

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 4, pp. 1027-1035, 2005

Thermophoresis in Dense Gases: a Study by Born-Green-Yvon Equation

Minsub Han*

Micro Thermal Research Center, Seoul National University, Seoul 151-742, Korea

Thermophoresis in dense gases is studied by using a multi-scale approach and Born-Yvon-Green (BYG) equation. The problem of a particle movement in an ambient dense gas under temperature gradient is divided into inter and outer ones. The pressure gradient in the inner region is obtained from the solutions of BYG equation. The velocity profile is derived from the conservation equations and calculated using the pressure gradient, which provides the particle velocity in the outer problem. It is shown that the temperature gradient applied to the quiescent ambient gas induces some pressure gradient and thus flow tangential to the particle surface in the interfacial region. The mechanism that induces the flow may be the dominant source of the thermophretic particle movement in dense gases. It is also shown that the particle velocity has a nonlinear relationship with the applied temperature gradient and decreases with increasing temperature.

Key Words : Colloid, YBG Equation, Thermoosmosis

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 4, pp. 1036-1043, 2005

An Experimental Study on the Thermal Performance of a Concentric Annular Heat Pipe

Joon Hong Boo*, Soo Yong Park

School of Aerospace and Mechanical Engineering, Hankuk Aviation University,

200-1, Hwajeon-dong, Deogyang-gu, Goyang-city, Gyeonggi-do, 412-791, Korea

Do Hyoung Kim

EWIC Co., Ltd., 7-1, Majang-ri, Gwangtan-myun, Paju-city, Gyeonggi-do, 413-851, Korea

Concentric annular heat pipes (CAHP) were fabricated and tested to investigate their thermal characteristics. The CAHPs were 25.4mm in outer diameter and 200mm in length. The inner surface of the heat pipes was covered with screen mesh wicks and they were connected by four bridge wicks to provide liquid return path. Three different heat pipes were fabricated to observe the effect of change in diameter ratios between 2.31 and 4.23 while using the same outer tube dimensions. The major concern of this study was the transient response as well as isothermal characteristics of the heat pipe outer surface, considering the application as uniform heating device. A better performance was achieved as the diameter ratio increased. For the thermal load of 180 W, the maximum temperature difference on the outer surface in the axial direction of CAHP was 2.3℃ while that of the copper block of the same outer dimension was 5.9℃. The minimum thermal resistance of the CAHP was measured to be 0.04℃/W. In regard to the transient response during start-up, the heat pipe showed almost no time lag to the heat source, while the copper block of the same outer dimensions exhibited about 25 min time lag.

Key Words : Concentric annular heat pipe, diameter ratio, fill charge ratio, start-up characteristics, isothermal characteristics

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 4, pp. 1044-1051, 2005

Isothermal Characteristics of a Rectangular Parallelepiped Sodium Heat Pipe

Joon Hong Boo*, Soo Yong Park

School of Aerospace and Mechanical Engineering, Hankuk Aviation University,

200-1, Hwajeon-dong, Deogyang-gu, Goyang-city, Gyeonggi-do, 412-791, Korea

The isothermal characteristics of a rectangular parallelepiped sodium heat pipe were investigated for high- temperature applications. The heat pipes was made of stainless steel of which the dimension was 140mm (L) x 95mm (W) x 46mm (H) and the thickness of the container was 5mm. Both inner surfaces of evaporator and condenser were covered with screen meshes to help spread of the liquid state working fluid. To provide additional path for the working fluid, a lattice structure covered with screen mesh was inserted in the heat pipe with simple screen mesh wick. The bottom surface of the heat pipe was heated by an electric heater and the top surface was cooled by circulating coolant. The concern in this study was to enhance the temperature uniformity at the bottom surface of the heat pipe while an uneven heat source up to 900W was in contact. The temperature distribution over the bottom surface was monitored at more than twenty six locations. It was found that the operating performance of the sodium heat pipe was critically affected by the inner wall temperature of the condenser region where the working fluid may be changed to a solid phase unless the temperature is higher than its melting point. The maximum temperature difference across the bottom surface was observed to be 114℃ for 850W thermal load and 100℃ coolant inlet temperature. The effects of fill charge ratio, coolant inlet temperature and operating temperature on thermal performance of heat pipe were analyzed and discussed.

Key Words : Sodium heat pipe, liquid metal, rectangular parallelepiped, isothermal characteristics, thermal performance, high temperature application

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 4, pp. 1052-1061, 2005

Experimental Study on the Thermal Performance of

a Small-scale Loop Heat Pipe with Polypropylene Wick

Joon Hong Boo*, Won Bok Chung

School of Aerospace and Mechanical Engineering, Hankuk Aviation University,

200-1, Hwajeon-dong, Deogyang-gu, Goyang-city, Gyeonggi-do, 412-791, KOREA

A small-scale loop heat pipe (LHP) with polypropylene wick was fabricated and tested for investigation of its thermal performance. The container and tubing of the system were made of stainless steel and several working fluids were tested including methanol, ethanol, and acetone. The heating area was 35 mm x 35 mm and nine axial grooves were provided in the evaporator to provide vapor passages. The pore size of the polypropylene wick inside the evaporator was varied from 0.5 mm to 25 mm. The inner diameter of liquid and vapor transport lines were 2.0 mm and 4.0 mm, respectively and the length of which were 0.5 m. The size of condenser was 40 mm (W) x 50 mm (L) in which ten coolant paths were provided. Start-up characteristics as well as steady-state performance was analyzed and discussed. The minimum thermal load of 10 W (0.8 W/cm2) and maximum thermal load of 80 W (6.5 W/cm2) were achieved using methanol as working fluid with the condenser temperature of 20°C with horizontal position.

Key Words: Loop heat pipe, polypropylene wick, heat transport limit, start-up characteristics

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 5, pp. 1065-1071, 2005

Prediction of Residual Stress Distribution in Multi-Stacked

Thin Film by Curvature Measurement and Iterative FEA

Hyeon Chang Choi

Department of Mechatronics Engineering, College of Engineering,

Tongmyong University of Information Technology, 535 Yongdang-dong, Nam-gu, Busan 608-711, Korea

Jun-Hyub Park*

Department of Mechatronics Engineering, College of Engineering,

Tongmyong University of Information Technology, 535 Yongdang-dong, Nam-gu, Busan 608-711, Korea

In this study, residual stress distribution in multi-stacked film by MEMS(Micro-Electro Mechanical System) process is predicted using Finite Element method(FEM). We develop a finite element program for residual stress analysis(RESA) in multi-stacked film. The RESA predicts the distribution of residual stress field in multi-stacked film. Curvatures of multi-stacked film and single layers which consist of the multi-stacked film are used as the input to the RESA. To measure those curvatures is easier than to measure a distribution of residual stress. To verify the RESA, mean stresses and stress gradients of single and multilayers are measured. The mean stresses are calculated from curvatures of deposited wafer by using Stoney’s equation. The stress gradients are calculated from the vertical deflection at the end of cantilever beam. To measure the mean stress of each layer in multi-stacked film, we measure the curvature of wafer with the left film after etching layer by layer in multi-stacked film.

Key words: MEMS, Residual Stress, Stress Distribution, Multi-Stacked Film, Stress Gradient

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 5, pp. 1072-1079, 2005

Concept Optimization for Mechanical Product Using Genetic Algorithm

Hong-Zhong Huang*

School of Mechatronics Engineering, University of Electronic Science and Technology of China,

Chengdu, Sichuan 610054, P.R. China

Rui-Feng Bo

School of Mechanical Engineering, Dalian University of Technology,

Dalian, Liaoning 116023, P.R. China

Xiang-Feng Fan

Department of Mechanical Engineering, University of Albert, Edmonton, Albert, T6G 2G8, Canada

Conceptual design is the first step in the overall process of product design. Its intrinsic uncertainty, imprecision, and lack of information lead to the fact that current conceptual design activities in engineering have not been computerized and very few CAD systems are available to support conceptual design. In most of the current intelligent design systems, approach of principle synthesis, such as morphology matrix, bond graphic, or design catalogues, is usually adopted to deal with the concept generation, in which optional concepts are generally combined and enumerated through function analysis. However, as a large number of concepts are generated, it is difficult to evaluate and optimize these design candidates using regular algorithm. It is necessary to develop a new approach or a tool to solve the concept generation. Generally speaking, concept generation is a problem of concept synthesis. In substance, this process of developing design candidate is a combinatorial optimization process, viz., the process of concept generation can be regarded as a solution for a state-place composed of multi-concepts. In this paper, genetic algorithm is utilized as a feasible tool to solve the problem of combinatorial optimization in concept generation, in which the encoding method of morphology matrix based on function analysis is applied, and a sequence of optimal concepts are generated through the search and iterative process which is controlled by genetic operators, including selection, crossover, mutation, and reproduction in GA. Several crucial problems on GA are discussed in this paper, such as the calculation of fitness value and the criteria for heredity termination, which have a heavy effect on selection of better concepts. The feasibility and intellectualization of the proposed approach are demonstrated with an engineering case. In this work concept generation is implemented using GA, which can facilitate not only generating several better concepts, but also selecting the best concept. Thus optimal concepts can be conveniently developed and design efficiency can be greatly improved.

Key words: Conceptual Design, Genetic Algorithm, Optimization, Concept Generation, intelligence

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 5, pp. 1080-1086, 2005

Multiobjective Optimization of Three-Stage Spur Gear Reduction

Units Using Interactive Physical Programming

Hong-Zhong Huang*

School of Mechatronics Engineering, University of Electronic Science and Technology of China,

Chengdu, Sichuan 610054, P.R. China

Zhi-Gang Tian, Ming J. Zuo

Department of Mechanical Engineering, University of Alberta, Edmonton, Alberta, T6G 2G8, Canada

The preliminary design optimization of multi-stage spur gear reduction units has been a subject of considerable interest, since many high-performance power transmission applications (e.g., automotive and aerospace) require high-performance gear reduction units. There are multiple objectives in the optimal design of multi-stage spur gear reduction unit, such as minimizing the volume and maximizing the surface fatigue life. It is reasonable to formulate the design of spur gear reduction unit as a multi-objective optimization problem, and find an appropriate approach to solve it. In this paper an interactive physical programming approach is developed to place physical programming into an interactive framework in a natural way. Class functions, which are used to represent the designer’s preferences on design objectives, are fixed during the interactive physical programming procedure. After a Pareto solution is generated, a preference offset is added into the class function of each objective based on whether the designer would like to improve this objective or sacrifice the objective so as to improve other objectives. The preference offsets are adjusted during the interactive physical programming procedure, and an optimal solution that satisfies the designer’s preferences is supposed to be obtained by the end of the procedure. An optimization problem of three-stage spur gear reduction unit is given to illustrate the effectiveness of the proposed approach.

Key words: Interactive Physical Programming, Physical Programming, Multiobjective Optimization, Three-Stage Spur Gear Reduction Unit, Preference

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 5, pp. 1087-1094, 2005

Thin-Shell Approach for Elastic Wave Propagation in a Pipe with Liquid

Jin Oh Kim*

Department of Mechanical Engineering, Soongsil University, Seoul 156-743, Korea

Joseph L. Rose

Department of Engineering Science & Mechanics, The Pennsylvania State University,

University Park, Pennsylvania 16802, U.S.A.

This paper presents the validity and limitation of the thin-shell approach for the analysis of elastic wave propagation in a pipe with nonviscous liquid. The phase velocities calculated by the thin-shell approach were compared with those calculated by the thick-cylinder approach. In contrast to the case of the empty pipe, where only two modes were obtained and the first mode was calculated in a limited frequency range, the results for the liquid-filled pipe exhibits a large number of modes due to the large number of branches of the apparent liquid mass. Several of the lowest modes of the waves in a liquid-filled pipe were calculated for various pipe thicknesses in a low frequency range. The thin-shell approach was valid for a reasonable range of pipe thicknesses.

Key Words : Elastic Wave, Axisymmetric Mode, Phase Velocity, Frequency, Shell, Pipe

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 5, pp. 1095-1106, 2005

CNC-implemented Fault Diagnosis and Web-based Remote Services

Dong-Hoon Kim*

Department of Intelligence & Precision Machines, Korea Institute of Machinery & Materials (KIMM),

Daejeon 305-343, Korea

Sun-Ho Kim

Department of Mechatronics Engineering, Dong-Eui University, Pusan 614-714, Korea

Kwang-Sik Koh

School of Electrical Engineering and Computer Science, Kyungpook National University,

Daegu 702-701, Korea

Recently, the conventional controller of machine-tool has been increasingly replaced by the PC-based open architecture controller, which is independent of the CNC vendor and on which it is possible to implement user-defined application programs. This paper proposes CNC-implemented fault diagnosis and web-based remote services for machine-tool with open architecture CNC. The faults of CNC machine-tool are defined as the operational faults occupied by over 70% of all faults. The operational faults are unpredictable as they occur without any warning. Two diagnostic models, the switching function and the step switching function, were proposed in order to diagnose faults efficiently. The faults were automatically diagnosed through the fault diagnosis system using the two diagnostic models. A suitable interface environment between CNC and developed application modules was constructed for the internal function of CNC. In addition, a suitable web environment was constructed for remote services. The web service functions, such as remote monitoring and remote control, were implemented, and their operability was tested through the web. The results obtained through this research could be a model of fault diagnosis and remote servicing for machine-tool with open architecture CNC.

Keywords: open architecture controller, CNC, fault diagnosis, remote services

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 5, pp. 1107-1115, 2005

Simultaneous Trajectory Tracking Control of Position and Force

with Pneumatic Cylinder Driving Apparatus

Ji-Seong Jang*

Division of Mechanical Engineering, Pukyong National University,

San 100, Yongdang-Dong, Nam-Gu, Busan 608-739, Korea

In this study, a position and force simultaneous trajectory tracking control algorithm is proposed for a driving apparatus that consists of two pneumatic cylinders connected in series. The controller applied to the driving apparatus is composed of a non-interaction controller to compensate for interaction between cylinders and a disturbance observer aimed to reduce the effect of model discrepancy that cannot be compensated by the non-interaction controller. The effectiveness of the proposed control algorithm is proved by experimental results.

Keywords: Compressibility, Low Stiffness, Pneumatic Cylinder, Position and Force Trajectory Tracking

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 5, pp. 1116-1122, 2005

Finite Element Analysis of Laser-Generated Ultrasound for Characterizing Surface-Breaking Cracks

Hyunjo Jeong*

Division of Mechanical and Automobile Engineering, Wonkwang University,

344-2 Sinyong-Dong, Iksan, Jeonbuk 570-749, Korea

A finite element method was used to simulate the wave propagation of laser-generated ultrasound and its interaction with surface breaking cracks in an elastic material. Thermoelastic laser line source on the material surface was approximated as a shear dipole and loaded as nodal forces in the plane-strain finite element (FE) model. The shear dipole-FE model was tested for the generation of ultrasound on the surface with no defect. The model was found to generate the Rayleigh surface wave. The model was then extended to examine the interaction of laser generated ultrasound with surface-breaking cracks of various depths. The crack-scattered waves were monitored to size the crack depth. The proposed model clearly reproduced the experimentally observed features that can be used to characterize the presence of surface-breaking cracks.

Key Words : Finite Clcment Analysis, Laser-Generated Ultrasound, Surface-Breaking Crack, Rayleigh Surface Wave, Shear Dipole Model, Crack Sizing

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 5, pp. 1123-1130, 2005

Petri Nets Based Coordination Component for CSCW Environment

Hong-Zhong Huang*

School of Mechatronics Engineering, University of Electronic Science and Technology of China,

Chengdu, Sichuan 610054, P.R. China

Feng Zhou, Xu Zu

School of Mechanical Engineering, Dalian University of Technology,

Dalian, Liaoning 116023, P.R. China

In view of the lack of efficient coordination of interdependent task in the collaborative design system, the mechanisms for temporal and resource coordination problems are established based on Petri Nets, respectively. Both of the mechanisms are encapsulated and implemented in the coordination component so as to increase the flexibility and acceptability of the system. We model the CSCW system based on Petri Nets for simulation, analysis and optimization. A case study on the overhead traveling crane is given to demonstrate and validate our theory.

Key words : CSCW, Coordination Mechanism, Temporal Interdependencies, Resource Management, Coordination Component

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 5, pp. 1131-1137, 2005

A Robust Algorithm for Roughness Laser Measurement based on

Light Power Regulation against Specimen Changes

Young-Ho Seo*

Graduate school, Department of Mechanical and Intelligent Systems Engineering,

Pusan National University, San30 Jangjeon-Dong, Keumjeong-Gu, Pusan, 609-735, Korea

Jung-Hwan Ahn

ERC/NSDM, Professor, School of Mechanical Engineering, Pusan National University,

San30 Jangjeon-Dong, Keumjeong-Gu, Pusan, 609-735, Korea

Methods for measuring surface roughness based on light reflectivity have advantages over methods based on light interference or diffraction, especially in in-situ, on-the-machine and in-process applications. However, measurement inconsistencies caused by changes in the specimen are still a drawback for field applications. In this study, we propose a new feedback-based algorithm to enhance the consistency against changes in the specimen. The algorithm is deduced from simulations based on light reflectance theory with typical modeled surfaces. The proposed method is similar to a digital controller and regulates the power of reflected light. Experiments varying heights and materials, verified the improvements in robustness of the method against measurement disturbances caused by specimen changes.

Keywords: Surface roughness, Reflected laser beam, Measurement robustness, Power regulating, Feedback control, Specimen changes

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 5, pp. 1138-1147, 2005

Analytical Development of a Robust Controller for Smart Structural Systems

Chul Hue Park*, Seong Il Hong and Hyun Chul Park

Department of Mechanical Engineering, Pohang University of Science and Technology (POSTECH),

Pohang, KyungBuk, 790-784, Korea

This paper aims at demonstrating the feasibility of active control of beams with a multiobjective state-feedback control technique.  The multiobjective state-feedback controller is designed on a linear matrix inequality (LMI) approach for the multiobjective synthesis.  The design objectives are to achieve a mix of H￥ performance and H2 performance satisfying constraints on the closed-loop pole locations in the face of model uncertainties.  The controller is also designed to reject the effects of the noise and external of disturbances.  For the theoretical analysis, the governing equation of motion is derived by Hamilton’s principle to describe the dynamics of a smart structural system.  Numerical examples are presented to demonstrate the effectiveness of the integrated robust controller in damping out the multiple vibration modes of the piezo/beam system.

Key word : Linear Matrix Inequality, Multiobjective State-feedback Control, Robust Control, Smart Structure System

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 5, pp. 1148-1157, 2005

The Effect of Suction and Injection on Unsteady Flow

of a Dusty Conducting Fluid in Rectangular Channel

Hazem Ali Attia*

Department of Mathematics, College of Science, Al-Qasseem University,

P.O. Box 237, Buraidah 81999, Kingdom of Saudi Arabia

In the present study, the unsteady Hartmann flow of a dusty viscous incompressible electrically conducting fluid under the influence of an exponentially decreasing pressure gradient is studied without neglecting the ion slip.  The parallel plates are assumed to be porous and subjected to a uniform suction from above and injection from below.  The fluid is acted upon by an external uniform magnetic field which is applied perpendicular to the plates.  An analytical solution for the governing equations of motion is obtained to yield the velocity distributions for both the fluid and dust particles.

Keywords ; Fluid mechanics, magnetofluid mechanics, two phase flow, dust particles, Hall current, ion slip

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 5, pp. 1158-1168, 2005

Computational Study on the Hemodynamics of the Bypass Shunt

Directly Connecting the Left Ventricle to a Coronary Artery

Eun Bo Shim*

Department of Mechanical Engineering, Kangwon National University,

Hyoja-Dong, Chucheon, Kangwon-Do 200-701, Republic of Korea

Byung Jun Lee

The Research Institute of Mechanical Technology, Pusan National University,

Jangjeon-Dong, Geumjeong-Gu, Busan 609-735, Republic of Korea

Hyung Jong Ko

Department of Mechanical Engineering, Kumoh National Institute of Technology,

Shinpyung-Dong, Kumi, Kyungbuk 730-701, Republic of Korea

A shunt from the left ventricle to the left anterior descending artery is being developed for coronary artery occlusive disease, in which the shunt or conduit connects the the left ventricle (LV) with the diseased artery directly at a point distal to the obstruction.  To aid in assessing and optimizing its benefit, a computational model of the cardiovascular system was developed and used to explore various design conditions.  Computational fluid dynamic analysis for the shunt hemodynamics was also done using a commercial finite element package. Simulation results indicate that in complete left anterior descending artery (LAD) occlusion, flow can be returned to approximately 65% of normal, if the conduit resistance is equal for forward and reverse flow.  The net coronary flow can increase to 80% when the backflow resistance is infinite.  The increases in flow rate produced by asymmetric flow resistance are enhanced considerably for a partial LAD obstruction, since the primary effect of resistance asymmetry is to prevent leakage back into the ventricle during diastole.  Increased arterial compliance has little effect on net flow with a symmetric shunt, but considerably augments it when the resistance is asymmetric.  The computational results suggest that an LV-LAD conduit will be beneficial when the resistance due to artery stenosis exceeds 27 PRU, if the resistance is symmetric. Fluid dynamic simulations for the shunt flow show that a recirculating region generated near the junction of the coronary artery with the bypass shunt. Secondary flow is induced in the cross-sectional plane perpendicular to the axis of the artery and is progressively attenuated downstream.

Keywords: Computational model, Coronary circulation, LV-LAD bypass shunt, Lumped parameter model, Device efficiency

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 5, pp. 1169-1181, 2005

Study on the Unsteady Wakes Past a Square Cylinder near a Wall

Tae-yoon Kim

School of Mechanical and Aerospace Engineering in Seoul National University, Seoul, Korea

Bo-sung Lee

Korea Institute of Science and Technology Information, Daejeon, Korea

Dong-ho Lee*

School of Mechanical and Aerospace Engineering in Seoul National University, Seoul, Korea

Experimental and numerical studies on the unsteady wake field behind a square cylinder near a wall were conducted to find out how the vortex shedding mechanism is correlated with gap flow. The computations were performed by solving unsteady 2-D Incompressible Reynolds Averaged Navier-Stokes equations with a newly developed e-SST turbulence model for more accurate prediction of large separated flows. Through spectral analysis and the smoke wire flow visualization, it was discovered that velocity profiles in a gap region have strong influences on the formation of vortex shedding behind a square cylinder near a wall. From these results, Strouhal number distributions could be found, where the transition region of the Strouhal number was at G/D=0.5~0.7 above the critical gap height. The primary and minor shedding frequencies measured in this region were affected by the interaction between the upper and the lower separated shear layer, and minor shedding frequency was due to the separation bubble on the wall. It was also observed that the position (y/G) and the magnitude of maximum average velocity (u/u∞) in the gap region affect the regular vortex shedding as the gap height increases.

Key Words : Shedding frequency, Separated Shear Layer, Separation Bubble, Vortex Shedding

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 5, pp. 1182-1193, 2005

An Investigation of Downcomer Boiling Effects During Reflood Phase Using TRAC-M Code

Woochong Chon*, Jae-Hoon Lee, Sang-Jong Lee

Safety Analysis Dept., Korea Nuclear Fuel Co., Ltd.,

493 Deokjin-dong, Yuseong-gu, Daejeon 305-353, Korea

The capability of TRAC-M code to predict downcomer boiling effect during reflood phase in postulated PWR LOCA is evaluated using the results of downcomer effective water head and Cylindrical Core Test Facility (CCTF) experiments, which were performed at JAERI. With a full height downcomer simulator, effective water head experiment was carried out to investigate the applicability of the TRAC-M best estimate LOCA code to evaluate the effective water head with superheated wall temperature in downcomer. In order to clarify the effect of the initial superheat of the downcomer wall on the system and the core cooling behaviors during the reflood phase, two sets of analysis were also performed with a CCTF.

Results show that TRAC-M code tends to under-predict downcomer effective water head and core differential pressure. However, the code results show a good agreement with the experimental results in downcomer temperature, heat flux and pressure. Finally, both experiment and calculation showed that the downcomer water head with the superheated downcomer wall is lower than that of the saturated wall temperature.

Key words : Downcomer boiling, LOCA, Reflood, TRAC-M, Effective water head, CCTF

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 5, pp. 1194-1205, 2005

Effects of Needle Response on Spray Characteristics in High Pressure Injector Driven by

Piezo Actuator for Common-Rail Injection System

Jinwook Lee, Kyoungdoug Min*

School of Mechanical and Aerospace Engineering, College of Engineering, Seoul National University,

San 56-1 Shinlim-Dong, Kwanak-Ku, Seoul 151-742, Korea

The common-rail injection systems, as a new diesel injection system for passenger car, have more degrees of freedom in controlling both the injection timing and injection rate with the high pressure. In this study, a piezo-driven injector was applied to a high pressure common-rail type fuel injection system for the control capability of the high pressure injector’s needle and firstly examined the piezo-electric characteristics of a piezo-driven injector. Also in order to analyze the effect of injector’s needle response driven by different driving method on the injection, we investigated the diesel spray characteristics in a constant volume chamber pressurized by nitrogen gas for two injectors, a solenoid-driven injector and a piezo-driven injector, both equipped with the same injection nozzle with sac type and 5-injection hole. The experimental method for spray visualization was based on back-light photography technique by utilizing a high speed framing camera. The macroscopic spray propagation was geometrically measured and characterized in term of the spray tip penetration, spray cone angle and spray tip speed. For the evaluation of the needle response of the above two injectors, we indirectly estimated the needle’s behavior with an accelerometer and injection rate measurement employing Bosch’s method was conducted. The experimental results show that the spray tip penetrations of piezo-driven injector were longer, on the whole, than that of the solenoid-driven injector. Besides we found that the piezo-driven injector have a higher injection flow rate by a fast neddle response and it was possible to control the injection rate slope in piezo-driven injector by altering the induced current.

Key Words : Piezo Actuator, Injector, Diesel Spray, Common-rail Type Fuel Injection System

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 5, pp. 1206-1215, 2005

Experiments on the Thermal Stratification in the Branch of NPP

Sang-Nyung Kim*, Seon-Hong Hwang, Ki-Hoon Yoon

Department of Nuclear Engineering, Kyunghee University,

Seocheon-ri #1, Kiheung-up, Youngin-city, Kyung-gi-do 449-701, Korea

The thermal stratification phenomena, frequently occurring in the component of nuclear power plant system such as pressurizer surge line, steam generator inlet nozzle, safety injection system (SIS), and chemical and volume control system (CVCS), can cause through-wall cracks, thermal fatigue, unexpected piping displacement and dislocation, and pipe support damage. The phenomenon is one of the unaccounted load in the design stage. However, the load have been found to be serious as nuclear power plant operation experience accumulates. In particular, the thermal stratification by the turbulent penetration or valve leak in the SIS and SCS pipe line can lead these safety systems to failure by the thermal fatigue. Therefore in this study an 1/10 scaledowned experimental rig had been designed and installed. And a series of experimental works had been executed to measure the temperature distribution (thermal stratification) in these systems by the turbulent penetration, valve leak, and heat transfer through valve. The results provided very valuable informations such as turbulent penetration depth, the possibility of thermal stratification by the heat transfer through valve, etc. Also the results are expected to be useful to understand the thermal stratification in these systems, establish the thermal stratification criteria and validate the calculation results by CFD Codes such as Fluent, Phenix, CFX.

Key Words:  Thermal Stratification, Turbulent Penetration Depth, Safety Injection System, Shutdown Cooling System, Valve Leakage, Thermal Fatigue, Heat Transfer Through Valves.

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 5, pp. 1216-1225, 2005

Dissolution Behavior and Hydrate Effect on CO2 Ocean Sequestration

Namjin Kim

Mechanical Engineering Research Institute, Inha University, Incheon 402-751, Korea

Chongbo Kim*

Department of Mechanical Engineering, Inha University, Incheon 402-751, Korea

CO2 ocean sequestration is one of the promising options to reduce CO2 concentration in the atmosphere because the ocean has vast capacity for CO2 absorption. Therefore, in the present investigation, calculations for solubility and dissolution behavior of liquid CO2 droplets released at 1000 m and 1500 m deep in the ocean from a moving ship and a fixed pipeline have been carried out in order to estimate the CO2 dissolution characteristics in the ocean. The results show liquid CO2 becomes CO2 bubble at around 500 m in depth, and the solubility of seawater is about 5% less than of pure water. Also, it is shown that the injection of liquid CO2 from a moving ship is a more effective method for dissolution than from a fixed pipeline, and the presence of hydrate on liquid CO2 acts as a resistant layer in dissolving liquid CO2.

Key words : Global Warming, CO2 Sequestration, Solubility, Hydrate, Dissolution

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 6, pp. 1229-1242, 2005

Heat Aging Effects on the Material Property and the Fatigue Life of Vulcanized Natural Rubber,

and Fatigue Life Prediction Equations

Jae-Hyeok Choi, Hee-Jin Kang, Hyun-Yong Jeong*,Tae-Soo Lee

Department of Mechanical Engineering, Sogang University,

1 Shinsoo-Dong, Mapo-Gu, Seoul 121-742, Korea

Sung-Jin Yoon

Research and Development Division, Hyundai Motor Company,

772-1 ChangDuk-Dong HwaSeong-Si Kyonggi-Do, S. Korea 445-707

When natural rubber is used for a long period of time, it becomes aged; it usually becomes hardened and loses its damping capability.  This aging process affects not only the material property but also the (fatigue) life of natural rubber.  In this paper the aging effects on the material property and the fatigue life were experimentally investigated.  In addition, several fatigue life prediction equations for natural rubber were proposed.  In order to investigate the aging effects on the material property, the load-stretch ratio curves were plotted from the results of the tensile test, the compression test and the simple shear test for virgin and heat-aged rubber specimens.  Rubber specimens were heat-aged in an oven at a temperature ranging from 50oC to 90oC for a period ranging from 2 days to 16 days.  In order to investigate the aging effects on the fatigue life, fatigue tests were conducted for differently heat-aged hourglass-shaped and simple shear specimens.  Moreover, finite element simulations were conducted for the specimens to calculate physical quantities occurring in the specimens such as the maximum value of the effective stress, the strain energy density, the first invariant of the Cauchy-Green deformation tensor and the maximum principal nominal strain.  Then, four fatigue life prediction equations based on one of the physical quantities could be obtained by fitting the equations to the test data.  Finally, the fatigue life of a rubber bush used in an automobile was predicted by using the prediction equations, and it was compared with the test data of the bush to evaluate the reliability of those equations.

Keywords: Heat-aging Effect, Natural Rubber, Fatigue Life, Fatigue Life Prediction Equation

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 6, pp. 1243-1252, 2005

A Real-Time DSP-Based Imbalance Analysis System for Rotating Machine with Vibration Signal

Hua Su, Linglong Huang, Kil To Chong*

Department of Electrical and Computer Engineering, Chonbuk National University,

664-14 Duckjin-Dong, Duckjin-Gu, Jeonju, Korea 561-756

This paper describes a new digital signal processor (DSP) imbalance measurement system dedicated to real-time vibration analysis on rotating machine. To accomplish real-time analysis, the vibration signals are on-line acquired and processed to analyze the mass imbalance and phase position. This is achieved through the use of FFT and Lissajous diagram. The method followed to analyze the mass imbalance with the chosen hardware and software solutions are described in detail in this paper. Several experimental tests demonstrate the efficiency and accuracy in imbalance analysis performance of the DSP system.

Key words: Digital Signal Processor, Mass Imbalance, FFT, Lissajous Diagram

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 6, pp. 1253-1267, 2005

Observability Analysis of Alignment Errors in GPS/INS

Mun Ki Lee

Department of Interdisciplinary Program in Mechatronics

Sinpyo Hong*

Advanced Ship Engineering Research Center

Man Hyung Lee

School of Mechanical Engineering, Pusan National University, Pusan 609-735, Korea

Sun-Hong Kwon, Ho-Hwan Chun

Department of Naval Architecture and Ocean Engineering, Pusan National University,

Pusan 609-735, Korea

Misalignment can be an important problem in the integration of GPS/INS. Observability analysis of the alignment errors in the integration of low-grade inertial sensors and multi-antenna GPS is presented in this paper. A control-theoretic approach is adopted to study the observability of time-varying error dynamics models. The relationship between vehicle motions and the observability of the errors in the lever arm and relative attitude between GPS antenna array and IMU is given.  It is shown that alignment errors can be made observable through maneuvering. The change of acceleration makes the components of the relative attitude error that are orthogonal to the direction of the acceleration change observable. The change of angular velocity makes the components of the lever arm error that are orthogonal to the direction of the angular velocity observable. The motion of constant angular velocity has no influence on the estimation of the lever arm.

Key words: GPS, INS, Lever arm, Alignment error, Observability

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 6, pp. 1268-1279, 2005

Gantry Robot with Extended Workspace for Pavement Sign Painting Operations

Daehie Hong

Associate Professor, Dept. of Mechanical Engineering, Korea Univ.,

5ga Anam-dong Sungbuk-gu Seoul 136-701, Korea

Woo-Chang Lee

LCDR., Naval Sea System Command, ROK Navy, P.O BOX 501-240,

Boonam-ri Namsun-myun Kyeryong-si Choongnam 321-929, Korea

Baeksuk Chu

Graduate Student, Dept. of Mechanical Engineering, Korea Univ., Seoul 136-701, Korea

Tae-Hyung Kim

Senior Researcher, Fire & Engineering Services Research Dept.,

Korea Institute of Construction Technology, Kyunggi-Do 411-712, Korea

Woo Chun Choi

Professor, Dept. of Mechanical Engineering, Korea Univ.,

5ga Anam-dong Sungbuk-gu Seoul 136-701, Korea

The current method for pavement sign marking operations is labor-intensive and very dangerous due to the exposure of workers to passing traffic. It also requires blocking traffic for a long period of time resulting serious traffic jam. This paper deals with the development of a robotic system for automating the pavement sign painting operations. The robotic system consists of gantry frame equipped with transverse drive rail and automatic paint spray system. The workspace of the gantry robot is extended to one-lane width with the transverse rail system. This research also includes the development of font data structures that contain the shape information of pavement signs, such as Korean letters, English letters and symbols. The robot path is generated with this font data through the procedures of scaling up/down and partitioning the signs to be painted depending on the workspace size.

Key Words : Field Robot, Construction Automation, Parement Sign Painting

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 6, pp. 1280-1289, 2005

Reliability Estimation of Buried Gas Pipelines in terms of Various Types of Random Variable Distribution

Ouk Sub Lee

School of Mechanical Engineering, InHa Univ., Incheon 402-751, Korea

Dong Hyeok Kim*

Department of Mechanical Engineering, InHa Univ., Incheon 402-751, Korea

This paper presents the effects of corrosion environments of failure pressure model for buried pipelines on failure prediction by using a failure probability. The FORM (first order reliability method) is used in order to estimate the failure probability in the buried pipelines with corrosion defects. The effects of varying distribution types of random variables such as normal, lognormal and Weibull distributions on the failure probability of buried pipelines are systematically investigated. It is found that the failure probability for the MB31G model is larger than that for the B31G model. And the failure probability is estimated as the largest for the Weibull distribution and the smallest for the normal distribution. The effect of data scattering in corrosion environments on failure probability is also investigated and it is recognized that the scattering of wall thickness and yield strength of pipeline affects the failure probability significantly. The normalized margin is defined and estimated. Furthermore, the normalized margin is used to predict the failure probability using the fitting lines between failure probability and normalized margin.

Key Words : Buried Pipeline, Reliability Estimation, Failure Probability, FORM(first order reliability method), Normal, Lognormal and Weibull Distributions, Corrosion, Failure Pressure Model, Normalized Margin

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 6, pp. 1290-1303, 2005

Internet-based Real-time Obstacle Avoidance of a Mobile Robot

Jae-Pyung Ko, Jang-Myung Lee*

Department of Electronics Engineering, Pusan National University, Pusan 609-735, Korea

In this research, a remote control system has been developed and implemented, which combines autonomous obstacle avoidance in real-time with force-reflective tele-operation. A tele-operated mobile robot is controlled by a local two-degrees-of- freedom force-reflective joystick that a human operator holds while he is monitoring the screen. In the system, the force-reflective joystick transforms the relation between a mobile robot and the environment to the operator as a virtual force which is generated in the form of a new collision vector and reflected to the operator. This reflected force makes the tele-operation of a mobile robot safe from collision in an uncertain and obstacle-cluttered remote environment. A mobile robot controlled by a local operator usually takes pictures of remote environments and sends the images back to the operator over the Internet. Because of limitations of communication bandwidth and the narrow view-angles of the camera, the operator cannot observe shadow regions and curved spaces frequently. To overcome this problem, a new form of virtual force is generated along the collision vector according to both distance and approaching velocity between an obstacle and the mobile robot, which is obtained from ultrasonic sensors. This virtual force is transferred back to the two-degrees-of-freedom master joystick over the Internet to enable a human operator to feel the geometrical relation between the mobile robot and the obstacle. It is demonstrated by experiments that this haptic reflection improves the performance of a tele-operated mobile robot significantly.

Key words: Tele-operation, Collision Vector, Force Reflection, Virtual Impedance, Obstacle Avoidance

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 6, pp. 1304-1312, 2005

A Study on the Body Attachment Stiffness for the Road Noise

Ki-Chang Kim*

Senior Research Engineer, Vehicle Development & Analysis Team, Hyundai Motor Company,

772-1, Jangduk-Dong, Whasung-Si, Gyunggi-Do, 445-706, Korea

Chan-Mook Kim

Professor, Graduate School of Automotive Engineering, Kookmin University,

861-1, Chongnung-dong, Songbuk-gu, Seoul, 136-702, Korea

The ride and noise characteristics of a vehicle are significantly affected by the vibration transferred to the body through the chassis mounting points in the engine and suspension. It is known that body attachment stiffness is an important factor of idle noise and road noise for NVH performance improvement. The body attachment stiffness serves as a route design aimed at isolating the vibration generated inside the car due to the exciting force of the engine or road. The test result of the body attachment stiffness is shown in the FRF curve data; the stiffness level and sensitive frequency band are recorded by the data distribution. The stiffness data is used for analyzing the parts that fail to meet the target stiffness at a pertinent frequency band. The analysis shows that the target frequency band is between 200 and 500 Hz. As a result of the comparison in a mounted suspension, the analysis data is comparable to the test data. From these results, there is a general agreement between the predicted and measured responses. This procedure makes it possible to find the weak points before a proto car is produced, and to suggest proper design guidelines in order to improve the stiffness of the body structure.

Key words : body attachment stiffness, bush dynamic stiffness, vibration isolation, NVH (Noise, Vibration and Harshness)

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 6, pp. 1313-1320, 2005

Hemodynamic Analysis of Coronary Artery Microcirculation using a Pig’s Morphometric Data

Sehyun Shin*, Jungsu Park

School of Mechanical Engineering, Kyungpook National University,

1370 Sangyeok-Dong, Buk-ku, Daegu, 702-701, Korea

Stenosed coronary artery may play an important role in various coronary heart diseases. However, it has not been known how much stenosed coronary artery affects coronary circulation system, quantitatively. The present study developed a mathematical model for microcirculation in the left common coronary artery (LCCA) with adopting a previously measured morphological data and mechanical properties of the coronary vessels. We examine the effect of percent diameter stenosis on blood flow rate and shear stress for two cases. Case I comprised of one-stenosed element at 10th order (% diameter stenosis are 10, 30, and 50, respectively). Case II consisted of completely occluded element at 10th order (number of occluded elements are 0, 1, and 2 out of 8, respectively). As the level of stenosis becomes severe, the shear stress increases significantly but the flow rate reduction was relatively small. However, for the occluded case, there was linearly proportional reduction of flow rate according to number of occluded elements. Either such high shear stress associated with coronary artery stenosis or reduced flow rate due to occlusion may cause atherosclerosis and myocardial ischemia.

Keywords: Left common coronary artery (LCCA), Hemodynamics, Stenosis, Occlusion

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 6, pp. 1321-1328, 2005

Effect of the Injection Parameters on Diesel Spray Characteristics

Kyu Keun Song*

Faculty of Mechanical Aerospace System Engineering, Chonbuk National University,

Chonbuk 561-756, Korea

Sang Cherl Sim

Graduate School, Department of Precision Mechanical Engineering, Chonbuk National University, Korea

Byong Koog Jung, Hyung Gon Kim

Automobile Hi-Technology Research Center, Chonbuk National University, Korea

Jang Heon Kim

Passenger Car Diesel Engine Test Team, Hyundai Motor company, Korea

The characteristics of the diesel spray have affected certain aspects of engine performance, such as the power, fuel consumption, and emissions. Therefore, this study was performed to investigate the effects of various injection parameters. In order to obtain the effect of injection parameters on diesel spray characteristics, the experiment is performed by using a high temperature and pressure chamber. The behaviors of the spray are visualized by using a high speed video camera, spray angle, penetration, and various other things.

The results of the experiment are summarized as follows.

1) The correlation of the spray penetration can be expressed as follows.

2) The correlation of the spray angle can be expressed as follows

3) The measured macro characteristics that include the spray tip penetration and spray angle corresponded with the established correlations.

Key Words : Spray tip penetration, Ambient gas density, Ambient gas temperature, Spray angle

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 6, pp. 1329-1337, 2005

Temperature Analysis for the Linear Cell in the Vapor Deposition Process

Jongwook Choi*, Sungcho Kim, Jeongsoo Kim

School of Mechanical and Automotive Engineering, Sunchon National University,

Suncheon, Jeonnam, 540-742, Korea

The OLED(Organic Light Emitting Diodes) display recently used for the information indicating device has many advantages over the LCD(Liquid Crystal Display), and its demand will be increased highly. The linear cell should be designed carefully considering the uniformity of thin film on the substrate. Its design needs to compute the temperature field analytically because the uniformity for the thin film thickness depends on the temperature distribution of the source(organic material). In the present study, the design of the linear cell will be modified or improved on the basis of the temperature profiles obtained for the simplified linear cell. The temperature distributions are numerically calculated through the STAR-CD program, and the grids are generated by means of the ICEM CFD program. As the results of the simplified linear cell, the temperature deviation was shown in the parabolic form among the both ends and the center of the source. In order to reduce the temperature deviation, the configuration of the rectangular ends of the crucible was modified to the circular type. In consequence, the uniform temperature is maintained in the range of about 90 percent length of the source. It is expected that the present methods and results on the temperature analysis can be very useful to manufacture the vapor deposition device.

Key Words : OLED(Organic Light Emitting Diodes), linear cell, uniformity of thin film, vapor deposition, radiative heat transfer

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 6, pp. 1338-1346, 2005

Effects of Thermal Contact Resistance on Film Growth Rate in a Horizontal MOCVD Reactor

Ik-Tae Im*, Nag Jung Choi

Dept. Automotive Engineering, Iksan National College,

194-5 Ma-dong, Iksan, Jeollabuk-do 570-752, Korea

Masakazu Sugiyama

Dept. Electronic Engineering, School of Engineering, University of Tokyo,

7-3-1 Hongo, Bunkyo-ku, Tokyo 113-8656 Japan

Yoshiyaki Nakano

Research Center for Advanced Science and Technology, University of Tokyo,

4-6-1 Komaba, Meguro-ku, Tokyo 153-8904 Japan

Yukihiro Shimogaki

Dept. Materials Engineering, School of Engineering, University of Tokyo,

7-3-1 Hongo, Bunkyo-ku, Tokyo 113-8656 Japan

Byoung Ho Kim

ADCOMTECH, 78-2 Munpyoung-dong, Daeduck-gu, Daejon 306-220 Korea

Kwang-Sun Kim

School of Mechatronics Engineering, Korea University of Technology and Education,

307 Gajon-ri, Byungchon-myon, Chonan 330-708 Korea

Effects of thermal contact resistance between heater and susceptor, susceptor and graphite board in a MOCVD reactor on temperature distribution and film growth rate were analyzed. One-dimensional thermal resistance model considering thermal contact resistance and heat transfer area was made up at first to find the temperature drop at the surface of graphite board. This one-dimensional model predicted the temperature drop of 18K at the board surface. Temperature distribution of a reactor wall from the three-dimensional computational fluid dynamics analysis including the gap at the wafer position showed the temperature drop of 20K. Film growth rates of InP and GaAs were predicted using computational fluid dynamics technique with chemical reaction model. Temperature distribution from the three-dimensional heat transfer calculation was used as a thermal boundary condition to the film growth rate simulations. Temperature drop due to the thermal contact resistance affected to the GaAs film growth a little but not to the InP film growth.

Key Words : Thermal Contact Resistance, Metalorganic Chemical Vapor Deposition(MOCVD), Computational Fluid Dynamics(CFD), InP, GaAs

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 6, pp. 1347-1357, 2005

Effects of Combustor-Level High Free-Stream Turbulence on Blade-Surface Heat/Mass Transfer in the Three-Dimensional Flow Region near the Endwall of a High-Turning Turbine Rotor Cascade

Sang Woo Lee*, Hyun Goo Kwon

School of Mechanical Engineering, Kumoh National Institute of Technology,

Gumi, Gyongbook 730-701, Korea

Byung-Kyu Park

School of Mechanical and Aerospace Engineering, Seoul National University, Seoul 151-742, Korea

Effects of combustor-level high free-stream turbulence on the blade-surface heat/mass transfer have been investigated in the three-dimensional flow region near the endwall within a high-turning turbine rotor cascade passage. Free-stream turbulence intensity and integral length scale in the high turbulence case are 14.7 percents and 80 mm, respectively. The result shows that there is no considerable discrepancy in the blade heat/mass transfer near the endwall between the low and high turbulence cases. As departing from the endwall, however, the deviation between the two cases becomes larger, particularly in the region where flow separation and re-attachment occur. Under the high turbulence, flow disturbances such as boundary-layer separation and re-attachment seem to be suppressed, which makes the blade heat/mass transfer more uniform. Moreover, there are some evidences that endwall vortices tend to be weakened under the high turbulence.

Key Words : Gas Turbine, Turbine Rotor, Combustor-level Turbulence, Endwall Flow Region, Blade Surface Heat/Mass Transfer

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 6, pp. 1358-1365, 2005

Numerical Study on NO Emission with Flue Gas Dilution in Air and Fuel Sides

Eun-Seong Cho, Suk Ho Chung*

School of Mechanical and Aerospace Engineering, Seoul National University, Seoul 151-744, Korea

Flue gas recirculation (FGR) is widely adopted to control NO emission in combustion systems.  Recirculated flue gas decreases flame temperature and reaction rate, resulting in the decrease in thermal NO production.  Recently, it has been demonstrated that the recirculated flue gas in fuel stream, that is, the fuel induced recirculation (FIR), could enhance much improved reduction in NO per unit mass of recirculated gas, as compared to conventional FGR in air.  In the present study, the effect of dilution methods in air and fuel sides on NO reduction has been investigated numerically by using N2 and CO2 as diluent gases to simulate flue gases.  Counterflow diffusion flames were studied in conjunction with the laminar flamelet model of turbulent flames.  Results show that CO2 dilution was more effective in NO reduction because of large temperature drop due to the larger specific heat of CO2 compared to N2.  Fuel dilution was more effective in reducing NO emission than air dilution when the same recirculation ratio of dilution gas is used by the increase in the nozzle exit velocity, thereby the stretch rate, with dilution gas added to fuel side.

Key Words : Flue gas recirculation (FGR), Fuel induced recirculation (FIR), Nitric oxides, Counterflow

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 6, pp. 1366-1377, 2005

Experimental Study on Flame Structure and Temperature

Characteristics in a Lean Premixed Model Gas Turbine Combustor

Jong Ho Lee, Chung Hwan Jeon*, Young June Chang

School of Mechanical Engineering, Pusan National University, Pusan, 609-735, Korea

Chul Woong Park

Laser metrology group, Korea Research Institute of Standards and Science, Daejon, 305-600, Korea

Jae Won Hahn

School of Mechanical Engineering, Yonsei University, Seoul, 120-749, South Korea

Experimental study was carried out in an atmospheric pressure, laboratory-scale dump combustor showing features of combustion instabilities. Flame structure and heat release rates were obtained from OH emission spectroscopy. Qualitative comparisons were made between line-integrated OH chemiluminescence image and Abel-transformed one. Local Rayleigh index distributions were also examined. Mean temperature, normalized standard deviation and temperature fluctuations were measured by coherent anti-Stokes Raman spectroscopy (CARS). To see the periodic behavior of oscillating flames, phase-resolved measurements were performed with respect to the pressure wave in the combustor. Results on system damping and driving characteristics were provided as a function of equivalence ratio. It also could be observed that phase resolved temperatures have been changed in a well-defined manner, while its difference between maximum and minimum reached up to 280K. These results would be expected to play an important role in better understanding of driving mechanisms and thermo-acoustic interactions.

Key Words : Combustion Instability, Phase-Resolved Gas Temperature, Coherent Anti-Stokes Raman Spectroscopy(CARS)

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 6, pp. 1378-1389, 2005

Nonequilibrium Heat Transfer Characteristics During Ultrafast

Pulse Laser Heating of a Silicon Microstructure

Seong Hyuk Lee*

Assistant Professor, School of Mechanical Engineering, Chung-Ang University,

221 Heukseok-Dong, Dongjak-Gu, Seoul 156-756, Korea

This work provides the fundamental knowledge of energy transport characteristics during very short-pulse laser heating of semiconductors from a microscopic viewpoint. Based on the self-consistent hydrodynamic equations, in-situ interactions between carriers, optical phonons, and acoustic phonons are simulated to figure out energy transport mechanism during ultrafast pulse laser heating of a silicon substrate through the detailed information on the time and spatial evolutions of each temperature for carriers, longitudinal optical (LO) phonons, acoustic phonons. It is found that nonequilibrium between LO phonons and acoustic phonons should be considered for ultrafast pulse laser heating problem, two-peak structures become apparently present for the subpicosecond pulses because of the Auger heating. A substantial increase in carrier temperature is observed for lasers with a few picosecond pulse duration, whereas the temperature rise of acoustic and phonon temperatures is relatively small with decreasing laser pulse widths. A slight lagging behavior is observed due to the differences in relaxation times and heat capacities between two different phonons. Moreover, the laser fluence has a significant effect on the   decaying rate of the Auger recombination.

Key Words : Ultra-short pulse, Micro-scale heat transfer, Carrier temperature, Optical phonon, Acoustic phonon, Nonequilibrium, Auger heating

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 7, pp. 1393-1404, 2005

A Study on Fatigue Damage Modeling using Neural Networks

Dong-Woo Lee

Department of Mechanical Engineering, Dong-A University, Busan 604-714, Korea

Soon-Hyeok Hong

Cooperative Laboratory Center, Pukyong National University, Busan 608-739, Korea

Seok-Swoo Cho*

Department of Vehicle Engineering, Samcheok National University, Samcheok 245-711, Korea

Won-Sik Joo

Department of Mechanical Engineering, Dong-A University, Busan 604-714, Korea

Fatigue crack growth and life have been estimated based on established empirical equations. In this paper, an alternative method using artificial neural network(ANN)-based model developed to predict fatigue damages simultaneously. To learn and generalize the ANN, fatigue crack growth rate and life data were built up using in-plane bending fatigue test results. Single fracture mechanical parameter or nondestructive parameter can't predict fatigue damage accurately but multiple fracture mechanical parameters or nondestructive parameters can. Existing fatigue damage modeling used this merit but limited real-time damage monitoring. Therefore, this study shows fatigue damage model using backpropagation neural networks on the basis of X-ray half breadth ratio B/Bo, fractal dimension Df and fracture mechanical parameters can estimate fatigue crack growth rate da/dN and cycle ratio N/Nf at the same time within engineering limit error(5%).

Key Words :   Fatigue Damage Modeling, Artificial Neural Networks(ANN), Fatigue Crack Growth Rate, Cycle Ratio, Estimated Mean Error

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 7, pp. 1405-1413, 2005

Statistical Approach to Analyze Vibration Localization Phenomena in Periodic Structural Systems

Sang Ha Shin

Graduate School, Hanyang University, Sungdong-Gu Haengdang-Dong 17, Seoul, Korea

Se Jung Lee

School of Mechanical Engineering, University of Seoul,

Dongdaemun-Gu Cheonnong-Dong 90, Seoul, Korea

Hong Hee Yoo

School of Mechanical Engineering, Hanyang University,

Sungdong-Gu Haengdang-Dong 17, Seoul, Korea

Malfunctions or critical fatigue problems often occur in mistuned periodic structural systems since their vibration responses may become much larger than those of perfectly tuned periodic systems. These are called vibration localization phenomena and it is of great importance to accurately predict the localization phenomena for safe and reliable designs of the periodic structural systems. In this study, a simple discrete system which represents periodic structural systems is employed to analyze the vibration localization phenomena. The statistical effects of mistuning, stiffness coupling, and damping on the vibration localization phenomena are investigated through Monte Carlo simulation. It is found that the probability of vibration localization was significantly influenced by the statistical properties except the standard deviation of coupling stiffness.

Key Words: Vibration Localization, Periodic Structures, Largest frequency response amplitude, Statistics, Probability, Monte Carlo simulation

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 7, pp. 1414-1423, 2005

Structural Vibration Control for Broadband Noise Attenuation in Enclosures

Kailash Krishnaswamy, Rajesh Rajamani

Department of Mechanical Engineering, University of Minnesota, Minneapolis, MN 55455, USA

Jong Jin Woo, Young Man Cho*

School of Mechanical and Aerospace Engineering, Seoul National University, Seoul 151-742, Korea

This paper develops and evaluates several strategies for structural vibration control with the objective of attenuating broadband noise inside a rectangular enclosure. The strategies evaluated include model-independent collocated control, model-based feedback control and a new “modal-estimate” feedback strategy. Collocated control requires no knowledge of model parameters and enjoys the advantage of robustness. However, effective broadband noise attenuation with colocated control requires a large number of sensor-actuator pairs. Model-based controllers, on the other hand, can be theoretically effective even with the use of a single actuator. However, they suffer from a lack of robustness and are unsuitable from a practical point of view for broadband structural vibration applications where the dynamic models are of large order and poorly known. A new control strategy is developed based on attenuating a few structural vibration modes that have the best coupling with the enclosure acoustics. Broadband attenuation of these important modes can be achieved using a single actuator, a limited number of accelerometers and limited knowledge of a few modal functions. Simulation results are presented to demonstrate the effectiveness of the developed strategy.

Keywords: structural control, noise attenuation, vibration control, acoustic enclosure

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 7, pp. 1424-1431, 2005

Analysis of Traumatic Brain Injury Using a Finite Element Model

Chang-Min Suh*

School of Mechanical Engineering, Kyungpook National University, Daegu, 702-701, Korea

Sung-Ho Kim

Dept. of Manufacturing Technology & Standard, Korean Agency for Technology and Standards,

Gwacheon, Gyeonggi, 427-716, Korea

Sang-Yeob Oh

Automotive Division, Catholic Sanggi College, Andong, Kyungpook, 760-711, Korea

In this study, head injury by impact force was evaluated by numerical analysis with 3-dimensional finite element (FE) model. Brain deformation by frontal head impact was analyzed to evaluate traumatic brain injury (TBI). The variations of head acceleration and intra-cranial pressure (ICP) during the impact were analyzed. Relative displacement between the skull and the brain due to head impact was investigated from this simulation. In addition, pathological severity was evaluated according to head injury criterion (HIC) from simulation with FE model. The analytic result of brain damage was accorded with that of the cadaver test performed by Nahum et al .(1977) and many medical reports. The main emphasis of this study is that our FE model was valid to simulate the traumatic brain injury by head impact and the variation of the HIC value was evaluated according to various impact conditions using the FE model.

Key Words : Traumatic Brain Injury(TBI), Finite Element Model, Head Injury Criterion(HIC), Brain Damage, Skull & Brain

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 7, pp. 1432-1440, 2005

High-Temperature Rupture of 5083-Al Alloy under Multiaxial Stress States

Ho-Kyung Kim*, Duk-Kyu Chun

Department of Automotive Engineering, Seoul National University of Technology,

172 Kongnung-dong, Nowon-ku, Seoul 139-743

Sung-Hoon Kim

Department of Structural Engineering, Seoul National University of Technology,

172 Kongnung-dong, Nowon-ku, Seoul Korea, 139-743

High-temperature rupture behavior of 5083-Al alloy was tested up to failure at 548K under multiaxial stress states: uniaxial tension using smooth bar specimens, biaxial shearing using double shear bar specimens, and triaxial tension using notched bar specimens. Rupture times were compared for uniaxial, biaxial, and triaxial stress states with respect to the maximum principal stress, the von Mises effective stress, and the principal facet stress. The results indicate that the von Mises effective and principal facet stresses give good correlation for the material investigated, and these parameters can predict creep life data under the multiaxial stress states with the rupture data obtained from specimens under the uniaxial stress. The results suggest that creep rupture of this alloy under the testing condition is controlled by cavitation coupled with highly localized deformation process, such as grain boundary sliding. It is also conceivable that strain softening controlled the highly localized deformation modes which result in cavitation damage in controlling rupture time of this alloy.

Key Words: Multiaxial stress states, High-temperature rupture, Principal facet stress, Creep cavitation, Damage tolerance

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 7, pp. 1441-1448, 2005

Fatigue Properties of Fine Grained Magnesium Alloys After Severe Plastic Deformation

Chin-Sung Chung

Bowon Light Metal Co., Hwasung-si, Kyungki-do, 445-893, Korea

Duk-Kyu Chun, Ho-Kyung Kim*

Department of Automotive Engineering, Seoul National University of Technology, Seoul, 139-743, Korea

Fine grained AZ31 and AZ61 magnesium alloys produced by equal channel angular pressing (ECAP) were tested for investigating tensile and fatigue properties, including microstructure, monotonic tensile flow, fatigue life and crack growth rate. For the two alloys, the yield stress of the ECAPed sample was lower than that of the unECAPed (=as received) sample, because of the fact that the softening effect due to texture anisotropy overwhelmed the strengthening effect due to grain refinement. Grain refinement of the AZ31 and AZ61 alloys through ECAP was found not to be significantly effective in increasing fatigue strength.

Keywords: Magnesium alloys; Equal channel angular pressing (ECAP); Fine grained microstructures; Fatigue crack growth rate; Fatigue strength

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 7, pp. 1449-1459, 2005

ALocal Flow Speed Measurement Using Tunable AC Thermal Anemometry

Won Seok Chung

Micro Thermal System Research Center, Seoul National University, Seoul 151-742, Korea

Ohmyoung Kwon*

Department of Mechanical Engineering, Korea University, Seoul 136-701, Korea

Joon Sik Lee

School of Mechanical and Aerospace Engineering, Seoul National University, Seoul 151-742, Korea

Young Ki Choi

School of Mechanical Engineering, Chung-Ang University, Seoul 156-756, Korea

Seungho Park

Department of Mechanical and System Design Engineering, Hongik University, Seoul 121-791, Korea

This paper shows the results of local flow speed measurement using tunable AC thermal anemometry, which is suitable for the accurate measurement of wide range flow speed. The measurement accuracy is verified through the comparison between the measurement data and the analytic solution of the sensor temperature oscillation in stationary fluid. The relation between the phase lag and the flow speed is experimentally investigated at various conditions. The measurement sensitivity for low flow speed improves in a low frequency region and that for high flow speed improves in a high frequency region. Also, the sensitivity increases with decreasing thermal conductivity of the surrounding fluid. The local flow speed could be measured as low as 1.5 mm/s and the highest measurement resolution was 0.05 mm/s in the range of 4.5 ~ 5.0 mm/s at 1 Hz in this experiment.

Key Words: Flow speed measurement, Steady periodic heat transfer, Complex temperature, 3ω voltage, Phase lag

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 7, pp. 1460-1468, 2005

A Theoretical Comparison of Two Possible Shape Memory Processes in Shape Memory

Alloy Reinforced Metal Matrix Composite

Jae Kon Lee*, Gi Dae Kim

School of Mechanical and Automotive Engineering, Catholic University of Daegu,

Gyeongsansi, Gyeongbuk, 712-702, Korea

Two possible shape memory processes, austenite to detwinned martensite transformation and twinned martensite to detwinned martensite transformation of a shape memory alloy have been modeled and examined. Eshelby’s equivalent inclusion method with Mori-Tanaka’s mean field theory is used for modeling of the shape memory processes of TiNi shape memory alloy reinforced aluminum matrix composite. The shape memory amount of shape memory alloy, plastic strain and residual stress in the matrix are computed and compared for the two processes. It is shown that the shape memory amount shows differences in a small prestrain region, but the plastic strain and the residual stress in the matrix show differences in the whole prestrain region. The shape memory process with initially martensitic state of the shape memory alloy would be favorable to the increase in the yield stress of the composite owing to the large compressive residual stress and plastic strain in the matrix.

Keywords: Shape memory processes, Shape memory alloy, Fiber reinforced composites, Prestrain, Residual stress, Plastic strain

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 7, pp. 1469-1477, 2005

Development and Application of New Evaluation System

for Ride Comfort and Vibration on Railway Vehicles

Wan-Suk Yoo*

CAELab, NRL, Pusan National University, Geumjeong-gu, Busan 609-735, Korea

Chang-Hwan Lee

Ph.D. candidate , CAELab, NRL, Pusan National University, Busan 609-735, Korea

Weui-Bong Jeong

Mechanical Engineering, Pusan National University, Busan 609-735, Korea

Sang-Hyun Kim

Environmental Engineering, Pusan National University, Busan 609-735, Korea

Vibrations related to ride comfort should be considered at the beginning of design stage. In general, ride comfort of human is mainly affected by vibration transmitted from the floor and seat. Also, vibration level is very important regarding with running safety on freight wagon. To ensure ride comfort for passenger coach and vibration level for freight wagon, tests had been repeated by different test procedures with several equipments. With different measuring and evaluations for these results, it took much time to evaluate test results. In this paper, a new evaluation procedure was developed combining several software for ride comfort and vibration level test on railway vehicles. In addition, this developed system is capable of ride comfort test and vibration test by a single integrated system that is capable of immediate reporting the test result. With this developed system, the comfort in a passenger coach and the vibration in a freight car were evaluated. And the simulation results from the proposed system are verified by a field test.

Key words: Ride Comfort, Vibration Level, Railway Vehicles

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 7, pp. 1478-1487, 2005

An Experimental Study of the Performance Characteristics with Four Different Rotor Blade Shapes on a Small Mixed-Type Turbine

Soo-Yong Cho*

Gyeongsang National University, Department of Mechanical and Aerospace Engineering (ReCAPT),

Gajoadong 900, Jinju, Gyeongnam 660-701, Korea

Tae-Hwan Cho

Gyeongsang National University, Department of Mechanical and Aerospace Engineering (ReCAPT),

Gajoadong 900, Jinju, Gyeongnam 660-701, Korea

Sang-Kyu Choi

Department of Advanced Industrial Technology, Korea Institute of Material and Machinery,

Jangdong 171, Daejeon 305-343, Korea

A small mixed-type turbine with a diameter of 19.9mm has been substituted for a rotational part of pencil-type air tool. Usually, a vane-type rotor is applied to the rotational part of the air tool. However, the vane-type rotor has some problems, such as friction, abrasion, and necessity of accurate assembly etc.,. These problems make the life time of the vane-type air tool short, but air tools operated by mixed-type turbines are free of friction and abrasion because the turbine rotor dose not contact with the casing. Moreover, it is assembled easily because of no axis offset. These characteristics are merits for using air tools, but loss of power is inevitable on a non-contacting type rotor due to flow loss, tip clearance loss, and profile loss etc.,. In this study, four different rotors are tested, and their characteristics are investigated by measuring the specific output power. Additionally, optimum nozzle location against the rotor is studied. Output powers are obtained through measured pressure, temperature, torque, rotational speed, and flow rate. The experimental results obtained with four different rotors show that the rotor blade shape greatly influences to the performance, and the optimum nozzle location exists near the mid span of the rotor.

Key Words : Mixed-Type Turbine, Rotor Blade Shape, Micro-Turbine, Air Tool, Turbine Performance

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 7, pp. 1488-1502, 2005

A Study on Development of the Three-Dimensional Numerical model to Analyze the Casting Process : Mold Filling and Solidification

Jinho Mok

Nano Cast Korea, Inchon 257-42, Korea

A three dimensional model was developed to analyze the mold filling and solidification in the casting processes.  The model uses the VOF method for the calculation of the free surface and the modified Equivalent Specific Heat method for the treatment of the latent heat evolution.  The solution procedure is based on the SIMPLER algorithm.  The complete model has been validated using the exact solutions for phase change heat transfer and the experimental results of broken water column.  The three-dimensional model has been applied to the benchmark test and the results were compared to those from experiment, a two-dimensional analysis, and another three dimensional numerical model.

Key Words : Mold Filling, Solidification, Free Surface, Phase Change, SIMPLER, VOF, Equivalent Specific Heat

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 7, pp. 1503-1516, 2005

Measurement of Developing Turbulent Flows in a 90-Degree Square Bend with Spanwise Rotation

Young Don Choi*

Professor, Department of Mechanical Engineering, Korea University,

Sungpukku, Seoul 136-701, Korea

Dong Chul Kim

Graduate School, Department of Mechanical Engineering, Korea University,

Sungpukku, Seoul 136-701, Korea

Kun Hee Lee

Associate Professor, Department of Mechanical Engineering, Wonkwang University,

Iksan, Chunbuk, 570-749, Korea

Mean flow and turbulence properties of developing turbulent flows in a 90 degree square bend with span-wise rotation are measured by a hot-wire anemometer. A slanted wire is rotated into 6 orientations and the voltage outputs from them are combined to obtain the mean velocity and the Reynolds stress components. Combined effects of the centrifugal and Coriolis forces due to the curvature and the rotation of the bend on the mean motion and turbulence structures are investigated experimentally. Results show that the two body forces can either enhance or counteract each other depending on the flow direction in the bend.

Key Words : Rotating Curved Duct, Hot-wire measurement, Reynolds Stress, Coriolis Force, Turbulent Flow

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 7, pp. 1517-1525, 2005

Free Surface Tracking for the Accurate Time Response Analysis of Nonlinear Liquid Sloshing

Jin-Rae Cho*, Hong-Woo Lee

School of Mechanical Engineering, Pusan National University, Busan 609-735, Korea

Liquid sloshing displays the highly nonlinear free surface fluctuation when either the external excitation is of large amplitude or its frequency approaches natural sloshing frequencies. Naturally, the accurate tracking of time-varying free surface configuration becomes a key task for the reliable prediction of the sloshing time-history response. However, the numerical instability and dissipation may occur in the nonlinear sloshing analysis, particularly in the long-time beating simulation, when two simulation parameters, the relative time-increment parameter   and the fluid mesh pattern, are not elaborately chosen. This paper intends to examine the effects of these two parameters on the potential-based nonlinear finite element method introduced for the large amplitude sloshing flow.

Key Words: Large Amplitude Sloshing, Nonlinear Finite Element Analysis, Numerical Instability and Dissipation, Relative Time-Increment Parameter, Fluid Mesh Pattern

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 8, pp. 1529-1543, 2005

Attitude Determination GPS/INS Integrated Navigation System with FDI Algorithm for a UAV

Sang Heon Oh

Department of Electronics Engineering, Chungnam National University,

220 Gung-dong, Yuseong-gu, Daejeon 305-764, Korea

Dong-Hwan Hwang

GNSS Technology Research Center, School of Electrical and Computer Engineering,

Chungnam National University, 220 Gung-dong, Yuseong-gu, Daejeon 305-764, Korea

Chansik Park

School of Electrical and Electronics Engineering, Chungbuk National University,

Cheongju 361-763, Korea

Sang Jeong Lee

GNSS Technology Research Center, School of Electrical and Computer Engineering,

Chungnam National University, 220 Gung-dong, Yuseong-gu, Daejeon 305-764, Korea

Se Hwan Kim

Navicom R&D Center, Navicom Co., Ltd., 100 Sinseong-dong, Yuseong-gu, Daejeon 305-345, Korea

Recently an unmanned aerial vehicle (UAV) has been widely used for military and civil applications. The role of a navigation system in the UAV is to provide navigation data to the flight control computer (FCC) for guidance and control. Since performance of the FCC is highly reliant on the navigation data, a fault in the navigation system may lead to a disastrous failure of the whole UAV. Therefore, the navigation system should possess a fault detection and isolation (FDI) algorithm.

This paper proposes an attitude determination GPS/INS integrated navigation system with an FDI algorithm for a UAV. Hardware for the proposed navigation system has been developed. The developed hardware comprises a commercial inertial measurement unit (IMU) and the integrated navigation package (INP) which includes an attitude determination GPS (ADGPS) receiver and a navigation computer unit (NCU). The navigation algorithm was implemented in a real-time operating system with a multitasking structure. To evaluate performance of the proposed navigation system, a flight test has been performed using a small aircraft. The test results show that the proposed navigation system can give accurate navigation results even in a high dynamic environment.

Key Words : Flight Test, GPS, INS, GPS/INS Integration System, Kalman Eilter, Integrity, Fault Detection, UAV

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 8, pp. 1544-1553, 2005

Design and Fabrication of a Micro PZT Cantilever Array Actuator for Applications in Fluidic Systems

Hyonse Kim,

School of Mechanical and Aerospace Engineering Seoul National University,

Shinlim-Dong, San 56-1, Kwanak-Gu Seoul 151-742, Korea

Chihyun In

MEMS Division, DAEWOO Electronics Corp., Kasan-dong, Kumchun-gu, Seoul 153-801, Korea

Gilho Yoon

Department of Mechanical Engineering, Solid Mechanics,Nils Koppels Alle,

DTU, Building 404, Office 131, DK-2800 Kgs. Lyngby, Denmark

Jongwon Kim*

School of Mechanical and Aerospace Engineering Seoul National University,

Shinlim-Dong, San 56-1, Kwanak-Gu Seoul 151-742, Korea

In this article, a micro cantilever array actuated by PZT films is designed and fabricated for micro fluidic systems. The design features for maximizing tip deflections and minimizing fluid leakage are described. The governing equation of the composite PZT cantilever is derived and the actuating behavior predicted. The calculated value of the tip deflection was 15 μm at 5 V. The fabrication process from SIMOX (Separation by oxygen ion implantation) wafer is presented in detail with the PZT film deposition process. The PZT films are characterized by investigating the ferroelectric properties, dielectric constant, and dielectric loss. Tip deflections of 12 μm at 5 V are measured, which agreed well with the predicted value. The 18 μl/s leakage rate of air was observed at a pressure difference of 1000 Pa. Micro cooler is introduced, and its possible application to micro compressor is discussed.

Key Words : Micro Cantilevers Array; PZT Film; Micro Fluidic System

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 8, pp. 1554-1567, 2005

Analysis of Internal Loading at Multiple Robotic Systems

Jae Heon Chung, Byung-Ju Yi*

School of Electrical Engineering and Computer Science, Hanyang University,

1271 sa-1 dong, Ansan, Gyeonggi-do, Korea

Whee Kuk Kim

Department of Control and Instrumentation Engineering, Korea University, Korea

When multiple robotics systems with several sub-chains grasp a common object, the inherent force redundancy provides a chance of utilizing internal loading. Analysis of grasping space based internal loading is proposed in this work since this method facilitates understanding the physical meaning of internal loadings in some applications,  as compared to usual operational space based approach. Investigation of the internal loading for a triple manipulator has been few as compared to a dual manipulator. In this paper, types of the internal loading for dual and triple manipulator systems are investigated by using the reduced row echelon method to analyze the null space of those systems. No internal loading condition is derived and several load distribution schemes are compared through simulation. Furthermore, it is shown that the proposed scheme based on grasping space is applicable to analysis of special cases such as three-fingered and three-legged robots having a point contact with the grasped object or ground.

Key Words: Multiple Robotics Systems, Internal Loading, Load Distribution

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 8, pp. 1568-1575, 2005

Transmission Loss Estimation of Three Dimensional Silencers with

Perforated Internal Structures Using Multi-domain BEM

Hyeon-Don Ju*

School of Fire & Disaster Prevention Engineering, Jinju International University, Chinju 660-759, Korea

Shi-Bok Lee

School of Mechanical Engineering, Pusan National University, Pusan 609-735, Korea

The calculation of the transmission loss of the silencers with complicated internal structures by the conventional BEM combined with the transfer matrix method is incorrect at best or impossible for 3-dimensional silencers due to its inherent plane wave assumption. On this consideration, we propose an efficient practical means to formulate algebraic overall condensed acoustic equations for the whole acoustic structure, where particle velocities on the domain interface boundaries are unknowns, and the solutions are used later to compute the overall transfer matrix elements, based on the multi-domain BEM data. The transmission loss estimation by the proposed method is tested by comparison with the experimental one on an air suction silencer with  perforated internal structures installed in air compressors. The method shows its viability by presenting the reasonably consistent anticipation of the experimental result.

Key Words : Transmission Loss, Overall Condensed Acoustic Equation, Multi-domain BEM(Boundary Element Method), Air Suction Silencer

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 8, pp. 1576-1581, 2005

A Swing-Arm On-Machine Inspection Method for Profile Measurement of Large Optical Surface in Lapping Process

In Kyoung Sung, Chang Jin Oh, Eung Suk Lee*, Ock Hyun Kim

School of Mechanical Engineering, Chungbuk National University, Choungju, 361-763, S-Korea

Generally, the optical components are fabricated by grinding, lapping, and polishing. And, those processes take long time to obtain such a high surface quality. Therefore, in the case of large optical component, the on-machine inspection (OMI) is essential. Because, the work piece is fragile and difficult to set up for fabricating and measuring. This paper is concerned about a swing-arm method for measuring surface profile of large optical concave mirror. The measuring accuracy and uncertainty for suggested method are studied. The experimental results show that this method is useful specially in lapping process with the accuracy of 3～5㎛. Those inspection data are provided for correcting the residual figuring error in lapping or polishing processes.

Key Words : Aspherical optics, Coordinate Measuring Machine (CMM), Lapping, LVDT (Linear Variable Differential Transformer), On-Machine Inspection (OMI), Profile measurement, Swing-Arm

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 8, pp. 1582-1596, 2005

Predicting the Impact of Subsurface heterogeneous Hydraulic Conductivity on the Stochastic Behavior of Well Draw down in a Confined Aquifer Using Artificial Neural Networks

Alaa El-Din Abdin

National Water Research Center-Ministry of Water Resources and Irrigation, Egypt

Mostafa A. M. Abdeen*

Dept. of Engineering Math. & Physics, Faculty of Engineering-Cairo University, Egypt

Groundwater flow and behavior have to be investigated based on heterogeneous subsurface formation since the homogeneity assumption of this formation is not valid. Over the past twenty years, stochastic approach and Monte Carlo technique have been utilized very efficiently to understand the groundwater flow behavior. However, these techniques require lots of computational and numerical efforts according to the various researchers' comments. Therefore, utilizing new techniques with much less computational efforts such as Artificial Neural Network (ANN) in the prediction of the stochastic behavior for the groundwater based on heterogeneous subsurface formation is highly appreciated.

The current paper introduces the ANN technique to investigate and predict the stochastic behavior of a well draw down in a confined aquifer based on subsurface heterogeneous hydraulic conductivity. Several ANN models are developed in this research to predict the unsteady two dimensional well draw down and its stochastic characteristics in a confined aquifer. The results of this study showed that ANN method with less computational efforts was very efficiently capable of simulating and predicting the stochastic behavior of the well draw down resulted from the continuous constant pumping in the middle of a confined aquifer with subsurface heterogeneous hydraulic conductivity.

Keywords : Artificial neural network, Groundwater, Well draw down, Stochastic, heterogeneous subsurface formation

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 8, pp. 1597-1610, 2005

Diagnosing the Cause of Operational Faults in Machine Tools with an Open Architecture CNC

Dong Hoon Kim*

Department of Intelligence & Precision Machines, Korea Institute of Machinery & Materials (KIMM),

Daejeon 305-343, Korea

Sun Ho Kim

Department of Mechatronics Engineering, Dong-Eui University, Pusan 614-714, Korea

Jun-Yeob Song

Department of Intelligence & Precision Machines, Korea Institute of Machinery & Materials (KIMM),

Daejeon 305-343, Korea

The conventional computerized numerical controller (CNC) of machine tools has been increasingly replaced by a PC-based open architecture CNC (OAC) that is independent of a CNC vendor. The OAC and machine tools with an OAC have led to a convenient environment in which user-defined applications can be efficiently implemented within a CNC. This paper proposes a method of diagnosing the cause of operational faults. The method is based on the status of a programmable logic controller in machine tools with an OAC. An operational fault is defined as a disability that occurs during the normal operation of machine tools. Operational faults constitute more than 70 percent of all faults and are also unpredictable because most of them occur without any warning. To quickly and correctly diagnose the cause of an operational fault, two diagnostic models are proposed: the switching function and the step switching function. The cause of the fault is logically diagnosed through a fault diagnosis system using diagnostic models. A suitable interface environment between a CNC and developed application modules is constructed to implement the diagnostic functions in the CNC domain. The results of the diagnosis were displayed on a CNC monitor for machine operators and transmitted to a remote site through a Web browser. The proposed diagnostic method and its results were useful to unskilled machine operators and reduced the machine downtime.

Keywords: Open architecture CNC; Diagnosing Causes; Operational faults; Machine Tools; Diagnostic models

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 8, pp. 1611-1620, 2005

Enhancing the Reconstruction of Acoustic Source Field using Wavelet Transformation

Byeongsik Ko

Korea Simulation Technology Inc., Hapjung-Dong, Mapo-Ku, Seoul 120-749, Korea

Seung-Yop Lee*

Department of Mechanical Engineering, Sogang University,

Shinsu-Dong, Mapo-Ku, Seoul 121-742, Korea

This paper shows the use of wavelet transformation combined with inverse acoustics to reconstruct the surface velocity of a noise source. This approach uses the boundary element analysis based on the measured sound pressure at a set of field points, the Helmholtz integral equations and wavelet transformation for reconstructing the normal surface velocity field. The reconstructed field can be diverged due to the small measurement errors in the case of nearfield acoustic holography (NAH) using an inverse boundary element method. In order to avoid this instability in the inverse problem, the reconstruction process should include some form of regularization for enhancing the resolution of source images. The usual method of regularization has been the truncation of wave vectors associated with small singular values, although the order of an optimal truncation is difficult to determine. In this paper, a wavelet transformation is applied to reduce the computation time for inverse acoustics and to enhance the reconstructed vibration field. The computational speed-up is achieved, with solution time being reduced to 14.5%.

Key Words : Wavelet, Boundary Element Method(BEM), Nearfield Acostic Holography(NAH), Acoustics

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 8, pp. 1621-1631, 2005

A Study on the Control Characteristics of ER Valve-FHA System and Durability Test

Sung-Cheol Jang

Department of Mechanical and Automation Engineering, Kyungnam University,

449 Wolyoung Dong, Masan, Kyungnam 631-701, Korea, Interim Full-time Instructor

Tae-Hyun Chang*

Department of Mechanical and Automation Engineering, Kyungnam University,

449 Wolyoung Dong, Masan, Kyungnam 631-701, Korea

In this paper, making the best use of the features of the electro-rheological(ER) valve, a two-port pressure control valve using ER fluids is proposed and manufactured. The ER-Valve characteristics are evaluated by changing the intensity of the electric field and the number of electrode. As only with electrical signal change to the ER-Valve in which ER fluid flowing, ER fluid flow is controlled, so development of simple ER-Valves have been tried. The ER-Valves and pressure drop check method are considered to be applied to the fluid power industry. Using the manufactured pressure control valve, a one-link manipulator with FHA(Flexible Hydraulic Actuator) is driven. As a result, it is experimentally confirmed that the pressure control valve using ER fluids is applicable to use in driving actuator. If it applies characteristics of the ER fluids, it will be able to apply in the control system for the ER Valve which occurs from industrial controller. After having durability test, shear stress increased regularly because of starch particles crushed by pump and particle size that was almost the same. Moreover, Ra of copper electrode increased about 1.56 times rather than before those of performing durability test, and Rz increased about 2.2 times.

Key Words : Flexible Hydraulic Actuator, ER-Valve, Manipulator, Control System, Industrial Controller, Durability Test

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 8, pp. 1632-1648, 2005

Reynolds Number Effects on the Non-Nulling Calibration of a Cone-Type Five-Hole Probe for

Turbomachinery Applications

Sang Woo Lee*, Sang Bae Jun

School of Mechanical Engineering, Kumoh National Institute of Technology,

188 Shinpyong, Gumi, Gyongbook 730-701, Korea

The effects of Reynolds number on the non-nulling calibration of a typical cone-type five-hole probe have been investigated for the representative Reynolds numbers in turbomachinery. The pitch and yaw angles are changed from -35 degrees to 35 degrees with an angle interval of 5 degrees at six probe Reynolds numbers in range between 6.60 ´ 103 and 3.17 ´ 104. The result shows that not only each calibration coefficient itself but also its Reynolds number dependency is affected significantly by the pitch and yaw angles. The Reynolds-number effects on the pitch- and yaw-angle coefficients are noticeable when the absolute values of the pitch and yaw angles are smaller than 20 degrees. The static-pressure coefficient is sensitive to the Reynolds number nearly all over the pitch- and yaw-angle range. The Reynolds-number effect on the total-pressure coefficient is found remarkable when the absolute values of the pitch and yaw angles are larger than 20 degrees. Through a typical non-nulling reduction procedure, actual reduced values of the pitch and yaw angles, static and total pressures, and velocity magnitude at each Reynolds number are obtained by employing the calibration coefficients at the highest Reynolds number (Re = 3.17 ´ 104) as input reference calibration data. As a result, it is found that each reduced value has its own unique trend depending on the pitch and yaw angles. Its general tendency is related closely to the variation of the corresponding calibration coefficient with the Reynolds number. Among the reduced values, the reduced total pressure suffers the most considerable deviation from the measured one and its dependency upon the pitch and yaw angles is most noticeable. In this study, the root-mean-square data as well as the upper and lower bounds of the reduced values are reported as a function of the Reynolds number. These data would be very useful in the estimation of the Reynolds-number effects on the non-nulling calibration.

Key Words: Five-Hole Probe, Non-Nulling Calibration, Reynolds Number, Turbomachinery

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 8, pp. 1649-1661, 2005

Heat Transfer of an Evaporating Liquid on a Horizontal Plate

Sang Woo Joo, Min Soo Park*, Min Suk Kim

School of Mechanical Engineering, Yeungnam University, Gyongsan, 712-749, Korea

We consider a horizontal static liquid layer on a planar solid boundary. The layer is evaporating when the plate is heated. Vapor recoil and thermo-capillary are discussed along with the effect of mass loss and vapor convection due to evaporating liquid and non-equilibrium thermodynamic effects. These coupled systems of equations are reduced to a single evolution equation for the local thickness of the liquid layer by using a long-wave asymptotics. The partial differential equation is solved numerically.

Key Words: Thermo-capillary, Evaporating liquid, Long-wave approximation, Evolution equation

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 8, pp. 1662-1669, 2005

Theoretical and Experimental Studies on Boiling Heat Transfer for the Thermosyphons with

Various Helical Grooves

Kyuil Han

School of Mechanical Engineering, Pukyong National University,

San 100, Yongdang-dong, Nam-ku, Pusan, 608-739, Korea

Dong-Hyun Cho*

Department of Computer Applied Mechanical Design Engineering, Daejin University,

Sundang-Dong, Pocheon-City, Kyonggi-Do, 487-711, Korea

Boiling heat transfer characteristics of a two-phase closed thermosyphons with various helical grooves are studied experimentally and a mathematical correlation is developed to predict the performance of such thermosyphons. The study focuses on the boiling heat transfer characteristics of  two-phase closed thermosyphons with copper tubes having 50, 60, 70, 80, 90 internal helical grooves. A two-phase closed thermosyphon with plain copper tube having the same inner and outer diameter as those of grooved tubes is also tested for comparison. Water, methanol and ethanol are used as working fluid. The effects of the number of grooves, various working fluids, operating temperature and heat flux are investigated experimentally. From these experimental results, a mathematical model is developed. In the present model, boiling of liquid pool in the evaporator is considered for the heat transfer mechanism of the thermosyphons. And also the effects of the number of grooves, the various working fluids, the operating temperature and the heat flux are brought into consideration. A good agreement between the boiling heat transfer coefficient of the thermosyphon estimated from experimental results and the predictions from the present mathematical correlation is obtained. The experimental results show that the number of grooves, the amount of the working fluid and the various working fluids are very important factors for the operation of thermosyphons. Also, the thermosyphons with internal helical grooves can be used to achieve some inexpensive and compact heat exchangers in low temperature.

Key Words : Boiling, Internal helical grooves, Heat transfer coefficient, Thermosyphon, Evaporator

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 8, pp. 1670-1681, 2005

In-Situ Diagnosis of Vapor-Compressed Chiller Performance for Energy Saving

Younggy Shin*,

Department of Mechanical Engineering, Sejong University, Seoul 143-747, Korea

Youngil Kim

School of Architecture, Seoul National University of Technology, Seoul 139-743, Korea

Guee-Won Moon, Seok-Weon Choi

Space Test Dept., Korea Aerospace Research Institute, Daejeon, Korea

Abstract: In-situ diagnosis of chiller performance is an essential step for energy saving business. The main purpose of the in-situ diagnosis is to predict the performance of a target chiller. Many models based on thermodynamics have been proposed for the purpose. However, they have to be modified from chiller to chiller and require profound knowledge of thermodynamics and heat transfer. This study focuses on developing an easy-to-use diagnostic technique that is based on adaptive neuro-fuzzy inference system (ANFIS). The effect of sample data distribution on training the ANFIS is investigated. It is found that the data sampling over 10 days during summer results in a reliable ANFIS whose performance prediction error is within measurement errors. The reliable ANFIS makes it possible to prepare an energy audit and suggest an energy saving plan based on the diagnosed chilled water supply system.

Key Words: centrifugal chiller, ESCO (Energy Saving Company), artificial neural network, ANFIS, COP, chilled water, dynamics, diagnosis

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 8, pp. 1682-1691, 2005

Space-Time Characteristics of the Wall Shear-Stress Fluctuations in an Axial Turbulent Boundary Layer

with Transverse Curvature

Dongshin Shin*

Department of Mechanical System Design Engineering, College of Engineering, Hongik University,

Seoul 121-791, Korea

Seungbae Lee

Department of Mechanical Engineering, College of Engineering, Inha University,

Incheon 402-751, Korea

Yang Na

CAESIT, Department of Mechanical Engineering, Konkuk University, Seoul 143-701, Korea

Direct numerical simulation database of an axial turbulent boundary layer is used to compute frequency and wave number spectra of the wall shear-stress fluctuations in a low-Reynolds number axial turbulent boundary layer. One-dimensional and two-dimensional power spectra of flow variables are calculated and compared. At low wave numbers and frequencies, the power of streamwise shear stress is larger than that of spanwise shear stress, while the powers of both stresses are almost the same at high wave numbers and frequencies. The frequency/streamwise wave number spectra of the wall flow variables show that large-scale fluctuations to the rms value is largest for the streamwise shear stress, while that of small-scale fluctuations to the rms value is largest for pressure. In the two-point auto-correlations, negative correlation occurs in streamwise separations for pressure, and in spanwise correlation for both shear stresses.

Key Words : Turbulent boundary layer, Transverse curvature, Direct numerical simulation

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 9, pp. 1695-1705, 2005

Time Optimal Attitude Maneuver Strategies for the Agile Spacecraft with Reaction Wheels and Thrusters

Byung-Hoon Lee

Graduate Student, School of Aerospace and Mechanical Engineering,

Hankuk Aviation University, Goyang 412-791, Korea

Bong-Un Lee

Graduate Student, Ph.D. candidate, School of Aerospace and Mechanical Engineering,

Hankuk Aviation University, Goyang 412-791, Korea

Hwa-Suk Oh*

Associate Professor, School of Aerospace and Mechanical Engineering,

Hankuk Aviation University, Goyang 412-791, Korea

Seon-Ho Lee,

Senior Researcher, Group of Satellite Control System,

Korea Aerospace Research Institute, Daejeon 305-333, Korea

Seung-Wu Rhee

Group Manager, Group of Satellite Control System,

Korea Aerospace Research Institute, Daejeon 305-333, Korea

Reaction wheels and thrusters are commonly used for the satellite attitude control. Since satellites frequently need fast maneuvers, the minimum time maneuvers have been extensively studied. When the speed of attitude maneuver is restricted due to the wheel torque capacity of low level, the combinational use of wheel and thruster is considered. In this paper, minimum time optimal control performances with reaction wheels and thrusters are studied. We first identify the features of the maneuvers of the satellite with reaction wheels only. It is shown that the time-optimal maneuver for the satellite with four reaction wheels in a pyramid configuration occurs on the fashion of single axis rotation. Pseudo control logic for reaction wheels is successfully adopted for smooth and chattering-free time-optimal maneuvers. Secondly, two different thrusting logics for satellite time-optimal attitude maneuver are compared with each other: constant time-sharing thrusting logic and varying time-sharing thrusting logic. The newly suggested varying time-sharing thrusting logic is found to reduce the maneuvering time dramatically. Finally, the hybrid control with reaction wheels and thrusters are considered. The simulation results show that the simultaneous actuation of reaction wheels and thrusters with varying time-sharing logic reduces the maneuvering time enormously. Spacecraft model is KOrea Multi-Purpose SATellite (KOMPSAT)-2 which is being developed in Korea as an agile maneuvering satellite.

Key words: Time-optimal control, Reaction Wheel, Thrusting logics, Hybrid control

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 9, pp. 1706-1710, 2005

Conversion of the Sonic Conductance C and the Critical Pressure Ratio b into the Airflow Coefficient μ

Szymon Grymek*

Chair of Machinery Design and Exploitation, Gda?sk University of Technology,

Narutowicza 11/12, 80?952 Gdansk, Poland

Tomasz Kiczkowiak

Chair of Control Systems, Technical University of Koszalin,

Raclawicka 15?17, 75?620 Koszalin, Poland

In a case of computer simulation used for the verification of pneumatic system performance one of the main problems is that various parameters can be used to describe flow characteristics of the system components. The Standard ISO 6358 offers two parameters: the sonic conductance C and the critical static pressure ratio b, but the parameters can not be directly utilised in an analysis of a pneumatic system. In the standard analysis there is applied the airflow coefficient m, but it is not presented in the vendors' catalogues. In the paper the numerical algorithm for calculation of the airflow coefficient m (which is required for computer simulation) as a function of sonic conductance C and a critical pressure ratio b (recommended by the standard) is presented. Additionally, because of the iterative character of the described algorithm, an artificial neural network approach to solve the problem is proposed.

Key Words: Pneumatics, ANN, CAD, Flow Properties

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 9, pp. 1711-1719, 2005

Resonance Frequency and Quality Factor Tuning in Electrostatic

Actuation of Nanoelectromechanical Systems

Dong Hwan Kim*

School of Mechanical Design and Automation Engineering,

Institute of Precision Machinery Technology, Seoul National University of Technology,

172 Gongreung-dong, Nowon-gu, Seoul, 139-743  Korea

Abstract:  In an electro statically actuated nanoelectromechanical system (NEMS) resonator, it is shown that both the resonance frequency and the resonance quality (Q) factor can be manipulated. How much the frequency and quality factor can be tuned by excitation voltage and resistance on a doubly-clamped beam resonator is addressed. A mathematical model for investigating the tuning effects is presented. All results are shown based on the feasible dimension of the nano resonator and appropriate external driving voltage, yielding up to 20 MHz resonance frequency. Such parameter tuning could prove to be a very convenient scheme to actively control the response of NEMS for a variety of applications.

Key words:  Nano Resonator, Resonance Shift, Quality Factor Shift, Parametric Resonance, NEMS, Electrostatic

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 9, pp. 1720-1730, 2005

Object-Transportation Control of Cooperative AGV Systems

Based on Virtual-Passivity Decentralized Control Algorithm

Jin Ho Suh

Department of Electrical Engineering, Dong-A University,

National Research Laboratory (NRL), 840, Hadan2-Dong Saha-gu, Busan, 604-714, Korea

Young Jin Lee

Department of Electrical Instrument and Control, Korea Aviation Polytechnic College,

438 Egeum-dong, Sachon City, Kyungnam, 664-180, Korea

Kwon Soon Lee*

Department of Electrical Engineering, Dong-A University,

National Research Laboratory (NRL), 840, Hadan2-Dong Saha-gu, Busan, 604-714, Korea.

Automatic guided vehicle in the factory has an important role to advance the flexible manufacturing system. In this paper, we propose a novel object-transportation control algorithm of cooperative AGV systems to apply decentralized control to multiple AGV systems. Each AGV system is under nonholonomic constraints and conveys a common object-transportation in a horizontal plain. Moreover it is shown that cooperative robot systems ensure stability and the velocities of augmented systems convergence to a scaled multiple of each desired velocity field for cooperative AGV systems. Finally, the application of proposed virtual passivity-based decentralized control algorithm via system augmentation is applied to trace a circle. Finally, the simulation and experimental results for the object-transportation by two AGV systems illustrates the validity of the proposed virtual-passivity decentralized control algorithm.

Key Words: Automatic guided vehicle (AGV), Decentralized control algorithm, Passivity, Passive velocity field control (PVFC), wheeled mobile robot (WMR), Lyapunov stability

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 9, pp. 1731-1741, 2005

Influence of Tip mass on Dynamic Behavior

of Cracked Cantilever Pipe Conveying Fluid with Moving Mass

Han-Ik Yoon*

Division of Mechanical Engineering, Dong-eui University,

995 Eomgwangno, Busanjin-Gu, Busan, 614-714, Korea

In-Soo Son

The Center for Industrial Technology, Dong-eui University,

995 Eomgwangno, Busanjin-Gu, 614-714, Korea

In this paper, we studied about the effect of the open crack and a tip mass on the dynamic behavior of a cantilever pipe conveying fluid with a moving mass. The equation of motion is derived by using Lagrange’s equation and analyzed by numerical method. The cantilever pipe is modelled by the Euler-Bernoulli beam theory. The crack section is represented by a local flexibility matrix connecting two undamaged pipe segments. The influences of the crack, the moving mass, the tip mass and its moment of inertia, the velocity of fluid, and the coupling of these factors on the vibration mode, the frequency, and the tip-displacement of the cantilever pipe are analytically clarified.

Key Words : Dynamic Behavior, Open Crack, Cantilever Pipe Conveying Fluid, Moving  Mass, Tip Mass, Euler-Bernoulli Beam, Flexibility Matrix

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 9, pp. 1742-1752, 2005

A Multi-target Tracking Algorithm for Application to Adaptive Cruise Control

Il-ki Moon

Department of Automotive Engineering, Hanyang University, Seoul, 133-791, korea

Kyongsu Yi*

School of Mechanical Engineering, Hanyang University, Seoul, 133-791, Korea

Derek Caveney, J. Karl Hedrick

Department of Mechanical Engineering, University of California, Berkeley, Berkeley, CA, USA 94720

This paper presents a Multiple Target Tracking (MTT) Adaptive Cruise Control (ACC) system which consists of three parts; a multi-model-based multi-target state estimator, a primary vehicular target determination algorithm, and a single-target adaptive cruise control algorithm. Three motion models, which are validated using simulated and experimental data, are adopted to distinguish large lateral motions from longitudinally excited motions. The improvement in the state estimation performance when using three models is verified in target tracking simulations. However, the performance and safety benefits of a multi-model-based MTT-ACC system is investigated via simulations using real driving radar sensor data. The MTT-ACC system is tested under lane changing situations to examine how much the system performance is improved when multiple models are incorporated. Simulation results show system response that is more realistic and reflective of actual human driving behavior.

KEY WORDS: Interacting Multiple Model, Probabilistic Data Association, Adaptive Cruise Control, Stop & Go Cruise Control, Advanced Safety Vehicle, Milli-meter Wave Radar

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 9, pp. 1753-1760, 2005

Eigenvalue Analysis of Double-span Timoshenko Beams by Pseudospectral Method

Jinhee Lee*

Department of Mechano-Informatics, Hongik University,

Chochiwon, Yeonki-kun, Choongnam, 339-701, Korea

The pseudospectral method is applied to the free vibration analysis of double-span Timoshenko beams. The analysis is based on the Chebyshev polynomials. Each section of the double-span beam has its own basis functions, and the continuity conditions at the intermediate support as well as the boundary conditions are treated separately as the constraints of the basis functions. Natural frequencies are provided for different thickness-to-length ratios and for different span ratios, which agree with those of Euler-Bernoulli beams when the thickness-to-length ratio is small but deviate considerably as the thickness-to-length ratio grows larger.

Key Words: Eigenvalue Analysis, Double-span Timoshenko Beam, Pseudospectral Method, Chebyshev Polynomials

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 9, pp. 1761-1772, 2005

A Numerical Analysis on the Curved Bileaflet Mechanical Heart Valve (MHV) : Leaflet Motion and Blood Flow in an Elastic Blood Vessel

Jin Seok Bang

Mechanical Engineering Department, Graduate School of Kyunghee University,

1 Seochon, Kihung, Yongin, Kyunggi, 449-701, Korea

Choeng Ryul Choi

College of Environmental Engineering, An Yang University,

Anyang 5-dong, Manan-gu, Anyang-shi, Kyunggi, 430-714, Korea

Chang Nyung Kim*

College of Advanced Technology, Kyunghee University,

1 Seochon, Kihung, Yongin, Kyunggi, 449-701, Korea

In blood flow passing through the mechanical heart valve (MHV) and elastic blood vessel, hemolysis and platelet activation causing thrombus formation can be seen owing to the shear stress in the blood. Also, fracture and deformation of leaflets can be observed depending on the shape and material properties of the leaflets which is opened and closed in a cycle. Hence, comprehensive study is needed on the hemodynamics which is associated with the motion of leaflet and elastic blood vessel in terms of fluid-structure interaction. In this paper, a numerical analysis has been performed for a three-dimensional pulsatile blood flow associated with the elastic blood vessel and curved bileaflet for multiple cycles in light of fluid-structure interaction. From this analysis fluttering phenomenon and rebound of the leaflet have been observed and recirculation and regurgitation have been found in the flow fields of the blood. Also, the pressure distribution and the radial displacement of the elastic blood vessel have been obtained. The motion of the leaflet and flow fields of the blood have shown similar tendency compared with the previous experiments carried out in other studies. The present study can contribute to the design methodology for the curved bileaflet mechanical heart valve. Furthermore, the proposed fluid-structure interaction method will be effectively used in various fields where the interaction between fluid flow and structure are involved.

Key words : Mechanical Heart Valve (MHV), Artery, Thrombus Formation, Henodynamics, Fluid-Structure Interaction (FSI)

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 9, pp. 1773-1780, 2005

Numerical Simulation of the Aluminum Alloys Solidification in Complex Geometries

Eliseu Monteiro, Abel Rouboa*

Engineering Department, University of UTAD, 5000, Vila Real, Portugal

The process of mould design in the foundry industry has been based on the intuition and experience of foundry engineers and designers. To bring the industry to a more scientific basis the design process should be integrated with scientific analysis such as heat transfer. The production by foundry techniques is influenced by the geometry configuration, which affects the solidification conditions and subsequent cooling. Numerical simulation and/or experiments make possible the selection of adequate materials, reducing cycle times and minimizing production costs. The main propose of this work is to study the heat transfer phenomena in the mould considering the phase change of the cast-part. Due to complex geometry of the mould, a block unstructured grid and a generalized curvilinear formulation engaged with the finite volume method is described and applied. Two types of boundary conditions, diffusive and Newtonian, are used and compared. The developed numerical code is tested in real case and the main results are compared with experimental data. The results showed that the solidification time is about 6 seconds for diffusive boundary conditions and 14.8 seconds for Newtonian boundary conditions. The use of the block unstructured grid in combination with a generalized curvilinear formulation works well with the finite volume method and allows the development of more efficient algorithms with better capacity to describe the part contours through a lesser number of elements.

Keywords : Solidification, Heat transfer, Phase change, Finite Volume

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 9, pp. 1781-1789, 2005

Non-Adiabatic Flamelet Modeling for Combustion Processes of Oxy-Natural Gas Flame

Gunhong Kim, Yongmo Kim*

Department of Mechanical Engineering, Hanyang University,

17 Haengdang-dong, Seongdong-gu, Seoul, 133-791, Korea

In order to realistically predict the combustion characteristics of the oxy-fuel flame, the present study employs the non-adiabatic flamelet approach. In this combustion model, the detailed equilibrium chemistry is utilized to accurately account for the thermal dissociation as well as to properly include the radiative cooling effects on the detailed chemistry. Numerical results indicate that the present approach has the capability to correctly capture the essential features and precise structure of the oxy-fuel flames. In this work, the detailed discussion has been made for the characteristics of oxy-fuel flames, the capability and defect of the present approach and also uncertainties of experimental data.

Key Words : Oxy-Fuel Combustion, Flamelet Model, Probability Density Function, Radiative Heat Transfer, Unstructured-Grid Finite Volume Method

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 9, pp. 1790-1800, 2005

Numerical Analysis of Pulsating Heat Pipe Based on Separated Flow Model

Jong-Soo Kim*

School of Mechanical Engineering, Pukyong National University,

San 100, Yongdang dong, Nam-gu, Pusan 608-737, Korea

Yong-Bin Im, Ngoc Hung Bui

Dept. of Refrigeration and Air Conditioning Eng., Graduate School of Pukyong National University,

San 100, Yongdang dong, Nam-gu, Pusan 608-737, Korea

The examination on the operating mechanism of a pulsating heat pipe (PHP) using visualization revealed that the working fluid in the PHP oscillated to the axial direction by the contraction and expansion of vapor plugs. This contraction and expansion is due to the formation and extinction of bubbles in the evaporating and condensing section, respectively. In this paper, a theoretical model of PHP was presented. The theoretical model was based on the separated flow model with two liquid slugs and three vapor plugs. The results show that the diameter, surface tension and charge ratio of working fluid have significant effects on the performance of the PHP. The following conclusions were obtained. The periodic oscillations of liquid slugs and vapor plugs were obtained under specified parameters. When the hydraulic diameter of the PHP was increased to d = 3 mm, the frequency of oscillation decreased. By increasing the charging ratio from 40 to 60 by volume ratio, the pressure difference between the evaporating section and condensing section increased, the amplitude of oscillation reduced, and the oscillation frequency decreased. The working fluid with higher surface tension resulted in an increase in the amplitude and frequency of oscillation. Also the average temperature of vapor plugs decreased.

Key Words: Pulsating Heat Pipe (PHP), Separated Flow Model, Heat Transport

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 9, pp. 1801-1810, 2005

Turbulent Flow over Thin Rectangular Riblets

O. A. El-Samni

Mechanical power Engineering Dept., The University of Alexandria,

El-Chatby, Alexandria  21411, Egypt

Hyun Sik, Yoon*, Ho Hwan, Chun

Advanced Ship Engineering Research Center (ASERC), Pusan National University,

San 30, Jangjeon-dong, Geumjeong-gu, Busan 609-735, South Korea

The effect of longitudinal thin rectangular riblets aligned with the flow direction on turbulent channel flow has been investigated using direct numerical simulation. The thin riblets have been modeled using the immersed boundary method (IBM) where the velocities at only one set of vertical nodes at the riblets positions are enforced to be zeros. Different spacings, ranging between 11 and 43 wall units, have been simulated aiming at getting the optimum spacing corresponding to the maximum drag reduction while keeping the height/spacing ratio at 0.5. Reynolds number based on the friction velocity   and the channel half depth   is set to 150. The flow is driven by adjusted pressure gradient so that the mass flow rate is kept constant in all the simulations. This study shows similar trend of the drag ratio to that of the experiments at the different spacings. Also, this research provides an optimum spacing of around 17 wall units leading to maximum drag reduction as experimental data. Explanation of drag increasing/decreasing mechanism is highlighted.

Keywords: Drag Reduction, Riblets, Turbulent Channel Flow, DNS, IBM, Flow Control

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 9, pp. 1811-1820, 2005

A CFD Study on Thermo-Acoustic Instability of Methane/Air Flames in Gas Turbine Combustor

Chae Hoon Sohn*

Department of Aerospace Engineering, Chosun University, Gwangju 501-759, Korea

Han Chang Cho

Research Institute of Industrial Science and Technology,

San 32 Hyoja-dong, Nam-gu, Pohang 790-600, Korea

Thermo-acoustic instability of methane/air flames in an industrial gas-turbine combustor is numerically investigated adopting CFD analysis. The combustor has 37 EV burners through which methane and air are mixed and then injected into the chamber. First, steady fuel/air mixing and flow characteristics established by the burner are investigated by numerical analysis with single burner. And then, based on information on the flow data, the burners are modeled numerically via equivalent swirlers, which facilitates the numerical analysis with the whole combustion system including the chamber and numerous burners. Finally, reactive flow fields within the chamber are investigated numerically by unsteady analysis and thereby, spontaneous instability is simulated. Based on the numerical results, scaling analysis is conducted to find out the instability mechanism in the combustor and the passive control method to suppress the instability is proposed and verified numerically.

Key Words : Thermo-Acoustic Instability, Gas-Turbine Combustor, Burners, Spontaneous Instability

Journal of Mechanicl Science and Technology (KSME I. J.), Vol. 19, No. 9, pp. 1821-1832, 2005

Hot-Fire Injector Test for Determination of Combustion Stability Boundaries Using Model Chamber

Chae Hoon Sohn*

Department of Aerospace Engineering, Chosun University, Gwangju 501-759, Korea

Woo-Seok Seol

Rocket Engine Department, Korea Aerospace Research Institute,

POBox 113, Yusung, Daejeon 305-600, Korea

Alexander A. Shibanov, Valery P. Pikalov

Research Institute of Chemical Building (NIICHIMMASH), Russia

This study realizes the conceptual method to predict combustion instability in actual full-scale combustion chamber of rocket engines by experimental tests with model (sub-scale) chamber. The model chamber was designed based on the methodologies proposed in the previous work regarding geometrical dimensions and operating conditions, and hot-fire test procedures were followed to obtain stability boundaries. From the experimental tests, two instability regions are presented by the parameters of combustion-chamber pressure and mixture (oxidizer/fuel) ratio, which are customary for combustor designers. It is found that instability characteristics in the chamber with the adopted jet injectors can be explained by the correlation between the characteristic burning or mixing time and the characteristic acoustic time. In each instability region, dynamic behaviors of flames are investigated to verify the hydrodynamically-derived characteristic lengths of the jet injectors. Large-amplitude pressure oscillation observed in upper instability region is found to be generated by lifted-off flames.

Key Words : Combustion Instability, Stability Boundary, Hot-Fire Injector Test, Model Combustion Chamber

Journal of Mechanicl Science and Technology, Vol. 19, No. 10, pp. 1835-1845, 2005

Safe Arm Design with MR-based Passive Compliant Joints and

Visco-elastic Covering for Service Robot Applications

Seong-Sik Yoon

Intelligent Systems Institute, National Institute of Advanced Industrial Science and Technology,

1-1-1 Umezono, Tsukuba-shi Ibaraki, 305-8568 Japan

Sungchul Kang*, Seung-kook Yun and Seung-Jong Kim

Intelligent Robotics Research Center and Tribology Research Center,

Korea Institute of Science and Technology, Hawolgok-dong 39-1, Sungbuk-ku, Seoul 136-791, Korea

Young-Hwan Kim

Intelligent Mechanical System Research Dept., Electro-Mechanical Research Institute Hyundai Heavy Industries Co., Ltd., Mabuk-ri, Kuseong-myun, Yongin-shi, Kyunggi-do 449-716 Korea

Munsang Kim

Intelligent Robotics Research Center, Korea Institute of Science and Technology,

Hawolgok-dong 39-1, Sungbuk-ku, Seoul 136-791, Korea

Abstract - In this paper a safe arm with passive compliant joints and visco-elastic covering is designed for human-friendly service robots. The passive compliant joint (PCJ) is composed of a magneto-rheological (MR) damper and a rotary spring. In addition to a spring component, a damper is introduced for damping effect and works as a rotary viscous damper by controlling the electric current according to the angular velocity of spring displacement. When a manipulator interacts with human or environment, the joints and cover passively operate and attenuate the applied collision force. The force attenuation property is verified through collision experiments showing that the proposed passive arm is safe in view of some evaluation measures.

Key Words:  Safety, Service Robot, Passive Compliant Joint, Magneto-rheological Fluid, Visco-elastic Covering

Journal of Mechanicl Science and Technology, Vol. 19, No. 10, pp. 1846-1855, 2005

A study of “Mode Selecting Stochastic Controller” for a dynamic system under random vibration

Yong-Kwan Kim, Jong-Bok Lee

Dynamic System Analysis and Control Lab., Dept. of Control and Instrumentation Engineering,

Korea University, 1, 5-Ka, Anam-Dong, Sungbuk-Ku, Seoul, 136-701, Korea

Hoon Heo*

Dept. of Control and Instrumentation Engineering, Korea University,

1, 5-Ka, Anam-Dong, Sungbuk-Ku, Seoul, 136-701, Korea

This paper presents a new stochastic controller applied on the vibration control system under irregular disturbances based on the mode selection scheme. Measured displacement and frequency characteristics are simultaneously used in designing a mode selecting controller. This technique is validated by applying to the suppression problem of a flexible beam with randomly vibrated circumstances.

The presented method, called Mode Selecting Stochastic Controller, uses the frequency measurement of the flexible system based on a Fast-Fourier transformation algorithm. This controller is constructed by combining mode selection method with previous known Stochastic Controller in real time.  Numerical simulations and several experiments are conducted to validate the proposed method. The performance of the proposed method is compared with a stochastic controller developed recently. This method was improved compared with previous one.

Key Words : Sfochastic Controller, White Noise, Monte Carlo Method, F-P-K(Fokker-Plank-Kolomogorv) Equation, Mode Selecting Unit

Journal of Mechanicl Science and Technology, Vol. 19, No. 10, pp. 1856-1863, 2005

A Study on a Vision Sensor System for Tracking the I-Butt Weld Joints

Jae-Woong Kim*

School of Mechanical Engineering, Yeungnam University,

Dae-dong, Kyongsan-si, Kyongbuk 712-749, Korea

Hee-Soo Bae

Korea Electric Power Research Institute, Munji-dong, Yusung-gu, Daejeon, 305-380, Korea

In this study, a visual sensor system for weld seam tracking the I-butt weld joints in GMA welding was constructed.  The sensor system consists of a CCD camera, a diode laser with a cylindrical lens and a band-pass-filter to overcome the degrading of image due to spatters and arc light.  In order to obtain the enhanced image, quantitative relationship between laser intensity and iris opening was investigated.  Throughout the repeated experiments, the shutter speed was set at 1/1000 second for minimizing the effect of spatters on the image, and therefore the image without the spatter traces could be obtained.  Region of interest was defined from the entire image and gray level of the searched laser stripe was compared to that of weld line.  The differences between these gray levels lead to spot the position of weld joint using central difference method.  The results showed that, as long as weld line is within ±15° from the longitudinal straight line, the system constructed in this study could track the weld line successfully. Since the processing time is no longer than 0.05 sec, it is expected that the developed method could be adopted to high speed welding such as laser welding.

Key Words : Vision sensor, Weld seam tracking, Region of interest, Image processing, Laser stripe, Gray level, Windowing, Central difference method, I-Butt weld joint

Journal of Mechanicl Science and Technology, Vol. 19, No. 10, pp. 1864-1874, 2005

Teleloperation of Field Mobile Manipulator with Wearable Haptic-based Multi-Modal User Interface

and Its Application to Explosive Ordnance Disposal

Dongseok Ryu

Intelligent Robotics Research Center, Korea Institute of Science and Technology, Seoul, Korea

Department of Mechanical Engineering, Korea University, Seoul, Korea

Chang-Soon Hwang

Intelligent Robotics Research Center, Korea Institute of Science and Technology, Seoul, Korea

Sungchul Kang*

Intelligent Robotics Research Center, Korea Institute of Science and Technology, Seoul, Korea

Munsang Kim

Intelligent Robotics Research Center, Korea Institute of Science and Technology, Seoul, Korea

Jae-Bok Song

Department of Mechanical Engineering, Korea University, Seoul, Korea

This paper describes a wearable multi-modal user interface design and its implementation for a teleoperated field robot system. Recently some teleoperated field robots are employed for hazard environment applications (e.g. rescue, explosive ordnance disposal, security). To complete these missions in outdoor environment, the robot system must have appropriate functions, accuracy and reliability. However, the more functions it has, the more difficulties occur in operation of the functions. To cope up with this problem, an effective user interface should be developed. Furthermore, the user interface is needed to be wearable for portability and prompt action. This research starts at the question: how to teleoperate the complicated slave robot easily. The main challenge is to make a simple and intuitive user interface with a wearable shape and size. This research provides multi-modalities such as visual, auditory and haptic sense. It enables an operator to control every functions of a field robot more intuitively. As a result, an EOD (explosive ordnance disposal) demonstration is conducted to verify the validity of the proposed wearable multi-modal user interface.

Key Words : wearable device, multi-modal interface, field robot, teleoperation, haptics

Journal of Mechanicl Science and Technology, Vol. 19, No. 10, pp. 1875-1884, 2005

Design of Neural Networks Model for Transmission Angle of a Modified Mechanism

Şahin Yıldırım*, Selçuk Erkaya, Şükrü Su and İbrahim Uzmay

Erciyes University, Engineering Faculty, Department of Mechanical Engineering Kayseri/TURKEY

This paper discusses Neural Networks as predictor for analyzing of transmission angle of slider-crank mechanism. There are different types of neural network algorithms obtained by using chain rules. The neural network is a feedforward neural network. On the other hand, the slider-crank mechanism is a modified mechanism by using an additional link between connecting rod and crank pin. Through extensive simulations, these neural network models are shown to be effective for prediction and analyzing of a modified slider-crank mechanism’s transmission angle.

Keywords: Transmission angle, Neural network, Slider-crank mechanism, Learning algorithms

Journal of Mechanicl Science and Technology, Vol. 19, No. 10, pp. 1885-1890, 2005

FEM Analysis of Plasticity-induced Error on Measurement

of Welding Residual Stress by the Contour Method

Shang Hyon Shin*

Department of Marine Engineering System, Mokpo Maritime University,

571 jukgyo-dong, Mokpo-si 530-729, Korea

The contour method relies on deformations that occur when a residually stressed component is cut along a plane. The method is based on the elastic superposition principle. When plasticity is involved in the relaxation process, stress error in the resulting measurement of residual stress would be caused. During the cutting the specimen is constrained at a location along the cut so that deformations are restrained as much as possible during cutting. With proper selection of the constraining location the plasticity effect can also be minimized. Typical patterns of longitudinal welding residual stress state were taken to assess the plasticity effect along with constraining locations.

Key words: Residual stress, Contour method, Plasticity effect, Stress error

Journal of Mechanicl Science and Technology, Vol. 19, No. 10, pp. 1891-1901, 2005

Identification of Damage on a Substructure with Measured Frequency Response Functions

Nam-Gyu Park

Nuclear Fuel Design Dep., Korea Nuclear Fuel Co. LTD.,

493, Deogjin-dong, Youseong-gu, Daejeon 305-353, Korea

Youn-Sik Park*

Center for Noise and Vibration Control, Dep. of Mech. Eng.,

Korea Advanced Institute of Science and Technology, Science Town, Daejeon 305-701, Korea

Recently the authors tried to find damage position only using measured frequency response functions. According to their work, it seems that the algorithm is very practical since it needs only measured frequency responses while other methods require exact analytic model. But when applying the method to a real structure, it requires lots of experiment. The authors, in this time, propose a method to reduce its experimental load by detecting damage within a substructure. This method searches damages not within an entire structure but within substructures. In addition, damage severity was treated in this paper since it is worthy to know damage severity. Optimization technique is used to estimate damage level using measured responses and damage model. Two test examples, a plate and a jointed structure, are chosen to verify the suggesting method.

Key Word : Damage Indentification, Frequency Response Functions

Journal of Mechanicl Science and Technology, Vol. 19, No. 10, pp. 1902-1909, 2005

Ethanolysis of Soybean Oil into Biodiesel : Process Optimization via Central Composite Design

Nakorn Tippayawong*, Eaksit Kongjareon, Wasan Jompakdee

Department of Mechanical Engineering, Faculty of Engineering, Chiang Mai University,

Chiang Mai 50200, Thailand

A process for production of ethyl ester for use as biodiesel has been studied. The sodium hydroxide catalyzed transesterification of soybean oil with ethanol was carried out at different molar ratio of alcohol to oil, reaction temperature and catalyst amount for a constant agitation in two hours of reaction time. Central composite design and response surface methodology were used to determine optimum condition for producing biodiesel. It was found that ethanol to oil ratio and catalyst concentration have a positive influence on ester conversion as well as interaction effects between the three factors considered. An empirical model obtained was able to predict conversion as a function of ethanol to oil molar ratio, reaction temperature and catalyst concentration adequately. Optimum condition for soybean ethyl ester production was found to be moderate ethanol to oil ratio (10.5:1), mild temperature range (70oC) and high catalyst concentrations (1.0%wt), with corresponding ester conversion of 93.0%.

Key words: Biodiesel, Ethyl Ester, Soybean Oil, Optimization, Central Composite Design

Journal of Mechanicl Science and Technology, Vol. 19, No. 10, pp. 1910-1918, 2005

Thickness Characteristics and Improved Surface Adhesion

of a Polypyrrole Actuator by Analysis of Polymerization Process

Jaewook Ryu

Microsystem Research Center, Korea Institute of Science and Technology,

P.O.BOX 131, Cheongryang, SEOUL 130-650, Korea

Senghwan Jung

Korea Bio-IT foundry center, Shinlim9-dong, Kwanak-gu, Seoul, 151-742, Korea

Seung-Ki Lee

School of Electrical, Electronics and Computer Engineering, Dankook University, Seoul, Korea

Byungkyu Kim*

School of Aerospace & Mechanical Engineering, Hankuk Aviation University,

200-1, Whajon-dong, Deokyang-gu, Koyang-city, Kyonggi-do, 412-791, Korea

Characterizing electrochemical polymerization of polypyrrole film on a substrate depends on many parameters.  Among them, potential difference and cumulative charges play important role.  The level of potential difference affects the quality of the polypyrrole.  On the contrary, cumulative charge affects the thickness of the polypyrrole.  The substrate surface is adjusted physically and chemically by treating with sandblasting and the addition of thiol for surface adhesion improvement.  Experimental results show that the sandblasted and thiol treated substrate provides better adhesion than non-sandblasted and non-thiol treated substrate.

Key Words : Polypyrrole, Actuator, Thiol, Electroactive polymer, Surface adhesion

Journal of Mechanicl Science and Technology, Vol. 19, No. 10, pp. 1919-1931, 2005

A Position Based Kinematic Method for the Analysis of Human Gait

Ahn Ryul Choi, Yong Hoon Rim

Department of Bio-Mechatronic Engineering, College of Life Science & Technology,

Sungkyunkwan University, 300 Chunchun, Jangan, Suwon, Kyunggi, 440-746, Korea

Youn Soo Kim

Department of Orthopedic Surgery, Holly Family Hospital,  Catholic University of Korea,

Sosa, Wonmi, Pucheon, Kyunggi, 420-717, Korea

Joung Hwan Mun*

Department of Bio-Mechatronic Engineering, College of Life Science & Technology,

Sungkyunkwan University, 300 Chunchun, Jangan, Suwon, Kyunggi, 440-746, Korea

Human joint motion can be kinematically described in three planes, typically the frontal, sagittal, and transverse, and related to experimentally measured data. The selection of reference systems is a prerequisite for accurate kinematic analysis and resulting development of the equations of motion. Moreover, the development of analysis techniques for the minimization of errors, due to skin movement or body deformation, during experiments involving human locomotion is a critically important step, without which accurate results in this type of experiment are an impossibility. The traditional kinematic analysis method is the Angular-based method (ABM), which utilizes the Euler angle or the Bryant angle. However, this analysis method tends to increase cumulative errors due to skin movement. Therefore, the objective of this study was to propose a new kinematic analysis method, Position-based method (PBM), which directly applies position displacement data to represent locomotion. The PBM presented here was designed to minimize cumulative errors via considerations of angle changes and translational motion between markers occurring due to skin movements. In order to verify the efficacy and accuracy of the developed PBM, the mean value of joint dislocation at the knee during one gait cycle and the pattern of three dimensional translation motion of the tibiofemoral joint at the knee, in both flexion and extension, were accessed via ABM and via new method, PBM, with a Local Reference system (LRS) and Segmental Reference system (SRS), and then the data were compared between the two techniques. Our results indicate that the proposed PBM resulted in improved accuracy in terms of motion analysis, as compared to ABM, with the LRS and SRS.

Key Words : Gait Analysis, Skin Movement, Human Motion, Knee Joint, Euler Angle, Bryant Angle, Kinematic

Journal of Mechanicl Science and Technology, Vol. 19, No. 10, pp. 1932-1938, 2005

Thermal Characteristics of Graphite Foam Thermosyphon for Electronics Cooling

Kyungbin Lim, Hongkoo Roh*

Department of Mechanical Engineering, Hanbat National University,

San16-1, Dukmyung-dong, Yuseong-gu, Daejeon 305-719, Korea

Graphite foams consist of a network of interconnected graphite ligaments and are beginning to be applied to thermal management of electronics. The thermal conductivity of the bulk graphite foam is similar to aluminum, but graphite foam has one-fifth the density of aluminum. This combination of high thermal conductivity and low density results in a specific thermal conductivity about five times higher than that of aluminum, allowing heat to rapidly propagate into the foam. This heat is spread out over the very large surface area within the foam, enabling large amounts of energy to be transferred with relatively low temperature difference. For the purpose of graphite foam thermosyphon design in electronics cooling, various effects such as graphite foam geometry, sub-cooling, working fluid effect, and liquid level were investigated in this study. The best thermal performance was achieved with the large graphite foam, working fluid with the lowest boiling point, a liquid level with the exact height of the graphite foam, and at the lowest sub-cooling temperature.

Key Words:  Graphite foam, Electronics Cooling, Thermosyphon

Journal of Mechanicl Science and Technology, Vol. 19, No. 10, pp. 1939-1949, 2005

The Experiments for the Enhancement of Regression Rate of Hybrid Rocket Fuel

Kyung-Hoon Shin , Changjin Lee*, Yung H. Yu

Department of Aerospace engineering, Konkuk University, Seoul 143-701, Korea

Many studies have been conducted to increase regression rate of solid fuel in hybrid rocket. One of them resorts to swirl flow since it can extend the residence time of oxidizer in the fuel grain. Also, metal wires may lead to increase the regression rate of solid fuel as shown in solid propellants. In this study, a series of experiments was designed to investigate the enhancement of regression rate of solid fuel by embedded metal wires and by fuel port grain. And fuel port was designed a helical configuration to attempt to induce swirl flow. PMMA with gaseous oxygen is the solid fuel used for investigation. Test results showed that embedded metal wires turned out to be ineffective method because only 3-4% increases in regression rate were observed. However, fuel port grain configuration yields higher burning performance of up to 50% increase in regression rate. Also pitch number as well as total impulse was found to be a design variable.

Key Word : Regression rate, Hybrid rocket, Metal wire, Helical grain

Journal of Mechanicl Science and Technology, Vol. 19, No. 10, pp. 1950-1956, 2005

Temperature Uniformity of the Glass Panel Heated in the Infrared Heating Chamber

Kong Hoon Lee*, Ook Joong Kim

Energy System Research Center, Korea Institute of Machinery and Materials,

171 Jang-dong, Yuseong-gu, Daejeon 305-343, Korea

An analysis has been carried out to investigate the effect of the reflectivity on the temperature distribution of a glass panel by infrared radiant heating. Halogen lamps are used to heat the panel, located near the top and bottom of the rectangular chamber. The thermal energy is transferred from the lamps to the panel only by radiation and it is considered by using view factor. The conductive transfer is limited inside the panel. The results show that the uniformity of the temperature distribution of the panel is improved and, at the same time, the time for heating increases as the wall reflectivity increases. The temperature difference between the center and the corner reaches a maximum in the early stage of the heating process and then decreases until it reaches a uniform steady-state value.

Key Words : Infrared Heating, Temperature University, Plasma Display Panel(PDP)

Journal of Mechanicl Science and Technology, Vol. 19, No. 10, pp. 1957-1963, 2005

Condensation Heat Transfer Coefficients of Flammable Refrigerants on Various Enhanced Tubes

Ki-Jung Park, Dongsoo Jung*

Department of Mechanical Engineering, Inha University, Inchon 402-751, Korea

In this study, external condensation heat transfer coefficients(HTCs) of six flammable refrigerants of propylene(R1270), propane(R290), isobutane(R600a), butane(R600), dimethylether(RE170), and HFC32 were measured at the vapor temperature of 39°C on a 1023 fpm low fin and Turbo-C tubes. All data were taken under the heat flux of 32~116 and 42~142 kW/m2 for the low fin and Turbo-C tubes respectively. Flammable refrigerants' data obtained on enhanced tubes showed a typical trend that external condensation HTCs decrease with increasing wall subcooling. HFC32 and DME showed up to 30% higher HTCs than those of HCFC22 due to their excellent thermophysical properties. Propylene, propane, isobutane, and butane showed similar or lower HTCs than those of HCFC22. Beatty and Katz’ correlation predicted the HTCs of the flammable refrigerants obtained on a low fin tube within a mean deviation of 7.3%. Turbo-C tube showed the best performance due to its 3 dimensional surface geometry for fast removal of condensate.

Keywords: External condensation, Flammable refrigerants, Hydrocarbons, Dimethylether, HFC32, Enhanced tubes

Journal of Mechanicl Science and Technology, Vol. 19, No. 11, pp. 1967-1974, 2005

The Subsurface Stress Field caused by both Normal Loading and Tangential Loading

Young-Pil Koo*

Mechanical Material & Parts Center, Busan Techno-Park, Geumjeong-gu, Busan 609-735, Korea

Tae-Wan Kim

Nanotribology Laboratory, Ohio State University,

Yong-Joo Cho

School of Mechanical Engineering,

Pusan National University, Geumjeong-gu, Busan 609-735, Korea

The subsurface stress field caused by both normal loads and tangential loads has been evaluated using the rectangular patch solution. The effect of tangential loading on the subsurface stress field has been investigated in detail for both the cylinder-on-cylinder contact and a spur gear teeth contact.

For the cylinder-on-cylinder contact, the subsurface stress fields are moved more to the direction of tangential loads and the positions where the maximum stress occur are getting closer to the surface with the increasing tangential loads. The subsurface stress fields of the gear teeth contact are expanded more widely to the direction of tangential loads with the increasing tangential loads. The friction coefficient of a gear teeth contact is low because they are operated in a lubricated condition, and therefore surface tractions in the EHL condition hardly affect on the subsurface stress field.

Key words: Subsurface Stress, Tangential Load, Elasto-Hydrodynamic Lubrication, Spur Gear

Journal of Mechanicl Science and Technology, Vol. 19, No. 11, pp. 1975-1987, 2005

Discretization of Nonlinear systems with Delayed Multi-Input

via Taylor Series and Scaling and Squaring Technique

Zhang Yuanliang, Kil To Chong*

Division of Electronics and Information Engineering Chonbuk National University,

Duckjin-Dong, Duckjin-Gu, Jeonju 561-756, Korea

An input time delay always exists in practical systems. Analysis of the delay phenomenon in a continuous-time domain is sophisticated. It is appropriate to obtain its corresponding discrete-time model for implementation via digital computers. In this paper a new scheme for the discretization of nonlinear systems using Taylor series expansion and the zero-order hold assumption is proposed. The mathematical structure of the new discretization method is analyzed. On the basis of this structure the sampled-data representation of nonlinear systems with time-delayed multi-input is presented. The delayed multi-input general equation has been derived. In particular, the effect of the time-discretization method on key properties of nonlinear control systems, such as equilibrium properties and asymptotic stability, is examined. Additionally, hybrid discretization schemes that result from a combination of the scaling and squaring technique (SST) with the Taylor series expansion are also proposed, especially under conditions of very low sampling rates. Practical issues associated with the selection of the method’s parameters to meet CPU time and accuracy requirements, are examined as well. A performance of the proposed method is evaluated using a nonlinear system with time delay: maneuvering an automobile.

Keywords: Multi-input; Nonlinear system, Scaling and Squaring technique, Stability, Taylor-series, Time-delay, Time-discretization

Journal of Mechanicl Science and Technology, Vol. 19, No. 11, pp. 1988-1997, 2005

Structural Integrity Evaluation for Interference-fit Flywheels

in Reactor Coolant Pumps of Nuclear Power Plants

June-soo Park*, Ha-cheol Song, Ki-seok Yoon, and Taek-sang Choi

Mechanical System Engineering Dept., Korea Power Engineering Company, Inc.,

150 Deokjin-dong, Yuseong-gu, Daejeon, 305-353, Korea

Jai-hak Park

Safety Engineering Dept., College of Engineering, Chungbuk National University

48 Gaesin-dong, Cheongju, Chungbuk, 361-763, Korea

This study is concerned with structural integrity evaluations for the interference-fit flywheels in reactor coolant pumps (RCPs) of nuclear power plants. Stresses in the flywheel due to the shrinkage loads at standstill and centrifugal loads at the RCP normal operation speed, design overspeed and joint-release speed are obtained using the finite element method (FEM), where release of the deformation-controlled stresses as a result of structural interactions during rotation is considered. Fracture mechanics evaluations for a series of cracks assumed to exist in the flywheel are conducted, considering ductile (fatigue) and non-ductile fracture, and stress intensity factors for the cracks are obtained using the finite element alternating method (FEAM). From analysis results, it is found that fatigue crack growth rates calculated are negligible for smaller cracks. Meanwhile, the material resistance to non-ductile fracture in terms of the critical stress intensity factor (KIC) and the nil-ductility transition reference temperature (RTNDT) are governing factors for larger cracks.

Key Word : Structural Integrity, Interface-Fit, Flywheel, Residual Stress, Reactor Coolant Pum

Journal of Mechanicl Science and Technology, Vol. 19, No. 11, pp. 1998-2006, 2005

Development of A Lane Departure Monitoring and Control System

Kunsoo Huh*

School of Mechanical Engineering, Hanyang University

17 Haengdang-Dong, Sungdong-Ku, Seoul 133-791, Korea

Daegun Hong

Dept. of Precision Mechanical Engineering, Hanyang University

17 Haengdang-Dong, Sungdong-Ku, Seoul 133-791, Korea

Jeffrey L. Stein

Department of Mechanical Engineering, University of Michigan, Ann Arbor, Michigan

The lane departure avoidance systems have been considered promising to assist human drivers in AVCS (Advanced Vehicle Control System). In this paper, a lane departure monitoring and control system is developed and evaluated in the hardware-in-the-loop simulations. This system consists of lane sensing, lane departure monitoring and active steering control subsystems. The road image is obtained based on a vision sensor and the lane parameters are estimated using image processing and Kalman Filter technique. The active steering controller for avoiding the lane departure is designed based on the lane departure metric. The proposed lane departure avoidance system is realized in a steering HILS (hardware-in-the-loop simulation) tool and its performance is evaluated with a driver in the loop.

Key Words : Lane Departure Monitoring, Lane Departure Avoidance, Lane Sensing, Active Steering Control

Journal of Mechanicl Science and Technology, Vol. 19, No. 11, pp. 2007-2015, 2005

Parallel Process System and Its Application to Steam Generator Structural Analysis

Yoon-Suk Chang, Han-Ok Ko, Jae-Boong Choi, Young-Jin Kim*

School of Mechanical Engineering, Sungkyunkwan University,

300 Chunchun-dong, Jangan-gu, Suwon, Kyonggi-do 440-746, Korea

Shinobu Yoshimura

Institute of Environmental Studies, University of Tokyo,

7-3-1 Hongo, Bunkyo-ku, Tokyo 113-8656, Japan

A large-scale analysis to evaluate complex material and structural behaviors is one of interesting topic in diverse engineering and scientific fields. Also, the utilization of massively parallel processors has been a recent trend of high performance computing. The objective of this paper is to introduce a parallel process system which consists of general purpose finite element analysis solver as well as parallelized PC cluster. The later was constructed using eight processing elements and the former was developed adopting both hierarchical domain decomposition method and balancing domain decomposition method. Then, to verify the efficiency of the established system, it was applied for structural analysis of steam generator in nuclear power plant. Since the prototypal evaluation results agreed well to the corresponding reference solutions it is believed that, after reinforcement of PC cluster by increasing number of processing elements, the promising parallel process system can be utilized as a useful tool for advanced structural integrity evaluation.

Key Words: ADVENTURE_Solid, Balancing Domain Decomposition, Hierarchical Domain Decomposition, Parallel Process System, PC Cluster, Steam Generator

Journal of Mechanicl Science and Technology, Vol. 19, No. 11, pp. 2016-2024, 2005

A Simple Mixed-Based Approach for Thin-Walled Composite Blades with Two-Cell Sections

Sung Nam Jung*, Il-Ju Park

School of Mechanical and Aerospace Engineering,

Chonbuk National University, Jeonju 561-756, Korea

In this work, a mixed beam approach that combines both the stiffness and the flexibility methods has been performed to analyze the coupled composite blades with closed, two-cell cross-sections. The Reissner’s semi-complementary energy functional is used to derive the beam force-displacement relations. Only the membrane part of the shell wall is taken into account to make the analysis simple and also to deliver a clear picture of the mixed method. All the cross-section stiffness coefficients as well as the distribution of shear across the section are evaluated in a closed-form through the beam formulation. The theory is validated against experimental test data, detailed finite element analysis results, and other analytical results for coupled composite blades with a two-cell airfoil section. Despite the simple kinematic model adopted in the theory, an accuracy comparable to that of two-dimensional finite element analysis has been obtained for cases considered in this study.

Key Words: Mixed Beam Approach, Coupled Composite Blades, Two-cell Airfoil Section, Closed-form Solution

Journal of Mechanicl Science and Technology, Vol. 19, No. 11, pp. 2025-2031, 2005

An Analytical Study on Prediction of Effective Properties

in Porous and Non-Porous Piezoelectric Composites

Jae-Kon Lee*

School of Mechanical and Automotive Engineering, Catholic University of Daegu,

Gyeongsansi, Gyeongbuk, 712-702, Korea

Eshelby type micromechanics model with a newly developed piezoelectric Eshelby tensor is proposed for predicting the effective electroelastic properties of the piezoelectric composite. The model is applied for piezoelectric solids containing both porosities and metal inhomogeneities. The effective electroelastic moduli of the composites such as stiffness, piezoelectric constants, and dielectric constants are predicted by the present model, which are extensively compared with the existing experimental results from the literatures. The validity of Eshelby type model for predicting the effective properties of the composite is thoroughly examined. It can be concluded from this study that a new mechanism is needed to compute correctly the dielectric constants among the effective properties of the composites.

Keywords: Piezoelectric composite, Porous composite, Non-porous composite, Effective electroelastic moduli, Piezoelectric Eshelby tensor

Journal of Mechanicl Science and Technology, Vol. 19, No. 11, pp. 2032-2039, 2005

On Implementation of the Finite Difference Lattice Boltzmann

Method with Internal Degree of Freedom to Edgetone

Hokeun Kang*

School of Mechanical and Aerospace Engineering · Institute of Marine Industry,

Gyeongsang National University, 445 Inpyeong-dong, Tongyeong, Gyeongnam, 650-160 Korea

Eunra Kim

Department of Civil Engineering · Research Center of Industrial Technology,

Chonbuk National University, 664-14 1ga Duckjin-Dong Duckjin-Gu Jeonju Jeonbuk, 561-756 Korea

The lattice Boltzman method (LBM) and the finite difference-based lattice Boltzmann method (FDLBM) are quite recent approaches for simulating fluid flow, which have been proven as valid and efficient tools in a variety of complex flow problems. They are considered attractive alternatives to conventional finite-difference schemes because they recover the Navier-Stokes equations and are computationally more stable, and easily parallelizable. However, most models of the LBM or FDLBM are for incompressible fluids because of the simplicity of the structure of the model. Although some models for compressible thermal fluids have been introduced, these models are for monatomic gases, and suffer from the instability in calculations. A lattice BGK model based on a finite difference scheme with an internal degree of freedom is employed and it is shown that a diatomic gas such as air is successfully simulated. In this research we present a 2-dimensional edge tone to predict the frequency characteristics of discrete oscillations of a jet-edge feedback cycle by the FDLBM in which any specific heat ratio  can be chosen freely. The jet is chosen long enough in order to guarantee the parabolic velocity profile of a jet at the outlet, and the edge is of an angle of  . At a stand-off distance  , the edge is inserted along the centerline of the jet, and a sinuous instability wave with real frequency is assumed to be created in the vicinity of the nozzle exit and to propagate towards the downstream. We have succeeded in capturing very small pressure fluctuations resulting from periodic oscillation of the jet around the edge.

Key Words : Finite Difference Lattice Boltzman Method, Edgetone, Feedback

Journal of Mechanicl Science and Technology, Vol. 19, No. 11, pp. 2040-2052, 2005

Determination of Diesel Sprays Characteristics in Real Engine

In-Cylinder Air Density and Pressure Conditions

R. Payri*, F. J. Salvador, J. Gimeno, V. Soare

CMT-Motores Termicos, Universidad Politecnica de Valencia,

Camino de Vera s/n, E-46022 Spain.

The present paper centers on the establishment of a quantified relationship between the macroscopic visual parameters of a Diesel spray and its most influential factors. The factors considered are the ambient gas density, as an external condition relative to the injection system, and nozzle hole diameter and injection pressure as internal ones. The main purpose of this work is to validate and extend the different correlations available in the literature to the present state of the Diesel engine, i.e. high injection pressure, small nozzle holes, severe cavitating conditions, etc. Five mono-orifice, axi-symmetrical nozzles with different diameters have been studied in two different test rigs from which one can reproduce solely the real engine in-cylinder air density, and the other, both the density and the pressure. A parametric study was carried out and it enabled the spray tip penetration to be expressed as a function of nozzle hole diameter, injection pressure and environment gas density. The temporal synchronization of the penetration and injection rate data revealed a possible explanation for the discontinuity observed as well by other authors in the spray’s penetration law. The experimental results obtained from both test rigs have shown good agreement with the theoretical analysis. There have been observed small but consistent differences between the two test rigs regarding the spray penetration and cone angle, and thus an analysis of the possible causes for these differences has also been included.

Key Words : Spray, Penetration, Correlations, Diesel Injection, Nozzle Geometry

Journal of Mechanicl Science and Technology, Vol. 19, No. 11, pp. 2053-2060, 2005

Hall Effect on Unsteady Couette fFlow with Heat Transfer Under

Exponential Decaying Pressure Gradient

Hazem Ali Attia

Dept. of Mathematics, College of Science, Al-Qasseem University,

P.O. Box 237, Buraidah 81999, KSA

The unsteady Couette flow of an electrically conducting, viscous, incompressible fluid bounded by two parallel non-conducting porous plates is studied with heat transfer taking the Hall effect into consideration.  An external uniform magnetic field and a uniform suction and injection are applied perpendicular to the plates while the fluid motion is subjected to an exponential decaying pressure gradient.  The two plates are kept at different but constant temperatures while the Joule and viscous dissipations are included in the energy equation.  The effect of the ion slip and the uniform suction and injection on both the velocity and temperature distributions is examined.

Key Words : Fluid mechanics, Hydromagnetic flow, Couette flow, Heat transfer, Finite difference

Journal of Mechanicl Science and Technology, Vol. 19, No. 11, pp. 2061-2067, 2005

Characteristics of Wave Exciting Forces on a Very Large Floating Structure with Submerged-Plate

Sang-Min Lee*

Research Institute of Maritime Industry, Korea Maritime University, Pusan 606-791, Korea

Chun-Beom Hong

Marine Research Institute, Samsung Heavy Industry Co., Daejeon 305-380, Korea

In this study, we focus on the submerged plate built into the Very Large Floating Structure with the partial openings of 5m long, which enables the reverse flow of incident wave to generate the wave breaking. The purpose of this study is to investigate the characteristics of wave exciting forces acting on the submerged plate and the fore part of VLFS. Firstly, we have carried out the extensive experiments to understand the characteristics of the wave exciting forces. Then we have performed the numerical simulations by applying the Marker and Cell method (MAC method) and compared with the experimental results. We discuss the validity of MAC method and the effects of the submerged plate on the motion of VLFS. As a result, we get the conclusion that the submerged plate is useful for reducing the wave exciting forces acting on the structure behind the submerged plate.

Key Words : Marker and Cell method, Submerged-plate, VLFS, Wave exciting forces

Journal of Mechanicl Science and Technology, Vol. 19, No. 11, pp. 2068-2076, 2005

The Effect of Oxygen and Carbon Dioxide Concentration on

Soot Formation in Nonpremixed Flames using Time Resolved LII Technique

Kwang Chul Oh*

Enviromental Parts R & D Center, Korea Automotive Technology Institute,

74 yongjung-Ri, Pungse-Myun, Chonan, Chungnam, 330-912, Republic of Korea

Hyun Dong Shin

Department of Mechanical Engineering, Korea Advanced Institute of Science and Technology,

373-1 Guseong-dong, Yuseong-gu, Daejon, 305-701, Republic of Korea

The influence of oxygen concentration and CO2 as diluent in oxidizer side on soot characteristics was studied by Laser Induced Incandescence, Time Resolved LII and Transmission Electron Microscopy photography in non-premixed coflowing flames. Through the comparison of TEM photographs and the decay rate of LII signal, suitable two delay times of TIRE-LII method and signal sensitivity (?STIRE-LII/?dp) were determined. The effects of O2 and CO2 as diluent in oxidizer side on soot formation are investigated with these calibrated techniques. The O2+CO2, N2, and [Ar+CO2] mixture in co-flow were used to isolate CO2 effects systematically. The number concentration of primary particle and soot volume fraction abruptly decrease by the addition of CO2 to the co-flow. This suppression is resulted from the short residence time in inception region because of the late nucleation and the decrease of surface growth distance by the low flame temperature due to the higher thermal capacity and the chemical change of CO2 including thermal dissociation. As the oxygen concentration increases, the number concentration of soot particles at the inception region increases and thus this increase of nucleation enhances the growth of soot particle.

Keywords: Soot, Laser diagnostics (TIRE-LII, LII), Diluents

Journal of Mechanicl Science and Technology, Vol. 19, No. 11, pp. 2077-2081, 2005

Effect of Boundary Condition History on the Symmetry

Breaking Bifurcation of Wall-Driven Cavity Flows

Ji Ryong Cho*

Department of Mechanical and Automotive Engineering, Inje University,

607 Obangdong, Kimhae 621-749, Korea

A symmetry breaking nonlinear fluid flow in a two-dimensional wall-driven square cavity taking symmetric boundary condition after some transients has been investigated numerically. It has been shown that the symmetry breaking critical Reynolds number is dependent on the time history of the boundary condition. The cavity has at least three stable steady state solutions for Re=300-375, and two stable solutions if Re>400. Also, it has also been showed that a particular solution among several possible solutions can be obtained by a controlled boundary condition.

Key Words: Cavity, Boundary Condition History, Symmetry Breaking Bifurcation, Multiplicity, Critical Reynolds number

Journal of Mechanicl Science and Technology,<Special Edition> Vol. 19, No. 11, pp. 2085-2090, 2005

Synthesis of CuInGaSe2 Nanoparticles by Low Temperature Colloidal Route

Ki-Hyun Kim, Young-Gab Chun, Kyung-Hoon Yoon*

Solar Cells Research Center, Korea Institute of Energy Research,

71-2 Jang-dong, Yusong-gu, Daejon, 305-343 Korea

Byung-Ok Park

Dept. of Inorganic Materials Engineering, Kyungpook National University,

1370 Sankyuk-dong, Puk-ku, Daegu, 702-701, Korea

CIGS nanoparticles were synthesized by a low temperature colloidal route for the absorber layer of photovoltaic devices. The CIGS nanoparticles were prepared by reacting CuI, InI3, GaI3 in pyridine with Na2Se in methanol at 0℃ under inert atmosphere. The reaction products of dark red and yellow colors were turned out to be NaI and CIGS nanoparticles, respectively, by ICP-AES and SEM-EDS analyses. Chalcopyrite structure of the CIGS nanoparticles was confirmed by XRD and TEM diffraction patterns. As compared to the particles from Cu0.9In0.8Ga0.3Se2 ratio, more uniform and smaller nanoparticles were obtained from Cu1.1In0.68Ga0.23Se1.91 stoichiometric ratio. The CIGS nanoparticles were measured to be in the ranges of 5-20 ㎚. However, tube like CIGS particles with length of several ㎛ and width in the range of 100-300 ㎚ were obtained from Cu0.9In0.8Ga0.3Se2, and Cu0.9In0.7Ga0.4Se2. The morphological change of the CIGS particles seems to be closely related to the ratio of Cu/(In+Ga).

Key words : Solar cell, CuInGaSe2, Absorber layer, Nanoparticles

Journal of Mechanicl Science and Technology,<Special Edition> Vol. 19, No. 11, pp. 2091-2095, 2005

Improvement of Rounding Effect in Chemical Mechanical

Polishing Process for Nano-Scale Manufacturing

Myung-Jin Chung

Dept. of Mechatronics Eng, Korea Polytechnic University,

2121, Jeongwang-dong, Siheung-si, Gyeonggi-do, Korea

In the present work, the rounding effect in the CMP process was examined in the process conditions such as the head pressure, platen and head speed, and deposition thickness. The rounding effect according to each process condition is measured from SEM and compared with each other. From the experimental results, CMP process condition to reduce the rounding effect is determined and the rounding effect has been improved from 55nm to 29nm, which is about 47% reduction.

Key Words : Rounding Effect, Chemical Mechanical Polishing, Head Pressure, Platen and Head Speed, Deposition Deph

Journal of Mechanicl Science and Technology,<Special Edition> Vol. 19, No. 11, pp. 2096-2104, 2005

A Study on the Fabrication of Micro Groove on Si Wafer using Chemical Mechanical Machining

Junmin Park

Dept. of Mech. and Pre. Eng, Pusan National University,

San 30, Changjeon-Dong, Kumjeong-Ku, Pusan, 609-735, Korea

Haedo Jeong*

School of Mechanical Eng., Pusan National University,

San 30, Changjeon-Dong, Kumjeong-Ku, Pusan, 609-735, Korea

Materials are either removed from or added to a device, usually in a selective manner with using thin and/or thick film manufacturing processes that transfer the lithographic patterns into integrated circuits (ICs) or three-dimensional micromachines. This study deals with material removal by chemically assisted mechanical micromachining. Two methods are used chemical mechanical machining method are introduced in this paper. One, mechanically assisted chemical etching, is applied to fabricate a micro beam such as cantilever, and another is chemically assisted mechanical micromachining to fabricate microstructure such as micropattern, microchannel. The results are discussed.

Key Words : Si Wafer, Microstructure, Chemical Assisted Mechanical Micromaching, Mechanically Assisted Chemical Etching Method

Journal of Mechanicl Science and Technology,<Special Edition> Vol. 19, No. 11, pp. 2105-2111, 2005

Contour Offset Algorithm (COA) in nano Replication Printing (nRP)

for Fabricating Nano-Precision Features

Tae Woo Lim, Sang Hu Park, Dong-Yol Yang*

Dep. of Mechanical Engineering ,KAIST, Daejeon, Korea

Shin Wook Yi, Hong Jin Kong

Dep. of Physics, KAIST, Daejeon, Korea

Kwang-Sup Lee

Dep. of Polymer Science and Engineering, Hannam Univ., Daejeon, Korea

A Contour Offset Algorithm (COA) has been developed to fabricate nano-precision figures or patterns in the range of several microns by a nano-Replication Printing (nRP) process. In the nRP process, a femtosecond laser illuminated on photosensitive monomer resin to induce polymerization of the liquid monomer according to a volume pixel (voxel) matrix which is transformed from a two-tone (black and white) bitmap file. After two-photon absorbed photopolymerization (TPP), a droplet of ethanol is dropt on a glass plate to remove the unnecessary remaining liquid resin, leaving only polymerized patterns on the glass plate. In the nRP process, the replicated patterns do not precisely coincide with the initial designs due to an essential shortage of nRP process. Fabricated patterns by means of the nRP process become larger than the design in the amount of the voxel radius. In this work, an outer contour matrix of an initial design was constructed and reduced according to an offset-ratio calculated by the COA in order to obtain more precise patterns. Both the effectiveness and the accuracy of the proposed algorithm were demonstrated through chosen example.

Key Words : Femtosecond Laser, Two Photon Polymerization, Contour Offset Algorithm(COA), Nano-Relication Printing(nRP)

Journal of Mechanicl Science and Technology,<Special Edition> Vol. 19, No. 11, pp. 2112-2121, 2005

A Study on the Effect of Pattern Pitch on Deformation Behaviors

for Surface Patterning by Using Nano-indenter

Sung Won Youn, Hyun Il Kim

Department of Mechanical and Precision Engineering, Pusan National University,

JangJung-dong, KumJung-gu, Busan, Korea

Chung Gil Kang

School of Mechanical Eng., Pusan National University, JangJung-dong, KumJung-gu, Busan, Korea

Nanoprobe-based lithography techniques have attracted tremendous interst. However, most of these techniques have the several technical problems still to be resolved such as low throughput, reproducibility, extensive processing time and tip-wear problem. We considered that a patterning process with a multi-array tip can be a solution. The purpose of this study is to build up the database in order to design a multi-array tip for patterning. In this study, the effects of tip-geometry factors (indenter shape and tip radius) and process parameters (pattern pitch and normal load) on the deformation behaviors and etching chracteristics of hard-brittle materials (Pyrex 7740 glass and silicon) were investigated by using both experiment and finite element analysis. The results of the investigation will be applied to the design of the multi-array tip for patterning.

Key Words: Lithography; Nanoscratch test; Silicon; Borosilicate; Wet etching

Journal of Mechanicl Science and Technology,<Special Edition> Vol. 19, No. 11, pp. 2122-2126, 2005

Electrochemical DNA Biosensor with Nanometer Scale Using Nano-Patterning Lithography Machine

SeungWoo Lee, SooYeon Park, JaeJong Lee*

Intelligence & Precision Machine Dept., KIMM, 171 Jang-dong, Yuseong-gu, Daejon, Korea

Major challenges in the field of electrochemical DNA hybridization biosensors are the immobilization of DNA and the detection of hybridization signals. The method of DNA immobilization using the nano-patterning machine and detection for DNA hybridization signals has been proposed. Here, two gold electrodes were deposited on SiO2 layer and the gap between the electrodes was fabricated by electron beam lithography. 3-aminopropyltriethoxysilane (APTES) solution was selectively treated to immobilize the amino-modified oligonucleotides onto the SiO2 layer between the electrodes. The recognition of DNA hybridization was accomplished by metallic aggregation of nano-particles. The results showed that DNA is immobilized with nanometer scales and the method for detecting hybridization signals is useful. The experimental results were verified by I-V curves. The conductance between two electrodes changed with the density of the Au-nanoparticles immobilized onto the oxide layer. These results can be applied to the DNA chip and the multi-functional sensors and it will be researched in the further study.

Key Words : Electrochemical, DNA Biosensor, Nano-Patterning, Nanometer Scale

Journal of Mechanicl Science and Technology,<Special Edition> Vol. 19, No. 11, pp. 2127-2132, 2005

Ionization Gauge by Carbon Nanotube Field Emission

In-Mook Choi*, Sam-Yong Woo and Boo-Shik Kim

Physical Division, Korea Research Institute of Standards and Science,

1 Doryong-dong, Yuseong-gu, Daejeon 305-340, Korea

A newly developed ionization gauge using carbon nanotube(CNT) field emission effect has been designed and manufactured. The fabricated ionization gauge is of a triode type, consisting of a cathode (carbon nanotube field emitter arrays), a grid and a collector. The principle involved here is that for a constant number of electrons available for ionization emitted from carbon nanotube arrays by the grid potential, a constant fraction of gas will be ionized and the number of ions collected in the collector will be proportional to the number of gas molecules in the chamber traversed by the electrons. Due to the excellent field emission characteristics of CNT, it is possible to make a cost effective cold cathode ionization gauge. A screen-printing method has been used to make the CNT cathode. The glass grid with Cr deposited by E-beam has been put on the cathode with a gap of 200 mm between the two electrodes. Using the voltage applied to the grid, the electrons emitted from the carbon nanotube ionize gas molecules in the chamber and the ionized molecules are gathered in the collector. At this time, the collector voltage is maintained at a lower level than that of the grid voltage to obtain a large ionization ratio. The current detected in the collector is proportional to the pressure in the chamber. The ionization characteristics are dependent on the gas and the voltage applied to the grid and collector. In this paper we have shown the various metrological characteristics of the simple pressure sensor utilizing carbon nanotube.

Key Words : Carbon Nanotube, Ionization Current, Screen Printing Method, Pressure Sensor, Field Emission

Journal of Mechanicl Science and Technology,<Special Edition> Vol. 19, No. 11, pp. 2133-2137, 2005

Guided Cell Growth through Surface Treatments

Yo Han Choi*, Seung S. Lee

Department of Mechanical Engineering, Korea Advanced Institute of Science and Technology,

373-1, Guseong-dong, Yuseong-gu, Daejeon, 305-701, Korea

This paper presents easy methods for guidance of animal cell growth in vitro. The surfaces of silicon wafers were treated using simple MEMS techniques in order for the formation of differentiated surfaces. Human epithelial cells incubated on these surfaces showed ordered growth and division patterns along the original design. These methods would be a useful basis in cell-based high throughput screenings and artificial skin

Key Words : Cell Culture, Cell Patterning

Journal of Mechanicl Science and Technology,<Special Edition> Vol. 19, No. 11, pp. 2138-2144, 2005

Electrical Conduction of Thiol Modified 60 bp Poly(dG)-Poly(dC)

DNA Molecules through Au Nanoparticles

Jongseung Hwang*, David Ahn

Institute of Quantum Information Processing and Systems, University of Seoul,

90 Jeonnong-dong, Dongdaemoon-gu, Seoul 130-743, Korea

Suheon Hong, Hyungkwon Kim, Sungwoo Hwang

Dept. of Electronics Engineering, Korea University, Anam-dong, Sungbuk-gu, Seoul 136-701, Korea

A novel transport measurement scheme of 60 base pairs of poly(dG)-poly(dC) DNA molecules using Au nanoparticles is devised and implemented. Thiol (-SH) terminations are synthesized at both 5’ and 3’ ends of the double stranded DNA molecules and they can be chemisorbed on the Au surface through sulfur atoms by covalent bonding. These thiol-modified ends make chemical bindings with Au nanoparticles and Au nano-gap electrodes, forming a stable electrode-DNA-nanoparticle-DNA-electrode conduction channel. This transport channel is self-formed and is stable due to robust bonding of thiol and Au. The current-voltage characteristic measured from our device shows a nonlinear behavior and the voltage gap is comparable to the result of previous experiment using the same molecules. This self-trapping method by thiol modified DNA molecules would also be a promising technique for efficient nanoparticle trapping.

Key Words: Au nanoparticle, DNA molecule, Self-trapping method

Journal of Mechanicl Science and Technology,<Special Edition> Vol. 19, No. 11, pp. 2145-2150, 2005

Near-Field Optical Patterning on Chloromethylated Polyimide

J. -B. Kim*, S. -J. Na,

Dept. of Mechanical Eng, KAIST, 373-1 Guseong-dong, Yuseong-gu, Daejeon, Korea

W. -S. Chang, and M. -J. Choi

Nanoprocess Group, KIMM

Near-field scanning optical microscopy(NSOM) coupled with laser is used in nano-scale processing to make nano-scale dots or nano-scale structure. Nano-sclae processing using NSOM coupled with laser can be applied to photo- chemical  etching process on crstalline silicon, to additive processes on some polymers, to subtraction processes on SAMs and other polymers. And it can be used to change material’s optical properties in nano-scale geometry. As above, nano-scale processing using NSOM coupled with laser has an advantage that it can be applied to various processes.

In this work, by using NSOM coupled with 266nm UV laser, nano-scale patterns were fabricated on chloromethylated polyimide(CMPI) films coated on silicon wafer. CMPI undergoes a fast photolysis under UV light. So, in the case of pattern fabrication on CMPI it is possible to fabricate patterns without development process. Possibilities for SMPI to be applied to nano-scale patterns fabrication were demonstrated. Compared to usual lithographic processes, the process proposed in this work is simple because development, one of  steps to fabricate nano-scale patterns, is not needed. And the finite-difference-time-domain(FDTD) method was employed to simulate the energy intensity distribution in the near-field. The simulation was executed for NSOM tip and UV laser. The influence of aperture size and tip-sample distance on the resolution of the lithographic process is discussed from the simulation results. Comparison of some simulation results with corresponding experimental results could confirm the validity of the simulation model proposed.

Key Words : Near-Field, Pattem Fabrication, SPM Lithography

Journal of Mechanicl Science and Technology,<Special Edition> Vol. 19, No. 11, pp. 2151-2156, 2005

Nano Structured Surface Modification of Tool Steel and its Beneficial Effects in Mechanical Properties

In Ho Cho*

Graduate School, SunMoon University, Asan, South Korea

Gil Ho Song

Technical Research Laboratories, Pohang Iron &Steel Co.,Ltd. Kwangyang, Korea

Chang Sik Kim, Azuma Nobuhide A. Combs, Jin Park,

DM R&D Institute, DesignMecha Co., Ltd. Asan, South Korea

Chang Min Suh

Department of Mechanical Engineering, Kyungpook University, Taegu, Korea

Jeong Hyun Park, Young Shik Pyoun

Department of Mechanical and Control Engineering, SunMoon Univ., Asan, South Korea

The industrial beneficial effects of nano-structured surface modification of tool steel (SKD 61) have been studying. Ultrasonic cold forging technology(UCFT) is one of severe plastic deformations for the improvement of mechanical properties by making nano-structure on surface. The basic mechanism of UCFT and experimental device for treatment of trimmer knives(SKD 61) are presented. Test results of UCFT treated knives in cold steel milling line and analysis why the improved service life is achieved are explained.

Key Words : Nano-Surface Modification, Ultrasonic Vibration, Property, Tool Steel

Journal of Mechanicl Science and Technology,<Special Edition> Vol. 19, No. 11, pp. 2157-2164, 2005

Design and Control of Flexure based XYθz Stage

Dongwoo. Kang*, Kihyun Kim, Youngman Choi, Daegab Gweon ,

NanoOptoMechatronics Lab., Department of Mechanical Engineering, KAIST, Daejeon, Korea

Sukwon Lee, Moongoo. Lee

Mechatronics Center, Samsung Electronics CO., LTD,

416 Maetan3-Dong, Paldal-Gu, Suwon,Gyeonggi, Korea,

This article presents the design and control of an ultraprecision XYqz stage with nanometer accuracy. The stage has a plane mechanism and symmetric hexagonal structure which consists of a monolithic flexure hinge mechanism with three piezoelectric actuators and six flexures preserving the plane motion. The symmetric design reduces the effect of temperature gradient on the structure.

Because the relationship between design variables and system parameters are quite complicated and there are some trade-offs among them, it is very difficult to set design variables manually and optimal design procedure is used. The objective of design is maximizing the 1st resonant frequency to improve the dynamic characteristics. The reason is that the stage must move with heavy load of about 20kg. The higher resonant frequency also makes the stage stiffer and stronger against the dynamic force and moment. This paper describes the procedures of selecting parameters for the optimal design and a mathematical formulation for the optimization problem. The stage was designed to attain ±10um in the X- and Y-direction and ±90arcsec in the yaw direction at the same time and have the 1st resonant frequencies of 455.5Hz in X- and Y-direction and 275.3Hz for yaw direction without load. The stage was fabricated according to the optimal design results and experimental results indicate that the design procedure is effective. A conventional PI control results are presented for ultraprecision motion.

Key Words : Precision Stage, Flexure, Piezoelectric Actuator, Nanotechnology, Optimal Design

Journal of Mechanicl Science and Technology,<Special Edition> Vol. 19, No. 11, pp. 2165-2171, 2005

Optimal Calibration for Rotating Analyzer Ellipsometer

Sunglim Park*

Optel Precision Co., 573-37 Eoyang-dong, Iksan, Korea

DaeGab Gweon

Dept. of Mechanical Eng., KAIST, Guseong-dong, Yuseong-gu, Daejeon, Korea

We have modeled most errors, which affect the measurement accuracy, with Jone’s matrix. From the simulation, we can characterize the errors and take good aids for selecting components and designing ellipsometer. The traditional residual method has good performance when there are only azimuth angle errors and extinction errors, but it has not good performance when there are other errors. We have proposed the optimal calibration method for overcoming the residual method. The optimal method selects error values to have the least square difference between the measured thickness and the simulated thickness. We can reduce the design variables to three, incident angle error, and azimuth angle errors of polarizer and analyzer. The optimization results are slightly different from the residual method, and have smaller standard deviation of errors than the residual method. The experiment shows good agreement with the simulations.

Key Words : Elliposmeter, Optimal Calibration

Journal of Mechanicl Science and Technology,<Special Edition> Vol. 19, No. 11, pp. 2172-2178, 2005

A Switchable Cantilver for a Chemically Sensitive Scanning Force Microscope

Dong-Weon Lee*

Department of Mechanical Systems Engineering, Chonnam National University, Gwangju, Korea

We describe a cantilever device for a novel ‘Time-Of-Flight Scanning Force Microscope (TOF-SFM)’ concept that has the capability of chemical analysis.  The cantilever device consists of a switchable cantilever (SC), a microfabricated extraction electrode, and a LEGO-type microstage, which combines two different systems.  It allows quasi-simultaneous topographical and chemical imaging of a sample surface to be performed in the same way as with conventional scanning probe techniques. This is achieved by the micromachined SC with a bimorph actuator that provides a reasonable switching speed in comparison with mechanically operated switches.  Secondly, a short tip-electrode distance to minimize the ions extraction voltage can be realized by LEGO-type microfabrication. The measured SC tip deflection is ~100 mm at 35 mW, corresponding to an estimated heater temperature of ~250 °C. The maximum switching speed between the two modes is ~10 msec, and the sensitivity DR/R of an integrated piezoresistive deflection sensor is ~6.7 ´ 10?7/nm. The tip-electrode distance is only 10 mm.  The TOF-SFM is currently integrated in an ultra-high-vacuum system to perform several measurements.

Journal of Mechanicl Science and Technology, Vol. 19, No. 12, pp. 2179-2186, 2005

The Lubrication Characteristics of the Vane Tip under Inlet

Pressure Boundary Conditions for an Oil Hydraulic Vane Pump

Ihn-Sung Cho

Division of Mechanical & Aerospace System Engineering, Chonbuk National University,

#664-14, 1 Ga, Duckjin-dong, Duckjin-ku, Jeonju, Jeonbuk 561-756, Korea

Seok-Hyung Oh

Faculty of Mechanical Engineering, Kunsan National University,

san 68, Miryong-dong, Kunsan, Jeonbuk, 573-701, Korea

Jae-Youn Jung*

Division of Mechanical & Aerospace System Engineering and RCIT, Chonbuk National University,

#664-14, 1 Ga, Duckjin-dong, Duckjin-ku, Jeonju, Jeonbuk, 561-756, Korea

The lubrication modes of line contact between the vane and the camring in an oil hydraulic vane pump have been investigated. First, variations of the radial acting force of a vane were calculated from previously measured results of the dynamic internal pressure in four chambers surrounding a vane. Next, distinctions of the lubrication modes were made using Hooke's chart, which represents an improvement over Johnson's chart. Finally, the influence of boundary conditions in the lubrication region on fluid film lubrication was examined by calculating film pressure distributions. The results show that the lubrication modes of the vane tip are a rigid-variable viscosity region. This region discharges pressure higher than 7MPa, and exerts a great influence on oil film pressure in the large arc section due to the Piezo-viscous effect.

Key Words : Inlet Pressure, Vane Pump, Lubrication, Lubrication Mode, Line Contact, Vane Tip

Journal of Mechanicl Science and Technology, Vol. 19, No. 12, pp. 2187-2196, 2005

A Finite Thin Circular Beam Element for In-Plane Vibration Analysis of Curved Beams

Chang-Boo Kim*, Jung-Woo Park, Sehee Kim, Chongdu Cho

Department of Mechanical Engineering, Inha University,

253, Yonghyun-Dong, Nam-Ku, Incheon, 402-751, Korea

In this paper, the stiffness and the mass matrices for the in-plane motion of a thin circular beam element are derived respectively from the strain energy and the kinetic energy by using the natural shape functions of the exact in-plane displacements which are obtained from an integration of the differential equations of a thin circular beam element in static equilibrium. The matrices are formulated in the local polar coordinate system and in the global Cartesian coordinate system with the effects of shear deformation and rotary inertia. Some numerical examples are performed to verify the element formulation and its analysis capability. The comparison of the FEM results with the theoretical ones shows that the element can describe quite efficiently and accurately the in-plane motion of thin circular beams. The stiffness and the mass matrices with respect to the coefficient vector of shape functions are presented in appendix to be utilized directly in applications without any numerical integration for their formulation.

Key Words : Thin Circular Beam, Finite Element, In-plane Motion, Natural Shape Function, Stiffness Matrix, Mass Matrix, Shear Deformation, Rotary Inertia

Journal of Mechanicl Science and Technology, Vol. 19, No. 12, pp. 2197-2204, 2005

A High-speed Miniature Screening Gaschromatograph with Flame Ionization Detector

Rahul Banik*, Dong-Yeon Lee, Dae-Gab Gweon

Department of Mechanical Engineering, Korea Advanced Institute of Science and Technology (KAIST),

373-1, Kusung-Dong, Yusong-Gu, Daejeon, 305-701, South Korea

The combination of Gas chromatography (GC) for separation and Flame Ionization Detection (FID) for detection and identification of the components of a mixture of compounds is a fast and strongly proved method of analytic chemistry. The objective of this research was to design a combined High-speed miniature screening Gas chromatograph along with a Flame Ionization Detector for quick, quantitative and qualitative analysis of gas components. This combined GC-FID system is suitable to detect the volatile and semi-volatile hydrocarbons present in a gas mixture. The construction made it less expensive, easy to use and movable. The complete gas path was developed. On/off valves, temperature and flow sensors and their interface electronics were used for controlling purpose. A Microcontroller was programmed to measure the temperature and gas flow using the sensors and to control and regulate them using the electronics and valves. A pocket PC with its touch screen served as a user interface for the system. Software was developed for the pocket PC, which makes the communication possible with the Microcontroller. The system parameters can be indicated in the Pocket PC as simple text and also the analysis result can be displayed.

Keywords: Gaschromatograph, Flame Ionization Detector, Microcontroller, Pocket PC

Journal of Mechanicl Science and Technology, Vol. 19, No. 12, pp. 2205-2212, 2005

Estimation of the Cutting Torque without a Speed Sensor During CNC Turning

Won Tae Kwon*,

Dept. of Mech. and Info. Eng., Univ. of Seoul,

90 Cheonnong-dong Tongdaemun-gu, Seoul 130-743, Korea

Ik jun Hong

Dept. of Mech. and Info. Eng., Univ. of Seoul,

90 Cheonnong-dong Tongdaemun-gu, Seoul 130-743, Korea

In this paper, the cutting torque of a CNC machine tool during machining is monitored through the internet. To estimate the cutting torque precisely, the spindle driving system is divided into two parts: electrical induction motor part and mechanical part. A magnetized current is calculated from the measured three-phase stator currents and used for the total torque estimation generated by a spindle motor. Slip angular velocity is calculated from the magnetized current directly, which got rid of the necessity of a spindle speed sensor. Since the frictional torque changes according to the cutting torque and the spindle rotational speed, an experiment is adopted to obtain the frictional torque as a function of the cutting torque and the spindle rotation speed. Then the cutting torque can be calculated by solving a 2nd order difference equation at a given cutting condition. A graphical programming method is used to implement the torque monitoring system developed in this study to the computer and at the same time monitor the torque of the spindle motor in real time through the internet. The cutting torque of the CNC lathe is estimated well within an about 3% error range in average in various cutting conditions.

Keywords: Internet Torque Monitoring, Magnetized Spindle Motor Current, Mechanical Friction

Journal of Mechanicl Science and Technology, Vol. 19, No. 12, pp. 2213-2223, 2005

Automated Feature-Based Registration for Reverse Engineering of Human Models

Yongtae Jun*

Department of Mechanical Engineering/Bioengineering Research Center, Sejong University,

Gunja-dong, Gwangjin-gu, Seoul 143-747, Korea

Kuiwon Choi

Biomedical Research Center, Korea Institute of Science and Technology,

Hawolgok-dong, Seongbuk-gu, Seoul 136-791, Korea

In order to reconstruct a full 3D human model in reverse engineering (RE), a 3D scanner needs to be placed arbitrarily around the target model to capture all part of the scanned surface. Then, acquired multiple scans must be registered, and merged since each scanned data set taken from different position is just given in its own local co-ordinate system. The goal of the registration is to create a single model by aligning all individual scans. It usually consists of two sub-steps: rough and fine registration. The fine registration process can only be performed after an initial position is approximated through the rough registration. Hence an automated rough registration process is crucial to realize a completely automatic RE system. In this paper an automated rough registration method for aligning multiple scans of complex human face is presented. The proposed method automatically aligns the meshes of different scans with the information of features that are extracted from the estimated principal curvatures of triangular meshes of the human face. Then the roughly aligned scanned data sets are further precisely enhanced with a fine registration step with the recently popular Iterative Closest Point (ICP) algorithm. Some typical examples are presented and discussed to validate the proposed system.

Key Words: Reverse Engineering, Registration, Feature Extraction, Digital Human Model

Journal of Mechanicl Science and Technology, Vol. 19, No. 12, pp. 2224-2230, 2005

An Analytical Study on Prediction of Effective Elastic Constants of Perforated Plate

Jae-Kon Lee, Jin-Gon Kim*

1School of Mechanical and Automotive Engineering, Catholic University of Daegu,

Gyeongsansi, Gyeongbuk, 712-702, Korea

In this study, the validity of the Eshelby-type model for predicting the effective Young’s modulus and in-plane Poisson’s ratio of the 2-dimensional perforated plate has been investigated in terms of the porosity size and its arrangement. The predicted results by the Eshelby-type model are compared with those by finite element analysis. Whenever the ratio of the porosity size to the specimen size becomes smaller than 0.07, the effective elastic constants predicted by finite element analysis are convergent regardless of the arrangement of the porosities. Under these conditions, the effective Young’s moduli of the perforated plate can be predicted within the accuracy of 5% by the Eshelby-type model, which overestimates and underestimates the effective Poisson’s ratios by 10% and 6% for the plates with periodically and non-periodically arranged porosities, respectively

Keywords: Perforated Plate, Effective Elastic Constants, Eshelby Method, Finite Element Analysis, Porosity Size, Porosity Arrangement

Journal of Mechanicl Science and Technology, Vol. 19, No. 12, pp. 2231-2244, 2005

Boundary Method for Shape Design Sensitivity Analysis in Solving Free-Surface Flow Problems

Joo Ho Cho*

School of Aerospace and Mechanical Engineering, Hankuk Aviation University,

200-1 Hwajon-Dong, Dukyang-Ku, Goyang-City, Gyunggi-Do 412-791, Korea

H. G. Kwak

Department of Aerospace and Mechanical Engineering, Hankuk Aviation University,

200-1 Hwajon-Dong, Dukyang-Ku, Goyang-City, Gyunggi-Do 412-791, Korea

R. V. Grandhi

Department of Mechanical and Materials Engineering, Wright State University,

3640 Colonel Glenn Highway, Dayton, OH, 45435, USA

An efficient boundary-based optimization technique is applied in the numerical computation of free surface flow problems, by reformulating them into the equivalent optimal shape design problems. While the sensitivity in the boundary method has mainly been calculated using the boundary element method (BEM) as an analysis means, the finite element method (FEM) is used in this study because of its popularity and easy-to-use features. The advantage of boundary method is that the design velocity vectors are needed only on the boundary, not over the whole domain. As such, a determination of the complicated domain design velocity field, which is necessary in the domain method, is eliminated, thereby making the process easy to implement and efficient. Seepage and supercavitating flow problem are chosen to illustrate the accuracy and effectiveness of the proposed method.

Key words : Boundary Method, Shape Design Sensitivity Analysis, Shape Optimization, Free Surface Flow, Seepage, Supercavitation

Journal of Mechanicl Science and Technology, Vol. 19, No. 12, pp. 2245-2252, 2005

A Numerical Analysis on Thermal Stratification Phenomenon by In-Leakage in a Branch Piping

Jong-Il Park*

Department of Building System Engineering, Dong-Eui University,

995, Eomgwang-No, Busanjin-Gu, Busan, 614-714, Korea

Thermal stratification in the branch piping of power plants can be generated by turbulent penetration or by valve leakage. In this study, a numerical analysis was performed to estimate the thermal stratification phenomenon by in-leakage in the SIS branch piping of nuclear power plant. Leakage rate, leakage area and leakage location were selected as evaluation factors to investigate the thermal stratification effect. As a result of the thermal stratification effect according to leakage rate, the maximum temperature difference between top and bottom of the horizontal piping was evaluated to be about 185K when the valve leakage rate was about 10 times as much as the allowed leakage rate. For leakage rate more than 10 times the allowed leakage rate, the temperature difference was rapidly decreased due to the increased mixing effect. In the result according to leakage area, the magnitude of temperature difference was shown in order of 3%, 1% and 5% leakage area of the total disk area. In the thermal stratification effect, according to the leakage location, temperature difference when leakage occurred in the lower disk was considerably higher than that of when leakage occurred in the upper disk.

Key Words : Piping, Thermal Stratification Phenomenon, Numerical Analysis

Journal of Mechanicl Science and Technology, Vol. 19, No. 12, pp. 2253-2262, 2005

A Study on the Mixture Formation Process of Diesel Fuel Spray in Unsteady and Evaporative Field

Jeongkuk Yeom, Jongsang Park, Sungsik Chung*

Department of Mechanical Engineering, Dong-A University, Busan 604-714, Korea

The focus of this work is placed on the analysis of the mixture formation mechanism under the evaporative diesel spray of impinging and free conditions. As an experimental parameter, ambient gas density was selected. Effects of density variation of ambient gas on liquid and vapor-phase inside structure of evaporation diesel spray were investigated. Ambient gas density was changed between ra=5.0 kg/m3 and 12.3 kg/m3. In the case of impinging spray, the spray spreading to the radial direction is larger due to the decrease of drag force of ambient gas in the case of the low density than that of the high density. On the other hand, in the case of free spray, in accordance with the increase in the ambient gas density, the liquid-phase length is getting short due to the increase in drag force of ambient gas. In order to examine the homogeneity of mixture consisted of vapor-phase fuel and ambient gas in the spray, image analysis was conducted with statistical thermodynamics based on the non-dimensional entropy (S) method. In the case of application of entropy analysis to diesel spray, the entropy value always increases. The entropy of higher ambient density is higher than that of lower ambient gas density during initial injection period.

Key Words : Mixture Formation, Diesel Impinging and Free Spray, Phase Change, Exciplex Fluorescence Method

Journal of Mechanicl Science and Technology, Vol. 19, No. 12, pp. 2263-2269, 2005

Numerical Study on Characteristics of Ship Wave According to Shape of Waterway Section

Chun-Beom Hong*

Marine Research Institute, Samsung Heavy Industries Co., Daejeon 305-380, Korea

Sang-Min Lee

Research Institute of Maritime Industry, Korea Maritime University, Pusan 606-791, Korea

The ship wave phenomena in the restricted waterway were investigated by a numerical analysis. The Euler and continuity equations were employed for the present study. The boundary fitted and moving grid system was adopted to enhance the computational efficiency. The convective terms in the governing equations and the kinematic free surface boundary condition were solved by the Constrained Interpolated Profile (CIP) algorithm in order to solve accurately wave heights in far field as well as near field. The advantage of the CIP method was verified by the comparison of the computed results by the CIP and the Maker and Cell (MAC) method. The free surface flow simulation around Wigley hull was performed and compared with the experiment for the sake of the validation of the numerical method. The present numerical scheme was applied to the free surface simulation for various canal sections in order to understand the effect of the sectional shape of waterways on the ship waves. The wave heights on the side wall and the shape of the wave patterns with their characteristics of flow are discussed.

Key Words : Ship Wave, Shallow Water, Waterway, Constrained Interpolated Profile (CIP) Algorithm

Journal of Mechanicl Science and Technology, Vol. 19, No. 12, pp. 2270-2280, 2005

An Experimental Study on Swirling Flow behind a Round Cylinder in the Horizontal Circular Tube

Tae-Hyun Chang*

Division of Mechanical and Automation Engineering, Kyungnam University,

449 Wolyoung Dong, Masan, Kyungnam, Korea.

Hae Soo Lee

Department of Mechanical Engineering, Kyungnam University, Graduate School,

449 Wolyoung Dong, Masan, Kyungnam, Korea.

An experimental study is performed for turbulent swirling flow behind a circular cylinder  using 2-D PIV technique. The Reynolds number investigated are 10,000, 15,000, 20,000 and 25,000. The mean velocity vector, time mean axial velocity, turbulence intensity, kinetic energy and Reynolds shear stress behind the cylinder are measured before and behind the round cylinder along the test tube. A comparison is included with non swirl flow behind a circular and square cylinder. The recirculation zones are showed asymmetric profiles.

Key Words : Wake, PIV, Swirling Flow, Recirculating Region

Journal of Mechanicl Science and Technology, Vol. 19, No. 12, pp. 2281-2288, 2005

An Analysis on Structure of Impinging and Free Diesel Spray with Exciplex Fluorescence Method in

High Temperature and Pressure Field

Jeongkuk Yeom*, Jongsang Park, Sungsik Chung*

Department of Mechanical Engineering, Dong-A University, Busan 604-714, Korea

Because an injected spray development process consists of impinging and free spray in the diesel engine, it is needed to analyze the impinging spray and free spray, simultaneously, in order to study the diesel spray behavior. To dominate combustion characteristics in diesel engine is interaction between injected fuel and ambient gas, that is, process of mixture formation. Also it is very important to analyze liquid and vapor phases of injected fuel on the investigation of mixing process, respectively and simultaneously. Therefore, in this study, the behavior characteristics of the liquid phase and the vapor phase of diesel spray was studied by using exciplex fluorescence method in high temperature and injection pressure field. Finally, it can be confirmed that the distribution of vapor concentration is more uniform in the case of the high injection than in that of the low injection pressure.

Key Words : Diesel Engine, Impinging and Free Diesel Spray, Exciplex Fluorescence Method, ECD-U2

Journal of Mechanicl Science and Technology, Vol. 19, No. 12, pp. 2289-2295, 2005

Flow Pattern and Pressure Drop of Pure Refrigerants and Their Mixture in Horizontal Tube

Tae Woo Lim*

Division of Marine System Engineering, Korea Maritime University, 1 Dongsam-dong, Yeongdo-Gu, Busan 606-791, Korea

Two-Phase flow pattern and pressure drop data were obtained for pure refrigerants R134a and R123 and their mixtures as test fluids in a horizontal tube. The flow pattern is observed through tubular sight glasses located at inlet and outlet of the test section. The flow map of Baker developed for air-water two-phase flow at atmospheric pressure failed to predict the observed flow patterns at the higher value of the mass velocity used in the present study. The map of Kattan et al. predicted the data well over the entire region of mass velocity selected in the present study. The measured pressure drop increased with an increase in vapor quality and mass velocity. A new two-phase multiplier was developed from a dimensional analysis of the frictional pressure drop data measured in the present experiment. This new multiplier was found successfully to correlate the frictional pressure drop.

Key Words : Flow Pattern map, Pressure Drop, Multiplier

Journal of Mechanicl Science and Technology, Vol. 19, No. 12, pp. 2296-2302, 2005

A Comparison of the Heat Transfer Performance

of Thermosyphon Using a Straight Groove and a Helical Groove

Kyuil Han

School of Mechanical Engineering, Pukyong National University,

San 100, Yongdang-dong, Nam-ku, Pusan, 608-739, Korea

Dong-Hyun, Cho*

Department of Mechanical Design Engineering, Daejin University,

San #11-1, Sundan-dong, Pochun-city, Kyonggi-do, 487-711, Korea

This study is focused on the comparison of heat transfer performance of two thermosyphons having 60 straight and helical internal grooves. Distilled water has been used as working fluid. Liquid fill charge ratio defined by the ratio of working fluid volume to total internal volume of thermosyphon, the inclination angle and operating temperature were used as experimental parameters. The heat flux and heat transfer coefficient are estimated from experimental results. The conclusions of this study may be summarized as follows; Liquid fill charge ratio, inclination angle and geometric shape of grooves were very important factors for the operation of thermosyphon. The optimum liquid fill charge ratio for the best heat flux were 30%. The heat transfer performance of helically grooved tube was higher than that of straight grooved tube in low inclination angle(less than 30˚), but the results were opposite in high inclination angle(more than 30˚). As far as optimum inclination angle concerns, range of 25˚ ~ 30˚ for a helically grooved tube and about 40˚ for a straight grooved tube are suggested angles for the best results.

Key Words : Thermosyphon, Internal Groove, Liquid Fill Charge Ratio, Heat Flux, Operating Temperature,Condensation, Evaporation

Journal of Mechanicl Science and Technology, Vol. 19, No. 12, pp. 2303-2311, 2005

Temperature Characteristics of Cascade Refrigeration System by Pressure Adjustment

Han-Shik Chung, Hyo-Min Jeong*

1School of Mechanical and Aerospace Engineering, the Institute of Marine Industry,

Gyeongsang National University, 445 Inpyeong-dong, Gyeongsang-namdo 650-160, Korea

Yeong-Geun Kim, Lubi Rahadiyan

2Graduate School, Department of Mechanical and Precision Engineering,

Gyeongsang National University, 445 Inpyeong-dong, Gyeongsang-namdo 650-160, Korea

Super low temperature has many applications nowadays, from the chemical processing, automotives manufacturing, plastic recycling, etc. Considering of its wide application in the present and the future, study of the super-low temperature refrigeration system should be actively carried out. Super low state temperature can be achieved by using multi-stage refrigeration system. This paper present the development and testing of cascade refrigerator system for achieving super-low temperature. On this experiment, two different types of HCFCs refrigerants are utilized, R-22 and R-23 were applied for the high stage and the low-pressure stage respectively. The lowest temperature in the low-pressure evaporator that can be achieved by this cascade refrigeration system is down to -85℃. This experiment is aimed to study the effect of inlet pressure of the low-pressure stage evaporator and low-pressure stage compressors inlet pressure characteristics to the overall temperature characteristics of cascade refrigeration system.

Key Words : Cascade Refrigerator system, High Pressure Stage, Low Pressure Stage, Variable Expansion Valve

Journal of Mechanicl Science and Technology, Vol. 19, No. 12, pp. 2312-2320, 2005

Computations of Droplet Impingement on Airfoils in Two-Phase Flow

Sang Dug Kim*, Dong Joo Song

School of Mechanical Engineering, Yeungnam University,

214-1, Dae-dong, Gyeongsan-si, Gyeongsangbuk-do, Korea 712-749

The aerodynamic effects of leading-edge accretion can raise important safety concerns since the formulation of ice causes severe degradation in aerodynamic performance as compared with the clean airfoil. The objective of this study is to develop a numerical simulation strategy for predicting the particle trajectory around an MS-0317 airfoil in the test section of the NASA Glenn Icing Research Tunnel and to investigate the impingement characteristics of droplets on the airfoil surface. In particular, predictions of the mean velocity and turbulence diffusion using turbulent flow solver and Continuous Random Walk method were desired throughout this flow domain in order to investigate droplet dispersion. The collection efficiency distributions over the airfoil surface in simulations with different numbers of droplets, various integration time-steps and particle sizes were compared with experimental data. The large droplet impingement data indicated the trends in impingement characteristics with respect to particle size; the maximum collection efficiency located at the upper surface near the leading edge, and the maximum value and total collection efficiency were increased as the particle size was increased. The extent of the area impinged on by particles also increased with the increment of the particle size, which is similar as compared with experimental data.

Key Words : Two-Phase Flow, Particle Trajectory Simulation, Leading-Edge Accretion, Continuous Random Walk Model

Journal of Mechanicl Science and Technology, Vol. 19, No. 12, pp. 2321-2329, 2005

A study on the Engine Downsizing Using Mechanical Supercharger

Jae-Il Bae*

Graduate School, Department of Mechanical Engineering, Dankook University,

San 8 Hannam-dong, Yongsan-gu, Seoul 140-714, Korea

Sin-Chul Bae

Department of Mechanical Engineering, Dankook University,

San 8 Hannam-dong, Youngsan-gu, Seoul 140-714, Korea

One means of fulfilling CO2 emission legislation is to downsize engines by boosting their power using turbochargers or mechanical superchargers.  This reduces fuel consumption by decreasing the engine displacement.  When a turbocharger, which is preferable to a mechanical supercharger in terms of fuel efficiency, is used, there is insufficient availability of exhaust gas energy at low engine speeds, resulting in an unfavorable engine response.  Therefore, mechanically driven superchargers have increased in popularity due to their quick response to changing speeds in the transient phase.  However, since a mechanical supercharger obtains its driving power from the engine, it is difficult to decrease its fuel consumption.  This remains a large negative factor for superchargers, despite their excellent dynamic performance.  This study aims to develop a power control concept to improve the fuel economy of a mechanical screw supercharger, which could then be used for engine downsizing.

Keywords:  Screw Supercharger, Inlet Throttle Body, External Bypass Valve, Internal Bypass Valve